PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® DPB1

Prod. No:	101.311.24/24u

101.311-04/04u

Lot No:    	29F

Expiry Date:    	2010-October-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 48 primer mixes used for DPB1 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified DPB1 alleles |
| --- | --- | --- | --- |
| 13 | 245 bp | 515 bp | 010101-010103, 030101-030102, 0502, 0902, 1301, 1302, 1402, 1702, 2102, 2501, 260101-260102, 2901, 3701, 4401, 5001, 5201, 5601, 6101N, 7801, 7901, 8801, 9001, 9201 |
| 23 | 220 bp | 515 bp | 010101-010103, 030101-030102, 0502, 1402, 1702, 1801, 200101-200102, 2102, 2501, 260101-260102, 2701, 3601, 5001, 5201, 5601, 6101N, 7801, 7901, 8501, 8701, 8901, 9001, 9201 |
| 33,4,5 | 100 bp | 430 bp | 010101-010103, 0302, 040101-040102, 0902, 110101-110102, 1301, 1302, 1501, 2002, 2102, 260101-260102, 2701, 3101, 3301, 3901, 4001, 5601, 6501, 6601, 7201, 7401, 8501, 8901, 9001, 9601, 9901 |
| 43,4 | 140 bp | 430 bp | 010101-010103, 0302, 040101-040102, 2102, 2401, 260101-260102, 2701, 2801, 3101, 3901, 4001, 4901, 5101, 5301, 5601, 6501, 6601, 7201, 7601, 8501, 8901, 9001, 9201, 9601, 9901 |
| 5 | 235 bp | 515 bp | 010101-010103, 0801, 0802, 1901, 2102, 5001, 5701, 6501, 6801, 7301, 7501, 8401, 9001 |
| 6 | 165 bp | 430 bp | 010101-010103, 0902, 1301, 2102, 260101-260102, 6501 |
| 7 | 160 bp | 430 bp | 010101-010103, 0902, 1301, 1302, 2102, 260101-260102, 5601, 6501, 7601, 9001, 9201 |
| 8 | 210 bp | 515 bp | 0102, 020102-020106, 0202, 0203, 040101-040102, 0402, 0403, 0501, 0602, 0801, 0802, 1502, 1601, 1802, 1901, 1902, 2201, 2301, 2401, 3201, 3301, 3801, 3901, 4001, 4601, 4701, 4801, 4901, 5101, 5301, 6001, 6201, 6301, 6501, 6801, 7101, 7501, 7701, 8001, 8101, 8201, 8401, 9401, 9601, 9701, 9901 |
| 93 | 165 bp | 430 bp | 0102, 020102-020105, 020106weakly, 0202, 0203, 0402, 0403, 0501, 0601, 0602, 0802, 1002, 1102, 1502, 1601, 1602, 1701, 1801, 1802, 1901, 1902, 200101-200102, 2101, 2201, 2301, 3001, 3201, 3401, 3601, 3801, 410101-410102, 4601, 4701, 4801, 5501, 5801, 5901, 6001, 6201, 6301, 6401N, 6901, 7101, 7701, 8001, 8201, 8301, 8601, 8701, 9101, 9301, 9401, 9501, 9701, 9801 |
| 10 | 220 bp | 515 bp | 020102-020106, 0202, 0203, 0403, 0801, 0802, 1601, 1802, 1901, 2201, 3201, 3301, 410101-410102, 4601, 4701, 4801, 7101, 8101, 9501 |
| 11 | 190 bp | 515 bp | 020102-020106, 040101-040102, 0402, 0602, 1002, 1102, 1602, 1802, 2301, 2401, 3201, 3301, 410101-410102, 4601, 4701, 5101, 5901, 6001, 6601, 7101, 7201, 7301, 7501, 7701, 8001, 8101, 8201, 8301, 8601, 9401, 9901 |
| 123,4 | 80 bp | 515 bp | 020102, 020103weakly, 020104-020106, 0601, 0801, 0901, 1001, 1102, 1601, 1602, 1701, 1802, 2901, 3201, 3701, 410101-410102, 4401, 4601, 4801, 6401N, 8101, 8601, 8801, 9301 |
| 13 | 180 bp | 430 bp | 0102, 0202, 0203, 0501, 0802, 1901, 2201, 2401, 3801, 4701, 9701 |
| 144 | 105 bp | 430 bp | 0102, 0202, 0203, 0501, 1702, 2101, 2201, 3601, 3801, 9701 |
| 15 | 200 bp | 430 bp | 0102, 0202, 0203, 1502, 1902, 4801, 9501, 9901 |
| 163,4 | 80 bp | 430 bp | 030101-030102, 0402, 0502, 0602, 1002, 1401, 1402, 1801, 1902, 200101-200102, 2501, 2801, 3501, 4501, 4901, 5001, 5101, 5301, 5701, 5901, 6001, 6101N, 6801, 7001, 7301, 7501, 7601, 7701, 7801, 7901, 8001, 8201, 8301, 9101, 9201, 9801 |
| 17 | 260 bp | 515 bp | 030101-030102, 0502, 0601, 0901, 0902, 1001, 110101-110102, 1301, 1302, 1401, 1402, 1701, 1702, 200101-200102, 2101, 2501, 260101-260102, 2701, 2901, 3001, 3501, 3601, 3701, 4401, 4501, 5201, 5401, 5501, 5601, 5801, 6101N, 6401N, 6701, 6901, 7001, 7601, 7801, 7901, 8501, 8701, 8801, 9101, 9201, 9301, 9801 |
| 18 | 180 bp | 430 bp | 030101-030102, 0502, 0601, 0901, 1401, 1402, 1701, 200101-200102, 2901, 3501, 4401, 6101N, 6401N, 6901, 7001, 7601, 7801, 8601, 8801, 9101, 9201, 9801 |
| 19 | 200 bp | 430 bp | 030101-030102, 0502, 0601, 110101-110102, 1401, 1402, 1702, 200101-200102, 2501, 2901, 4401, 4501, 5201, 5601, 6101N, 6401N, 6701, 6901, 7001, 7401, 7601, 7801, 8701, 9101, 9201 |
| 20 | 235 bp | 515 bp | 030101-030102, 0502, 0901, 0902, 1001, 1301, 1302, 1401, 1402, 1702, 2501, 260101-260102, 2901, 3501, 3701, 4401, 4501, 5201, 5401, 5601, 6101N, 6701, 7001, 7601, 7801, 7901, 8801, 9201 |
| 213,4 | 100 bp | 430 bp | 030101-030102, 0502, 0901, 1401, 1402, 2901, 3501, 4401, 5001, 5701, 6101N, 7001, 7601, 7801, 8801, 9201 |
| 223 | 185 bp | 430 bp | 040101-040102, 2002, 2401, 3301, 3901, 4901, 5101, 6601, 7201, 8101, 9601, 9901 |
| 234 | 145 bp | 430 bp | 0102, 0501, 1502, 1702, 1902, 3401, 3601, 3801, 6201, 6301, 9701 |
| 246 | 195, 265 bp | 515 bp | 0203, 0302, 0403, 0501, 0801, 0802, 1601, 1901, 2201, 3101, 3801, 5701, 6301, 6501, 6801, 8401, 9701 |
| 257 | 190, 265 bp | 515 bp | 0501, 1702, 2101, 2201, 3601, 3801, 4401, 5801, 6301, 7001, 9701 |
| 264 | 75 bp | 430 bp | 0601, 0901, 1701, 2901, 4401, 4601, 6401N, 8601, 8801 |
| 274 | 95 bp | 430 bp | 0601, 1002, 1701, 200101-200102, 4601, 6401N, 6901, 8001, 8601, 9101, 9801 |
| 28 | 200 bp | 515 bp | 0901, 0902, 1001, 1102, 1301, 1302, 1602, 1701, 2002, 2101, 260101-260102, 2701, 3001, 3501, 3601, 3701, 5401, 5501, 5801, 6601, 7901, 8501, 8601, 8801, 9301, 9801 |
| 29 | 220 bp | 515 bp | 0901, 1001, 1602, 1701, 3001, 5401, 5501, 5801, 8601 |
| 30 | 185 bp | 430 bp | 0901, 1401, 1701, 3501, 7601, 8601, 9101, 9801 |
| 314 | 120 bp | 430 bp | 010101-010103, 0302, 0403, 0501, 0801, 0802, 0902, 1001, 110101-110102, 1301, 1302, 1601, 1702, 1901, 2101, 2102, 2201, 2501, 260101-260102, 2701, 3001, 3101, 3601, 3701, 3801, 4501, 5201, 5401, 5501, 5601, 5801, 6301, 6501, 6701, 6801, 7901, 8401, 8501, 8701, 8901, 9001, 9301, 9701 |
| 324,8 | 75, 195 bp | 430 bp | 110101-110102, 7801 |
| 334 | 140 bp | 430 bp | 0902, 1301, 1302, 2002, 3301, 8101 |
| 34 | 210 bp | 515 bp | 1401, 4501, 6701, 7601, 9101 |
| 35 | 195 bp | 430 bp | 1501, 7401 |
| 36 | 260 bp | 515 bp | 1501, 1801, 2801, 3401, 4001, 5301, 6201 |
| 379 | 185, 255 bp | 515 bp | 0102?, 0203?, 0302?, 0402, 0403?, 0601?, 0801?, 1001-1102?, 1302?, 1402?, 1501, 1502-1802?, 1902-2701?, 2801, 290101-3901?, 4001, 410101-410102?, 4401-5201?, 5301, 5401-7301?, 7401, 7501-9901? |
| 384 | 100 bp | 515 bp | 0403, 1502, 2301, 3401, 5201, 5501, 5801, 6201, 6301, 6701, 7101, 8701, 9501 |
| 39 | 210 bp | 515 bp | 0302, 1002, 2801, 3101, 3401, 5701, 5901, 7201, 7301, 9501 |
| 404,10 | 95, 180 bp | 430 bp | 0102?, 0203?, 0302?, 0403?, 0601?, 0801?, 0902, 1001-1102?, 1302?, 1402?, 1502-1802?, 1902-2901?, 3001, 3101-410102?, 4401-5301?, 5401, 5501-9901? |
| 414,11 | 75, 230 bp | 515 bp | 3101, 3401, 7701, 9401 |
| 424,12 | 140, 185, 285 bp | 430 bp | 3201, 8201, 9701 |
| 434,13 | 65, 190 bp | 430 bp | 0102?, 0203?, 0302?, 0403?, 0501, 0502, 0601?, 0801?, 1001-1102?, 1302?, 1402?, 1502-1802?, 1901, 1902-3301?, 3401, 3501-410102?, 4401-6101N?, 6201, 6301-9901? |
| 4414 | 195, 245, 275 bp | 430 bp | 1402, 2102, 3801, 6401N |
| 454,15 | 120, 190, 245 bp | 430 bp | 1002, 1802, 2002, 3901, 4601, 4901, 8001, 8601, 9601 |
| 46 | 205 bp | 515 bp | 410101-410102, 6001, 8301, 9601 |
| 4716 | 165, 255 bp | 515 bp | 0102?, 020102-020106, 0202, 0203?, 0302?, 040101-040102, 0403?,0601?, 0602, 0801?, 0802, 1001-1102?, 1302?, 1402?, 1502-1802?, 1902-410102?, 4401, 4501-9901? |
| 4817 | 210, 280 bp | 515 bp | 6101N, 8501 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DPB1 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DPB1 typing. In addition, wells number 2, 5, 8, 10, 11, 12, 17, 20, 24, 25, 28, 29, 34, 36, 37, 38, 39, 41, 46, 47 and 48 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3Primer mixes 1, 2, 3, 4, 9, 12, 16, 21 and 22 may yield less specific PCR products than the other DPB1 primer mixes.

4Specific PCR fragments shorter than 150 base pairs are less intense and not as sharp as longer specific bands.

5Primer mix 3 may give rise to non-specific amplifications and primer dimer formation.

6Primer mix 24: Specific PCR fragment of 195 bp in the DPB1*0203 allele. Specific PCR fragment of 265 bp in the DPB1*0302, 0403, 0501, 0801, 0802, 1601, 1901, 2201, 3101, 3801, 5701, 6301, 6501, 6801, 8401 and 9701 alleles.

7Primer mix 25: Specific PCR fragment of 190 bp in the DPB1*0501, 1702, 2101, 2201, 3601, 3801, 4401, 5801, 6301 and 9701 alleles. Specific PCR fragment of 265 bp in the DPB1*7001 allele.

8Primer mix 32: Specific PCR fragment of 75 bp in the DPB1*7801 allele. Specific PCR fragment of 195 bp in the DBB1*110101-110102 alleles.

9Primer mix 37: Specific PCR fragment of 185 bp in the DPB1*1501, 2801, 5301, 4001 and 7401 alleles. Specific PCR fragment of 255 bp in the DPB1*0402 allele. The 3rd exon of many DPB1 alleles is not sequenced and thus the primer pair in primer mix 37 matching the DPB1*0402 sequence motif in the 3rd exon may amplify other DPB1 alleles.

10Primer mix 40: Specific PCR fragment of 95 bp in the DPB1*0902 allele. Specific PCR fragment of 180 bp in the DPB1*3001 and 5401 alleles. The 1st exon of most DPB1 alleles is not sequenced and thus the primer pair in primer mix 40 matching the DPB1*0902 sequence motif in the 1st exon may amplify other DPB1 alleles.

Primer mix 40 may give rise to nonspecific amplifications.

11Primermix 41: Specific PCR fragment of 75 bp in the DPB1*7701 allele. Specific PCR fragment of 230 bp in the DPB1*3101, 3401 and 9401 alleles.

12Primer mix 42: Specific PCR fragment of 140 bp in the DPB1*9701 allele. Specific PCR fragment of 185 bp in the DPB1*3201 allele. Specific PCR fragment of 285 bp in the DPB1*8201 allele.

13Primer mix 43: Specific PCR fragment of 65 bp in the DPB1*0501, 0502 and 1901 alleles. Specific PCR fragment of 190 bp in the DPB1*3401 and 6201 alleles. The 4th exon of most DPB1 alleles is not sequenced and thus the primer pair in primer mix 43 matching the DPB1*0501, 0502 and 1901 sequence motif in the 4th exon may amplify other DPB1 alleles.

14Primer mix 44: Specific PCR fragment of 195 bp in the DPB1*1402 and 2102  alleles. Specific PCR fragment of 245 in the DPB1*3801 allele. Specific PCR fragment of 275 bp in the DPB1*6401N allele.

15Primer mix 45: Specific PCR fragment of 120 bp in the DPB1*1002, 4601, 8001 and 8601 alleles. Specific PCR fragment of 190 bp in the DPB1*2002, 3901, 4901 and 9601 alleles. Specific PCR fragment of 245 bp in the DPB1*1802 allele.

16Primer mix 47: Specific PCR fragment of 165 bp in the DPB1*4401 allele. Specific PCR fragment of 255 bp in the DPB1*020102-0202, 040101-040102 , 0602 and 0802 alleles.

The 3rd exon of many DPB1 alleles is not sequenced and thus the primer pair in primer mix 47 matching the DPB1*0201, 0202, 0401, 0602 and 0802 sequence motif in the 3rd exon may amplify other DPB1 alleles.

17Primer mix 48: Specific PCR fragment of 210 bp in the DPB1*6101N allele. Specific PCR fragment of 280 bp in the DPB1*8501 allele.

‘?’, nucleotide sequence information not available for the primer matching sequence.

1The sequence of the DPB1*02011 allele has been shown to be identical to DPB1*02012. DPB1*0701 has never been assigned. DPB1*1201 has never been assigned.

The sequence of the DPB1*4201 allele has been shown to be identical to DPB1*3101. The sequence of the DPB1*4301 allele has been shown to be identical to DPB1*2801.

2Primer mix 24: Specific PCR fragment of 195 bp in the DPB1*0203 allele. Specific PCR fragment of 265 bp in the DPB1*0302, 0403, 0501, 0801, 0802, 1601, 1901, 2201, 3101, 3801, 5701, 6301, 6501, 6801, 8401 and 9701 alleles.

Primer mix 25: Specific PCR fragment of 190 bp in the DPB1*0501, 1702, 2101, 2201, 3601, 3801, 4401, 5801, 6301 and 9701 alleles. Specific PCR fragment of 265 bp in the DPB1*7001 allele.

Primer mix 32: Specific PCR fragment of 75 bp in the DPB1*7801 allele. Specific PCR fragment of 195 bp in the DBB1*110101-110102 alleles.

Primer mix 37: Specific PCR fragment of 185 bp in the DPB1*1501, 2801, 5301, 4001 and 7401 alleles. Specific PCR fragment of 255 bp in the DPB1*0402 allele. The 3rd exon of many DPB1 alleles is not sequenced and thus the primer pair in primer mix 47 matching the DPB1*0402 sequence motif in the 3rd exon may amplify other DPB1 alleles.

Primer mix 40: Specific PCR fragment of 95 bp in the DPB1*0902 allele. Specific PCR fragment of 180 bp in the DPB1*3001 and 5401 alleles. The 1st exon of most DPB1 alleles is not sequenced and thus the primer pair in primer mix 40 matching the DPB1*0902 sequence motif in the 1st exon may amplify other DPB1 alleles.

Primer mix 40 may give rise to nonspecific amplifications.

Primermix 41: Specific PCR fragment of 75 bp in the DPB1*7701 allele. Specific PCR fragment of 230 bp in the DPB1*3101, 3401 and 9401 alleles.

Primer mix 42: Specific PCR fragment of 140 bp in the DPB1*9701 allele. Specific PCR fragment of 185 bp in the DPB1*3201 allele. Specific PCR fragment of 285 bp in the DPB1*8201 allele.

Primer mix 43: Specific PCR fragment of 65 bp in the DPB1*0501, 0502 and 1901 alleles. Specific PCR fragment of 190 bp in the DPB1*3401 and 6201 alleles. The 4th exon of most DPB1 alleles is not sequenced and thus the primer pair in primer mix 43 matching the DPB1*0501, 0502 and 1901 sequence motif in the 4th exon may amplify other DPB1 alleles.

Primer mix 44: Specific PCR fragment of 195 bp in the DPB1*1402 and 2102  alleles. Specific PCR fragment of 245 in the DPB1*3801 allele. Specific PCR fragment of 275 bp in the DPB1*6401N allele.

Primer mix 45: Specific PCR fragment of 120 bp in the DPB1*1002, 4601, 8001 and 8601 alleles. Specific PCR fragment of 190 bp in the DPB1*2002, 3901, 4901 and 9601 alleles. Specific PCR fragment of 245 bp in the DPB1*1802 allele.

Primer mix 47: Specific PCR fragment of 165 bp in the DPB1*4401 allele. Specific PCR fragment of 255 bp in the DPB1*020102-0202, 040101-040102 , 0602 and 0802 alleles.

The 3rd exon of many DPB1 alleles is not sequenced and thus the primer pair in primer mix 47 matching the DPB1*0201, 0202, 0401, 0602 and 0802 sequence motif in the 3rd exon may amplify other DPB1 alleles.

Primer mix 48: Specific PCR fragment of 210 bp in the DPB1*6101N allele. Specific PCR fragment of 280 bp in the DPB1*8501 allele.

‘w’, might be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.