PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® DQ low resolution

Prod. No:	101.201-48/48u

101.201-12/12u

Lot No:    	11S

Expiry Date:    	2015-October-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 8 primer mixes used for DQ low resolution SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | DQ serology3 | Amplified DQB1 alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 225 bp | 515 bp | 5 | *05:01:01:01-05:18 |
| 26 | 220 bp, 270 bp | 430 bp | 1, 5, 6 | *06:01:01-06:52 |
| 3 | 210 bp | 430 bp | 2 | *02:01:01-02:07 |
| 4 | 220 bp | 515 bp | 3, 7 | *03:01:01:01-03:01:06, 03:04, 03:09-03:10, 03:13-03:14, 03:16, 03:19, 03:21-03:22, 03:24, 03:27-03:29, 03:35-03:36, 03:42, 03:44 |
| 55 | 130 bp | 515 bp | 6, 8 | *03:02:01-03:02:05, 03:05:01-03:05:04, 03:07-03:08, 03:11, 03:18, 03:32, 03:37, 06:29 |
| 65,7 | 135 bp | 515 bp | 2, 3, 9 | *02:03, 03:03:02:01-03:03:04, 03:06, 03:12, 03:15, 03:20, 03:25-03:26, 03:30-03:31, 03:33-03:34, 03:38-03:41, 03:43, 04:03:01-04:03:02, 06:51 |
| 75,6 | 145 bp, 185 bp | 515 bp | 3, 7, 8, 9 | *03:01:01:01-03:44 |
| 85 | 160 bp | 430 bp | 4 | *04:01:01-04:08 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DQ low resolution SSP typings.

When the primers in a primer mix can give rise to HLA-specific PCR products of more than one length this is indicated if the size difference is more than 20 base pairs. Size differences of 20 base pairs or less are not given. For high resolution SSP kits the respective lengths of the HLA-specific PCR product(s) are given for the alleles amplified by these primer mixes.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DQ low resolution typing.

In addition, wells number 4 to 7 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3The serological split of the DQB1*05:05 to 05:18, DQB1*06:06 to 06:07, 06:10, 06:13, 06:15 to 06:24 and 06:27 to 06:52, the DQB1*02:06 and 02:07 the DQB1*03:02:02-03:02:04, 03:03:03, 03:05:02,  03:07 to 03:09 and 03:11 to 03:44 and the DQB1*04:03 to 04:08 alleles is not known. The grouping of not serologically defined alleles is taken from the expert-assigned serological grouping in Tissue Antigens (2009) 73:95-170.

4For several DQB1 alleles 1st and/or 3rd exon(s) and beyond, as well as intron nucleotide sequences, are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in these regions are conserved within allelic groups.

5Primer mixes 5 to 8 may give a lower yield of HLA-specific PCR products than the other DQ low resolution primer mixes.

6The primer pair in well 2 and 7 will in some samples give rise to two HLA-specific PCR fragments.

7Primer mix 6 may have a tendency to giving rise to primer oligomer formation.

‘ser’, serological HLA specificity.

1The sequence of the DQB1*03031 allele has been shown to be identical to DQB1*03:03:02.

2The serological split of the DQB1*05:05 to 05:18, DQB1*06:06 to 06:07, 06:10, 06:13, 06:15 to 06:24 and 06:27 to 06:52, the DQB1*02:06 and 02:07 the DQB1*03:02:02-03:02:04, 03:03:03, 03:05:02,  03:07 to 03:09 and 03:11 to 03:44 and the DQB1*04:03 to 04:08 alleles is not known. The grouping of not serologically defined alleles is taken from the expert-assigned serological grouping in Tissue Antigens (2009) 73:95-170.

3The primer pairs in wells 2 and 7 will in some samples give rise to two HLA-specific PCR fragments.

‘ser’, serological HLA specificity.

Change in revision R01 compared to R00:

- The serological HLA specificities have been corrected in the Interpretation table.

Change in revision R02 compared to R01:

- Primer mix 6 may have a tendency to giving rise to primer oligomer formation. A footnote has been added in the Specificity Table.

Change in revision R03 compared to R02:

- Primer mixes 5, 6 and 7 may give a lower yield of HLA-specific PCR products than the other DQ low resolution primer mixes.  Footnotes have been added in the Specificity Table.