PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® DQB1 high resolution

for frequent alleles

Prod. No:	101.221-12 – including Taq pol.

101.221-12u– without Taq pol.

Lot No:    	43E

Expiry Date:    	2010-April-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ug/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 47 primer mixes used for DQB1 high resolution for frequent alleles SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified DQB1 alleles |
| --- | --- | --- | --- |
| 14 | 120 bp | 515 bp | 020101-0202, 0204, 0205 |
| 24 | 85 bp | 430 bp | 0203 |
| 3 | 145 bp | 515 bp | 020101-020102, 0204, 0205, 030101-030204, 030302-0321, 0401, 0402, 050101-0505, 060101-0634 |
| 45,6 | 140, 180 bp | 430 bp | 0202, 0203, 0205 |
| 57 | 145, 185 bp | 430 bp | 0204, 0505, 060202weakly |
| 63 | 165 bp | 515 bp | 030101-030104, 0304, 0309, 0313, 0316, 0319, 0321 |
| 73 | 220 bp | 515 bp | 030101-030104, 0304, 0309, 0310, 0313, 0314, 0316, 0319, 0321 |
| 83 | 135 bp | 515 bp | 020101-0202, 0204, 0205, 030201-030204, 0307, 0308, 0311, 0318, 0629 |
| 93,8 | 190, 220 bp | 515 bp | 020101-0205, 030201-030204, 030302-030303, 030501-0308, 0311, 0312, 0315, 0318-0320, 0401, 0402 |
| 10 | 135 bp | 430 bp | 0304, 0314 |
| 114,9 | 95, 130 bp | 430 bp | 030501-030504, 0317, 0320 |
| 124 | 125 bp | 430 bp | 0306, 0308, 060202, 060302 |
| 134,10 | 110, 140 bp | 430 bp | 0307, 0315, 0316 |
| 1411 | 135, 260 bp | 430 bp | 0309, 0311 |
| 153 | 135 bp | 430 bp | 0310, 0312, 0314, 060101-060103 |
| 163 | 260 bp | 515 bp | 030101-030104, 0304, 0309, 0310, 0312-0314, 0316, 0319, 0321 |
| 1712 | 165, 300 bp | 430 bp | 0313, 0634 |
| 185,13 | 190, 220 bp | 430 bp | 0318, 0628 |
| 19 | 135 bp | 515 bp | 030101-030204, 030302-0315, 0317-0321 |
| 20 | 130 bp | 430 bp | 030101-030102, 030104, 030302-030303, 0306, 0309, 0310, 0312, 0313, 0315, 0317, 0319-0321 |
| 21 | 205 bp | 515 bp | 0401 |
| 223 | 205 bp | 430 bp | 0402 |
| 23 | 135 bp | 430 bp | 050101-050102 |
| 244 | 120 bp | 430 bp | 050201-050202, 0505 |
| 254 | 95 bp | 515 bp | 050202-050302 |
| 264 | 120 bp | 430 bp | 0504 |
| 27 | 210 bp | 430 bp | 060101-060202, 060502?, 0606?, 0610-061102, 0613, 0616, 0618-0620, 0624, 0629, 0633 |
| 28 | 185 bp | 430 bp | 060201-060202, 0614-0616, 0619, 0620, 0623, 0624, 0633 |
| 29 | 130 bp | 430 bp | 060301-060302, 0607, 061102, 0614, 0626N, 0628, 0630-0632 |
| 30 | 160 bp | 430 bp | 060301-060302, 060402, 0607, 060801, 061101-061102, 0626N, 0628, 0630-0632 |
| 31 | 170 bp | 515 bp | 060301-060302, 060801-060802, 061102, 0612, 0614, 0621, 0626N, 0628, 0631 |
| 32 | 210 bp | 515 bp | 060401-060403, 0607, 0617, 0621, 0625, 0634 |
| 33 | 170 bp | 430 bp | 060401-0607, 0609, 0618, 0625, 0627, 0632, 0634 |
| 34 | 130 bp | 430 bp | 060401-060501, 0606, 060801-0609, 0612, 0617, 0618, 0621, 0627, 0634 |
| 35 | 260 bp | 515 bp | 060501, 060502?, 0606?, 0620, 0631 |
| 36 | 210 bp | 430 bp | 060501, 060502?, 0606?, 0609, 0612, 0615, 0622 |
| 37 | 180 bp | 430 bp | 0606 |
| 384,14 | 95, 185 bp | 430 bp | 0610, 0614 |
| 39 | 190 bp | 430 bp | 0613, 0616, 0622 |
| 404,15 | 110, 150 bp | 430 bp | 0321, 0623 |
| 415 | 175 bp | 430 bp | 0617, 0624, 0630 |
| 42 | 135 bp | 430 bp | 0610, 0625 |
| 4316 | 215, 265 bp | 515 bp | 0626N, 0633 |
| 44 | 160 bp | 430 bp | 060201-060202, 0610, 0613-0616, 0620, 0623, 0624, 0629, 0633 |
| 45 | 130 bp | 515 bp | 0607, 0615 |
| 4617 | 160, 210 bp | 515 bp | 060301-060302, 060801-060802, 0614, 0621, 0627, 0628, 0630-0632 |
| 473 | 155 bp | 430 bp | 0401, 0402, 0619 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DQB1 high resolution typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DQB1 high resolution for frequent alleles typing.

In addition, wells number 3, 6, 7, 8, 9, 16, 19, 21, 25, 31, 32, 35, 43, 45 and 46 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3Primer mixes 6, 7, 8, 9, 15, 16, 22 and 47 may yield less specific PCR products than the other DQB1 primer mixes.

4Specific PCR fragments shorter than 125 base pairs are less intense and not as sharp as longer specific bands.

5Primer mixes 4, 18 and 41 may give to rise to primer oligomer formation.

6Primer mix 4: Specific PCR fragment of 140 bp in the DQB1*0202 and 0203 alleles. Specific PCR fragment of 180 bp in the DQB1*0205 allele.

7Primer mix 5: Specific PCR fragment of 145 bp in the DQB1*0204 allele. Specific PCR fragment of 185 bp in the DQB1*0505 and 060202weakly alleles.

8Primer mix 9: Specific PCR fragment of 190 bp in DQB1*030501-030504, 0319 and the DQB1*0401-0402 alleles. Specific PCR fragment of 220 bp in the DQB1*0306-0308, 0311, 0312, 0315, 0318, 0320 and the DQB1*020201-0205 alleles. Specific PCR fragments of 190 and 220 bp (both specific PCR fragments may  not be obtained) in the DQB1*030201-030204 and DQB1*030302-030303 alleles.

9Primer mix 11: Specific PCR fragment of 95 bp in the DQB1*0320 allele. Specific PCR fragment of130 bp in the DQB1*030501-030504 and 0317 alleles.

10Primer mix 13: Specific PCR fragment of 110 bp in the DQB1*0315 allele. Specific PCR fragment of 140 bp in the DQB1*0307 and 0316 alleles.

11Primer mix 14: Specific PCR fragment of 135 bp in the DQB1*0309 allele. Specific PCR fragment of 260 bp in the DQB1*0311 allele.

12Primer mix 17: Specific PCR fragment of 165 bp in the DQB1*0313 allele. Specific PCR fragment of 300 bp in the DQB1*0634 allele.

13Primer mix 18: Specific PCR fragment of 190 bp in the DQB1*0628 allele. Specific PCR fragment of 220 bp in the DQB1*0318 allele.

14Primer mix 38: Specific PCR fragment of 95 bp in DQB1*0614 allele. Specific PCR fragment of 185 bp in the DQB1*0610 allele.

15Primer mix 40: Specific PCR fragment of 110 bp in the DQB1*0623 allele. Specific PCR fragment of 150 bp in the DQB1*0321 allele.

16Primer mix 43: Specific PCR fragment of 215 bp in the DQB1*0626N allele. Specific PCR fragment of 265 bp in the DQB1*0633 allele.

17Primer mix 46: Specific PCR fragment of 160 bp in the DQB1*060301-060302, 060801-060802, 0614, 0621, 0628 and 0630 to 0632 alleles. Specific PCR fragment of 210 bp in the DQB1*0627 allele.

‘?’, nucleotide sequence information not available for the primer matching sequence.

1The sequence of the DQB1*03031 allele has been shown to be identical to DQB1*030302.

2Primer mix 4: Specific PCR fragment of 140 bp in the DQB1*0202 and 0203 alleles. Specific PCR fragment of 180 bp in the DQB1*0205 allele.

Primer mix 5: Specific PCR fragment of 145 bp in the DQB1*0204 allele. Specific PCR fragment of 185 bp in the DQB1*0505 and 060202weakly alleles.

Primer mix 9: Specific PCR fragment of 190 bp in DQB1*030501-030504, 0319 and the DQB1*0401-0402 alleles. Specific PCR fragment of 220 bp in the DQB1*0306-0308, 0311, 0312, 0315, 0318, 0320 and the DQB1*020201-0205 alleles. Specific PCR fragments of 190 and 220 bp (both specific PCR fragments may  not be obtained) in the DQB1*030201-030204 and DQB1*030302-030303 alleles.

Primer mix 11: Specific PCR fragment of 95 bp in the DQB1*0320 allele. Specific PCR fragment of130 bp in the DQB1*030501-030504 and 0317 alleles.

Primer mix 13: Specific PCR fragment of 110 bp in the DQB1*0315 allele. Specific PCR fragment of 140 bp in the DQB1*0307 and 0316 alleles.

Primer mix 14: Specific PCR fragment of 135 bp in the DQB1*0309 allele. Specific PCR fragment of 260 bp in the DQB1*0311 allele.

Primer mix 17: Specific PCR fragment of 165 bp in the DQB1*0313 allele. Specific PCR fragment of 300 bp in the DQB1*0634 allele.

Primer mix 18: Specific PCR fragment of 190 bp in the DQB1*0628 allele. Specific PCR fragment of 220 bp in the DQB1*0318 allele.

Primer mix 38: Specific PCR fragment of 95 bp in DQB1*0614 allele. Specific PCR fragment of 185 bp in the DQB1*0610 allele.

Primer mix 40: Specific PCR fragment of 110 bp in the DQB1*0623 allele. Specific PCR fragment of 150 bp in the DQB1*0321 allele.

Primer mix 43: Specific PCR fragment of 215 bp in the DQB1*0626N allele. Specific PCR fragment of 265 bp in the DQB1*0633 allele.

Primer mix 46: Specific PCR fragment of 160 bp in the DQB1*060301-060302, 060801-060802, 0614, 0621, 0628 and 0630 to 0632 alleles. Specific PCR fragment of 210 bp in the DQB1*0627 allele.

‘w’, might be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.