PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® DQB1 high resolution

for frequent alleles

Prod. No:	101.221-12 – including Taq pol.

101.221-12u– without Taq pol.

Lot No:    	55R

Expiry Date:    	2015-June-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 63+1 primer mixes used for DQB1 high resolution for frequent alleles SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified DQB1 alleles3 |
| --- | --- | --- | --- |
| 14 | 120 bp | 515 bp | *02:01:01-02:02, 02:04-02:07 |
| 24 | 85 bp | 430 bp | *02:03 |
| 3 | 145 bp | 515 bp | *02:01:01-02:01:05, 02:04-02:05, 02:07, 03:01:01:01-03:23, 03:25-03:44, 04:01:01-04:08, 05:01:01:01-05:13, 05:15-05:16, 06:01:01-06:37, 06:39-06:50, 06:52 |
| 48 | 140 bp, 195 bp | 430 bp | *02:02-02:03, 02:06, 03:28 |
| 59 | 145 bp, 180 bp | 515 bp | *02:04, 05:06-05:07 |
| 65 | 165 bp | 515 bp | *03:01:01:01-03:01:06, 03:04, 03:09, 03:13, 03:16, 03:19, 03:21-03:22, 03:24, 03:27-03:29, 03:35-03:36, 03:42, 03:44 |
| 7 | 220 bp | 515 bp | *03:01:01:01-03:01:06, 03:04, 03:09-03:10, 03:13-03:14, 03:16, 03:19, 03:21-03:22, 03:24, 03:27-03:29, 03:35-03:36, 03:42, 03:44 |
| 8 | 135 bp | 515 bp | *02:01:01-02:02, 02:04-02:07, 03:02:01-03:02:05, 03:07-03:08, 03:11, 03:18, 03:32, 03:37, 06:29 |
| 96,10 | 175 bp, 220 bp | 515 bp | *02:01:01-02:07, 03:02:01-03:03:04, 03:05:01-03:08, 03:11-03:12, 03:13?-03:14?, 03:15, 03:16?-03:17?, 03:18-03:20, 03:23, 03:25-03:26, 03:30-03:34, 03:37-03:41, 03:43, 03:44?, 04:01:01-04:08 |
| 107 | 135 bp | 430 bp | *03:04, 03:14 |
| 114,11 | 95 bp, 130 bp | 430 bp | *03:05:01-03:05:04, 03:17, 03:20 |
| 124,12 | 65 bp, 115 bp, 135 bp | 430 bp | *03:06, 03:08, 03:25, 03:40, 06:02:02, 06:03:02 |
| 134,13 | 110 bp, 140 bp | 430 bp | *03:07, 03:15-03:16 |
| 1414 | 135 bp, 260 bp | 430 bp | *03:09, 03:11, 03:26 |
| 1515 | 135 bp, 250 bp | 430 bp | *03:10, 03:12, 03:14, 03:27, 06:01:01-06:01:06, 06:43 |
| 16 | 260 bp | 515 bp | *03:01:01:01-03:01:06, 03:04, 03:09-03:10, 03:12-03:14, 03:16, 03:19, 03:21-03:22, 03:24, 03:27-03:29, 03:35-03:36, 03:42, 03:44 |
| 174,6,16 | 110 bp, 165 bp, 195 bp, 300 bp | 430 bp | *03:13, 03:28, 06:23, 06:34 |
| 187, 17 | 130 bp, 190 bp, 220 bp | 430 bp | *03:18, 03:24, 06:28 |
| 19 | 135 bp | 515 bp | *03:01:01:01-03:15, 03:17-03:22, 03:24, 03:26-03:44 |
| 207 | 130 bp | 430 bp | *02:03, 03:01:01:01-03:01:02, 03:01:04-03:01:06, 03:03:02:01-03:03:04, 03:06, 03:09-03:10, 03:12-03:13, 03:15-03:17, 03:19-03:24, 03:26-03:31, 03:33-03:36, 03:38-03:44 |
| 217 | 205 bp | 515 bp | *04:01:01-04:01:02, 04:05-04:08 |
| 22 | 205 bp | 430 bp | *04:02:01-04:03:01, 04:04 |
| 23 | 135 bp | 430 bp | *05:01:01:01-05:01:03, 05:07, 05:11-05:12 |
| 244 | 120 bp | 430 bp | *05:02:01-05:02:03, 05:05, 05:14 |
| 254 | 95 bp | 515 bp | *05:02:02, 05:03:01:01-05:03:05, 05:06, 05:08-05:10, 05:13, 05:15-05:16 |
| 264,5 | 115 bp | 430 bp | *06:02:01-06:03:02, 06:05:01?-06:07:01?, 06:08:01?-06:08:02?, 06:10?-06:11:02?, 06:13?-06:33?, 06:35?, 06:37?, 06:39, 06:40?, 06:44, 06:45?-06:46?, 06:47, 06:48?-06:50? |
| 27 | 210 bp | 430 bp | *06:01:01-06:02:02, 06:05:02?-06:06?, 06:10-06:11:02, 06:13, 06:16, 06:18-06:20, 06:24, 06:29, 06:33, 06:35, 06:37, 06:43, 06:45, 06:47-06:50 |
| 28 | 185 bp | 430 bp | *06:02:01-06:02:02, 06:14:01-06:16, 06:19-06:20, 06:23-06:24, 06:33, 06:37, 06:46-06:50 |
| 29 | 130 bp | 430 bp | *06:03:01-06:03:02, 06:07:01-06:07:02, 06:11:02, 06:14:01, 06:26N, 06:28, 06:30-06:32, 06:40-06:41, 06:44 |
| 305,18 | 160 bp, 245 bp | 430 bp | *03:06, 03:23, 03:25, 04:04-04:05, 06:03:01-06:03:02, 06:04:02, 06:07:01, 06:08:01, 06:11:01-06:11:02, 06:26N, 06:28, 06:30-06:32, 06:40-06:41, 06:44 |
| 31 | 170 bp | 515 bp | *06:03:01-06:03:02, 06:08:01-06:08:02, 06:11:02-06:12, 06:14:01, 06:21, 06:26N, 06:28, 06:31, 06:40-06:41, 06:44 |
| 32 | 210 bp | 515 bp | *06:04:01-06:04:03, 06:07:01-06:07:02, 06:17, 06:21, 06:25, 06:34, 06:36, 06:38-06:39, 06:52 |
| 337 | 170 bp | 430 bp | *06:04:01-06:05:02, 06:06w, 06:07:01-06:07:02, 06:09, 06:18, 06:25, 06:27, 06:32, 06:34, 06:36, 06:38-06:39, 06:52 |
| 344,19 | 95 bp, 130 bp | 430 bp | *05:07, 06:04:01-06:05:01, 06:06, 06:08:01-06:09, 06:12, 06:17-06:18, 06:21, 06:27, 06:34, 06:36, 06:38-06:39, 06:42, 06:52 |
| 357,20 | 160 bp, 255 bp | 515 bp | *03:27, 03:31, 06:05:01, 06:05:02?-06:06?, 06:20, 06:31, 06:35, 06:45 |
| 367 | 210 bp | 430 bp | *06:05:01, 06:05:02?-06:06?, 06:09, 06:12, 06:15, 06:22, 06:42, 06:46 |
| 375 | 180 bp | 430 bp | *06:06 |
| 384,6,21 | 100 bp, 130 bp, 185 bp | 430 bp | *03:01:04, 05:04, 05:08, 06:10, 06:14:01-06:14:02 |
| 397 | 180 bp | 430 bp | *03:29-03:30, 06:13, 06:16, 06:22, 06:29 |
| 404,22 | 95 bp, 150 bp | 430 bp | *03:21, 06:40 |
| 416,23 | 185 bp, 205 bp, 300 bp | 430 bp | *03:22, 06:17, 06:24, 06:30, 06:38, 06:42, 06:52 |
| 424,6,24 | 100 bp, 135 bp, 195 bp | 515 bp | *03:06, 03:25, 03:41, 04:03:01-04:03:02, 04:06, 06:10, 06:25 |
| 434,6,25 | 110 bp, 155 bp, 185 bp, 215 bp, 250 bp | 515 bp | *02:05, 06:26N, 06:33, 06:37 |
| 444,26 | 110 bp, 160 bp | 430 bp | *03:42, 06:02:01-06:02:02, 06:10, 06:13-06:16, 06:20, 06:23-06:24, 06:29, 06:33, 06:37, 06:46-06:50 |
| 45 | 130 bp | 515 bp | *06:07:01-06:07:02, 06:15, 06:36, 06:46 |
| 4627 | 160 bp, 210 bp | 515 bp | *06:03:01-06:03:02, 06:08:01-06:08:02, 06:14:01-06:14:02, 06:21, 06:27-06:28, 06:30-06:32, 06:40-06:41, 06:44 |
| 474,5,28 | 110 bp, 155 bp | 430 bp | *03:30, 03:42, 04:01:01-04:03:02, 04:06-04:08, 06:19 |
| 48 | 165 bp | 430 bp | *03:32, 03:43, 04:07 |
| 494,29 | 110 bp, 155 bp | 430 bp | *03:33, 03:35, 05:14 |
| 5030 | 200 bp, 240 bp | 430 bp | *03:34, 03:37-03:38 |
| 514,31 | 125 bp, 245 bp | 430 bp | *02:06, 03:24, 03:36, 03:39 |
| 524 | 95 bp | 430 bp | *03:06?-03:08?, 03:11?-03:18?, 03:19, 03:20?, 03:23?, 03:26?, 03:37?, 03:40?, 03:44?, 04:08 |
| 53 | 190 bp | 430 bp | *05:09 |
| 54 | 190 bp | 430 bp | *05:10, 05:12 |
| 554,5 | 115 bp | 515 bp | *06:04:01-06:04:03, 06:05:01?-06:07:01?, 06:07:02, 06:08:01?-06:08:02?, 06:09, 06:10?-06:11:02?, 06:12, 06:13?-06:33?, 06:34, 06:35?, 06:36, 06:37?, 06:38, 06:40?, 06:41-06:42, 06:45?-06:46?, 06:48?-06:50?, 06:52 |
| 564,33 | 100 bp, 220 bp | 430 bp | *06:43-06:44, 06:47 |
| 575 | 185 bp | 430 bp | *02:07, 03:01:01:01-03:01:06, 03:04, 03:06?-03:08?, 03:09-03:10, 03:11?-03:18?, 03:20?, 03:21-03:22, 03:23?, 03:24, 03:26?, 03:27-03:29, 03:33?-03:34?, 03:35-03:36, 03:37?, 03:40?, 03:42, 03:44? |
| 58 | 185 bp | 430 bp | *05:05, 05:11 |
| 594,5 | 95 bp | 430 bp | *03:44, 05:13 |
| 60 | 190 bp | 430 bp | *05:15 |
| 61 | 200 bp | 430 bp | *05:16 |
| 62 | 225 bp | 430 bp | *03:30, 06:05:02, 06:15, 06:22, 06:37, 06:48 |
| 63 | 180 bp | 430 bp | *06:50 |
| 6434 | Neg. Control | - | - |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DQB1 high resolution typings.

When the primers in a primer mix can give rise to HLA-specific PCR products of more than one length this is indicated if the size difference is more than 20 base pairs. Size differences of 20 base pairs or less are not given. For high resolution SSP kits the respective lengths of the HLA-specific PCR product(s) are given for the alleles amplified by these primer mixes.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DQB1 high resolution for frequent alleles typing.

In addition, wells number 3, 5 to 9, 16, 19, 21, 25, 31, 32, 35, 42, 43, 45, 46 and 55 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several DQB1 alleles 1st and/or 3rd exon(s) and beyond, as well as intron nucleotide sequences, are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in these regions are conserved within allelic groups.

4HLA-specific PCR products shorter than 125 base pairs have a lower intensity and are less sharp than longer PCR products.

5Primer mixes 6, 26, 30, 37, 47, 55, 57 and 59 may give rise to a lower yield of HLA-specific PCR product than the other DQB1 primer mixes, most pronounced in primer mix 26.

6Primer mixes 9, 17, 38, 41, 42 and 43 have a tendency to giving rise to primer oligomer formation.

7Primer mixes 10, 18, 20, 21, 33, 35, 36 and 39 may have tendencies of unspecific amplifications.

8Primer mix 4: Specific PCR fragment of 140 bp in the DQB1*02:02-02:03 and 02:06 alleles. Specific PCR fragment of 195 bp in the DQB1 *03:28 allele.

9Primer mix 5: Specific PCR fragment of 145 bp in the DQB1*02:04 allele. Specific PCR fragment of 180 bp in the DQB1*05:06-05:07 alleles.

10Primer mix 9: Specific PCR fragment of 175 bp in DQB1*03:05:01-03:05:04, 03:13?-03:14?, 03:16?-03:17?, 03:19, 03:44?, 04:01:01-04:02 and 04:04-04:08 alleles. Specific PCR fragment of 220 bp in the DQB1*02:01:01-02:07 alleles. Specific PCR fragments of 175 and 220 bp in the DQB1*03:02:01-03:03:04, 03:06-03:08, 03:11-03:12, 03:15, 03:18, 03:20, 03:23, 03:25-03:26, 03:30-03:34, 03:37-03:41, 03:43 and 04:03:01-04:03:02 alleles. Both specific PCR fragments may  not be obtained.

11Primer mix 11: Specific PCR fragment of 95 bp in the DQB1*03:20 allele. Specific PCR fragment of 130 bp in the DQB1*03:05:01-03:05:04 and 03:17 alleles.

12Primer mix 12: Specific PCR fragment of 65 bp in the DQB1*03:40 allele. Specific PCR fragment of 115 bp in the DQB1*03:06 and 03:25 alleles. Specific PCR fragment of 135 bp in the DQB1*03:08, 06:02:02 and 06:03:02 alleles.

13Primer mix 13: Specific PCR fragment of 110 bp in the DQB1*03:15 allele. Specific PCR fragment of 140 bp in the DQB1*03:07 and 03:16 alleles.

14Primer mix 14: Specific PCR fragment of 135 bp in the DQB1*03:09 allele. Specific PCR fragment of 260 bp in the DQB1*03:11 and 03:26 alleles.

15Primer mix 15: Specific PCR fragment of 135 bp in the DQB1*03:10, 03:12, 03:14, 06:01:01-06:01:06 and 06:43 alleles. Specific PCR fragment of 250 bp in the DQB1*03:27 alleles.

16Primer mix 17: Specific PCR fragment of 110 bp in the DQB1*06:23 allele. Specific PCR fragment of 165 bp in the DQB1*03:13 allele. Specific PCR fragment of 195 bp in the DQB1*03:28 allele. Specific PCR fragment of 300 bp in the DQB1*06:34 allele.

17Primer mix 18: Specific PCR fragment of 130 bp in the DQB1*03:24 allele Specific PCR fragment of 190 bp in the DQB1*06:28 allele. Specific PCR fragment of 220 bp in the DQB1*03:18 allele.

18Primer mix 30: Specific PCR fragment of 160 bp in DQB1*03:23, 06:03:01-06:03:02, 06:04:02, 06:07:01, 06:08:01, 06:11:01-06:11:02, 06:26N, 06:28, 06:30-06:32, 06:40-06:41 and 06:44 alleles. Specific PCR fragment of 245 bp in the DQB1*03:06, 03:25 and 04:04-04:05 alleles.

19Primer mix 34: Specific PCR fragment of 95 bp in DQB1*05:07 allele. Specific PCR fragment of 130 bp in the DQB1*06:04:01-06:05:01, 06:06, 06:08:01-06:09, 06:12, 06:17-06:18, 06:21, 06:27, 06:34, 06:36, 06:38-06:39, 06:42 and 06:52 alleles.

20Primer mix 35: Specific PCR fragment of 160 bp in DQB1*03:27 and 06:35 allele. Specific PCR fragment of 255 bp in the DQB1*03:31, 06:05:01, 06:05:02?-06:06?, 06:20, 06:31 and 06:45  alleles.

21Primer mix 38: Specific PCR fragment of 100 bp in DQB1*06:14:01 and 06:14:02 alleles. Specific PCR fragment of 130 bp in the DQB1*03:01:04, 05:04 and 05:08 alleles. Specific PCR fragment of 185 bp in the DQB1*06:10 allele.

22Primer mix 40: Specific PCR fragment of 95 bp in the DQB1*06:40 allele. Specific PCR fragment of 150 bp in the DQB1*03:21 allele.

23Primer mix 41: Specific PCR fragment of 185 bp in the DQB1*06:17, 06:24, 06:30, 06:38 and 06:42 alleles. Specific PCR fragment of 205 bp in the DQB1*03:22 allele. Specific PCR fragment of 300 bp in the DQB1 *06:52 allele.

24Primer mix 42: Specific PCR fragment of 100 bp in the DQB1 *03:41 and 04:06 alleles. Specific PCR fragment of 135 bp in the DQB1*06:10 and 06:25 alleles. Specific PCR fragment of 195 bp in the DQB1*03:06, 03:25 and 04:03:01-04:03:02 alleles.

25Primer mix 43: PCR fragment of 110 bp in the DQB1*06:37 allele. Specific PCR fragment of 155 bp in the DQB1*02:05 allele. Specific PCR fragments of 185 and 215 bp in the DQB1*06:26N allele. Specific PCR fragment of 250 bp in the DQB1*06:33 allele.

26Primer mix 44: Specific PCR fragment of 110 bp in the DQB1 *03:42 allele. Specific PCR fragment of 160 bp in the DQB1*06:02:01-06:02:02, 06:10, 06:13-06:16, 06:20, 06:23-06:24, 06:29, 06:33, 06:37, 06:46-06:50 alleles.

27Primer mix 46: Specific PCR fragment of 160 bp in the DQB1*06:21 allele. Specific PCR fragment of 210 bp in the DQB1*06:27, 06:30 and 06:32 alleles. Specific PCR fragment of 160 and 210 bp in the DQB1*06:03:01-06:03:02, 06:08:01-06:08:02, 06:14:01-06:14:02, 06:28, 06:31, 06:40-06:41 and 06:44 alleles (both specific PCR fragments may not be obtained).

28Primer mix 47: Specific PCR fragment of 110 bp in the DQB1*03:42 allele. Specific PCR fragment of 155 bp in the DQB1*03:30, 04:01:01-04:03:02, 04:06-04:08, 06:19 allele.

29Primer mix 49: PCR fragment of 110 bp in the DQB1*03:33 allele. Specific PCR fragment of 155 bp in the DQB1*03:35 and 05:14 alleles.

30Primer mix 50: PCR fragment of 200 bp in the DQB1*03:37-03:38 allele. Specific PCR fragment of 240 bp in the DQB1*03:34 allele.

31Primer mix 51: PCR fragment of 125 bp in the DQB1*03:36 and 03:39 alleles. Specific PCR fragment of 245 bp in the DQB1*02:06 and 03:24 allele.

33Primer mix 56: PCR fragment of 100 bp in the DQB1*06:44 and 06:47 alleles. Specific PCR fragment of 220 bp in the DQB1*06:43 allele.

34Primer mix 64 contains a negative control, which will amplify more than 95% of HLA amplicons as well as the amplicons generated by control primer pairs. PCR product sizes range from 75 to 200 base pairs. The PCR product generated by the control primer pair is 430 base pairs.

‘?’, nucleotide sequence information not available for the primer matching sequence.

‘w’, might be weakly amplified.

1The sequence of the DQB1*03031 allele has been shown to be identical to DQB1*03:03:02.

2The DQB1*06:35 and 06:45 alleles may be distinguished by the different sizes of the specific PCR products generated by primer mix 35.

3Primer mix 64 contains a negative control, which will amplify more than 95% of HLA amplicons as well as the amplicons generated by control primer pairs. PCR product sizes range from 75 to 200 base pairs. The PCR product generated by the control primer pair is 430 base pairs.

4Primer mix 4: Specific PCR fragment of 140 bp in the DQB1*02:02-02:03 and 02:06 alleles. Specific PCR fragment of 195 bp in the DQB1 *03:28 allele.

Primer mix 5: Specific PCR fragment of 145 bp in the DQB1*02:04 allele. Specific PCR fragment of 180 bp in the DQB1*05:06-05:07 alleles.

Primer mix 9: Specific PCR fragment of 175 bp in DQB1*03:05:01-03:05:04, 03:13?-03:14?, 03:16?-03:17?, 03:19, 03:44?, 04:01:01-04:02 and 04:04-04:08 alleles. Specific PCR fragment of 220 bp in the DQB1*02:01:01-02:07 alleles. Specific PCR fragments of 175 and 220 bp in the DQB1*03:02:01-03:03:04, 03:06-03:08, 03:11-03:12, 03:15, 03:18, 03:20, 03:23, 03:25-03:26, 03:30-03:34, 03:37-03:41, 03:43 and 04:03:01-04:03:02 alleles. Both specific PCR fragments may  not be obtained.

of 130 bp in the DQB1*03:05:01-03:05:04 and 03:17 alleles.

Primer mix 12: Specific PCR fragment of 65 bp in the DQB1*03:40 allele. Specific PCR fragment of 115 bp in the DQB1*03:06 and 03:25 alleles. Specific PCR fragment of 135 bp in the DQB1*03:08, 06:02:02 and 06:03:02 alleles.

Primer mix 13: Specific PCR fragment of 110 bp in the DQB1*03:15 allele. Specific PCR fragment of 140 bp in the DQB1*03:07 and 03:16 alleles.

Primer mix 14: Specific PCR fragment of 135 bp in the DQB1*03:09 allele. Specific PCR fragment of 260 bp in the DQB1*03:11 and 03:26 alleles.

Primer mix 15: Specific PCR fragment of 135 bp in the DQB1*03:10, 03:12, 03:14, 06:01:01-06:01:06 and 06:43 alleles. Specific PCR fragment of 250 bp in the DQB1*03:27 alleles.

Primer mix 17: Specific PCR fragment of 110 bp in the DQB1*06:23 allele. Specific PCR fragment of 165 bp in the DQB1*03:13 allele. Specific PCR fragment of 195 bp in the DQB1*03:28 allele. Specific PCR fragment of 300 bp in the DQB1*06:34 allele.

Primer mix 18: Specific PCR fragment of 130 bp in the DQB1*03:24 allele Specific PCR fragment of 190 bp in the DQB1*06:28 allele. Specific PCR fragment of 220 bp in the DQB1*03:18 allele.

Primer mix 30: Specific PCR fragment of 160 bp in DQB1*03:23, 06:03:01-06:03:02, 06:04:02, 06:07:01, 06:08:01, 06:11:01-06:11:02, 06:26N, 06:28, 06:30-06:32, 06:40-06:41 and 06:44 alleles. Specific PCR fragment of 245 bp in the DQB1*03:06, 03:25 and 04:04-04:05 alleles.

Primer mix 34: Specific PCR fragment of 95 bp in DQB1*05:07 allele. Specific PCR fragment of 130 bp in the DQB1*06:04:01-06:05:01, 06:06, 06:08:01-06:09, 06:12, 06:17-06:18, 06:21, 06:27, 06:34, 06:36, 06:38-06:39, 06:42 and 06:52 alleles.

Primer mix 35: Specific PCR fragment of 160 bp in DQB1*03:27 and 06:35 allele. Specific PCR fragment of 255 bp in the DQB1*03:31, 06:05:01, 06:05:02?-06:06?, 06:20, 06:31 and 06:45  alleles.

Primer mix 38: Specific PCR fragment of 100 bp in DQB1*06:14:01 and 06:14:02 alleles. Specific PCR fragment of 130 bp in the DQB1*03:01:04, 05:04 and 05:08 alleles. Specific PCR fragment of 185 bp in the DQB1*06:10 allele.

Primer mix 40: Specific PCR fragment of 95 bp in the DQB1*06:40 allele. Specific PCR fragment of 150 bp in the DQB1*03:21 allele.

Primer mix 41: Specific PCR fragment of 185 bp in the DQB1*06:17, 06:24, 06:30, 06:38 and 06:42 alleles. Specific PCR fragment of 205 bp in the DQB1*03:22 allele. Specific PCR fragment of 300 bp in the DQB1 *06:52 allele.

Primer mix 42: Specific PCR fragment of 100 bp in the DQB1 *03:41 and 04:06 alleles. Specific PCR fragment of 135 bp in the DQB1*06:10 and 06:25 alleles. Specific PCR fragment of 195 bp in the DQB1*03:06, 03:25 and 04:03:01-04:03:02 alleles.

Primer mix 43: PCR fragment of 110 bp in the DQB1*06:37 allele. Specific PCR fragment of 155 bp in the DQB1*02:05 allele. Specific PCR fragments of 185 and 215 bp in the DQB1*06:26N allele. Specific PCR fragment of 250 bp in the DQB1*06:33 allele.

Primer mix 44: Specific PCR fragment of 110 bp in the DQB1 *03:42 allele. Specific PCR fragment of 160 bp in the DQB1*06:02:01-06:02:02, 06:10, 06:13-06:16, 06:20, 06:23-06:24, 06:29, 06:33, 06:37, 06:46-06:50 alleles.

Primer mix 46: Specific PCR fragment of 160 bp in the DQB1*06:21 allele. Specific PCR fragment of 210 bp in the DQB1*06:27, 06:30 and 06:32 alleles. Specific PCR fragment of 160 and 210 bp in the DQB1*06:03:01-06:03:02, 06:08:01-06:08:02, 06:14:01-06:14:02, 06:28, 06:31, 06:40-06:41 and 06:44 alleles (both specific PCR fragments may not be obtained).

of 155 bp in the DQB1*03:30, 04:01:01-04:03:02, 04:06-04:08, 06:19 allele.

Primer mix 49: PCR fragment of 110 bp in the DQB1*03:33 allele. Specific PCR fragment of 155 bp in the DQB1*03:35 and 05:14 alleles.

Primer mix 50: PCR fragment of 200 bp in the DQB1*03:37-03:38 allele. Specific PCR fragment of 240 bp in the DQB1*03:34 allele.

Primer mix 51: PCR fragment of 125 bp in the DQB1*03:36 and 03:39 alleles. Specific PCR fragment of 245 bp in the DQB1*02:06 and 03:24 allele.

Primer mix 56: PCR fragment of 100 bp in the DQB1*06:44 and 06:47 alleles. Specific PCR fragment of 220 bp in the DQB1*06:43 allele.

‘w’, might be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.

Change in revision R02 compared to R01:

- Primer mix 52 does not amplify the DQB1*06:49 allele. This has been corrected in the Specificity and Interpretation tables.