PHOTO DOCUMENT

Olerup SSP AB

Olerup SSPTM DQB1*03

Prod. No:	101.214-24/06 – including Taq pol.

101.214-24u/06u – without Taq pol.

Lot No:    	Y07

Expiry Date:    	2009-July-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ug/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 16 primer mixes used for DQB1*03 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified DQB1*033 | Other amplified DQB1 Alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 165 bp | 515 bp | 030101-030103, 0304, 0309, 0313, 0316, 0319 |  |
| 2 | 220 bp | 515 bp | 030101-030103, 0304, 0309, 0310, 0313, 0314, 0316, 0319 |  |
| 35 | 135 bp | 515 bp | 030201-030204, 0307, 0308, 0311, 0318 | 020101-0202, 0204, 0205, 0629 |
| 46 | 190, 220 bp | 515 bp | 030201-030204, 030302-030303, 030501-0308, 0311, 0312, 0315, 0318-0320 | 020101-0205, 0401, 0402 |
| 5 | 135 bp | 430 bp | 0304, 0314 |  |
| 65,7 | 95, 130 bp | 430 bp | 030501-030504, 0317, 0320 |  |
| 75 | 115 bp | 430 bp | 0306 |  |
| 85,8 | 110, 140, 220 bp | 430 bp | 0307, 0315, 0316, 0318 |  |
| 95 | 135 bp | 430 bp | 0308 | 060302 |
| 105,9 | 135, 220, 260 bp | 430 bp | 0309, 0311, 0318 |  |
| 115 | 135 bp | 430 bp | 0310, 0312, 0314 | 060101-060103 |
| 12 | 260 bp | 515 bp | 030101-030103, 0304, 0309, 0310, 0312-0314, 0316, 0319 |  |
| 13 | 165 bp | 430 bp | 0313 |  |
| 145 | 130 bp | 515 bp | 030101-030103, 0304, 0309, 0310, 0313, 0314, 0319 |  |
| 155 | 135 bp | 515 bp | 030101-0315, 0317-0320 |  |
| 165 | 130 bp | 430 bp | 030101-03010, 030302-030303, 0306, 0309, 0310, 0312, 0313, 0315, 0317, 0319, 0320 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DQB1*03 SSP subtypings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 bp or more. Size differences shorter than 20 bp are not given. For high resolution SSP kits the length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control band may sometimes be observed. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most tubes, or a band of 515 base pairs, for some tubes.

Tube number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DQB1*03 subtyping.

In addition, tubes number 2, 3, 4, 12, 14 and 15 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several DQB1 alleles only partial second exon nucleotide sequences are available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences of DQB1 alleles are conserved within allelic groups.

4Due to the sharing of sequence motifs, non-DQB1*03 alleles will be amplified by primer mixes 3, 4, 9 and 11.

5Specific PCR fragments shorter than 150 base pairs are less intense and not as sharp as longer specific bands.

6Primer mix 4: Specific PCR fragment of 190 bp in DQB1*030501-030504, 0319 and the DQB1*0401-0402 alleles. Specific PCR fragment of 220 bp in the DQB!*0306-0308, 0311, 01312, 0315, 0318, 0320 and the DQB1*020101-0205 alleles. Specific PCR fragments of 190 and 220 bp (both specific PCR fragments may  not be obtained) in the DQB1*030201-030204 and DQB1*030302-030303 alleles.

7Primer mix 6: Specific PCR fragment of 95 bp in the DQB1*0620 allele. Specific PCR fragment of 130 bp in the DQB1*030501-030504 and 0317 alleles.

8Primer mix 8: Specific PCR fragment of 110 bp in the DQB1*0315 allele. Specific PCR fragment of 140 bp in the DQB1*0307 and 0316 alleles. Specific PCR fragment of 220 bp in the DQB1*0318 allele.

9Primer mix 10: Specific PCR fragment of 135 bp in the DQB1*0309 allele. Specific PCR fragment of 220 bp in the DQB1*0318 allele. Specific PCR fragment of 260 bp in the DQB1*0311 allele.

1The sequence of the DQB1*030301 allele has been shown to be identical to DQB1*030302.

2Primer mix 4: Specific PCR fragment of 190 bp in DQB1*030501-030504, 0319 and the DQB1*0401-0402 alleles. Specific PCR fragment of 220 bp in the DQB!*0306-0308, 0311, 01312, 0315, 0318, 0320 and the DQB1*020201-0205 alleles. Specific PCR fragments of 190 and 220 bp (both specific PCR fragments may  not be obtained) in the DQB1*030201-030204 and DQB1*030302-030303 alleles.

Primer mix 6: Specific PCR fragment of 95 bp in the DQB1*0620 allele. Specific PCR fragment of 130 bp in the DQB1*030501-030504 and 0317 alleles.

Primer mix 8: Specific PCR fragment of 110 bp in the DQB1*0315 allele. Specific PCR fragment of 140 bp in the DQB1*0307 and 0316 alleles. Specific PCR fragment of 220 bp in the DQB1*0318 allele.

Primer mix 10: Specific PCR fragment of 135 bp in the DQB1*0309 allele. Specific PCR fragment of 220 bp in the DQB1*0318 allele. Specific PCR fragment of 260 bp in the DQB1*0311 allele.

Changes in revision R01 compared to R00:

- DQB1*0401 and 0402 added to alleles amplified by primer mix 4 in the Specificity Table.