PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® DQB1*03

Prod. No:	101.214-24/24u

101.214-06/06u

Lot No:    	22G

Expiry Date:    	2011-October-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 23 primer mixes used for DQB1*03 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified DQB1*03 alleles3 | Other amplified DQB1 alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 165 bp | 515 bp | *030101-030104, 0304, 0309, 0313, 0316, 0319, 0321, 0322, 0324 |  |
| 2 | 220 bp | 515 bp | *030101-030104, 0304, 0309, 0310, 0313, 0314, 0316, 0319, 0321, 0322, 0324 |  |
| 35 | 135 bp | 515 bp | *030201-030204, 0307, 0308, 0311, 0318 | *020101-0202, 0204, 0205, 0629 |
| 4 | 220 bp | 515 bp | *030201-030303, 0306-0308, 0311, 0312, 0315, 0318, 0320, 0323, 0325 | *020101-0205, 0403 |
| 55 | 135 bp | 430 bp | *0304, 0314 |  |
| 65,7 | 95 bp, 130 bp | 430 bp | *030501-030504, 0317, 0320 |  |
| 75 | 115 bp | 430 bp | *0306, 0325 |  |
| 85,8 | 110 bp, 140 bp | 430 bp | *0307, 0315, 0316 |  |
| 95 | 135 bp | 430 bp | *0308 | *060202, 060302 |
| 105,9 | 135 bp, 260 bp | 430 bp | *0309, 0311 |  |
| 115,6 | 135 bp | 430 bp | *0310, 0312, 0314 | *060101-060104 |
| 12 | 260 bp | 515 bp | *030101-030104, 0304, 0309, 0310, 0312-0314, 0316, 0319, 0321, 0322, 0324 |  |
| 13 | 165 bp | 430 bp | *0313 |  |
| 145 | 130 bp | 515 bp | *030101-030104, 0304, 0309, 0310, 0313, 0314, 0319, 0321, 0322, 0324 |  |
| 155 | 135 bp | 515 bp | *030101-0315, 0317-0322, 0324 |  |
| 165 | 130 bp | 430 bp | *030101, 030102, 030104, 030302, 030303, 0306, 0309, 0310, 0312, 0313, 0315-0317, 0319-0324 | *0203 |
| 17 | 220 bp | 430 bp | *0318 |  |
| 18 | 175 bp | 515 bp | *030201-030303, 030501-030504, 0306?-0308?, 0311?-0318?, 0319, 0320?, 0323?, 0325 | *040101-0403 |
| 196 | 175 bp | 515 bp | *030101-030104, 0304, 0306?-0308?, 0309, 0310, 0311?-0318?, 0320?, 0321, 0322, 0323?, 0324 |  |
| 20 | 150 bp | 430 bp | *0321 |  |
| 21 | 160 bp | 515 bp | *0322 |  |
| 22 | 160 bp | 515 bp | *0323 | *060301, 060302, 060402, 0607, 060801, 061101, 061102, 0626N, 0628, 0630-0632 |
| 235 | 130 bp | 430 bp | *0324 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DQB1*03 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DQB1*03 subtyping.

In addition, wells number 2, 3, 4, 12, 14, 15, 18, 19, 21 and 22 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several DQB1 alleles only partial second exon nucleotide sequences are available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences of DQB1 alleles are conserved within allelic groups.

4Due to the sharing of sequence motifs, non-DQB1*03 alleles will be amplified by primer mixes 3, 4, 9, 11, 16, 18 and 22.

5Specific PCR fragments shorter than 150 base pairs are less intense and not as sharp as longer specific bands.

6Primer mixes11 and 19 may give rise to nonspecific amplifications.

7Primer mix 6: Specific PCR fragment of 95 bp in the DQB1*0320 allele. Specific PCR fragment of 130 bp in the DQB1*030501-030504 and 0317 alleles.

8Primer mix 8: Specific PCR fragment of 110 bp in the DQB1*0315 allele. Specific PCR fragment of 140 bp in the DQB1*0307 and 0316 alleles.

9Primer mix 10: Specific PCR fragment of 135 bp in the DQB1*0309 allele. Specific PCR fragment of 260 bp in the DQB1*0311 allele.

‘?’, nucleotide sequence information not available for the primer matching region.

1The sequence of the DQB1*030301 allele has been shown to be identical to DQB1*030302.

2Primer mix 6: Specific PCR fragment of 95 bp in the DQB1*0320 allele. Specific PCR fragment of 130 bp in the DQB1*030501-030504 and 0317alleles.

Primer mix 8: Specific PCR fragment of 110 bp in the DQB1*0315 allele. Specific PCR fragment of 140 bp in the DQB1*0307 and 0316 alleles.

Primer mix 10: Specific PCR fragment of 135 bp in the DQB1*0309 allele. Specific PCR fragment of 260 bp in the DQB1*0311 allele.

‘?’, nucleotide sequence information not available for the primer matching region.