PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® DQB1*03

Prod. No:	101.214-24/24u

101.214-06/06u

Lot No:    	44R

Expiry Date:    	2015-June-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for DQB1*03 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified DQB1*03 alleles3 | Other amplified DQB1 alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 165 bp | 515 bp | *03:01:01:01-03:01:06, 03:04, 03:09, 03:13, 03:16, 03:19, 03:21-03:22, 03:24, 03:27-03:29, 03:35-03:36, 03:42, 03:44 |  |
| 2 | 220 bp | 515 bp | *03:01:01:01-03:01:06, 03:04, 03:09-03:10, 03:13-03:14, 03:16, 03:19, 03:21-03:22, 03:24, 03:27-03:29, 03:35-03:36, 03:42, 03:44 |  |
| 3 | 135 bp | 515 bp | *03:02:01-03:02:05, 03:07-03:08, 03:11, 03:18, 03:32, 03:37 | *02:01:01-02:02, 02:04-02:07, 06:29 |
| 4 | 220 bp | 515 bp | *03:02:01-03:03:04, 03:06-03:08, 03:11-03:12, 03:15, 03:18, 03:20, 03:23, 03:25-03:26, 03:30-03:34, 03:37-03:41, 03:43 | *02:01:01-02:07, 04:03:01-04:03:02 |
| 5 | 135 bp | 430 bp | *03:04, 03:14 |  |
| 65,10 | 95 bp, 130 bp | 430 bp | *03:05:01-03:05:04, 03:17, 03:20 |  |
| 75,9 | 115 bp | 430 bp | *03:06, 03:25, 03:42 |  |
| 85,11 | 110 bp, 140 bp | 430 bp | *03:07, 03:15-03:16 |  |
| 95,12 | 65 bp, 135 bp | 430 bp | *03:08, 03:40 | *06:02:02, 06:03:02 |
| 1013 | 135 bp, 260 bp | 430 bp | *03:09, 03:11, 03:26 |  |
| 117 | 135 bp | 430 bp | *03:10, 03:12, 03:14 | *06:01:01-06:01:06, 06:43 |
| 12 | 260 bp | 515 bp | *03:01:01:01-03:01:06, 03:04, 03:09-03:10, 03:12-03:14, 03:16, 03:19, 03:21-03:22, 03:24, 03:27-03:29, 03:35-03:36, 03:42, 03:44 |  |
| 13 | 165 bp | 430 bp | *03:13 |  |
| 147 | 130 bp | 515 bp | *03:01:01:01-03:01:06, 03:04, 03:09-03:10, 03:13-03:14, 03:19, 03:21-03:22, 03:24, 03:27-03:29, 03:35-03:36, 03:42, 03:44 |  |
| 15 | 135 bp | 515 bp | *03:01:01:01-03:15, 03:17-03:22, 03:24, 03:26-03:44 |  |
| 167 | 130 bp | 430 bp | *03:01:01:01-03:01:02, 03:01:04-03:01:06, 03:03:02:01-03:03:04, 03:06, 03:09-03:10, 03:12-03:13, 03:15-03:17, 03:19-03:24, 03:26-03:31, 03:33-03:36, 03:38-03:44 | *02:03 |
| 1714 | 220 bp, 170 bp | 430 bp | *03:18, 03:43 |  |
| 18 | 175 bp | 515 bp | *03:02:01-03:03:04, 03:05:01-03:05:04, 03:06?-03:08?, 03:11?-03:18?, 03:19, 03:20?, 03:23?, 03:25, 03:26?, 03:30-03:32, 03:33?-03:34?, 03:37?, 03:38-03:39, 03:40?, 03:41, 03:43, 03:44? | *04:01:01-04:08 |
| 198 | 175 bp | 515 bp | *03:01:01:01-03:01:06, 03:04, 03:06?-03:08?, 03:09-03:10, 03:11?-03:18?, 03:20?, 03:21-03:22, 03:23?, 03:24, 03:26?, 03:27-03:29, 03:33?-03:34?, 03:35-03:36, 03:37?, 03:40?, 03:42, 03:44? |  |
| 20 | 150 bp | 430 bp | *03:21 |  |
| 21 | 160 bp | 515 bp | *03:22 |  |
| 22 | 160 bp | 515 bp | *03:23 | *06:03:01-06:03:02, 06:04:02, 06:07:01, 06:08:01, 06:11:01-06:11:02, 06:26N, 06:28, 06:30-06:32, 06:40-06:41, 06:44 |
| 235,6,15 | 95 bp, 130 bp | 430 bp | *03:24, 03:41 |  |
| 2416 | 120 bp, 210 bp | 430 bp | *03:27, 03:39 |  |
| 2517 | 170 bp, 240 bp | 430 bp | *03:29, 03:34 |  |
| 26 | 180 bp | 430 bp | *03:30 | *06:29 |
| 278,18 | 175 bp, 250 bp | 430 bp | *03:31-03:32 |  |
| 28 | 200 bp | 430 bp | *03:37-03:38 |  |
| 295,6,19 | 110 bp, 165 bp | 515 bp | *03:33, 03:35 |  |
| 30 | 135 bp | 430 bp | *03:36 |  |
| 31 | 195 bp | 430 bp | *03:28 |  |
| 325 | 100 bp | 430 bp | *03:44 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DQB1*03 SSP typings.

When the primers in a primer mix can give rise to HLA-specific PCR products of more than one length this is indicated if the size difference is more than 20 base pairs. Size differences of 20 base pairs or less are not given. For high resolution SSP kits the respective lengths of the HLA-specific PCR product(s) are given for the alleles amplified by these primer mixes.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DQB1*03 subtyping.

In addition, wells number 2 to 4, 12, 14, 15, 18, 19, 21, 22 and 29 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several DQB1 alleles 1st and/or 3rd exon(s) and beyond, as well as intron nucleotide sequences, are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in these regions are conserved within allelic groups.

4Due to the sharing of sequence motifs, non-DQB1*03 alleles will be amplified by primer mixes 3, 4, 9, 11, 16, 18, 22 and 26.

5HLA-specific PCR products shorter than 125 base pairs have a lower intensity and are less sharp than longer PCR products.

6Primer mixes 23 and 29 may have a tendency to giving rise to primer oligomer formation.

7Primer mixes 11, 14 and 16 may have tendencies of unspecific amplifications.

8Primer mixes 19 and 27 may give rise to a lower yield of HLA-specific PCR product than the other DQB1*03 primer mixes.

9In primer mix 7, the positive control band may be slightly weaker than in the other DQB1*03 primer mixes.

10Primer mix 6: Specific PCR fragment of 95 bp in the DQB1*03:20 allele. Specific PCR fragment of 130 bp in the DQB1*03:05:01-03:05:04 and 03:17 alleles.

11Primer mix 8: Specific PCR fragment of 110 bp in the DQB1*03:15 allele. Specific PCR fragment of 140 bp in the DQB1*03:07 and 03:16 alleles.

12Primer mix 9: Specific PCR fragment of 65 bp in the DQB1*03:40 allele. Specific PCR fragment of 135 bp in the DQB1*03:08 and the DQB1*06:02:02 and 06:03:02 alleles.

13Primer mix 10: Specific PCR fragment of 135 bp in the DQB1*03:09 allele. Specific PCR fragment of 260 bp in the DQB1*03:11 and 03:26 alleles.

14Primer mix 17: Specific PCR fragment of 170 bp in the DQB1*03:43 allele. Specific PCR fragment of 220 bp in the DQB1*03:18 allele.

15Primer mix 23: Specific PCR fragment of 95 bp in the DQB1*03:41 allele. Specific PCR fragment of 130 bp in the DQB1*03:24 allele.

16Primer mix 24: Specific PCR fragment of 120 bp in the DQB1*03:39 allele. Specific PCR fragment of 210 bp in the DQB1*03:27 allele.

17Primer mix 25: Specific PCR fragment of 170 bp in the DQB1*03:29 allele. Specific PCR fragment of 240 bp in the DQB1*03:34 allele.

18Primer mix 27: Specific PCR fragment of 175 bp in the DQB1*03:32 allele. Specific PCR fragment of 250 bp in the DQB1*03:31 allele.

19Primer mix 29: Specific PCR fragment of 110 bp in the DQB1*03:33 allele. Specific PCR fragment of 165 bp in the DQB1*03:35 allele.

‘?’, nucleotide sequence information not available for the primer matching region.

1The sequence of the DQB1*03031 allele has been shown to be identical to DQB1*03:03:02.

2Primer mix 6: Specific PCR fragment of 95 bp in the DQB1*03:20 allele. Specific PCR fragment of 130 bp in the DQB1*03:05:01-03:05:04 and 03:17 alleles.

Primer mix 8: Specific PCR fragment of 110 bp in the DQB1*03:15 allele. Specific PCR fragment of 140 bp in the DQB1*03:07 and 03:16 alleles.

Primer mix 9: Specific PCR fragment of 65 bp in the DQB1*03:40 allele. Specific PCR fragment of 135 bp in the DQB1*03:08 and the DQB1*06:02:02 and 06:03:02 alleles.

Primer mix 10: Specific PCR fragment of 135 bp in the DQB1*03:09 allele. Specific PCR fragment of 260 bp in the DQB1*03:11 and 03:26 alleles.

Primer mix 17: Specific PCR fragment of 170 bp in the DQB1*03:43 allele. Specific PCR fragment of 220 bp in the DQB1*03:18 allele.

Primer mix 23: Specific PCR fragment of 95 bp in the DQB1*03:41 allele. Specific PCR fragment of 130 bp in the DQB1*03:24 allele.

Primer mix 24: Specific PCR fragment of 120 bp in the DQB1*03:39 allele. Specific PCR fragment of 210 bp in the DQB1*03:27 allele.

Primer mix 25: Specific PCR fragment of 170 bp in the DQB1*03:29 allele. Specific PCR fragment of 240 bp in the DQB1*03:34 allele.

Primer mix 27: Specific PCR fragment of 175 bp in the DQB1*03:32 allele. Specific PCR fragment of 250 bp in the DQB1*03:31 allele.

Primer mix 29: Specific PCR fragment of 110 bp in the DQB1*03:33 allele. Specific PCR fragment of 165 bp in the DQB1*03:35 allele.

‘?’, nucleotide sequence information not available for the primer matching region.