PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® DQB1*06

Prod. No:	101.212-24/24u

101.212-04/04u

Lot No:    	08N

Expiry Date:    	2014-July-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for DQB1*06 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified DQB1*06 alleles3 | Amplified non-DQB1*06 alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 220 bp | 515 bp | *06:01:01-06:01:06, 06:35, 06:43 |  |
| 2 | 210 bp | 430 bp | *06:01:01-06:02:02, 06:05:02?-06:06?, 06:10-06:11:02, 06:13, 06:16, 06:18-06:20, 06:24, 06:29, 06:33, 06:35, 06:37, 06:43, 06:47 |  |
| 3 | 185 bp | 430 bp | *06:02:01-06:02:02, 06:14:01-06:16, 06:19-06:20, 06:23-06:24, 06:33, 06:37, 06:47 |  |
| 4 | 130 bp | 430 bp | *06:03:01-06:03:02, 06:07:01-06:07:02, 06:11:02, 06:14:01, 06:26N, 06:28, 06:30-06:32, 06:40-06:41, 06:44 |  |
| 5 | 160 bp | 430 bp | *06:03:01-06:03:02, 06:04:02, 06:07:01, 06:08:01, 06:11:01-06:11:02, 06:26N, 06:28, 06:30-06:32, 06:40-06:41, 06:44 | *03:23 |
| 6 | 170 bp | 515 bp | *06:03:01-06:03:02, 06:08:01-06:08:02, 06:11:02-06:12, 06:14:01, 06:21, 06:26N, 06:28, 06:31, 06:40-06:41, 06:44 |  |
| 7 | 210 bp | 515 bp | *06:04:01-06:04:03, 06:07:01-06:07:02, 06:17, 06:21, 06:25, 06:34, 06:36, 06:38-06:39 |  |
| 86 | 175 bp | 430 bp | *06:04:01-06:07:02, 06:09, 06:18, 06:25, 06:27, 06:32, 06:34, 06:36, 06:38-06:39 |  |
| 96 | 130 bp | 430 bp | *06:04:01-06:05:01, 06:06, 06:08:01-06:09, 06:12, 06:17-06:18, 06:21, 06:27, 06:34, 06:36, 06:38-06:39, 06:42 |  |
| 109 | 260 bp | 515 bp | *06:05:01, 06:05:02?-06:06?, 06:20w, 06:31 |  |
| 11 | 210 bp | 430 bp | *06:05:01, 06:05:02?-06:06?, 06:09, 06:12, 06:15, 06:22, 06:42 |  |
| 12 | 180 bp | 430 bp | *06:06 |  |
| 13 | 185 bp | 430 bp | *06:10 |  |
| 14 | 130 bp | 430 bp | *06:13, 06:22 |  |
| 155,8,10 | 100 bp, 185 bp | 430 bp | *06:14:01-06:14:02, 06:29 |  |
| 16 | 195 bp | 430 bp | *06:16 |  |
| 175 | 110 bp | 430 bp | *06:23 |  |
| 187 | 175 bp | 430 bp | *06:17, 06:24, 06:30, 06:42 |  |
| 19 | 135 bp | 430 bp | *06:10, 06:25, 06:36 |  |
| 205,11 | 110 bp, 215 bp | 515 bp | *06:26N, 06:37 |  |
| 21 | 160 bp | 430 bp | *06:02:01-06:02:02, 06:10, 06:13-06:16, 06:20, 06:23-06:24, 06:29, 06:33, 06:37, 06:47 |  |
| 2212 | 130 bp, 195 bp | 515 bp | *06:07:01-06:07:02, 06:15, 06:38 |  |
| 23 | 160 bp | 515 bp | *06:03:01-06:03:02, 06:08:01-06:08:02, 06:14:01-06:14:02, 06:21, 06:28, 06:31, 06:40-06:41, 06:44 |  |
| 24 | 155 bp | 430 bp | *06:19 | *03:30, 04:01:01-04:03:02, 04:06-04:08 |
| 25 | 210 bp | 430 bp | *06:03:01-06:03:02, 06:08:01-06:08:02, 06:14:01-06:14:02, 06:27-06:28, 06:30-06:32, 06:40-06:41, 06:44 |  |
| 2613 | 165 bp, 190 bp | 430 bp | *06:28, 06:35 |  |
| 2714 | 205 bp, 265 bp | 430 bp | *06:33, 06:40 |  |
| 28 | 300 bp | 430 bp | *06:34 |  |
| 295 | 90 bp | 430 bp | *06:04:01-06:05:01, 06:05:02?-06:06?, 06:07:01-06:07:02, 06:09, 06:15, 06:22, 06:25, 06:34, 06:36, 06:38-06:39 |  |
| 305,6 | 115 bp | 430 bp | *06:02:01-06:03:02, 06:05:01?-06:07:01?, 06:08:01?-06:08:02?, 06:10?-06:11:02?, 06:13?-06:33?, 06:35?, 06:37?, 06:39, 06:40?, 06:44, 06:47 |  |
| 315,8,15 | 100 bp, 220 bp | 430 bp | *06:43-06:44, 06:47 |  |
| 325,6 | 125 bp | 430 bp | *06:04:01-06:04:03, 06:05:01?-06:06?, 06:07:01-06:07:02, 06:08:01?-06:08:02?, 06:09, 06:10?-06:11:02?, 06:12, 06:13?-06:33?, 06:34, 06:35?, 06:36, 06:37?, 06:40?, 06:41-06:42 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DQB1*06 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DQB1*06 subtyping.

In addition, wells number 6, 7, 10, 20, 22 and 23 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several DQB1 alleles only second exon nucleotide sequences are available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences of DQB1 alleles are conserved within allelic groups.

4Due to the sharing of sequence motif between DQB1 alleles, the DQB1*03:23 alleles will be amplified by primer mix 5, and the DQB1*03:30, 04:01:01-04:03:02 and 04:06-04:08 alleles will be amplified by primer mix 24.

5Specific PCR fragments shorter than 125 base pairs have a lower intensity than longer PCR bands.

6Primer mix 8, 9, 30 and 32 may yield less specific PCR product than the other DQB1*06 primer mixes, most pronounced in primer mix 32.

7Primer mix 18 may give rise to primer oligomer formation.

8Primer mixes 15 and 31 may give rise to unspecific amplifications.

9The nucleotide sequence of codon 14 of the DQB1*06:05:02 allele is not yet known. If codon 14 is CTg, then the DQB1*06:05:02 allele will retain its name and will be amplified by the primer pair in well No. 10. If the sequence of codon 14 is ATg, then DQB1*06:05:02 will be renamed to DQB1*06:09:02 (Steven Marsh personal communication), and will not be amplified by the primer pair in well No. 10.

10Primer mix 15: Specific PCR fragment of 100 bp in the DQB1*06:14:01 and *06:14:02 alleles. Specific PCR fragment of 185 bp in the DQB1*06:29 allele.

11Primer mix 20: Specific PCR fragment of 110 bp in the DQB1*06:37 allele. Specific PCR fragment of 215 bp in the DQB1*06:26N allele.

12Primer mix 22: Specific PCR fragment of 130 bp in the DQB1*06:07:01-06:07:02 and 06:15 alleles. Specific PCR fragment of 195 bp in the DQB1*06:38 allele.

13Primer mix 26: Specific PCR fragment of 165 bp in the DQB1*06:35 allele. Specific PCR fragment of 190 bp in the DQB1*06:28 allele.

14Primer mix 27: Specific PCR fragment of 205 bp in the DQB1*06:40 allele. Specific PCR fragment of 265 bp in the DQB1*06:33 allele.

15Primer mix 31: Specific PCR fragment of 100 bp in the DQB1*06:44 and 06:47 alleles. Specific PCR fragment of 220 bp in the DQB1*06:43 allele.

‘w’, might be weakly amplified.

“?”, nucleotide sequence information is not available for the primer matching sequence.

1The nucleotide sequence of the DQB1*06:45 and DQB1*06:46 alleles are not yet retrievable

2Primer mix 15: Specific PCR fragment of 100 bp in the DQB1*06:14:01 and *06:14:02 alleles. Specific PCR fragment of 185 bp in the DQB1*06:29 allele.

Primer mix 20: Specific PCR fragment of 110 bp in the DQB1*06:37 allele. Specific PCR fragment of 215 bp in the DQB1*06:26N allele.

Primer mix 22: Specific PCR fragment of 130 bp in the DQB1*06:07:01-06:07:02 and 06:15 alleles. Specific PCR fragment of 195 bp in the DQB1*06:38 allele.

Primer mix 26: Specific PCR fragment of 165 bp in the DQB1*06:35 allele. Specific PCR fragment of 190 bp in the DQB1*06:28 allele.

Primer mix 27: Specific PCR fragment of 205 bp in the DQB1*06:40 allele. Specific PCR fragment of 265 bp in the DQB1*06:33 allele.

Primer mix 31: Specific PCR fragment of 100 bp in the DQB1*06:44 and 06:47 alleles. Specific PCR fragment of 220 bp in the DQB1*06:43 allele.

“?”, nucleotide sequence information is not available for the primer matching sequence.

‘w’, might be weakly amplified.

Change in revision R01 compared to R00:

- A footnote (no. 3), concerning primers in incompletely sequenced regions, has been added to the specificity table.

Changes in revision R02 compared to R01:

- Primer mix 15 may give rise to unspecific amplifications.

- The DQB1*06:20 allele is weakly amplified by primer mix 10. This has been changed in the specificity and interpretation tables.

Change in revision R03 compared to R02:

- A typing error in the foot-notes to the Interpretation Table has been corrected: The nucleotide sequence of the DQB1*06:45 and DQB1*06:46 alleles are not yet retrievable.