PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® DQB1*06:02,DQA1*01:02

Prod. No:	101.901-24/24u

Lot No:    	96K

Expiry Date:    	2013-July-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 8 primer mixes used for DQB1*06:02,DQA1*01:02 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified alleles3 |
| --- | --- | --- | --- |
| 1 | 210 bp | 515 bp | DQB1*06:01:01-06:02:02, 06:05:02?-06:06?, 06:10-06:11:02, 06:13, 06:16, 06:18-06:20, 06:24, 06:29, 06:33, 06:35, 06:37 |
| 2 | 185 bp | 430 bp | DQB1*06:02:01-06:02:02, 06:14:01-06:16, 06:19-06:20, 06:23-06:24, 06:33, 06:37 |
| 35 | 170 bp | 430 bp | DQA1*01:01:01-01:02:04, 01:04:01-01:07 |
| 4 | 145 bp | 430 bp | DQA1*01:02:01-01:03, 01:06 |
| 54 | 95 bp | 430 bp | DQA1*01:06 |
| 66 | 155 bp, 195 bp | 430 bp | DQB1*06:01:01w-06:01:06w, 06:16, 06:19, DQB1*03:30, 04:01:01-04:03:02, 04:06 |
| 74,7 | 115 bp, 225 bp, 265 bp | 430 bp | DQB1*06:20, 06:23, 06:31, 06:33, 06:37 |
| 84,5,8 | 60 bp, 175 bp, 220 bp | 430 bp | DQB1*06:03:01-06:05:01, 06:05:02?-06:06?, 06:07:01-06:09, 06:12, 06:14:01-06:15, 06:17, 06:21-06:22, 06:24-06:28, 06:30-06:32, 06:34, 06:36, 06:38-06:39 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DQB1*06:02,DQA1*01:02 subtyping.

3Due to sharing of sequence motifs, the DQB1*03:30 as well as some DQB1*04 allele are amplified by primer mix 6.

4Short specific PCR fragments are less intense and not as sharp as longer specific bands.

5Primer mixes 3 and 8 may give rise to a primer dimer artifact.

6Primer mix 6: Specific PCR product of 155 bp in the DQB1*06:01:01w-06:01:06w and 06:19 and in the DQB1*03:30, 04:01:01-04:03:02 and 04:06 alleles. Specific PCR product of 195 bp in the DQB1*06:16 allele.

7Primer mix 7: Specific PCR product of 115 bp in the DQB1*06:37 allele. Specific PCR product of 225 bp in the DQB1*06:23 allele. Specific PCR product of 265 bp in the DQB1*06:20, 06:31 and 06:33 alleles.

8Primer mix 8: Specific PCR product of 60 bp in the DQB1*06:03:01-06:03:02, 06:08:01-06:08:02, 06:14:01-06:14:02, 06:26-06:28, 06:31-06:32

allele.Specific PCR product of 175 bp in the DQB1*06:24 alleles. Specific PCR product of 220 bp in the DQB1*06:05:01, 06:05:02?-06:06?, 06:09, 06:12, 06:15, 06:22 allele. Specific PCR product of 60 and 175 bp the DQB1*06:30 allele. Specific PCR product of 60 and 220 bp in the DQB1*06:04:01-06:04:03, 06:07:01-06:07:02, 06:21, 06:25, 06:34, 06:36, 06:38-06:39 allele. Specific PCR product of 60, 175 and 220 bp in the DQB1*06:17 allele. All specific bands may not always be visible.

‘?’, nucleotide sequence of the primer matching region is not available for this allele.

‘w’, might be weakly amplified.

1Primer mix 6: Specific PCR product of 155 bp in the DQB1*06:01:01w-06:01:06w and 06:19 and in the DQB1*03:30, 04:01:01-04:03:02 and 04:06 alleles. Specific PCR product of 195 bp in the DQB1*06:16 allele.

Primer mix 7: Specific PCR product of 115 bp in the DQB1*06:37 allele. Specific PCR product of 225 bp in the DQB1*06:23 allele. Specific PCR product of 265 bp in the DQB1*06:20, 06:31 and 06:33 alleles.

Primer mix 8: Specific PCR product of 60 bp in the DQB1*06:03:01-06:03:02, 06:08:01-06:08:02, 06:14:01-06:14:02, 06:26-06:28, 06:31-06:32

allele.Specific PCR product of 175 bp in the DQB1*06:24 alleles. Specific PCR product of 220 bp in the DQB1*06:05:01, 06:05:02?-06:06?, 06:09, 06:12, 06:15, 06:22 allele. Specific PCR product of 60 and 175 bp the DQB1*06:30 allele. Specific PCR product of 60 and 220 bp in the DQB1*06:04:01-06:04:03, 06:07:01-06:07:02, 06:21, 06:25, 06:34, 06:36, 06:38-06:39 allele. Specific PCR product of 60, 175 and 220 bp in the DQB1*06:17 allele. All specific bands may not always be visible.

‘?’, nucleotide sequence of the primer matching region is not available for this allele.

‘w’, might be weakly amplified.