PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® DRB1*08

Prod. No:	101.127-12/12u

101.127-04/04u

Lot No:    	79R

Expiry Date:    	2015-July-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 24 primer mixes used for DRB1*08 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified DRB1*08 alleles3 | Other amplified DRB1 alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 165 bp | 515 bp | *08:01:01-08:01:05, 08:03:02-08:03:03, 08:05-08:06, 08:10, 08:12, 08:14, 08:16-08:18, 08:22-08:23, 08:26-08:27, 08:29, 08:32-08:33, 08:35-08:40, 08:43, 08:46-08:49 |  |
| 26 | 165 bp | 430 bp | *08:02:01-08:02:04, 08:04:01-08:04:07, 08:09, 08:13, 08:21, 08:24, 08:28, 08:30:01-08:30:03, 08:42, 08:44-08:45 | *12:09, 13:17, 13:116, 14:15, 14:52, 14:126 |
| 37 | 195 bp | 430 bp | *08:01:01-08:02:04, 08:04:01-08:09, 08:11, 08:16-08:17, 08:21-08:22, 08:24, 08:26, 08:28, 08:31, 08:39, 08:41-08:44 | *11:67, 12:02:01-12:02:05, 12:13, 12:15-12:16:01, 12:18-12:21, 12:23, 12:26-12:27, 12:31N-12:33, 12:37, 14:15, 14:73 |
| 4 | 195 bp | 430 bp | *08:03:02-08:03:03, 08:10, 08:12, 08:14-08:15, 08:18-08:19, 08:23, 08:25, 08:27, 08:29-08:30:03, 08:32-08:38, 08:40, 08:45-08:47, 08:49 | *12:01:01-12:01:04, 12:03:02-12:06, 12:08-12:11, 12:14, 12:17, 12:22, 12:24N-12:25, 12:28-12:30, 12:34-12:36, 13:17, 13:116 |
| 56 | 225 bp | 515 bp | *08:01:01-08:04:07, 08:06-08:13, 08:15-08:17, 08:19-08:20, 08:22-08:23, 08:26-08:28, 08:30:01-08:30:03, 08:32-08:39, 08:42, 08:44-08:46, 08:48-08:49 | *11:23, 11:25, 11:45, 11:55, 11:64, 11:67, 11:119, 13:13, 13:18, 13:47, 13:55, 13:119, 14:03:01-14:03:02, 14:12:01-14:12:02, 14:15, 14:27, 14:40, 14:55, 14:63, 14:67, 14:77-14:78, 14:84-14:85, 14:89, 14:102, 14:115-14:116 |
| 6 | 215 bp | 430 bp | *08:05, 08:18, 08:24-08:25, 08:31, 08:40-08:41, 08:47 | *12:01:01-12:21, 12:23-12:37, 13:17, 13:116, 14:31, 14:52 |
| 7 | 250 bp | 430 bp | *08:01:01-08:03:03, 08:05, 08:07-08:09, 08:11, 08:13-08:19, 08:21, 08:23-08:27, 08:29-08:30:03, 08:32-08:49 | *12:16:01, 12:22, 14:68, 14:93 |
| 87 | 250 bp | 430 bp | *08:04:01-08:04:07, 08:06, 08:10, 08:12, 08:22, 08:28, 08:31 | *11:67, 12:01:01-12:15, 12:17-12:21, 12:23-12:37, 13:17, 13:116, 14:04, 14:11, 14:15, 14:28, 14:31, 14:50, 14:52, 14:71, 14:73, 14:76, 14:79, 14:107, 14:120, 14:126 |
| 9 | 150 bp | 430 bp | *08:09, 08:21, 08:35 | *14:15, 14:40, 14:55, 14:77, 14:84 |
| 108 | 205 bp, 250 bp | 515 bp | *08:12, 08:22, 08:40 | *12:01:01-12:02:05, 12:04-12:15, 12:17-12:18, 12:20-12:21, 12:23-12:37, 13:17, 13:116, 14:28 |
| 11 | 170 bp | 515 bp | *08:08, 08:15, 08:31, 08:41 | *11:67, 12:04, 14:04, 14:11, 14:28, 14:31, 14:50, 14:68, 14:71, 14:73, 14:76, 14:79, 14:93, 14:107, 14:120 |
| 125,9 | 95 bp, 145 bp, 195 bp | 430 bp | *08:13, 08:27, 08:44, 08:48 | *12:12 |
| 1310 | 135 bp, 165 bp, 260 bp | 430 bp | *08:11, 08:33, 08:39 |  |
| 14 | 135 bp | 430 bp | *08:17, 08:28, 08:37, 08:45 | *11:67, 12:01:01-12:20, 12:22-12:37, 13:17 |
| 15 | 175 bp | 430 bp | *08:19, 08:25, 08:34, 08:49 | *12:01:01-12:03:03, 12:05-12:08, 12:10-12:17, 12:19-12:32, 12:34-12:37 |
| 165 | 70 bp | 430 bp | *08:03:02-08:03:03, 08:10, 08:12, 08:14, 08:18-08:19, 08:23, 08:27, 08:29, 08:32-08:33, 08:35-08:38, 08:40, 08:46-08:47, 08:49 | *04:12, 04:86, 04:106, 07:12, 13:03:01-13:04, 13:12:01-13:13, 13:30, 13:32-13:33:03, 13:38, 13:48, 13:58, 13:65-13:66:02, 13:81, 13:89, 13:93-13:95, 13:101, 13:115, 13:118, 13:120, 13:122, 13:139, 14:63, 14:78 |
| 175,11 | 75 bp, 175 bp | 430 bp | *08:04:01, 08:04:02w-08:04:03w, 08:04:04-08:04:07, 08:06, 08:10, 08:12, 08:14, 08:20, 08:22, 08:28 | *04:12, 04:18, 04:25, 04:58, 11:25, 11:67, 11:119, 13:18, 14:12:01-14:12:02, 14:15, 14:78, 14:84, 15:21 |
| 1812 | 150 bp, 225 bp | 430 bp | *08:20, 08:32 | *11:23, 11:25, 11:45, 11:55, 11:64, 11:119, 13:13, 13:18, 13:47, 13:55, 13:119, 14:03:01-14:03:02, 14:12:01-14:12:02, 14:27, 14:40, 14:55, 14:63, 14:67, 14:77-14:78, 14:84-14:85, 14:89, 14:102, 14:115-14:116 |
| 195,13 | 100 bp, 165 bp, 180 bp | 515 bp | *08:07, 08:16, 08:38, 08:49 |  |
| 205 | 125 bp | 515 bp | *08:06, 08:10, 08:12, 08:22 | *03:12, 04:10:01-04:12, 04:67, 04:91, 04:126, 13:04, 13:32, 13:48, 13:58, 13:75, 13:81, 13:89, 13:93-13:94, 13:108, 14:65, 14:78, 15:12 |
| 215 | 120 bp | 515 bp | *08:17, 08:28, 08:37, 08:45 | *11:23, 11:25, 11:45, 11:55, 11:64, 11:67, 11:119, 13:18, 13:119, 15:21 |
| 2214 | 130 bp, 165 bp, 215 bp | 430 bp | *08:19, 08:23, 08:29 | *14:04, 14:11, 14:28, 14:68, 14:71, 14:73, 14:93, 14:120, 14:126 |
| 23 | 250 bp | 430 bp | *08:04:01, 08:04:02w-08:04:03w, 08:04:04-08:04:07, 08:06, 08:10, 08:28, 08:31 | *11:67, 12:03:02-12:03:03, 12:19, 13:17, 13:116, 14:04, 14:11, 14:15, 14:31, 14:50, 14:52, 14:73, 14:76, 14:79, 14:107, 14:120, 14:126 |
| 245,15 | 125 bp, 175 bp | 430 bp | *08:14, 08:26, 08:35-08:36:02 | *03:12, 13:32, 13:65, 13:93, 13:120, 13:139, 14:13, 14:63, 14:65, 14:78, 14:85 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DRB1*08SSP subtypings.

When the primers in a primer mix can give rise to HLA-specific PCR products of more than one length this is indicated if the size difference is more than 20 base pairs. Size differences of 20 base pairs or less are not given. For high resolution SSP kits the respective lengths of the HLA-specific PCR product(s) are given for the alleles amplified by these primer mixes.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DRB1*08 subtyping.

In addition, wells number 5, 10, 11 and 19 to 21 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several DRB1 alleles 1st and/or 3rd exon(s) and beyond, as well as intron nucleotide sequences, are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in these regions are conserved within allelic groups.

4Due to the sharing of sequence motifs within the DR52 group of DRB1 alleles, non-DRB1*08 alleles are amplified by primer mixes 2 to 12, 14 to 18 and 20 to 24.

5HLA-specific PCR products shorter than 125 base pairs have a lower intensity and are less sharp than longer PCR products.

6Primer mixes 2 and 5 may have tendencies of unspecific amplifications.

7Primer mixes 3 and 8 have a tendency to giving rise to primer oligomer formation.

8Primer mix 10: Specific PCR fragment of 205 bp in the DRB1*08:40 and in the DRB1*13:17 and 13:116 alleles. Specific PCR fragment of 250 bp in the DRB1*08:12 and 08:22 and in the DRB1*12:01:01-12:02:05, 12:04-12:15, 12:17-12:18, 12:20-12:21, 12:23-12:37 and 14:28 alleles.

9Primer mix 12: Specific PCR fragment of 95 bp in the DRB1*08:27 allele. Specific PCR fragment of 145 bp in the DRB1 *08:44 allele. Specific PCR fragment of 195 bp in the DRB1*08:13 and 08:48 and in the DRB1*12:12 alleles.

10Primer mix 13: Specific PCR fragment of 135 bp in the DRB1*08:33 allele. Specific PCR fragment of 165 bp in the DRB1*08:11 allele. Specific PCR fragment of 260 bp in the DRB1*08:39 allele.

11Primer mix 17: Specific PCR fragment of 75 bp in the DRB1*08:04:01, 08:04:04-08:04:07, 08:06, 08:10, 08:12, 08:20, 08:22 and 08:28 and in the DRB1*04:12, 04:18, 04:25, 04:58, 11:25, 11:67, 11:119, 13:18, 14:12:01-14:12:02, 14:15, 14:78, 14:84 and 15:21 alleles. Specific PCR fragment of 175 bp in the DRB1*08:14 allele.

12Primer mix 18: Specific PCR fragment of 150 bp in the DRB1*08:32 allele. Specific PCR fragment of 225 bp in the DRB1*08:20 and in the DRB1*11:23, 11:25, 11:45, 11:55, 11:64, 11:119, 13:13, 13:18, 13:47, 13:55, 13:119, 14:03:01-14:03:02, 14:12:01-14:12:02, 14:27, 14:40, 14:55, 14:63, 14:67, 14:77-14:78, 14:84-14:85, 14:89, 14:102 and 14:115-14:116 alleles.

13Primer mix 19: Specific PCR fragment of 100 bp in the DRB1*08:16 and 08:38 alleles. Specific PCR fragment of 165 bp in the DRB1*08:07 allele. Specific PCR fragment of 180 bp in the DRB1*08:49 allele.

14Primer mix 22: Specific PCR fragment of 130 bp in the DRB1*08:23 allele. Specific PCR fragment of 165 bp in the DRB1*08:19 allele. Specific PCR fragment of 215 bp in the DRB1*08:29 and in the DRB1*14:04, 14:11, 14:28, 14:68, 14:71, 14:73, 14:93, 14:120 and 14:126 alleles.

15Primer mix 24: Specific PCR fragment of 125 bp in the DRB1*08:26 and 08:35-08:36:02 and in the DRB1*03:12, 13:32, 13:65, 13:93, 13:120, 13:139, 14:13, 14:63, 14:65, 14:78 and 14:85 alleles. Specific PCR fragment of 175 bp in the DRB1*08:14 allele.

‘w’, may be weakly amplified.

1The sequence of the DRB1*080301 allele has been shown to be identical to DRB1*08:03:02.

2DRB1*08 alleles in bold lettering are listed as confirmed alleles on the on the IMGT/HLA web page www.ebi.ac.uk/imgt/hla, release 3.10.0, October 2012.

3The DRB1*08:20 and DRB1*14:12:01-14:12:02 give rise to identical amplification patterns with the DRB1*08 subtyping kit. These two alleles can be distinguished by the DR low resolution kit and/or the DRB1*14 subtyping kit.

4Primer mix 10: Specific PCR fragment of 205 bp in the DRB1*08:40 and in the DRB1*13:17 and 13:116 alleles. Specific PCR fragment of 250 bp in the DRB1*08:12 and 08:22 and in the DRB1*12:01:01-12:02:05, 12:04-12:15, 12:17-12:18, 12:20-12:21, 12:23-12:37 and 14:28 alleles.

Primer mix 12: Specific PCR fragment of 95 bp in the DRB1*08:27 allele. Specific PCR fragment of 145 bp in the DRB1 *08:44 allele. Specific PCR fragment of 195 bp in the DRB1*08:13 and 08:48 and in the DRB1*12:12 alleles.

Primer mix 13: Specific PCR fragment of 135 bp in the DRB1*08:33 allele. Specific PCR fragment of 165 bp in the DRB1*08:11 allele. Specific PCR fragment of 260 bp in the DRB1*08:39 allele.

Primer mix 17: Specific PCR fragment of 75 bp in the DRB1*08:04:01, 08:04:04-08:04:07, 08:06, 08:10, 08:12, 08:20, 08:22 and 08:28 and in the DRB1*04:12, 04:18, 04:25, 04:58, 11:25, 11:67, 11:119, 13:18, 14:12:01-14:12:02, 14:15, 14:78, 14:84 and 15:21 alleles. Specific PCR fragment of 175 bp in the DRB1*08:14 allele.

Primer mix 18: Specific PCR fragment of 150 bp in the DRB1*08:32 allele. Specific PCR fragment of 225 bp in the DRB1*08:20 and in the DRB1*11:23, 11:25, 11:45, 11:55, 11:64, 11:119, 13:13, 13:18, 13:47, 13:55, 13:119, 14:03:01-14:03:02, 14:12:01-14:12:02, 14:27, 14:40, 14:55, 14:63, 14:67, 14:77-14:78, 14:84-14:85, 14:89, 14:102 and 14:115-14:116 alleles.

Primer mix 19: Specific PCR fragment of 100 bp in the DRB1*08:16 and 08:38 alleles. Specific PCR fragment of 165 bp in the DRB1*08:07 allele. Specific PCR fragment of 180 bp in the DRB1*08:49 allele.

Primer mix 22: Specific PCR fragment of 130 bp in the DRB1*08:23 allele. Specific PCR fragment of 165 bp in the DRB1*08:19 allele. Specific PCR fragment of 215 bp in the DRB1*08:29 and in the DRB1*14:04, 14:11, 14:28, 14:68, 14:71, 14:73, 14:93, 14:120 and 14:126 alleles.

Primer mix 24: Specific PCR fragment of 125 bp in the DRB1*08:26 and 08:35-08:36:02 and in the DRB1*03:12, 13:32, 13:65, 13:93, 13:120, 13:139, 14:13, 14:63, 14:65, 14:78 and 14:85 alleles. Specific PCR fragment of 175 bp in the DRB1*08:14 allele.

‘w’, may be weakly amplified.