PHOTO DOCUMENT

Olerup SSP AB

Olerup SSPTM DRB3

Prod. No:	101.121-24/04 – including Taq pol.

101.121-24u/04u – without Taq pol.

Lot No:    	Y16

Expiry Date:    	2009-July-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ug/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 24 primer mixes used for DRB3 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified DRB3 alleles3 | Amplified DRB14 alleles |
| --- | --- | --- | --- | --- |
| 15,6,14 | 100, 210 bp | 515 bp | 010101-0108, 0110, 0111, 0205, 0217, 030101-030102, 0303 | 1130weakly, 1367, 1446 |
| 25 | 125 bp | 430 bp | 010101-0106, 0108, 0110, 0111, 030101-030102, 0303 | 0807weakly, 0819weakly, 0825weakly, 1331weakly, 1346weakly, 1354weakly, 1448 weakly |
| 35 | 95 bp | 515 bp | 010101-0102, 0104-0108, 0110, 0111 |  |
| 45 | 85 bp | 430 bp | 0102 |  |
| 55 | 95 bp | 430 bp | 0103 | 1446 |
| 6 | 190 bp | 430 bp | 0104 |  |
| 75 | 90 bp | 515 bp | 0105 |  |
| 85 | 120 bp | 430 bp | 0106, 0108 | 1446 |
| 9 | 165 bp | 430 bp | 0107, 0201-0208, 0211, 0213-0222 |  |
| 10 | 185 bp | 430 bp | 0109, 0201-0204, 0206-0214, 0216-0222, 0302 |  |
| 11 | 270 bp | 515 bp | 0201, 0204, 030101- 0302 |  |
| 125,7 | 90, 145 bp | 515 bp | 0201, 0204, 0217 | 1143, 1150, 1459 |
| 13 | 270 bp | 515 bp | 010101- 0111, 020201-0203, 0205-0213, 0215-0222, 0303 | 1130, 1367, 1446 |
| 149 | 185 bp | 515 bp | 0107, 0109, 020201-020205, 0205-0213, 0215-0219, 0222 | 100101-100102weakly, 1149weakly |
| 155,8 | 120, 180 bp | 430 bp | 0203, 0216, 030101-0303 |  |
| 165,9,10 | 100, 155 bp | 515 bp | 0109, 0204, 0215, 0216, 0219, 0222 | 1144weakly, 1149weakly, 1150weakly |
| 175 | 120 bp | 430 bp | 0108, 0206, 0220 | 1367, 1446 |
| 185 | 100 bp | 430 bp | 0109, 0207, 0209, 0221 |  |
| 1911 | 180, 270 bp | 515 bp | 0208, 0214, 0218 | 1130 |
| 2012 | 165, 180 bp | 430 bp | 010101-0106, 0108-0111, 0209, 0210, 0216, 030101-0303 | 1130, 1367, 1446 |
| 215,13,14 | 125, 180, 210 bp | 430 bp | 0110, 0211, 0216 |  |
| 2215 | 185, 245 bp | 430 bp | 0111, 0212 |  |
| 23 | 195 bp | 515 bp | 0213 |  |
| 24 | 185 bp | 430 bp | 0209, 0218, 0219, 0221, 030101-0303 | 1130 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DRB3 SSP subtypings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 bp or more. Size differences shorter than 20 bp are not given. For high resolution SSP kits the length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control band may sometimes be observed. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most tubes, or a band of 515 base pairs, for some tubes.

Tube number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DRB3 subtyping.

In addition, tubes number 3, 7, 11, 12, 13, 14, 16, 19 and 23 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several DRB alleles only partial second exon nucleotide sequences are available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in the first hyperpolymorphic region of the second exon of DRB alleles are conserved within allelic groups and that unknown sequences of codons 87 to 92 are identical with the DRB1*0101 consensus sequence.

4Due to the sharing of sequence motifs between DRB3 and DRB1 alleles, primer mixes 1, 2, 5, 8, 12 to 14, 16, 17, 20 and 24 will amplify a few DRB1 alleles.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6Primer mix 1: Specific PCR fragment of 100 bp in the DRB3*010101 to 0108, 0110, 0111, 0205, 030101-030102, 0303 and DRB1*1130, 1367 and 1146 alleles. Specific PCR fragment of 210 bp in the DRB3*0217 allele.

7Primer mix 12: Specific PCR fragment of 90 bp in the DRB3*0217 allele. Specific PCR fragment of 145 bp in the DRB3*0201, 0204 and DRB1*1143, 1150 and 1459 alleles.

8Primer mix 15: Specific PCR fragment of 120 bp DRB3*0203, 030101 to 0303 alleles. Specific PCR fragment of 180 bp in the DRB3*0216 allele.

9Primer mixes 14 and 16 has a tendency to giving rise to nonspecific amplifications.

10Primer mix 16: Specific PCR fragment of 100 bp in the DRB3*0216 allele. Specific PCR fragment of 155 bp in the DRB3*0109, 0204, 0215, 0219 and 0222 and DRB1*1144, 1149 and 1150 alleles.

11Primer mix 19: Specific PCR fragment of 180 bp DRB3*0208, 0218 and DRB1*1130 alleles. Specific PCR fragment of 270 bp in the DRB3*0214 allele.

12Primer mix 20: Specific PCR fragment of 165 bp DRB3*010101 to 0106, 0108 to 0111, 0209, 0210, 030101 to 0303 and DRB1*1130, 1367 and 1446 alleles. Specific PCR fragment of 180 bp in the DRB3*0216 allele.

13Primer mix 21: Specific PCR fragment of 125 bp in the DRB3*0110. Specific PCR fragment of 180 bp in the DRB3*0216 allele. Specific PCR fragment of 210 bp in the DRB3*0211 allele.

14Primer mixes 1 and 21 may give rise to a primer oligomer formation.

15Primer mix 22: Specific PCR fragment of 185 bp in the DRB3*0111 allele. Specific PCR fragment of 245 bp in the DRB3*0212 allele.

1Primer mix 1: Specific PCR fragment of 100 bp in the DRB3*010101 to 0108, 0110, 0111, 0205, 030101-030102, 0303 and DRB1*1130, 1367 and 1146 alleles. Specific PCR fragment of 210 bp in the DRB3*0217 allele.

Primer mix 12: Specific PCR fragment of 90 bp in the DRB3*0217 allele. Specific PCR fragment of 145 bp in the DRB3*0201, 0204 and DRB1*1143, 1150 and 1459 alleles.

Primer mix 15: Specific PCR fragment of 120 bp DRB3*0203, 030101 to 0303 alleles. Specific PCR fragment of 180 bp in the DRB3*0216 allele.

Primer mix 16: Specific PCR fragment of 100 bp in the DRB3*0216 allele. Specific PCR fragment of 155 bp in the DRB3*0109, 0204, 0215, 0219 and 0222 and DRB1*1144, 1149 and 1150 alleles.

Primer mix 19: Specific PCR fragment of 180 bp DRB3*0208, 0218 and DRB1*1130 alleles. Specific PCR fragment of 270 bp in the DRB3*0214 allele.

Primer mix 20: Specific PCR fragment of 165 bp DRB3*010101 to 0106, 0108 to 0111, 0209, 0210, 030101 to 0303 and DRB1*1130, 1367 and 1446 alleles. Specific PCR fragment of 180 bp in the DRB3*0216 allele.

Primer mix 21: Specific PCR fragment of 125 bp in the DRB3*0110. Specific PCR fragment of 180 bp in the DRB3*0216 allele. Specific PCR fragment of 210 bp in the DRB3*0211 allele.

Primer mix 22: Specific PCR fragment of 185 bp in the DRB3*0111 allele. Specific PCR fragment of 245 bp in the DRB3*0212 allele.

‘w’, might be weakly amplified.

Change in revision R01 compared to R00:

- The length of the internal positive control band in primer mix 16 has been corrected to 515 bp in the Specificity and Interpretation Tables.