PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® DRB4

Prod. No:	101.122-24/24u

101.122-06/06u

Lot No:    	45G

Expiry Date:    	2011-October-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 12 primer mixes used for DRB4 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified DRB4 alleles |
| --- | --- | --- | --- |
| 1 | 185 bp | 515 bp | *01010101, 01030101-010304, 0105-0107 |
| 2 | 140 bp | 430 bp | *0102 |
| 33 | 130 bp | 430 bp | *01010101, 0104?, 0105?, 0106, 0107?, 0201N, 0301N |
| 4 | 245 bp | 515 bp | *01010101-01030101, 010302-0104, 0105?, 0106, 0107, 0201N |
| 54 | 155 bp | 430 bp | *01030102N |
| 6 | 190 bp | 430 bp | *0104 |
| 75 | 155 bp | 430 bp | *0102-010304, 0104?, 0105?, 0107? |
| 8 | 290 bp | 515 bp | *01010101, 0104?-0107?, 0201N?, 0301N |
| 96 | 155 bp | 515 bp | *0105 |
| 10 | 85 bp | 515 bp | *0201N |
| 11 | 110 bp | 430 bp | *0106 |
| 12 | 210 bp | 430 bp | *0107 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DRB4 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DRB4 subtyping.

In addition, wells number 4, 8, 9 and 10 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3Primer mix 3 may yield somewhat less specific PCR product than the other DRB4 primer mixes.

4Primer mix 5 may have tendencies of unspecific amplifications.

5The DRB1*15010101 to DRB1*1541 and DRB1*160101 to DRB1*160502 and DRB1*1607 to DRB1*1615 alleles might be faintly amplified by primer mix 7.

6Primer mix 9 might have tendencies of primer dimer formation.

‘?’ The nucleotide sequences of the 3rd exon of the DRB4*0104, DRB4*0105 and DRB4*0107 alleles are not yet available. Thus, it is not known whether the DRB4*0104, DRB4*0105 and DRB4*0107 alleles will be amplified by primer mix 3 or 7. The complete 2nd exon nucleotide sequence of the DRB4*0105 allele is not known. Thus, it is not known whether the DRB4*0105 allele will be amplified by primer mix 4 or not. Second intron sequences of the DRB4*0104 to DRB4*0107 and the DRB4*0201N alleles is not known. Thus, it is not known whether  these alleles will be amplified by primer mix 8 or not.

1The DRB1*15010101 to DRB1*1541 and DRB1*160101 to DRB1*160502 and DRB1*1607 to DRB1*1615 alleles might be faintly amplified by primer mix 7.

2The DRB4*01010102N allele has been renamed to DRB4*01030102N.