Olerup SSP®

Olerup SSP® DRB5

Prod. No:	101.123-24/24u

101.123-06/06u

Lot No:    	49R

Expiry Date:    	2015-May-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

PHOTO DOCUMENT

Specificities and sizes of the PCR products of the 16 primer mixes used for DRB5 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified DRB53 alleles | Other amplified DRB alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 255 bp | 515 bp | *01:01:01-01:05, 01:07-01:14, 02:03 | DRB1*09:07 |
| 2 | 210 bp | 515 bp | *01:01:01-01:05, 01:07-01:10N, 01:12-01:14, 02:04 | DRB1*09:07 |
| 36 | 225 bp | 430 bp | *01:01:01-01:02, 01:04-01:05, 01:07-01:10N, 01:12-01:14, 02:05 | DRB1*09:07 |
| 45,7,8 | 100 bp, 150 bp | 430 bp | *01:01:01-01:01:02, 01:04, 01:06-01:07, 01:09, 01:11, 02:06 |  |
| 5 | 150 bp | 515 bp | *01:01:01, 01:05, 01:07, 01:09, 01:13 |  |
| 6 | 145 bp | 430 bp | *01:02-01:03, 01:05, 01:08N, 01:10N |  |
| 7 | 150 bp | 430 bp | *01:02-01:03, 01:08N, 01:10N |  |
| 8 | 215 bp | 430 bp | *01:03, 01:06, 01:11, 02:02-02:04, 02:06 |  |
| 99 | 175 bp, 225 bp | 430 bp | *01:04, 01:13 |  |
| 1010 | 130 bp, 160 bp | 430 bp | *01:07, 01:12 |  |
| 11 | 200 bp | 430 bp | *01:06, 01:11, 02:02-02:03, 02:06 |  |
| 12 | 185 bp | 515 bp | *02:02, 02:04-02:06 |  |
| 13 | 195 bp | 430 bp | *01:08N |  |
| 145,11 | 110 bp, 210 bp | 430 bp | *01:09, 01:14 |  |
| 15 | 240 bp | 430 bp | *01:10N, 01:12 | DRB1*09:07 |
| 16 | 140 bp | 430 bp | *02:05 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DRB5 SSP subtypings.

When the primers in a primer mix can give rise to HLA-specific PCR products of more than one length this is indicated if the size difference is more than 20 base pairs. Size differences of 20 base pairs or less are not given. For high resolution SSP kits the respective lengths of the HLA-specific PCR product(s) are given for the alleles amplified by these primer mixes.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the DRB5 subtyping.

In addition, wells number 2, 5 and 12 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several DRB alleles 1st and/or 3rd exon(s) and above, as well as intron nucleotide sequences, are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in these regions are conserved within allelic groups and that unknown sequences of codons 87 to 92 are identical with the DRB1*01:01 consensus sequence.

4Due to the sharing of sequence motifs between DRB alleles the DRB1*09:07 allele will be amplified by primer mixes 1, 2, 3 and 15.

5HLA-specific PCR products shorter than 125 base pairs have a lower intensity and are less sharp than longer PCR products.

6Primer mix 3 frequently gives rise to an extra band longer than the control band. This band should be disregarded in the interpretation of DRB5 SSP typings.

7Primer mix 4 has a tendency to giving rise to primer oligomer formation.

8Primer mix 4: Specific PCR fragment of 100 bp in the DRB5*01:01:01-01:01:02, 01:04, 01:06-01:07, 01:09 and 01:11 alleles. Specific PCR fragment of 150 bp in the DRB5*02:06 allele.

9Primer mix 9: Specific PCR fragment of 175 bp in the DRB5*01:13 allele. Specific PCR fragment of 225 bp in the DRB5*01:04 allele.

10Primer mix 10: Specific PCR fragment of 130 bp in the DRB5*01:07 allele. Specific PCR fragment of 160 bp in the DRB5*01:12 allele.

11Primer mix 14: Specific PCR fragment of 110 bp in the DRB5*01:14 allele. Specific PCR fragment of 210 bp in the DRB5*01:09 allele.

1The DRB5*0201 allele has been shown to be identical to DRB5*02:02.

2Primer mix 4: Specific PCR fragment of 100 bp in the DRB5*01:01:01-01:01:02, 01:04, 01:06-01:07, 01:09 and 01:11 alleles. Specific PCR fragment of 150 bp in the DRB5*02:06 allele.

Primer mix 9: Specific PCR fragment of 175 bp in the DRB5*01:13 allele. Specific PCR fragment of 225 bp in the DRB5*01:04 allele.

Primer mix 10: Specific PCR fragment of 130 bp in the DRB5*01:07 allele. Specific PCR fragment of 160 bp in the DRB5*01:12 allele.

Primer mix 14: Specific PCR fragment of 110 bp in the DRB5*01:14 allele. Specific PCR fragment of 210 bp in the DRB5*01:09 allele.