PHOTO DOCUMENT

Olerup SSP AB

Olerup SSPTM HLA-A low resolution

Prod. No:	101.401-48/12 – including Taq pol.

101.401-48u/12u – without Taq pol.

Lot No:    	X92

Expiry Date:    	2009-June-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ug/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 23 primer mixes used for HLA-A low resolution SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | HLA-A serology3 | Amplified HLA-A alleles4,10 |
| --- | --- | --- | --- | --- |
| 15 | 120, 145 bp | 800 bp | A1, A36 | 01010101-0104N, 0106-0127N, 3601-3604 |
| 26 | 135, 200, 255 bp | 1070 bp | A2 | 02010101-0222, 0224-023501, 023503-0247, 0249-0297, 0299, 9201-9221, 9223-9226 |
| 37 | 205, 235 bp | 1070 bp | A1, A3, A11, A32, A34, A36 | 0112, 0119, 0121, 03010101-0317, 0319-0330, 1125, 3204, 3402-3404, 3407, 3408, 3602 |
| 47 | 190 bp | 800 bp | A1, A2, A3, A11, A24, A26, A30, A36 | 01010101-0104N, 0106, 0107, 0109-0111N, 0113, 0116N-0118N, 0120-0127N, 0278, 0312, 0318, 110101-1132, 2619, 3008, 3604 |
| 5 | 160, 535 bp | 800 bp | A3, A23, A24, A31, A32 | 0330, 2301-2316, 24020101-2411N, 2413-2415, 2417-2479, 3108, 3205, 3213 |
| 6 | 165, 200 bp | 800 bp | A2, A23, A24, A29, A80 | 9222, 2301-2316, 2405, 2424, 2465, 2907, 8001 |
| 7 | 175, 205 bp | 1070 bp | A2, A23, A24, A26 | 021701-021702weakly, 2314, 24020101-2411N, 2413, 2417-2450, 2454-2456, 2458-2463, 2465-2479, 2616 |
| 8 | 165, 200 bp | 800 bp | A2, A3, A11, A25, A26, A32, A34, A66, A68, A69 | 0255, 0324, 1110, 250101-2506, 260101-2606, 2608-2615, 2617, 2618, 2620-2635, 3215, 3401-3408, 6601-6606, 680101-6840, 6901 |
| 95 | 75 bp | 800 bp | A2, A25, A32 | 9224, 250101-2506, 320101-3202, 3204, 3206-3215 |
| 105 | 85 bp | 1070 bp | A26, A33 | 260101-2602, 2604, 260701-2618, 2620, 2622-2629, 2632-2635, 3313 |
| 115,7,8 | 80, 175, 500 bp | 1070 bp | A1, A2, A11, A24, A26, A31, A34, A66 | 0113, 0227, 110101-1132, 2419, 2444, 2603, 2606, 2621, 3103, 3401-3408, 6601, 6604-6606 |
| 12 | 185 bp | 800 bp | A11, A25, A26, A31, A34, A43, A66 | 1111, 2506, 2609, 3103, 3104, 3401-3408, 4301, 6602, 6603 |
| 137 | 175, 225 bp | 1070 bp | A1, A2, A3, A25, A26, A34, A43, A66 | 0113, 0234-023503, 0256, 0262, 9203, 03010101-0307, 0309-0311N, 0313-0330, 250101-2505, 260101-260105, 2602weakly, 2603, 2605-2608, 2610-2633, 2635, 3408, 4301, 6601, 6604-6606 |
| 14 | 200, 240 bp | 1070 bp | A29, A33 | 29010101-2916, 3313 |
| 155 | 90 bp | 1070 bp | A30 | 300101-3004, 3006-3022 |
| 16 | 180, 210 bp | 1070 bp | A29, A31 | 2914, 310102-3118 |
| 17 | 180 bp | 1070 bp | A29, A32 | 2913, 320101-3203, 3205-3215 |
| 18 | 200 bp | 1070 bp | A33, A68 | 3301, 330301-3313, 6829 |
| 19 | 160, 200 bp | 800 bp | A74 | 7401-7412N |
| 20 | 155, 240 bp | 800 bp | A2, A210, A25, A30, A68 | 0210, 0234-023503, 0239, 0246, 0248, 0250, 0252, 0256, 0262, 0270, 0273, 0278, 0293, 0295, 9203, 9210, 9214, 9217, 9222, 2505, 3008, 680101-6840 |
| 21 | 240, 375 bp | 800 bp | A2, A26, A68, A69 | 0255, 2622, 6829, 6901 |
| 225,9 | 85, 240 bp | 800 bp | A2, A30, A36 | 0234-023503, 0246, 0248, 0256, 0262, 0270, 0278, 9203, 3008, 3601-3604 |
| 235 | 75, 160 bp | 800 bp | A2, A26, A68, A80 | 0255, 2603, 2605, 2606, 2621, 2630, 6805, 6815, 6820, 8001 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-A low resolution SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 bp or more. Size differences shorter than 20 bp are not given. For high resolution SSP kits the length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control band may sometimes be observed. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most tubes, or a band of 800 base pairs, for some tubes.

Tube number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-A low resolution typing.

In addition, tubes number 4, 5, 6, 8, 9, 12, 19 to 23 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3The serological reactivity of all HLA-A alleles is not known. In this table we used the information published in Tissue Antigens 1999: 54: 409-437, also available at the www.worldmarrow.org web site and also inferred the serological grouping from the naming of the sequence-defined allele.

4For several HLA-A alleles only partial 1st exon nucleotide sequences are available. We assume that unknown sequences are conserved within allelic groups.

The nucleotide sequence of the A*0128 allele is not yet retrievable from the GenBank or EMBL data banks.

5Specific PCR fragments shorter than 125 base pairs have a lower intensity than longer PCR bands.

6The primer pairs in vial 2 will in most samples give rise to two specific PCR fragments.

7Primer mixes 3, 4, 11 and 13 may give rise to nonspecific amplifications.

6The primer pairs in vial 11 will in most samples give rise to two to three specific PCR fragments.

9Primer mix 22 might faintly amplify most A*11 alleles.

10The A*0318 and A*2619 alleles will give rise to identical amplification patterns. These two alleles can be separated by the respective high resolution SSP primer sets.

The A*2314, A*2405, A*2424 and A*2465 alleles will give rise to identical amplification patterns. These four alleles can be separated by the respective high resolution SSP primer sets.

‘w’, might be weakly amplified.

1The nucleotide sequence of the A*0128 allele is not yet retrievable from the GenBank or EMBL data banks.

The sequence of the A*0105N has been shown to be identical to A*0104N.

The sequence of the A*0223 allele has been shown to be identical to A*0222.

The sequence of the A*0298 allele has been shown to be identical to A*0296.

The  sequence of the A*2401 allele has been shown to be in error.

The sequence of the A*2412 allele has been shown to be identical to A*2408.

The A*2416 allele has been renamed to A*3108.

The sequence of the A*3005 allele has been shown to be identical to A*3004.

The sequence of the A*31011 allele has been shown to be identical to A*31012.

The sequence of the A*3302 allele has been shown to be identical to A*3303.

2The serological reactivity of all HLA-A alleles is not known. In this table we used the information published in Tissue Antigens 1999: 54: 409-437, also available at the www.worldmarrow.org web site and also inferred the serological grouping from the naming of the sequence-defined allele.

3The A*0318 and A*2619 alleles will give rise to identical amplification patterns. These two alleles can be separated by the respective high resolution SSP primer sets.

4The A*2314, A*2405, A*2424 and A*2465 alleles will give rise to identical amplification patterns. These four alleles can be separated by the respective high resolution SSP primer sets.

5The primer pairs in vial 2 will in most samples give rise to two specific PCR fragments.

The primer pairs in vial 11 will in most samples give rise to two to three specific PCR fragments.

‘w’, might be weakly amplified.