PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-A low resolution

Prod. No:	101.401-48/48u

101.401-12/12u

Lot No:    	62G

Expiry Date:    	2011-November-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 23 primer mixes used for HLA-A low resolution SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | HLA-A serology3 | Amplified HLA-A alleles4,10,11 |
| --- | --- | --- | --- | --- |
| 15 | 120 bp, 145 bp | 800 bp | A1, A36 | *01010101-0104N, 0106-0145, 3601-3604 |
| 26 | 135 bp, 200 bp, 255 bp | 1070 bp | A2, A19, A28, A203, A210 | *02010101-020115, 020117-020119, 020121-022202, 0224-023501, 023503-0247, 0249-029702, 0299, 9201-9221, 9223-9228, 9230-9295 |
| 312 | 205 bp, 235 bp | 1070 bp | A1, A3, A11, A32, A34, A36 | *0112, 0119, 0121, 03010101-0317, 0319-0362, 1125, 2492, 3029, 3204, 3402-3404, 3407, 3408, 3602 |
| 4 | 190 bp | 800 bp | A1, A2, A3, A11, A26, A30, A36 | *01010101-0104N, 0106, 0107, 0109-0111N, 0113, 0116N-0118N, 0120-0129, 0131N-0145, 0278, 9269, 0312, 0318, 110101-1127, 1129-1153, 2619, 3008, 3604 |
| 5 | 160 bp, 535 bp | 800 bp | A3,A9,A23, A24, A31, A32 | *0330, 230101-2322, 24020101-2411N, 241301-2415, 2417-2464, 2466-2488, 2490N-2499, 3108, 3205, 3213 |
| 6 | 165 bp, 200 bp | 800 bp | A2,A9,A23, A24, A29, A80 | *9222, 230101-2322, 2405, 241302, 2424, 2907, 8001, B*1827 |
| 77 | 175 bp, 200 bp | 1070 bp | A2, A23, A24, A26, A33 | *021701w, 021702w, 2314, 24020101-2411N, 241301, 241302, 2417-2450, 2454-2456, 2458-2463, 2466-2491, 2493, 2495-2499, 2616, 3319, 6845 |
| 8 | 165 bp, 200 bp | 800 bp | A2, A3, A10, A11, A25, A26, A28,A32, A34, A66, A68, A69 | *0255, 0324, 0350, 1110, 250101-2510, 260101-2606, 2608-2615, 2617, 2618, 2620-2641, 3215, 340101-3408, 6601-6611, 680101-6848, 6901 |
| 95 | 75 bp | 800 bp | A25, A32 | *250101-2510, 320101-3202, 3204, 3206-3220 |
| 105,7 | 85 bp | 1070 bp | A2, A10, A26, A33 | *9246, 260101-2602, 2604, 260701-2618, 2620, 2622-2629, 2632-2641, 3313 |
| 115,6,7 | 80 bp, 175 bp, 500 bp | 1070 bp | A1, A11, A24, A26, A31, A34, A66 | *0113, 0128, 110101-1127, 1129-1153, 2419, 2444, 2603, 2606, 2621, 3103, 340101-3408, 6601, 6604-6610 |
| 12 | 185 bp | 800 bp | A11, A25, A26, A31, A34, A43, A66 | *1111, 2506, 2609, 3103, 3104, 340101-3408, 4301, 6602, 6603 |
| 13 | 175 bp, 225 bp | 1070 bp | A1, A2, A3, A25, A26, A34, A43, A66, A74 | *0113, 0234-023503, 025601, 025602, 0262, 9203, 9235, 03010101-0307, 0309-0311N, 0313-0331, 0333-0335, 0337-0340, 0342-0356, 0358, 0360-0362, 250101-2505, 2507-2510, 260101-260112, 2602w, 2603, 2605-2608, 2610-2633, 2635-2641, 3408, 4301, 6601, 6604-6611, 7413 |
| 14 | 200 bp, 240 bp | 1070 bp | A29, A33 | *29010101-2920, 3313 |
| 155 | 90 bp, 135 bp, 205 bp | 1070 bp | A1, A30 | *0113, 0128, 0343, 300101-3004, 3006-3020, 3022-3031 |
| 16 | 370 bp, 395 bp | 1070 bp | A31, A32 | *2914, 310102-3127, 3205 |
| 17 | 150 bp, 180 bp | 1070 bp | A29, A32 | *0343, 2913, 320101-3203, 3205-3220 |
| 18 | 200 bp | 1070 bp | A33, A68 | *330101-330103, 330301-3328, 6829 |
| 19 | 160 bp, 200 bp | 800 bp | A74 | *2919, 7401-7414N |
| 208 | 155 bp, 200 bp, 240 bp | 800 bp | A2, A210, A25, A68 | *0210, 0234-023503, 0239, 0246, 0248, 0250, 0252, 025601, 025602, 0262, 0270, 0273, 0278, 0293, 0295, 9203, 9210, 9214, 9217, 9222, 9229, 9256, 2494, 2505, 680101-6848 |
| 21 | 240 bp, 375 bp | 800 bp | A2, A24, A26, A68, A69 | *0255, 2482, 2622, 3322, 6609, 6829, 6901 |
| 225,9 | 85 bp, 240 bp | 800 bp | A2, A36 | *0234-023503, 0246, 0248, 025601, 025602, 0262, 0270, 0278, 9203, 9229, 3601-3604 |
| 235,7 | 75 bp, 160 bp | 800 bp | A2, A26, A68, A80 | *0255, 2603, 2605, 2606, 2621, 2630, 3324, 6805, 6815, 6820, 8001 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-A low resolution SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengthS of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-A low resolution typing.

In addition, wells number 4, 5, 6, 8, 9, 12, 19 to 23 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3The serological reactivity of all HLA-A alleles is not known. In this table we use the information in the HLA Dictionary 2008 on the www.ebi.ac.uk/imgt/hla web site, the information available at the www.worldmarrow.org web site, the expert-assigned serological grouping in Tissue Antigens (2009) 73:95-170 and have also inferred the serological grouping from the naming of the sequence-defined allele.

4For several HLA-A alleles only partial 1st exon nucleotide sequences are available. We assume that unknown sequences are conserved within allelic groups.

Nucleotide sequence information is available for only exons 2 and 3 of many HLA Class I alleles and for only exon 2 of many HLA Class II alleles and not for other exons or for the introns of these alleles. We assume that unknown sequences in these exons and in the introns are conserved within loci and within allelic groups.

5Specific PCR fragments shorter than 125 base pairs have a lower intensity and are less sharp than longer PCR bands.

6The primer pairs in vial 2 and 11 will in most samples give rise to two specific PCR fragments.

7Primer mixes 7, 10, 11 and 23 may yield less specific PCR product than the other primer mixes.

8Primer mix 20 may give rise to nonspecific amplifications.

9Primer mix 22 might faintly amplify most A*11 alleles.

10The A*0318 and A*2619 alleles will give rise to identical amplification patterns. These two alleles can be separated by the respective high resolution SSP primer sets.

The A*2314, A*2405, A*241302 and A*2424 alleles will give rise to identical amplification patterns. These four alleles can be separated by the respective high resolution SSP primer sets.

The A*2631 and A*6611 alleles will give rise to identical amplification patterns. These two alleles can be separated by the respective high resolution SSP primer sets.

11Primer mix 6 will amplify the B*1827 allele.

12Primer mix 3 may faintly amplify the A*30:04, 30:06, 30:17 and 30:29 alleles.

‘w’, might be weakly amplified.

1The A*0318 and A*2619 alleles will give rise to identical amplification patterns. These two alleles can be separated by the respective high resolution SSP primer sets.

The A*2314, A*2405, A*2424 and A*2465 alleles will give rise to identical amplification patterns. These two alleles can be separated by the respective high resolution SSP primer sets.

The A*2631 and A*6611 alleles will give rise to identical amplification patterns. These two alleles can be separated by the respective high resolution SSP primer sets.

The sequence of the A*0105N has been shown to be identical to A*0104N.

The A*020116 allele has been renamed to A*9234.

The A*020120 has been renamed to A*020118.

The sequence of the A*0223 allele has been shown to be identical to A*0222.

The sequence of the A*0298 allele has been shown to be identical to A*0296.

The A*1128 allele has been renamed to A*111502.

The  sequence of the A*2401 allele has been shown to be in error.

The sequence of the A*2412 allele has been shown to be identical to A*2408.

The A*2416 allele has been renamed to A*3108.

The A*2465 allele has been renamed to A*241302.

The sequence of the A*3005 allele has been shown to be identical to A*3004.

The A*3021 allele has been renamed to A*301102.

The sequence of the A*31011 allele has been shown to be identical to A*310102.

The sequence of the A*3302 allele has been shown to be identical to A*3303.

2The serological reactivity of all HLA-A alleles is not known. In this table we use the information in the HLA Dictionary 2008 on the www.ebi.ac.uk/imgt/hla web site, the information available at the www.worldmarrow.org web site, the expert-assigned serological grouping in Tissue Antigens (2009) 73:95-170 and have also inferred the serological grouping from the naming of the sequence-defined allele.

3The primer pairs in vials 2 and 11 will in most samples give rise to two specific PCR fragments.

‘w’, may be weakly amplified.

Changes in revision R01 compared to R00:

- Primer mix 3 may faintly amplify the A*30:04, 30:06, 30:17 and 30:29 alleles.