PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-A low resolution

Prod. No:	101.401-48/48u

101.401-12/12u

Lot No:    	02N

Expiry Date:    	2014-April-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 31+1 primer mixes used for HLA-A low resolution SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | HLA-A serology3 | Amplified HLA-A alleles4,5,6 |
| --- | --- | --- | --- | --- |
| 17,9 | 120 bp, 145 bp | 800 bp | A1, A36 | *01:01:01:01-01:01:31, 01:01:33-01:04N, 01:06-01:33, 01:35-01:68, 01:70-01:101, 36:01-36:05 |
| 28 | 210 bp, 255 bp, 365 bp, 415 bp | 800 bp | A2,A19, A28, A203, A210, A3, A11, A9, A26, A30, A68 | *02:01:01:01-02:01:15, 02:01:17-02:01:19, 02:01:21-02:22:02, 02:24:01-02:35:01, 02:35:03-02:47, 02:49-02:77, 02:78w, 02:79:01-02:97:02, 02:99, 02:101:01-02:128, 02:130-02:323, 02:325-02:326, 03:01:03w, 03:09w, 03:23:01w, 03:89 w, 03:108 w, 11:06w, 11:18 w, 24:28w, 24:89w, 26:03:01-26:03:02w, 26:06w, 26:07:02w, 26:21w, 26:30w, 30:13w, 30:16w, 30:44w, 30:46w, 68:05w, 68:15w, 68:20w, 68:30w |
| 39 | 235 bp | 1070 bp | A3,A32/A3, A36 | *03:01:01:01-03:01:29, 03:01:31-03:04:02, 03:06-03:09, 03:11N-03:17, 03:19-03:39, 03:41, 03:43-03:74, 03:76-03:94, 03:96-03:97, 03:99-03:104, 03:106-03:121, 03:123-03:132, 32:04, 36:02 |
| 4 | 190 bp | 800 bp | A1,A3,A11, A30, A36, A68 | *01:01:01:01-01:01:22, 01:01:24-01:04N, 01:06-01:07, 01:09-01:11N, 01:13, 01:16N-01:18N, 01:20-01:29, 01:31N-01:33, 01:35-01:78, 01:80-01:98, 01:100-01:101, 02:78, 02:169, 03:12, 03:18, 03:88, 11:01:01-11:27, 11:29-11:106, 26:19, 30:08, 36:04, 68:13, 68:66 |
| 58,16 | 160 bp, 535 bp | 800 bp | A3, A9, A23, A24, A2403, A31, A32 | *01:95, 03:30, 23:01:01-23:46, 24:02:01:01-24:11N, 24:13:01-24:15, 24:17-24:64, 24:66-24:88, 24:90N-24:128, 24:130-24:182, 31:08, 32:05, 32:13 |
| 611 | 135 bp, 175 bp, 210 bp | 800 bp | A9,A23, A24, A29, A80 | *23:01:01-23:46, 24:05, 24:13:02, 24:24, 29:07, 31:29, 80:01-80:02, B*18:27 |
| 78 | 175 bp, 205 bp | 1070 bp | A2, A9, A23, A24, A2403, A26, A33 | *02:17:01w-02:17:02w, 23:14, 24:02:01:01-24:11N, 24:13:01-24:13:02, 24:17-24:50, 24:54-24:56, 24:58-24:63, 24:66-24:91, 24:93, 24:95-24:113, 24:115-24:137, 24:139-24:182, 26:16, 33:19, 68:45 |
| 88 | 165 bp, 200 bp | 800 bp | A2/A28, A3, A10, A11, A25, A26, A32, A34, A66, A68, A69 | *01:51, 02:55, 03:24, 03:50, 11:10, 25:01:01-25:16, 26:01:01-26:06, 26:08-26:15, 26:17-26:18, 26:20-26:43:02, 26:45-26:63, 26:65-26:69, 29:28, 32:15, 33:51, 34:01:01-34:09, 66:01-66:16, 68:01:01:01-68:83, 69:01 |
| 97,15 | 75 bp | 800 bp | A25, A32 | *25:01:01-25:16, 32:01:01-32:02, 32:04, 32:06-32:36 |
| 107 | 85 bp | 1070 bp | A10, A26, A33 | *01:51, 01:83, 02:146, 26:01:01-26:02, 26:04, 26:07:01-26:18, 26:20, 26:22-26:29, 26:31-26:43:02, 26:45-26:69, 33:13, 33:48 |
| 117,8 | 80 bp, 175 bp, 500 bp | 1070 bp | A1, A9, A11, A26, A31, A34, A66 | *01:13, 01:28, 03:63, 03:88, 11:01:01-11:27, 11:29-11:106, 24:19, 24:44, 26:03:01-26:03:02, 26:06, 26:21, 31:03, 34:01:01-34:08, 66:01, 66:04-66:11, 66:13-66:15, 80:02 |
| 127 | 125 bp, 185 bp | 800 bp | A3, A10, A25, A26, A31, A34, A43, A66 | *02:309, 03:01:19, 11:11, 25:05-25:06, 26:09, 26:54, 31:03-31:04, 34:01:01-34:09, 43:01, 66:02-66:03, 66:16 |
| 13 | 175 bp, 225 bp | 1070 bp | A1, A2, A3, A10, A25, A26, A34, A43, A66 | *01:13, 02:34-02:35:03, 02:56:01-02:56:02, 02:62, 02:103, 02:135, 03:01:01:01-03:01:22, 03:01:24-03:07, 03:09-03:11N, 03:13-03:31, 03:33-03:35, 03:37-03:40, 03:42-03:56, 03:58, 03:60-03:71, 03:73-03:87, 03:90-03:106, 03:109-03:110, 03:112-03:132, 25:01:01-25:05, 25:07-25:16, 26:01:01-26:01:20, 26:01:22, 26:02w, 26:03:01-26:03:02, 26:05-26:08, 26:10-26:33, 26:35-26:43:02, 26:45-26:69, 30:55, 34:08, 43:01, 66:01, 66:04-66:15, 68:71, 74:13 |
| 147 | 100 bp, 200 bp, 240 bp | 1070 bp | A26, A29, A31, A34 | *02:237, 02:309, 03:95, 26:19, 26:22, 29:01:01:01-29:31, 31:03-31:04, 33:13, 33:48, 34:04, 66:09 |
| 157,8,10-12 | 90 bp, 135 bp, 205 bp | 1070 bp | A1, A30 | *01:13, 01:28, 03:43, 03:82, 30:01:01-30:04:02, 30:06-30:20, 30:22-30:55, 31:35 |
| 16 | 240 bp, 370 bp, 395 bp | 1070 bp | A31, A32 | *02:237, 03:95, 29:14, 31:01:02-31:54, 32:05 |
| 17 | 140 bp, 180 bp | 1070 bp | A32, A74 | *01:95, 03:43, 03:82, 29:13, 31:35, 32:01:01-32:03, 32:05-32:36, 74:07 |
| 18 | 200 bp | 1070 bp | A33, A68 | *02:243, 33:01:01-33:01:06, 33:03:01-33:50, 68:29 |
| 19 | 160 bp, 200 bp | 800 bp | A74 | *29:19, 74:01-74:15 |
| 2011 | 220 bp, 245 bp | 800 bp | A2, A25, A28, A68 | *02:34-02:35:03, 02:46, 02:48, 02:56:01-02:56:02, 02:62, 02:70, 02:78, 02:103, 02:129, 25:05, 26:54, 68:01:01:01-68:83 |
| 21 | 240 bp, 375 bp | 800 bp | A2/A28, A26, A68, A69 | *02:55, 02:243, 24:82, 26:22, 33:22, 66:09, 68:29, 69:01 |
| 227,13 | 85 bp, 240 bp | 800 bp | A2, A36 | *02:34-02:35:03, 02:46, 02:48, 02:56:01-02:56:02, 02:62, 02:70, 02:78, 02:103, 02:129, 36:01-36:05 |
| 237,11 | 70 bp, 160 bp, 240 bp, 495 bp | 800 bp | A2/A28, A24/A3, A26, A36, A68, A80 | *02:55, 03:41, 03:63, 03:75, 03:88, 24:18, 26:03:01-26:03:02, 26:05-26:06, 26:21, 26:30, 33:24, 36:02, 68:05, 68:15, 68:20, 80:01 |
| 24 | 360 bp |  | A3, A10, A26, A31, A66 | *02:135, 02:309, 03:01:19, 25:13, 26:30, 26:65, 31:04, 34:09, 66:02-66:03, 66:12, 66:16 |
| 25 | 190 bp, 400 bp | 1070 bp | A1, A29, A30, A31, A32, A33, A74 | *01:02, 01:20, 29:01:01:01-29:29, 29:31, 30:01:01-30:04:02, 30:06-30:11:02, 30:13-30:17, 30:19-30:20, 30:22-30:30, 30:32-30:40, 30:42-30:54, 31:01:02-31:08, 31:10-31:27, 31:29-31:54, 32:01:01-32:23, 32:25-32:36, 33:01:01-33:01:06, 33:03:01-33:51, 74:01-74:15 |
| 26 | 195 bp, 225 bp | 800 bp | A1, A36, A43 | *01:01:01:01-01:02, 01:04N, 01:07-01:11N, 01:13, 01:16N-01:18N, 01:21-01:33, 01:35-01:52N, 01:54-01:62, 01:64, 01:67-01:72, 01:74-01:97, 01:99-01:101, 03:18, 11:11, 11:94, 36:04, 43:01 |
| 2710 | 205 bp | 1070 bp | A1, A3, A11, A30, A31, A32, A34 | *01:12, 01:19, 01:21, 02:156, 03:01:01:01-03:01:01:03, 03:01:03-03:01:05, 03:01:07-03:01:13, 03:01:15-03:17, 03:19-03:49, 03:51-03:53, 03:55-03:63, 03:67-03:74, 03:76-03:94, 03:96-03:126, 03:128-03:132, 11:25, 11:31, 11:35, 11:60, 24:92, 30:04:01-30:04:02, 30:06, 30:09, 30:17, 30:29, 30:46, 31:03-31:04, 32:04, 33:49, 34:02:01, 34:03-34:04, 34:07-34:09 |
| 287,10 | 100 bp | 1070 bp | A2, A3, A9, A11, A23, A24, A28, A29, A30, A66, A68, A69 | *02:34-02:35:03, 02:56:01-02:56:02, 02:62, 02:78, 02:103, 03:01:01:01-03:07, 03:09-03:28, 03:30-03:31, 03:33, 03:35, 03:37-03:40, 03:42-03:61, 03:64-03:87, 03:90-03:106, 03:109-03:132, 11:12, 23:13, 24:07, 24:24, 24:108, 24:112, 24:131, 29:01:01:01-29:18, 29:21-29:29, 29:31, 30:01:01-30:01:05, 30:08, 30:11:01-30:11:02, 30:14L-30:20, 30:23-30:26, 30:30, 30:35-30:43, 30:48-30:49, 30:52-30:55, 32:17, 34:09, 66:02, 66:12, 66:16, 68:01:01:01-68:02:04, 68:06-68:14, 68:16-68:19, 68:21:01-68:30, 68:32-68:39, 68:41-68:71, 68:73-68:83, 69:01, 74:13 |
| 2912 | 260 bp | 800 bp | A3, A11, A26, A30, A68, A74 | *03:09, 03:108, 11:06, 11:18, 26:03:01-26:03:02, 26:06, 26:21, 26:30, 29:19, 30:13, 30:16, 30:44, 30:46, 33:24, 68:05, 68:15, 68:20, 74:06 |
| 3014 | 180 bp | 1070 bp | A25, A10, A26, A43, A66 | *02:135, 25:01:01-25:05, 25:07-25:16, 26:01:01-26:01:20, 26:01:22-26:03:02, 26:05-26:08, 26:10-26:33, 26:35-26:43:02, 26:45-26:69, 32:26, 43:01, 66:01, 66:04-66:15 |
| 317 | 110 bp, 195 bp | 1070 bp | A34 | *34:01:01-34:02:02, 34:04-34:05, 34:07-34:09 |
| 3217 | - | - | - | Negative control |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-A low resolution SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-A low resolution typing.

In addition, wells number 2, 4 to 6, 8, 9, 12, 19 to 23, 26 and 29 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3The serological reactivity of all HLA-A alleles is not known. In this table we use the expert-assigned serological grouping in Tissue Antigens (2009) 73:95-170 and the serological grouping of the sequence-defined allele.

4Nucleotide sequence information is available for only exons 2 and 3 of many HLA Class I alleles and for only exon 2 of many HLA Class II alleles and not for other exons or for the introns of these alleles. We assume that unknown sequences in these exons and in the introns are conserved within loci and within allelic groups.

5The A*23:14 and the A*24:05 and 24:13:02 alleles will give rise to identical amplification patterns. These three alleles can be separated by the respective high resolution SSP primer sets.

6Primer mix 6 will amplify the B*18:27 allele.

7Specific PCR fragments shorter than 125 base pairs have a lower intensity and are less sharp than longer PCR bands.

8The primer pairs in wells 2, 5, 7, 8, 11 and 15 will in many samples give rise to two or three HLA-specific PCR fragments.

9In primer mix 1, the positive control band may be slightly weaker than for other HLA-A low primer mixes.

10Primer mixes 15, 27 and 28 may yield less specific PCR product than the other primer mixes.

11Primer mixes 6, 15, 20 and 23 may have a tendency of primer dimer formation.

12Primer mixes 15 and 29 may have tendencies of unspecific amplifications.

13Primer mix 22 might faintly amplify most A*11 alleles.

14Primer mix 30 may generate a false positive band of about 500 base pairs. This band should be disregarded when interpreting HLA-A low resolution typings.

15Primer mix 9 may weakly amplify the A*34 alleles.

16In primer mix 5, the specific PCR product of 535 base pairs may be difficult to distinguish from the internal control band. The alleles giving rise to a product of this size are the following: A*01:95, 23:09, 24:02:06, 24:02:27, 24:08, 24:24, 24:29 , 24:42, 24:67, 24:116, 24:137, 24:140, 24:145, 24:156, 24:171 and 32:13.

17Primer mix 32 contains a negative control, which will amplify more than 95% of HLA amplicons as well as the amplicons generated by control primer pairs. PCR product sizes range from 75 to 200 base pairs. The PCR product generated by the control primer pair is 430 base pairs.

‘w’, might be weakly amplified.

1The sequence of the A*0105N has been shown to be identical to A*01:04N.

The A*01:34N allele has been renamed to A* 01:01:38L.

The A*020116 allele has been renamed to A*02:134.

The A*020120 allele has been renamed to A*02:01:18.

The sequence of the A*0223 allele has been shown to be identical to A*02:22:01.

The sequence of the A*0298 allele has been shown to be identical to A*02:96.

The A*02:100 allele has never been assigned.

The A*1128 allele has been renamed to A*11:15:02.

The A*11:53 allele has been shown to be identical to corrected sequence of A*11:02:01.

The sequence of the A*2401 allele has been shown to be in error.

The sequence of the A*2412 allele has been shown to be identical to A*24:08.

The A*2416 allele has been renamed to A*31:08.

The A*2465 allele has been renamed to A*24:13:02.

The A*26:44 allele has been renamed to A*26:43:02.

The sequence of the A*3005 allele has been shown to be identical to A*30:04.

The A*3021 allele has been renamed to A*30:11:02.

The sequence of the A*31011 allele has been shown to be identical to A*31:01:02.

The sequence of the A*3302 allele has been shown to be identical to A*33:03:01.

2The serological reactivity of all HLA-A alleles is not known. In this table we use the expert-assigned serological grouping in Tissue Antigens (2009) 73:95-170 and the serological grouping of the sequence-defined allele.

3The primer pairs in wells 2, 5, 7, 8, 11 and 15 will in many samples give rise to two or three HLA-specific PCR fragments.

4The A*23:14 and the A*24:05 and 24:13:02 alleles will give rise to identical amplification patterns. These four alleles can be separated by the respective high resolution SSP primer sets.

5Primer mix 32 contains a negative control, which will amplify more than 95% of HLA amplicons as well as the amplicons generated by control primer pairs. PCR product sizes range from 75 to 200 base pairs. The PCR product generated by the control primer pair is 430 base pairs.

‘w’, may be weakly amplified.

Change in revision R01 compared to R00:

- The HLA-A*68:13 allele is amplified by primer mix 4. This has been corrected in the specificity and interpretation tables.

Change in revision R02 compared to R01:

- A footnote has been added to the specificity table, stating that primer mix 9 may weakly amplify the A*34 alleles.

Change in revision R03 compared to R02:

- The HLA-A*01:02 and 01:20 alleles are amplified by primer mix 25. This has been corrected in the specificity and interpretation tables.

Changes in revision R04 compared to R03:

- The HLA-A*03:01:03, 03:09, 03:23:01, 03:89, 03:108, 11:06, 11:18, 24:28, 24:89, 26:03:01-26:03:02, 26:06, 26:07:02, 26:21, 26:30, 30:13, 30:16, 30:44, 30:46, 68:05, 68:15, 68:20 and 68:30 alleles are weakly amplified by primer mix 2. This has been corrected in the Specificity and Interpretation Tables.

- Primer mix 17 does not amplify the HLA-A*36:02 allele. This has been corrected in the Specificity and Interpretation Tables.

Change in revision R06 compared to R05:

- Primer mix 30 amplifies the A*32:26 allele. This has been corrected in the Specificity and Interpretation Tables.