PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-A low resolution

Prod. No:	101.401-48/48u

101.401-12/12u

Lot No:    	71R

Expiry Date:    	2015-October-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 31+1 primer mixes used for HLA-A low resolution SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | HLA-A serology3 | Amplified HLA-A alleles4,5,6 |
| --- | --- | --- | --- | --- |
| 17 | 120 bp, 145 bp | 800 bp | A1, A36 | *01:01:01:01-01:01:31, 01:01:33-01:04N, 01:06-01:33, 01:35-01:68, 01:70-01:122, 36:01-36:05 |
| 28 | 175 bp, 215 bp, 255 bp, 365 bp, 415 bp | 800 bp | A2,A19, A28, A203, A210 | *02:01:01:01-02:01:15, 02:01:17-02:01:19, 02:01:21-02:01:81, 02:01:83-02:22:02, 02:24:01-02:35:01, 02:35:03-02:47, 02:49-02:77, 02:78w, 02:79:01-02:97:02, 02:99, 02:101:01-02:128, 02:130-02:392 |
| 3 | 235 bp | 1070 bp | A3,A32/A3, A36 | *03:01:01:01-03:01:29, 03:01:31-03:01:34, 03:01:36-03:04:03, 03:06-03:09, 03:11N-03:17:02, 03:19-03:39, 03:41, 03:43-03:74, 03:76-03:94, 03:96-03:97, 03:99-03:104, 03:106-03:121, 03:123-03:134, 03:136-03:161N, 11:130, 32:04, 36:02 |
| 4 | 190 bp | 800 bp | A1,A3,A11, A30, A36, A68 | *01:01:01:01-01:01:22, 01:01:24-01:01:47, 01:01:49-01:04N, 01:06-01:07, 01:09-01:11N, 01:13, 01:16N-01:18N, 01:20-01:29, 01:31N-01:33, 01:35-01:78, 01:80-01:83:01, 01:83:02w, 01:84-01:98, 01:100-01:122, 02:78, 02:169, 03:12, 03:18, 03:88, 03:135, 11:01:01-11:27, 11:29-11:52Q, 11:54-11:132, 26:19, 26:72, 30:08, 36:04, 68:13:01, 68:66, C*03:174, C*08:69 |
| 58,15 | 160 bp, 535 bp | 800 bp | A3, A9, A23, A24, A2403, A31, A32 | *01:95, 03:30, 03:152, 23:01:01-23:55, 24:02:01:01-24:11N, 24:13:01-24:15, 24:17-24:64, 24:66-24:88, 24:90N-24:128, 24:130-24:210, 24:212-24:214, 24:216-24:222N, 31:08, 32:05, 32:13, 33:53 |
| 613 | 135 bp, 195 bp, 205 bp | 800 bp | A9,A23, A24, A29, A80 | *23:01:01-23:55, 24:24, 24:71, 29:07, 30:56, 31:29, 80:01:01:01-80:02, B*18:27 |
| 78 | 175 bp, 205 bp | 1070 bp | A2, A9, A23, A24, A2403, A26, A33 | *02:17:01w-02:17:02w, 23:14:01-23:14:02, 24:02:01:01-24:11N, 24:13:01-24:13:02, 24:17-24:50, 24:54-24:56, 24:58-24:63, 24:66-24:91, 24:93, 24:95-24:113, 24:115-24:137, 24:139-24:187, 24:189-24:210, 24:212-24:214, 24:216-24:221, 26:16, 33:19, 68:45 |
| 88 | 165 bp, 200 bp | 800 bp | A2/A28, A3, A10, A11, A25, A26, A32, A34, A66, A68, A69 | *01:51, 02:55, 03:24, 03:50, 11:10, 25:01:01-25:16, 25:18-25:22, 26:01:01-26:06, 26:08-26:15, 26:17-26:18, 26:20-26:43:02, 26:45-26:63, 26:65-26:71N, 26:73-26:80, 29:28, 32:15, 33:51, 34:01:01-34:10N, 66:01-66:19, 68:01:01:01-68:96, 69:01 |
| 97,14 | 75 bp | 800 bp | A25, A32 | *25:01:01-25:22, 32:01:01-32:01:13, 32:02, 32:04, 32:06-32:37, 32:39-32:55, B*07:81, B*08:52, B*18:67, B*38:41, B*53:05, B*53:16 |
| 107 | 80 bp, 240 bp | 800 bp | A10, A26, A33 | *01:43, 01:51, 11:17, 11:40, 26:01:01-26:02, 26:04, 26:07:01-26:20, 26:22-26:29, 26:31-26:43:02, 26:45-26:77, 26:79-26:80, 33:13, 33:48, 43:01, 68:84 |
| 117,8 | 80 bp, 175 bp, 500 bp | 1070 bp | A1, A9, A11, A26, A31, A34, A66 | *01:13, 01:28, 03:63, 03:88, 11:01:01-11:27, 11:29-11:52Q, 11:54-11:132, 24:19, 24:44, 26:03:01-26:03:02, 26:06, 26:21, 26:78, 34:01:01-34:08, 34:10N, 66:01, 66:04-66:11, 66:13-66:14, 66:17-66:19, 80:02 |
| 127 | 125 bp, 185 bp | 800 bp | A3, A10, A25, A26, A31, A34, A43, A66 | *02:309, 03:01:19, 11:11, 25:05-25:06, 26:09, 26:54, 31:03-31:04, 34:01:01-34:10N, 43:01, 66:02-66:03, 66:16 |
| 13 | 175 bp, 225 bp | 1070 bp | A1, A2, A3, A10, A25, A26, A34, A43, A66 | *01:13, 02:34-02:35:03, 02:56:01-02:56:02, 02:62, 02:103, 02:135, 03:01:01:01-03:01:22, 03:01:24-03:07, 03:09-03:11N, 03:13-03:31, 03:33-03:35, 03:37-03:40, 03:42-03:56, 03:58, 03:60-03:71, 03:73-03:87, 03:90-03:106, 03:109-03:110, 03:112-03:141, 03:143-03:151, 03:153-03:161N, 25:01:01-25:05, 25:07-25:22, 26:01:01-26:01:20, 26:01:22-26:01:27, 26:02w, 26:03:01-26:03:02, 26:05-26:08, 26:10-26:28, 26:29w, 26:30-26:33, 26:35-26:43:02, 26:45-26:48, 26:49w, 26:50-26:72, 26:74-26:77, 26:79-26:80, 30:55, 34:08, 43:01, 66:01, 66:04-66:09, 66:10w, 66:11-66:15, 66:17-66:19, 68:71, 74:13 |
| 147 | 80 bp, 115 bp, 200 bp, 240 bp | 1070 bp | A26, A29, A31, A34 | *02:237, 02:309, 03:95, 26:19, 26:22, 29:01:01:01-29:45, 30:57, 33:13, 33:48, 66:09 |
| 157-10 | 90 bp, 135 bp, 205 bp | 1070 bp | A1, A30 | *01:13, 01:28, 03:43, 03:82, 11:113, 30:01:01-30:04:02, 30:06-30:20, 30:22-30:70N, 31:35 |
| 16 | 240 bp, 370 bp, 395 bp | 1070 bp | A31, A32 | *02:237, 03:95, 29:14, 31:01:02-31:70, 32:05, 33:53 |
| 17 | 140 bp, 180 bp | 1070 bp | A32, A36, A74 | *01:95, 03:43, 03:82, 29:13, 29:39, 31:35, 32:01:01-32:03, 32:05-32:55, 74:07 |
| 18 | 200 bp | 1070 bp | A33, A68 | *02:243, 33:01:01-33:01:07, 33:03:01-33:37, 33:39-33:50, 33:52-33:64, 68:29 |
| 19 | 160 bp, 200 bp | 800 bp | A74 | *29:19, 29:39, 74:01-74:17 |
| 20 | 220 bp, 245 bp | 800 bp | A2, A25, A28, A68 | *02:34-02:35:03, 02:46, 02:48, 02:56:01-02:56:02, 02:62, 02:70, 02:78, 02:103, 02:129, 25:05, 26:54, 68:01:01:01-68:96 |
| 21 | 240 bp, 375 bp | 800 bp | A2/A28, A26, A68, A69 | *02:55, 02:243, 24:82, 26:22, 33:22, 66:09, 68:29, 69:01 |
| 227,11 | 85 bp, 240 bp | 800 bp | A2, A36 | *02:34-02:35:03, 02:46, 02:48, 02:56:01-02:56:02, 02:62, 02:70, 02:78, 02:103, 02:129, 31:62, 36:01-36:05 |
| 237 | 70 bp, 160 bp, 240 bp, 495 bp | 800 bp | A2/A28, A24/A3, A26, A36, A68, A80 | *02:55, 03:41, 03:63, 03:75, 03:88, 11:130, 24:18, 24:204, 24:213, 26:03:01-26:03:02, 26:05-26:06, 26:21, 26:30, 26:78, 33:24, 36:02, 68:05, 68:15, 68:20, 80:01:01:01-80:01:01:02 |
| 24 | 360 bp |  | A3, A10, A26, A31, A66 | *02:135, 02:309, 03:01:19, 25:13, 26:30, 26:65, 31:04, 34:09, 66:02-66:03, 66:12, 66:16 |
| 25 | 190 bp, 400 bp | 1070 bp | A1, A29, A30, A31, A32, A33, A74 | *29:01:01:01-29:29, 29:31-29:45, 30:01:01-30:04:02, 30:06-30:11:02, 30:13-30:17, 30:19-30:20, 30:22-30:30, 30:32-30:40, 30:42-30:54, 30:56-30:59N, 30:61-30:70N, 31:01:02-31:08, 31:10-31:27, 31:29-31:70, 32:01:01-32:03, 32:05-32:23, 32:25-32:48N, 32:50-32:55, 33:01:01-33:01:07, 33:03:01-33:37, 33:39-33:64, 74:01-74:17 |
| 26 | 195 bp, 225 bp | 800 bp | A1, A36, A43 | *01:01:01:01-01:02, 01:04N, 01:07-01:11N, 01:13, 01:16N-01:18N, 01:21-01:33, 01:35-01:52N, 01:54-01:62, 01:64, 01:67-01:72, 01:74-01:97, 01:99-01:122, 03:18, 03:135, 11:11, 11:94, 11:112, 36:04, 43:01 |
| 279 | 205 bp | 1070 bp | A1, A3, A11, A30, A31, A32, A34 | *01:12, 01:19, 01:21, 02:156, 02:338, 03:01:01:01-03:01:05, 03:01:07-03:01:13, 03:01:15-03:17:02, 03:19-03:49, 03:51-03:53, 03:55-03:63, 03:67-03:74, 03:76-03:94, 03:96-03:126, 03:128-03:134, 03:136-03:139, 03:141-03:152, 03:154-03:161N, 11:25, 11:31, 11:35, 11:60, 24:92, 30:04:01-30:04:02, 30:06, 30:09, 30:17, 30:29, 30:46, 31:03-31:04, 32:04, 33:49, 34:02:01-34:04, 34:07-34:10N |
| 287,9 | 100 bp | 1070 bp | A2, A3, A9, A11, A23, A24, A28, A29, A30, A66, A68, A69 | *02:34-02:35:03, 02:56:01-02:56:02, 02:62, 02:78, 02:103, 03:01:01:01-03:07, 03:09-03:28, 03:30-03:31, 03:33, 03:35, 03:37-03:40, 03:42-03:61, 03:64-03:87, 03:90-03:106, 03:109-03:151, 03:153-03:161N, 11:12, 23:13, 24:07, 24:24, 24:108, 24:112, 24:131, 29:01:01:01-29:18, 29:21-29:29, 29:31-29:33, 29:35-29:45, 30:01:01-30:01:07, 30:08, 30:11:01-30:11:02, 30:14L-30:20, 30:23-30:26, 30:30, 30:35-30:43, 30:48-30:49, 30:52-30:56, 30:58-30:60, 30:62-30:63, 30:65, 32:17, 34:09, 66:02, 66:12, 66:16, 68:01:01:01-68:02:05, 68:06-68:14, 68:16-68:19, 68:21:01-68:30, 68:32-68:39, 68:41-68:71, 68:73-68:84, 68:86-68:89, 68:91-68:92, 68:94N-68:96, 69:01, 74:13 |
| 2910 | 260 bp | 800 bp | A3, A11, A26, A30, A68, A74 | *03:09, 03:108, 11:06, 11:18, 26:03:01-26:03:02, 26:06, 26:21, 26:30, 26:78, 29:19, 30:13, 30:16, 30:44, 30:46, 33:24, 68:05, 68:15, 68:20, 74:06 |
| 3012 | 180 bp | 1070 bp | A25, A10, A26, A43, A66 | *02:135, 25:01:01-25:05, 25:07-25:17, 25:19-25:22, 26:01:01-26:01:20, 26:01:22-26:03:02, 26:05-26:08, 26:10-26:33, 26:35-26:43:02, 26:45-26:72, 26:74-26:77, 26:79-26:80, 32:26, 43:01, 66:01, 66:04-66:15, 66:17-66:19 |
| 317 | 110 bp | 1070 bp | A34 | *34:01:01-34:02:03, 34:04-34:05, 34:07-34:10N |
| 3216 | - | - | - | Negative control |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-A low resolution SSP typings.

When the primers in a primer mix can give rise to HLA-specific PCR products of more than one length this is indicated if the size difference is more than 20 base pairs. Size differences of 20 base pairs or less are not given. For high resolution SSP kits the respective lengths of the HLA-specific PCR product(s) are given for the alleles amplified by these primer mixes.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-A low resolution typing.

In addition, wells number 2, 4 to 6, 8 to 10, 12, 19 to 23, 26 and 29 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3The serological reactivity of all HLA-A alleles is not known. In this table we use the expert-assigned serological grouping in Tissue Antigens (2009) 73:95-170 and the serological grouping of the sequence-defined allele.

4For several HLA Class I alleles 1st and/or 4th exon(s) and beyond, as well as intron nucleotide sequences, are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in these regions are conserved within allelic groups.

5The A*23:14:01-23:14:02 and the A*24:05, 24:71 and 24:199 alleles will give rise to identical amplification patterns. These three alleles can be separated by the respective high resolution SSP primer sets.

6Due to sharing of sequence motifs, primer mix 4 will amplify C*03:174 and C*08:69, primer mix 6 will amplify the B*18:27 allele, primer mix 9 will amplify B*07:81, B*08:52, B*18:67, B*38:41, B*53:05 and B*53:16 alleles.

7HLA-specific PCR products shorter than 125 base pairs have a lower intensity and are less sharp than longer PCR products.

8The primer pairs in wells 2, 5, 7, 8, 11 and 15 will in many samples give rise to two or three HLA-specific PCR fragments.

9Primer mixes 15, 27 and 28 may give rise to a lower yield of HLA-specific PCR product than the other HLA-A low primer mixes.

10Primer mixes 15 and 29 may have tendencies of unspecific amplifications.

11Primer mix 22 might faintly amplify most A*11 alleles.

12Primer mix 30 may generate a false positive band of about 500 base pairs. This band should be disregarded when interpreting HLA-A low resolution typings.

13Primer mix 6 may give rise to a lower yield of A*23 alleles than the other A low primer mixes.

14Primer mix 9 may faintly amplify A*34 alleles.

15In primer mix 5, the specific PCR product of 535 base pairs may be difficult to distinguish from the internal control band. The alleles giving rise to a product of this size are the following: A*01:95, 23:09, 23:51, 24:02:06, 24:02:27, 24:08, 24:24, 24:29 , 24:42, 24:67, 24:116, 24:137, 24:140, 24:145, 24:156, 24:171, 24:191, 24:192 and 32:13.

16Primer mix 32 contains a negative control, which will amplify more than 95% of HLA amplicons as well as the amplicons generated by control primer pairs. PCR product sizes range from 75 to 200 base pairs. The PCR product generated by the control primer pair is 430 base pairs.

‘w’, might be weakly amplified

1The sequence of the A*0105N has been shown to be identical to A*01:04N.

The A*01:34N allele has been renamed A*01:01:38L.

The A*020116 allele has been renamed to A*02:134.

The A*020120 allele has been shown to be identical to A*02:01:18.

The A*02:01:82 allele has been shown to be identical to A*02:01:84.

The sequence of the A*0223 allele has been shown to be identical to A*02:22:01.

The sequence of the A*0298 allele has been shown to be identical to A*02:96.

The A*02:100 allele has never been assigned.

The A*1128 allele has been renamed to A*11:15:02.

The A*11:53 allele has been shown to be identical to the corrected sequence of A*11:02:01.

The sequence of the A*2401 allele has been shown to be in error.

The sequence of the A*2412 allele has been shown to be identical to A*24:08.

The A*2416 allele has been renamed to A*31:08.

The A*2465 allele has been renamed to A*24:13:02.

The sequence of the A*24:211 allele has been shown to be identical to A*24:135:02.

The A*26:44 allele has been renamed to A*26:43:02.

The sequence of the A*3005 allele has been shown to be identical to A*30:04.

The A*3021 allele has been renamed to A*30:11:02.

The sequence of the A*31011 allele has been shown to be identical to A*31:01:02.

The sequence of the A*3302 allele has been shown to be identical to A*33:03:01.

The sequence of the A*33:38 allele has been shown to be identical to A*33:44.

2The serological reactivity of all HLA-A alleles is not known. In this table we use the expert-assigned serological grouping in Tissue Antigens (2009) 73:95-170 and the serological grouping of the sequence-defined allele.

3The primer pairs in wells 2, 5, 7, 8, 11 and 15 will in many samples give rise to two or three HLA-specific PCR fragments.

4The A*23:14:01-23:14:02 and the A*24:71 alleles will give rise to identical amplification patterns. These alleles can be separated by the respective high resolution SSP primer sets.

5Primer mix 32 contains a negative control, which will amplify more than 95% of HLA amplicons as well as the amplicons generated by control primer pairs. PCR product sizes range from 75 to 200 base pairs. The PCR product generated by the control primer pair is 430 base pairs.

‘w’, may be weakly amplified.

Changes in revision R01 compared to R00:

- In primer mix 5, the specific PCR product of 535 base pairs may be difficult to distinguish from the internal control band. A foot note has been added to the Specificity Table.

- Primer mix 6 does not amplify the A*24:05 and A*24:199 alleles. This has been corrected in the Specificity and Interpretation Tables.

Change in revision R02 compared to R01:

- Primer mix 30 amplifies the A*32:26 allele. This has been corrected in the Specificity and Interpretation Tables.

Change in revision R03 compared to R02:

- Primer mix 11 does not amplify the A*31:03 and A*66:15 alleles. This has been corrected in the Specificity and Interpretation tables.

Change in revision R04 compared to R03:

- Primer mix 25 does not amplify the A*32:04 allele. This has been corrected in the Specificity and Interpretation tables.