PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-A*01

Prod. No:	101. 411-24/24u

101.411-06/-06u

Lot No:    	06N

Expiry Date:    	2014-July-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 48 primer mixes used for HLA-A*01 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-A*01 alleles | Other amplified HLA-A alleles3 |
| --- | --- | --- | --- | --- |
| 1 | 235 bp | 800 bp | *01:01:01:01-01:01:22, 01:01:24-01:02, 01:04N, 01:06-01:07, 01:09-01:11N, 01:13, 01:15N-01:18N, 01:21-01:33, 01:35-01:40, 01:42-01:62, 01:64-01:65, 01:67-01:72, 01:74-01:88, 01:90-01:101 | *03:18, 11:01:01-11:01:20, 11:01:22-11:03, 11:05-11:25, 11:29-11:34, 11:36-11:47, 11:49, 11:51-11:89, 11:91-11:100, 11:102-11:109N, 36:04 |
| 2 | 145 bp | 1070 bp | *01:01:01:01-01:01:31, 01:01:33-01:01:43, 01:03-01:04N, 01:06-01:17, 01:18Nw, 01:19, 01:21-01:23, 01:24w, 01:25-01:33, 01:35-01:42, 01:44-01:68, 01:70-01:79, 01:81-01:101 | *36:01-36:05 |
| 34 | 120 bp | 800 bp | *01:02, 01:20 |  |
| 4 | 305 bp | 1070 bp | *01:03 | *11:26, 26:32, 26:70, 33:13, 36:03, 74:10 |
| 5 | 470 bp | 1070 bp | *01:04N | *03:21N, 11:21N, 23:07N, 24:11N |
| 64,7 | 125 bp, 210 bp | 1070 bp | *01:09, 01:60 | *26:31 |
| 7 | 215 bp | 800 bp | *01:06 | *02:156, 03:01:30, 03:05, 03:42, 03:98, 03:105, 03:122, 11:24:01-11:25, 11:31, 11:35, 30:01:01-30:03, 30:07-30:16, 30:18-30:20, 30:22-30:27N, 30:30-30:45, 30:48-30:51, 30:53-30:55, 31:03-31:04, 33:49, 34:02:01-34:04, 34:07-34:09, 80:01-80:02 |
| 84,8 | 110 bp, 180 bp | 1070 bp | *01:01:01:02N, 01:07, 01:23, 01:51, 01:83 | *31:35 |
| 95 | 235 bp | 1070 bp | *01:08, 01:27N |  |
| 109 | 155 bp, 270 bp | 800 bp | *01:10, 01:29 | *11:14w, 11:50Q, 30:26, 80:01w-80:02w |
| 1110 | 135 bp, 275 bp | 800 bp | *01:11N, 01:13, 01:28 | *31:35 |
| 124,6 | 85 bp | 800 bp |  | *36:01-36:05 |
| 13 | 205 bp | 1070 bp | *01:12, 01:19, 01:21 | *02:156w, 03:02:01-03:02:02, 03:07w, 03:10, 03:31-03:32, 03:42w, 03:73, 03:76, 03:82, 03:90, 03:106, 03:113, 03:133, 11:31w, 11:35w, 11:60, 24:92, 30:04:01w-30:04:02w, 30:06w, 30:09, 30:17w, 30:29w, 30:46w, 31:03w-31:04w, 33:49w |
| 144,11 | 75 bp, 120 bp | 1070 bp | *01:13, 01:17, 01:59 |  |
| 15 | 235 bp | 1070 bp | *01:12, 01:14, 01:19 | *02:156, 03:01:01:01-03:01:05, 03:01:07-03:01:29, 03:01:31-03:17, 03:19-03:39, 03:41-03:74, 03:76-03:94, 03:96-03:97, 03:99-03:104, 03:106-03:133, 11:04, 11:27, 11:35, 24:92, 30:01:01-30:04:02, 30:06-30:13, 30:15-30:20, 30:22-30:27N, 30:29-30:42, 30:44-30:46, 30:48-30:51, 30:53-30:55, 31:03-31:04, 32:04, 33:49, 34:02:01-34:04, 34:07-34:09, 36:01-36:02, 36:05 |
| 1612 | 180 bp, 235 bp | 1070 bp | *01:01:01:02N, 01:15N |  |
| 17 | 210 bp | 1070 bp | *01:16N |  |
| 18 | 135 bp | 1070 bp | *01:01:01:01-01:04N, 01:06, 01:08-01:12, 01:14-01:27N, 01:29-01:33, 01:35-01:68, 01:70-01:94, 01:96-01:101 | *36:01-36:05 |
| 195 | 170 bp | 1070 bp | *01:18N, 01:30 | *02:262, 24:22, 24:160 |
| 204,13 | 65 bp, 425 bp | 800 bp | *01:10, 01:19, 01:21, 01:26 |  |
| 214,14 | 125 bp, 255 bp | 1070 bp | *01:20, 01:44, 01:66 | *02:19, 02:36-02:37, 02:54, 02:255, 24:14, 24:93 |
| 22 | 590 bp | 1070 bp | *01:22N |  |
| 235 | 165 bp | 1070 bp | *01:24, 01:30 | *02:262, 24:22, 24:160 |
| 24 | 215 bp | 1070 bp | *01:12, 01:19, 01:25 | *03:02:01-03:02:02, 03:10, 03:31-03:32, 03:65, 03:69N, 03:73, 03:76, 03:82, 03:90, 03:106, 03:113, 11:01:01-11:01:03, 11:01:05-11:07, 11:09-11:22, 11:27, 11:29-11:30, 11:32-11:34, 11:36-11:43, 11:45-11:47, 11:49, 11:51-11:93, 11:95-11:100, 11:102-11:109N, 24:92 |
| 254 | 85 bp | 1070 bp | *01:31N, 01:51, 01:59 |  |
| 26 | 545 bp | 1070 bp | *01:32, 01:45 | *03:78, 11:108 |
| 274,15 | 110 bp, 160 bp | 1070 bp | *01:33, 01:87N |  |
| 284,5 | 95 bp | 1070 bp | *01:01:38L | *24:02:03Q |
| 29 | 155 bp | 800 bp | *01:35 | *03:77 |
| 305 | 140 bp | 1070 bp | *01:37, 01:95 |  |
| 31 | 240 bp | 1070 bp | *01:38, 01:63 |  |
| 324,16 | 110 bp, 140 bp | 1070 bp | *01:43, 01:57N | C*07:191N |
| 33 | 180 bp | 800 bp | *01:61 | *03:22:01-03:22:02, 03:42, 11:33:01-11:33:02, 30:01:01-30:04:02, 30:06-30:20, 30:22-30:27N, 30:29-30:34, 30:36-30:46, 30:48-30:51, 30:53, 30:55, 31:03-31:04, 33:49, 34:02:01-34:04, 34:07-34:09 |
| 344,17 | 125 bp, 215 bp | 800 bp | *01:58, 01:60 | *26:31 |
| 354,18 | 105 bp, 185 bp | 800 bp | *01:47, 01:49 |  |
| 364,19 | 90 bp, 175 bp | 1070 bp | *01:53N-01:54 |  |
| 374,20 | 65 bp, 150 bp | 1070 bp | *01:65, 01:92 |  |
| 384,21 | 100 bp, 180 bp | 1070 bp | *01:50, 01:62 | *02:315, 03:85 |
| 39 | 205 bp | 800 bp | *01:39 | *24:26 |
| 40 | 160 bp | 1070 bp | *01:36 |  |
| 41 | 140 bp | 1070 bp | *01:48 |  |
| 424,22 | 110 bp, 190 bp | 1070 bp | *01:64, 01:87N |  |
| 43 | 550 bp | 1070 bp | *01:45, 01:56N | *03:78, 11:69N, 11:108 |
| 444,23 | 65 bp, 245 bp | 1070 bp | *01:46, 01:98 | *24:87, B*07:64 |
| 454,5,24 | 65 bp, 140 bp | 1070 bp | *01:52N, 01:98 | *24:87, B*07:64 |
| 464,25 | 85 bp, 155 bp | 800 bp | *01:40, 01:81 | *03:26, 11:77 |
| 475,26 | 295 bp, 325 bp | 1070 bp | *01:41-01:42 | *11:48 |
| 484,5 | 95 bp | 1070 bp | *01:55, 01:81 | *03:26, 11:77 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-A*01 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-A*01 subtyping.

In addition, wells number 3, 7, 10 to 12, 20, 29, 33 to 35, 39 and 46 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3Due to the sharing of sequence motifs between HLA-A alleles non-HLA-A*01 alleles will be amplified by primer mixes 1, 2, 4 to 8, 10 to 13, 15, 18, 19, 21, 23,  24, 26, 28, 29, 33, 34, 38, 39 and 43 to 48. In addition, the B*07:64 allele will be amplified by primer mixes 44 and 45 and the C*07:191N allele will be amplified by primer mix 32.

4Short specific PCR fragments are less intense and not as sharp as longer specific bands.

5Primer mixes 9, 19, 23, 28, 30, 45, 47 and 48 may give rise to non-specific amplifications.

6Primer mix 12 might faintly amplify the most A*11, the A*02:27, 02:267, 31:24,C*07:25 and C*16:24 alleles.

7Primer mix 6: Specific PCR fragment of 125 bp in the A*01:60 and A*26:31 alleles. Specific PCR fragment of 210 bp in the A*01:09 allele.

8Primer mix 8: Specific PCR fragment of 110 bp in the A*01:07, 01:23, 01:51 and 01:83 and the A*31:35 alleles. Specific PCR fragment of 180 bp in the A*01:01:01:02N allele.

9Primer mix 10: Specific PCR fragment of 155 bp in the A*01:10 and in the A*11:14w, 11:50Q, 30:26 and 80:01w-80:02w alleles. Specific PCR fragment of 270 bp in the A*01:29 allele.

10Primer mix 11: Specific PCR fragment of 135 bp in the A*01:13 and 01:28 and in the A*31:35 alleles. Specific PCR fragment of 275 bp in the A*01:11N allele.

11Primer mix 14: Specific PCR fragment of 75 bp in the A*01:59 allele. Specific PCR fragment of 120 bp in the A*01:13 and 01:17 alleles.

12Primer mix 16: Specific PCR fragment of 180 bp in the A*01:01:01:02N allele. Specific PCR fragment of 235 bp in the A*01:15N allele.

13Primer mix 20: Specific PCR fragment of 65 bp in the A*01:10, A*01:21 and A*01:26 alleles. Specific PCR fragment of 425 bp in the A*01:19 allele.

14Primer mix 21: Specific PCR fragment of 125 bp in the A*01:44 allele. Specific PCR fragment of 255 bp in the A*01:20 and 01:66 and in the A*02:19, 02:36-02:37, 02:54, 02:255, 24:14 and 24:93 alleles.

15Primer mix 27: Specific PCR fragment of 110 bp in the A*01:87N allele. Specific PCR fragment of 160 bp in the A*01:33 allele.

16Primer mix 32: Specific PCR fragment of 110 bp in the A*01:57N and the C*07:191N alleles. Specific PCR fragment of 140 bp in the A*01:43 allele.

17Primer mix 34: Specific PCR fragment of 125 bp in the A*01:60 and A*26:31 alleles. Specific PCR fragment of 215 bp in the A*01:58 allele.

18Primer mix 35: Specific PCR fragment of 105 bp in the A*01:47 allele. Specific PCR fragment of 185 bp in the A*01:49 allele.

19Primer mix 36: Specific PCR fragment of 90 bp in the A*01:54 allele. Specific PCR fragment of 175 bp in the A*01:53N allele.

20Primer mix 37: Specific PCR fragment of 65 bp in the A*01:65 allele. Specific PCR fragment of 150 bp in the A*01:92 allele.

21Primer mix 38: Specific PCR fragment of 100 bp in the A*01:50 allele. Specific PCR fragment of 180 bp in the A*01:62 and the A*02:315 and 03:85 alleles.

22Primer mix 42: Specific PCR fragment of 110 bp in the A*01:87N allele. Specific PCR fragment of 190 bp in the A*01:64 allele.

23Primer mix 44: Specific PCR fragment of 65 bp in the A*01:98 and the A*24:87 and B*07:64 alleles. Specific PCR fragment of 245 bp in the A*01:46 allele.

24Primer mix 45: Specific PCR fragment of 65 bp in the A*01:98 and the A*24:87 and B*07:64 alleles. Specific PCR fragment of 140 bp in the A *01:52N allele.

25Primer mix 46: Specific PCR fragment of 85 bp in the A*01:81 and the A*03:26 and 11:77 alleles. Specific PCR fragment of 155 bp in the A*01:40 allele.

26Primer mix 47: Specific PCR fragment of 295 bp in the A*01:41 and A*11:48 alleles. Specific PCR fragment of 325 bp in the A*01:42 allele.

‘w’, might be weakly amplified.

1The nucleotide sequence of the A*0105N allele has been shown to be identical to A*01:04N.

The A*01:34N allele has been shown to be expressed at low levels and renamed A*01:01:38L.

2HLA-A*01 alleles in bold lettering are listed as confirmed alleles on the on the IMGT/HLA web page www.ebi.ac.uk/imgt/hla, release 3.6.0, October 2011.

3The A*01:47 and 01:49 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 35.

4The A*01:50 and 01:62 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 38.

5The A*01:53N and 01:54 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 36.

6The A*01:65 and 01:92 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 37.

7The A*01:69 and the A*03:18, 11:01:04, 11:08, 11:23, 11:44 and 11:94 alleles give rise to identical amplification patterns with the HLA-A*01 primer set. These alleles can be distinguished by the HLA-A low resolution and/or the HLA-A*03 and HLA-A*11 kits.

8Primer mix 6: Specific PCR fragment of 125 bp in the A*01:60 and A*26:31 alleles. Specific PCR fragment of 210 bp in the A*01:09 allele.

Primer mix 8: Specific PCR fragment of 110 bp in the A*01:07, 01:23, 01:51 and 01:83 and the A*31:35 alleles. Specific PCR fragment of 180 bp in the A*01:01:01:02N allele.

Primer mix 10: Specific PCR fragment of 155 bp in the A*01:10 and in the A*11:14w, 11:50Q, 30:26 and 80:01w-80:02w alleles. Specific PCR fragment of 270 bp in the A*01:29 allele.

Primer mix 11: Specific PCR fragment of 135 bp in the A*01:13 and 01:28 and in the A*31:35 alleles. Specific PCR fragment of 275 bp in the A*01:11N allele.

Primer mix 14: Specific PCR fragment of 75 bp in the A*01:59 allele. Specific PCR fragment of 120 bp in the A*01:13 and 01:17 alleles.

Primer mix 16: Specific PCR fragment of 180 bp in the A*01:01:01:02N allele. Specific PCR fragment of 235 bp in the A*01:15N allele.

Primer mix 20: Specific PCR fragment of 65 bp in the A*01:10, A*01:21 and A*01:26 alleles. Specific PCR fragment of 425 bp in the A*01:19 allele.

Primer mix 21: Specific PCR fragment of 125 bp in the A*01:44 allele. Specific PCR fragment of 255 bp in the A*01:20 and 01:66 and in the A*02:19, 02:36-02:37, 02:54, 02:255, 24:14 and 24:93 alleles.

Primer mix 27: Specific PCR fragment of 110 bp in the A*01:87N allele. Specific PCR fragment of 160 bp in the A*01:33 allele.

Primer mix 32: Specific PCR fragment of 110 bp in the A*01:57N and the C*07:191N alleles. Specific PCR fragment of 140 bp in the A*01:43 allele.

Primer mix 34: Specific PCR fragment of 125 bp in the A*01:60 and A*26:31 alleles. Specific PCR fragment of 215 bp in the A*01:58 allele.

Primer mix 35: Specific PCR fragment of 105 bp in the A*01:47 allele. Specific PCR fragment of 185 bp in the A*01:49 allele.

Primer mix 36: Specific PCR fragment of 90 bp in the A*01:54 allele. Specific PCR fragment of 175 bp in the A*01:53N allele.

Primer mix 37: Specific PCR fragment of 65 bp in the A*01:65 allele. Specific PCR fragment of 150 bp in the A*01:92 allele.

Primer mix 38: Specific PCR fragment of 100 bp in the A*01:50 allele. Specific PCR fragment of 180 bp in the A*01:62 and the A*02:315 and 03:85 alleles.

Primer mix 42: Specific PCR fragment of 110 bp in the A*01:87N allele. Specific PCR fragment of 190 bp in the A*01:64 allele.

Primer mix 44: Specific PCR fragment of 65 bp in the A*01:98 and the A*24:87 and B*07:64 alleles. Specific PCR fragment of 245 bp in the A*01:46 allele.

Primer mix 45: Specific PCR fragment of 65 bp in the A*01:98 and the A*24:87 and B*07:64 alleles. Specific PCR fragment of 140 bp in the A *01:52N allele.

Primer mix 46: Specific PCR fragment of 85 bp in the A*01:81 and the A*03:26 and 11:77 alleles. Specific PCR fragment of 155 bp in the A*01:40 allele.

Primer mix 47: Specific PCR fragment of 295 bp in the A*01:41 and A*11:48 alleles. Specific PCR fragment of 325 bp in the A*01:42 allele.

‘w’, might be weakly amplified.

Changes in revision R01 compared to R00:

- Primer mix 9, but not primer mix 8, may give rise to non-specific amplifications. The foot-notes to the Specificity Table have been corrected.