PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-A*11

Prod. No:	101. 416-12/12u

101.416-04/04u

Lot No:    	30F

Expiry Date:    	2010-November-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for HLA-A*11 SSP typing.

| Primer Mix | Approx. Size of spec. PCR product1 | Size of control band2 | Amplified HLA-A*11 alleles3 | Other amplified HLA-A alleles3 |
| --- | --- | --- | --- | --- |
| 14 | 195 bp | 800 bp | 110101-110109, 1103-1113, 111501-111502, 1120-1127, 1129-1136 | 0113, 0117, 0234-023503, 0256, 0262, 0278, 9203, 03010101-0307, 0309-0331, 0333-0335, 0337-0339, 2419, 2613, 2619, 2633, 29010101-2912, 2914-2917, 3018, 340101-3408, 6601, 6602, 6604, 6606, 6607, 680101-680202, 6806-6814, 6816-6819, 6821-6830, 6832-6835, 6837-6843, 6901 |
| 2 | 270 bp | 1070 bp | 110201-110203, 1114, 1116 |  |
| 3 | 190 bp | 1070 bp | 1103, 1133 | 0322, 300101-3004, 3006-3020, 3022-3025, 3103, 3104, 3402-3404, 3407, 3408 |
| 44 | 235 bp | 1070 bp | 1104, 1127, 1135 | 0112, 0114, 0119, 03010101-0317, 0319-0339, 300101-3004, 3006-3013, 3015-3020, 3022-3025, 3103, 3104, 3204, 3402-3404, 3407, 3408, 3601, 3602 |
| 5 | 180 bp | 800 bp | 1105 |  |
| 67,8 | 185, 550 bp | 1070 bp | 1106, 1118, 1122 | 0238, 9201, 9235, 2603, 2606, 2621, 2630, 2636 |
| 74,6 | 215 bp | 1070 bp | 1108 | 01010101-0102, 0104N, 0107-0111N, 0113-0118N, 0121-0124, 0126-0130, 0318, 3004, 3006, 3017, 3601, 3602weakly, 3604 |
| 85 | 95 bp | 1070 bp | 1109, 1134 |  |
| 97 | 200 bp | 800 bp | 1107 |  |
| 105 | 120 bp | 1070 bp | 1110 | 250101-2506, 260101-2606, 2608-2618, 2620-2629, 2632-2637, 3313, 340101-3408, 6601, 6604-6607, B*0818, B*7301 |
| 11 | 215 bp | 800 bp | 110101-110103, 110104weakly, 110105-1107, 1109-1122, 1127, 1129, 1130, 1132-1134, 1136 | 0112, 0119, 0125weakly, 0302, 0310, 0331, 0332 |
| 12 | 235 bp | 1070 bp | 110101-110103, 110104weakly, 110105-1103, 1105-1125, 1129-1134, 1136 | 01010101-0102, 0104N, 0106, 0107, 0109-0111N, 0113, 0116N-0118N, 0121-0130, 0318, 3604 |
| 135,9 | 90, 200 bp | 800 bp | 1111, 1134 | 4301 |
| 145 | 100 bp | 1070 bp | 110101-1111, 1113-1116, 1120-1127, 1129-1136 | 0113, 0117, 2502, 2613, 2619, 2633, 340101-340102 weakly ,3402-3404, 3405weakly, 3406, 3408, 6601, 6604, 6606, 6607 |
| 155,10 | 100, 215 bp | 1070 bp | 1112, 112402, 1125, 1131, 1135 | 0106, 0234-023503 weakly, 0256, 0262, 0278, 9203, 03010101-0331, 0333-0339, 2424, 29010101-2903, 2904weakly, 2905-2917, 300101-3003, 3007-3020, 3022-3025, 3103, 3104, 3204, 3402-3404, 3406-3408, 6602, 6606, 680101-680202, 6806-6814, 6816-6819, 6821-6830, 6832-6839, 6841-6843, 6901 |
| 165,7 | 95 bp | 1070 bp | 1113 |  |
| 17 | 200 bp | 1070 bp | 1114 | 0110, 300101-3003, 3007, 3008, 3010-3016, 3018-3020, 3022, 3024, 3025, 8001 |
| 18 | 245 bp | 1070 bp | 111501 |  |
| 1911 | 175, 220 bp | 1070 bp | 1116, 1123, 1135 |  |
| 20 | 240 bp | 1070bp | 1117, 1136 | 260101-2602, 2604, 260701-2615, 2617-2619, 2622-2629, 2631-2634, 2636, 2637, 4301 |
| 215,6 | 100 bp | 1070 bp | 1117, 1119 | 01010101-0104N, 0106, 0108-0112, 0114-0116N, 0118N-0130, 2444weakly, 250101-250102, 2503-2506, 260101-2612, 2614-2618, 2620-2629, 2631, 2632, 2634-2637, 3103, 3313, 3601-3604, 4301, 6605, 7410, 8001 |
| 22 | 230 bp | 1070 bp | 1106, 1118 | 0205-020604, 020606, 0208, 0210, 0214, 0221, 0228, 0241, 0244, 0251, 0254, 0257, 0261, 0272, 0279, 0284, 0291, 0299, 9206, 9208, 9222, 9226, 9227, 9237, 9242-9244, 2603, 2606, 2621, 2630, 6815 |
| 235 | 80 bp | 800 bp | 1103, 1108, 1120, 1125 | 020301-020302weakly, 0213, 0226, 0238, 9217 weakly, 9248weakly, 6842weakly |
| 244 | 470 bp | 1070 bp | 1121N | 0104N, 0321N, 2307N, 2411N |
| 25 | 215 bp | 1070 bp | 112401 | 030102, 8001 |
| 26 | 305 bp | 1070 bp | 1126 | 0103, 2632, 3313, 3603, 7410 |
| 27 | 250 bp | 1070 bp | 1127 | 01010101-0102, 0104N, 0106-0119, 0121-0130, 0318, 8001 |
| 28 | 245 bp | 800 bp | 111502 |  |
| 295 | 80 bp | 1070 bp | 1110 | 0255, 0324, 2603, 2606, 2621, 2630, 3301, 330301-3307, 3310-3312, 3314-3316, 3318, 3319, 340101, 3402-3408, 6601-6607, 680101-6809, 6811N, 6812, 6815-6829, 6831-6835, 6838-6843, 6901 |
| 30 | 265 bp | 1070 bp | 1129 |  |
| 31 | 285 bp | 1070 bp | 1130 |  |
| 3212 | 205, 295 | 1070 bp | 1131, 1132, 1135 | 0307, 3004, 3006, 3009, 3017, 3103, 3104 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-A*11 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-A*11 subtyping.

In addition, wells number 5, 9, 11, 13, 23 and 28 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3Due to the sharing of sequence motifs between HLA-A alleles some non-HLA-A*11 alleles will be amplified by primer mixes 1, 3, 4, 6, 7 and 10 to 15, 17, 20 to 27, 29 and 32.

4Primer mixes 1, 4, 7 and 24 may give rise to nonspecific amplifications.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6The specific primer pair in primer mixes 7 and 21 may yield less specific PCR product than the other A*11 primer mixes.

7Primer mixes 6, 9 and 16 have a tendency of giving rise to primer oligomer formation. Most pronounced for primer mix 6.

8Primer mix 6: Specific PCR product of 185 bp in the A*1122 allele. Specific PCR product of 550 bp in the A*1106, 1118 and A*0238, 9201, 9235, 2603, 2606, 2621, 2630 and 2636 alleles.

9Primer mix 13: Specific PCR fragment of 90 bp in the A*1134 allele. Specific PCR fragment of 200 bp in the A*1111 and A*4301 alleles.

10Primer mix 15: Specific PCR fragment of 100 bp in the A*1112 and A*0234-023503 weakly, 0256, 0262, 0278, 9203, 0302, 0310, 0318, 0331, 2424, 29010101-2903, 2904weakly, 2905-2917, 3017, 3217, 6602, 6606, 680101-680202, 6806-6814, 6816-6819, 6821-6830, 6832-6839, 6841-6843 and 6901 alleles.

Specific PCR fragment of 215 bp in the A*112402, 1125, 1131, 1135 and A*0106, 0308, 0329, 0330, 0334, 0336N, 0341, 300201-300204, 3003, 3007, 3009, 3010, 3012, 3013, 3022, 3103, 3104, 3204, 3402-3404, 3406-3408 alleles.

Specific PCR fragment of 100 and 215 bp in the A*03010101030106, 0303N-0307, 0309, 0311N-0317, 0319-0328, 0333, 0335, 0337-0340, 0342, 300101-300102, 3008, 301101-301102, 3014L-3016, 3018-3020, 3023-3026 alleles, please note that both PCR fragments may not be obtained.

11Primer mix 19: Specific PCR product of 175 bp in the A*1116 and 1135 alleles. Specific PCR product of 220 bp in the A*1123 allele.

12Primer mix 32: Specific PCR fragment of 205 bp in the A*1131, 1135 and A*0307, 3004, 3006, 3009, 3017, 3103 and 3104 alleles. Specific PCR fragment of 295 bp in the A*1132 allele.

1The A*1128 allele has been renamed to A*111502.

2Primer mix 6: Specific PCR product of 185 bp in the A*1122 allele. Specific PCR product of 550 bp in the A*1106, 1118 and A*0238, 9201, 9235, 2603, 2606, 2621, 2630 and 2636 alleles.

5Primer mix 13: Specific PCR fragment of 90 bp in the A*1134 allele. Specific PCR fragment of 200 bp in the A*1111 and A*4301 alleles.

Primer mix 15: Specific PCR fragment of 100 bp in the A*1112 and A*0234-023503 weakly, 0256, 0262, 0278, 9203, 0302, 0310, 0318, 0331, 2424, 29010101-2903, 2904weakly, 2905-2917, 3017, 3217, 6602, 6606, 680101-680202, 6806-6814, 6816-6819, 6821-6830, 6832-6839, 6841-6843 and 6901 alleles. Specific PCR fragment of 215 bp in the A*112402, 1125, 1131, 1135 and A*0106, 0308, 0329, 0330, 0334, 0336N, 0341, 300201-300204, 3003, 3007, 3009, 3010, 3012, 3013, 3022, 3103, 3104, 3204, 3402-3404, 3406-3408 alleles. Specific PCR fragment of 100 and 215 bp in the A*03010101030106, 0303N-0307, 0309, 0311N-0317, 0319-0328, 0333, 0335, 0337-0340, 0342, 300101-300102, 3008, 301101-301102, 3014L-3016, 3018-3020, 3023-3026 alleles, please note that both PCR fragments may not be obtained.

Primer mix 19: Specific PCR product of 175 bp in the A*1116 and 1135 alleles. Specific PCR product of 220 bp in the A*1123 allele.

Primer mix 32: Specific PCR fragment of 205 bp in the A*1131, 1135 and A*0307, 3004, 3006, 3009, 3017, 3103 and 3104 alleles. Specific PCR fragment of 295 bp in the A*1132 allele. ‘

w’, may be weakly amplified.

Changes in revision R02 compared to R01:

Typographic errors have been corrected in the Interpretation Table.