PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-A*11

Prod. No:	101. 416-12/12u

101.416-04/04u

Lot No:    	01H

Expiry Date:    	2012-April-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for HLA-A*11 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-A*11 alleles3 | Other amplified HLA-A alleles4 |
| --- | --- | --- | --- | --- |
| 16 | 195 bp | 800 bp | *110101-110116, 1103-1113, 111501, 111502, 1120-1127, 1129-1137, 1139, 1141-1144, 1146-1152, 1154, 1155 | *0113, 0234-023503, 025601, 025602, 0262, 0278, 9203, 03010101-030108, 030110-0307, 0309-0331, 0333-0335, 0337-0340, 0342-0356, 0358-0374, 2419, 3018, 340101-3408, 6601, 6602, 6604, 6606-6610, 6612, 680101-680204, 6806-6814, 6816-6819, 6821-6830, 6832-6835, 6837-6845, 6847, 6848, 6901, 7413 |
| 2 | 270 bp | 1070 bp | *110201-110203, 1114, 1116, 1138 |  |
| 3 | 190 bp | 1070 bp | *1103, 1133 | *0322, 0342, 300101-3004, 3006-3020, 3022-3027N, 3029-3034, 3103, 3104, 3402w, 3403, 3404w, 3407w, 3408w |
| 46 | 235 bp | 1070 bp | *1104, 1127, 1135 | *0112, 0114, 0119, 9256, 03010101-0317, 0319-0339, 0341-0374, 2492, 300101-3004, 3006-3013, 3015-3020, 3022-3027N, 3029-3034, 3103, 3104, 3204, 3402-3404, 3407, 3408, 3601, 3602, 3605 |
| 511 | 180 bp, 210 bp | 800 bp | *1105 | *6608 |
| 612 | 195 bp, 550 bp | 1070 bp | *1106, 1107, 1118, 1122 | *0238, 9201, 9235, 9254, 2511, 2603, 2606, 2621, 2630, 2636 |
| 76,7 | 215 bp | 1070 bp | *1108, 1144, 1150 | *01010101-0102, 0104N, 0107-0111N, 0113-0118N, 0121-0124, 0126-0140, 0142-0151, 0318, 0350, 0366, 3004, 3006, 3017, 3029, 3601, 3602, 3604, 3605 |
| 85 | 100 bp | 800 bp | *1109, 1134 |  |
| 95,8 | 85 bp | 800 bp | *1127, 1138, 1139 | *0126, 2459 |
| 105,13 | 120 bp, 280 bp, | 1070 bp | *1110, 1143, 1152 | *0151, 250101-2511, 260101-2606, 2608-2618, 2620-2629, 2632-2642, 3103, 3313, 340101-3408, 6601, 6604-6611, B*0818, B*7301 |
| 11 | 215 bp | 800 bp | *110101-1107, 1109-1122, 1127, 1129, 1130, 1132-1134, 1136-1143, 1145-1147, 1149, 1151-1152, 1154-1155 | *0112, 0119, 0125w, 0302, 0310, 0331, 0332, 0365, 0369N, 0373, 2492 |
| 12 | 235 bp | 1070 bp | *110101-1103, 1105-1125, 1129-1134, 1136-1147, 1149, 1151-1152, 1154-1155 | *01010101-0102, 0104N, 0106, 0107, 0109-0111N, 0113, 0116N-0118N, 0121-0140, 0142-0151, 0318, 3604 |
| 135,8,14 | 90 bp, 195 bp | 800 bp | *1111, 1134 | *4301 |
| 145 | 100 bp | 1070 bp | *110101-1111, 1113-1116, 1120-1127, 1129-1139, 1141-1152, 1154-1155 | *0113, 0117, 0363, 2502, 2613, 2619, 2633, 340101w, 340102w, 3402-3404, 3405w, 3406, 3408, 6601, 6604, 6606-6611 |
| 155,15 | 100 bp, 215 bp | 800 bp | *1112, 112402, 1125, 1131, 1135 | *0106, 0234w-023503w, 025601, 025602, 0262, 0278, 9203, 9256, 03010101-0331, 0333-0374, 2424, 29010101-2903, 2904w, 2905-2918, 2921, 2922, 300101-300204, 3003, 3007-3020, 3022-3027N, 3030-3034, 3103, 3104, 3204, 3217, 3402-3404, 3406-3408, 6602, 6606, 6612, 680101-680204, 6806-6814, 6816-6819, 6821-6823, 6825-6830, 6832-6839, 6841-6848, 6901, 7413 |
| 165, 8,16 | 95 bp, 205 bp | 1070 bp | *1107, 1113, 1154 |  |
| 17 | 205 bp | 1070 bp | *1114, 1150 | *0110, 300101-3003, 3007, 3008, 3010-3016, 3018-3020, 3022, 3024-3026, 3030-3034, 8001 |
| 18 | 235 bp | 1070 bp | *111501, 1147 |  |
| 196,9,10,17 | 175 bp, 220 bp, 265 bp | 1070 bp | *1116, 1123, 1135, 1142, 1146 | *9256 |
| 2018 | 175 bp, 240 bp | 800 bp | *1117, 1136, 1140, 1142 | *0143, 260101-2602, 2604, 260701-2615, 2617-2619, 2622-2629, 2631-2634, 2636-2642, 4301 |
| 215,7 | 100 bp | 1070 bp | *1117, 1119, 1140 | *01010101-0104N, 0106, 0108-0112, 0114-0116N, 0118N-0151, 0341, 2444w, 250101, 250102, 2503-2511, 260101-2612, 2614-2618, 2620-2629, 2631, 2632, 2634-2642, 3103, 3313, 3601-3605, 4301, 6605, 7410, 8001 |
| 2219 | 150 bp, 230 bp | 1070 bp | *1106, 1118, 1137 | *020501-020604, 020606-020609, 0208, 0210, 0214, 0221, 0228, 0241, 0244, 0251, 0254, 0257, 0261, 0272, 0279, 0284, 0291, 0299, 9206, 9208, 9222, 9226, 9227, 9237, 9242-9244, 9254, 9269, 9270, 9272, 9278-9280, 2603, 2606, 2621, 2630, 6815 |
| 235 | 80 bp | 800 bp | *1103, 1108, 1120, 1125 | *020301w, 020302w, 0213, 0226, 0238, 0299, 9217w, 9248w, 927101, 927102, 6842w |
| 246,20 | 295 bp, 470 bp | 1070 bp | *1121N, 1148 | *0104N, 0141, 0321N, 2307N, 2411N |
| 257 | 220 bp | 1070 bp | *112401, 1147 | *030102, 300205, 8001 |
| 2621 | 305 bp, 370 bp | 1070 bp | *1126, 1141 | *0103, 2632, 3313, 3603, 7410 |
| 2722 | 210 bp, 260 bp | 1070 bp | *1117, 1127, 1138, 1139, 1155 | *01010101-0102, 0104N, 0106-0119, 0121-0140, 0142-0151, 0318, 2492, 8001 |
| 2823 | 240 bp, 280 bp | 800 bp | *111502, 1149, 1152 | *2635 |
| 295 | 80 bp | 1070 bp | *1110 | *0255, 0324, 2603, 2606, 2621, 2630, 330101-330103, 330301-3307, 3310-3312, 3314-3316, 3318-3320, 3322-3329, 340101-3408, 6601-6610, 6612, 680101-6809, 6811N, 6812, 6815-6829, 6831-6835, 6837-6845, 6847, 6848, 6901 |
| 3024 | 235 bp, 265 bp | 1070 bp | *1129, 1145, 1155 | *6611 |
| 319,25 | 230 bp, 285 bp | 1070 bp | *1130, 1143, 1149 | *3103, 3313 |
| 326,26 | 205 bp, 265 bp, 295 bp | 1070 bp | *1131, 1132, 1135, 1150, 1151 | *0121, 9256, 0307, 0342, 3004, 3006, 3009, 3017, 3029, 3103, 3104 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-A*11 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-A*11 subtyping.

In addition, wells number 5, 8, 9, 11, 13, 15, 20, 23 and 28 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3The A* 1113 and A*1154 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 16. The A* 1132 and A*1151 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 32.

4Due to the sharing of sequence motifs between HLA-A alleles some non-HLA-A*11 alleles will be amplified by primer mixes 1, 3 to 7, 9 to 15, 17 and 19 to 32.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6Primer mixes 1, 4, 7, 19, 24 and 32 may give rise to nonspecific amplifications.

7Primer mixes 7, 21 and 25 may give a lower yield of specific PCR product than the other A*11 primer mixes.

8Primer mixes 9, 13 and 16 have a tendency of giving rise to primer oligomer formation.

9Primer mixes 19 and 31 may give rise to a long unspecific amplification product of about 700 bp. This band should be disregarded when interpreting the A*11 SSP typings.

10Primer mix 19 has a tendency of giving rise to a weaker positive control band than the other A*11 primer mixes.

11Primer mix 5: Specific PCR product of 180 bp in the A*1105 allele. Specific PCR product of 210 bp in the A*6608 allele.

12Primer mix 6: Specific PCR product of 195 bp in the A*1107 and 1122 alleles. Specific PCR product of 550 bp in the A*1106 and 1118 and the A*0238, 9201, 9235, 9254, 2511, 2603, 2606, 2621, 2630 and 2636 alleles.

13Primer mix 10: Specific PCR fragment of 120 bp in the A*1110, 0151, 250101-2511, 260101-2606, 2608-2618, 2620-2629, 2632-2634, 2636-2642, 340101-3408, 6601, 6604-6611, B*0818, B*7301 allele. Specific PCR fragment of 280 bp in the A*1143 and 1152 and the A*3103 alleles. Specific PCR fragment of 120 and 280 bp in the A*2635 and 3313 alleles.

14Primer mix 13: Specific PCR fragment of 90 bp in the A*1134 allele. Specific PCR fragment of 195 bp in the A*1111 and A*4301 alleles.

15Primer mix 15: Specific PCR fragment of 100 bp in the A*1112 and the A*0234w-023503w, 025601, 025602, 0262, 0278, 9203, 030102, 0302,0310, 0318, 0331, 0350, 0365, 0366, 0369, 0373, 2424, 29010101-2903, 2904w, 2905-2918, 2921, 2922, 3217, 6602, 6612, 680101-680204, 6806-6814, 6816-6819, 6821-6823, 6825-6830, 6832-6839, 6841-6848, 6901 and 7413 alleles. Specific PCR fragment of 215 bp in the A*112402, 1125, 1131 and 1135 and the A*0106, 9256, 030103, 030110, 0308, 0329, 0330, 0334, 0336, 0341, 0362, 0363, 300201-300204, 3003, 3007, 3009, 3010 3012, 3013, 3022, 3027N, 3031-3034, 3103, 3104, 3204, 3402-3404, 3407 and 3408 alleles. Specific PCR fragment of 100 and 215 bp in the A*03010101-03010103, 030103-030109, 030111-031117, 0303N-0307, 0309, 0311N-0317, 0319-0328, 0333, 0335, 0337-0340, 0342-0349, 0351-0361, 0364, 0367, 0368N, 0370-0372, 0374, 300101, 300102, 3008, 301101, 301102, 3014L-3020, 3023-3026 and 3030 alleles. Both PCR fragments may not always be obtained.

16Primer mix 16: Specific PCR fragment of 95 bp in the A*1113 allele. Specific PCR fragment of 205 bp in the A*1107 and 1154 alleles.

17Primer mix 19: Specific PCR product of 175 bp in the A*1116, 1135 and 1142 and the A*9256 alleles. Specific PCR product of 220 bp in the A*1123 allele. Specific PCR product of 265 bp in the A*1146 allele.

18Primer mix 20: Specific PCR fragment of 175 bp in the A*1142 allele. Specific PCR fragment of 240 bp in the A*1117, 1136 and 1140 and the A*0143, 260101-2602, 2604, 260701-2615, 2617-2619, 2622-2629, 2631-2634, 2636-2642 and  4301 alleles.

19Primer mix 22: Specific PCR fragment of 150 bp in the A*1137 allele. Specific PCR fragment of 230 bp in the A*1106 and 1118 and the A*020501-020604, 020606-020609, 0208, 0210, 0214, 0221, 0228, 0241, 0244, 0251, 0254, 0257, 0261, 0272, 0279, 0284, 0291, 0299, 9206, 9208, 9222, 9226, 9227, 9237, 9242-9244, 9254, 9269, 9270, 9272, 9278-9280, 2603, 2606, 2621, 2630 and 6815 alleles.

20Primer mix 24: Specific PCR fragment of 295 bp in the A*1148 and the A*0141 alleles. Specific PCR fragment of 470 bp in the A*1121N and the A*0104N, 0321N, 2307N and A*2411N alleles.

21Primer mix 26: Specific PCR fragment of 305 bp in the A*1126 and the A*0103, 2632, 3313, 3603 and A*7410 alleles. Specific PCR fragment of 370 bp in the A*1141 allele.

22Primer mix 27: Specific PCR fragment of 210 bp in the A*1117 allele. Specific PCR fragment of 260 bp in the A*1127, 1138, 1139 and 1155 and the A*01010101-0102, 0104N, 0106-0119, 0121-0140, 0142, 0144-0151, 0318, 2492 and 8001 alleles. Specific PCR fragment of 210 and 260 bp in the A*0143 allele.

23Primer mix 28: Specific PCR fragment of 240 bp in the A*111502 and 1149 alleles. Specific PCR fragment of 280 bp in the A*1152 and the A*2635 alleles.

24Primer mix 30: Specific PCR fragment of 235 bp in the A* 1145 and the A*6611 alleles. Specific PCR fragment of 265 bp in the A* 1129 and 1155 alleles.

25Primer mix 31: Specific PCR fragment of 230 bp in the A* 1149 allele. Specific PCR fragment of 285 bp in the A*1130 and 1143 and the A*3103 and 3313 alleles.

26Primer mix 32: Specific PCR fragment of 205 bp in the A* 1131 and 1135 and the A*0121, 9256, 0307, 0342, 3004, 3006, 3009, 3017, 3029, 3103 and 3104 alleles. Specific PCR fragment of 265 bp in the A*1151 allele. Specific PCR fragment of 295 bp in the A*1132 and A*1150 alleles.

‘w’, may be weakly amplified.

1The A*1128 allele has been renamed to A*111502.

2The A* 1113 and A*1154 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 16.

3The A* 1132 and A*1151 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 32.

4Primer mix 5: Specific PCR product of 180 bp in the A*1105 allele. Specific PCR product of 210 bp in the A*6608 allele.

Primer mix 6: Specific PCR product of 195 bp in the A*1107 and 1122 alleles. Specific PCR product of 550 bp in the A*1106 and 1118 and the A*0238, 9201, 9235, 9254, 2511, 2603, 2606, 2621, 2630 and 2636 alleles.

Primer mix 10: Specific PCR fragment of 120 bp in the A*1110, 0151, 250101-2511, 260101-2606, 2608-2618, 2620-2629, 2632-2634, 2636-2642, 340101-3408, 6601, 6604-6611, B*0818, B*7301 allele. Specific PCR fragment of 280 bp in the A*1143 and 1152 and the A*3103 alleles. Specific PCR fragment of 120 and 280 bp in the A*2635 and 3313 alleles.

Primer mix 13: Specific PCR fragment of 90 bp in the A*1134 allele. Specific PCR fragment of 195 bp in the A*1111 and A*4301 alleles.

Primer mix 15: Specific PCR fragment of 100 bp in the A*1112 and the A*0234w-023503w, 025601, 025602, 0262, 0278, 9203, 030102, 0302,0310, 0318, 0331, 0350, 0365, 0366, 0369, 0373, 2424, 29010101-2903, 2904w, 2905-2918, 2921, 2922, 3217, 6602, 6612, 680101-680204, 6806-6814, 6816-6819, 6821-6823, 6825-6830, 6832-6839, 6841-6848, 6901 and 7413 alleles. Specific PCR fragment of 215 bp in the A*112402, 1125, 1131 and 1135 and the A*0106, 9256, 030103, 030110, 0308, 0329, 0330, 0334, 0336, 0341, 0362, 0363, 300201-300204, 3003, 3007, 3009, 3010 3012, 3013, 3022, 3027N, 3031-3034, 3103, 3104, 3204, 3402-3404, 3407 and 3408 alleles. Specific PCR fragment of 100 and 215 bp in the A*03010101-03010103, 030103-030109, 030111-031117, 0303N-0307, 0309, 0311N-0317, 0319-0328, 0333, 0335, 0337-0340, 0342-0349, 0351-0361, 0364, 0367, 0368N, 0370-0372, 0374, 300101, 300102, 3008, 301101, 301102, 3014L-3020, 3023-3026 and 3030 alleles. Both PCR fragments may not always be obtained.

Primer mix 16: Specific PCR fragment of 95 bp in the A*1113 allele. Specific PCR fragment of 205 bp in the A*1107 and 1154 alleles.

Primer mix 19: Specific PCR product of 175 bp in the A*1116, 1135 and 1142 and the A*9256 alleles. Specific PCR product of 220 bp in the A*1123 allele. Specific PCR product of 265 bp in the A*1146 allele.

Primer mix 20: Specific PCR fragment of 175 bp in the A*1142 allele. Specific PCR fragment of 240 bp in the A*1117, 1136 and 1140 and the A*0143, 260101-2602, 2604, 260701-2615, 2617-2619, 2622-2629, 2631-2634, 2636-2642 and  4301 alleles.

Primer mix 22: Specific PCR fragment of 150 bp in the A*1137 allele. Specific PCR fragment of 230 bp in the A*1106 and 1118 and the A*020501-020604, 020606-020609, 0208, 0210, 0214, 0221, 0228, 0241, 0244, 0251, 0254, 0257, 0261, 0272, 0279, 0284, 0291, 0299, 9206, 9208, 9222, 9226, 9227, 9237, 9242-9244, 9254, 9269, 9270, 9272, 9278-9280, 2603, 2606, 2621, 2630 and 6815 alleles.

Primer mix 24: Specific PCR fragment of 295 bp in the A*1148 and the A*0141 alleles. Specific PCR fragment of 470 bp in the A*1121N and the A*0104N, 0321N, 2307N and A*2411N alleles.

Primer mix 26: Specific PCR fragment of 305 bp in the A*1126 and the A*0103, 2632, 3313, 3603 and A*7410 alleles. Specific PCR fragment of 370 bp in the A*1141 allele.

Primer mix 27: Specific PCR fragment of 210 bp in the A*1117 allele. Specific PCR fragment of 260 bp in the A*1127, 1138, 1139 and 1155 and the A*01010101-0102, 0104N, 0106-0119, 0121-0140, 0142, 0144-0151, 0318, 2492 and 8001 alleles. Specific PCR fragment of 210 and 260 bp in the A*0143 allele.

Primer mix 28: Specific PCR fragment of 240 bp in the A*111502 and 1149 alleles. Specific PCR fragment of 280 bp in the A*1152 and the A*2635 alleles.

Primer mix 30: Specific PCR fragment of 235 bp in the A* 1145 and the A*6611 alleles. Specific PCR fragment of 265 bp in the A* 1129 and 1155 alleles.

Primer mix 31: Specific PCR fragment of 230 bp in the A* 1149 allele. Specific PCR fragment of 285 bp in the A*1130 and 1143 and the A*3103 and 3313 alleles.

Primer mix 32: Specific PCR fragment of 205 bp in the A* 1131 and 1135 and the A*0121, 9256, 0307, 0342, 3004, 3006, 3009, 3017, 3029, 3103 and 3104 alleles. Specific PCR fragment of 265 bp in the A*1151 allele. Specific PCR fragment of 295 bp in the A*1132 and A*1150 alleles.

5Modified sequences as of allele database 3.7.0: A*11:02:01 corrected at position 899 and the A*11:53 allele shown to be identical to the correct sequence of A*11:02:01. As a consequence, the A*11:02:01-11:02:03 alleles are not amplified by primer mix 5.

‘w’, may be weakly amplified.

Change in revision R01 compared to R00:

- Modified sequences as of allele database 3.7.0: A*11:02:01 corrected at position 899 and the A*11:53 allele shown to be identical to the correct sequence of A*11:02:01. As a consequence, the A*11:02:01-11:02:03 alleles are not amplified by primer mix 5.

Change in revision R02 compared to R01:

- The HLA-A*3402, 3404 and 3407-3408 alleles are weakly amplified by primer mix 3. This has been changed in the Specificity and Interpretation Tables.