PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-A*23

Prod. No:	101.421-06/06u

Lot No:    	54M

Expiry Date:    	2014-March-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for HLA-A*23 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-A*23 alleles3 | Other amplified HLA Class I alleles4 |
| --- | --- | --- | --- | --- |
| 16 | 210 bp | 800 bp | *23:01:01-23:01:07, 23:03:01-23:46 | *02:17:01-02:17:02, 02:108, 02:110, 02:268, 02:300, 02:303, 24:13:01-24:13:02, 24:18, 24:24, 24:94, 29:07, 31:29, B*18:27 |
| 2 | 160 bp | 1070 bp | *23:01:01-23:02, 23:05-23:42, 23:44-23:46 | *02:19, 02:36-02:37, 02:54, 02:255, 24:02:01:01-24:02:41, 24:02:43-24:02:51, 24:04-24:09N, 24:11N, 24:13:01-24:15, 24:17, 24:19-24:20, 24:24-24:32, 24:34-24:64, 24:66-24:74, 24:76-24:93, 24:95-24:109, 24:111-24:124, 24:126-24:137, 24:139-24:157, 24:159-24:166, 24:168-24:182, 33:19, 68:26, 68:65 |
| 35,8 | 125 bp, 270 bp | 800 bp | *23:03:01-23:03:02, 23:25 | *24:21:01, 29:07, 31:29, B*18:27 |
| 45,9 | 90 bp, 200 bp | 1070 bp | *23:18, 23:28 | *24:77 |
| 5 | 230 bp | 800 bp | *23:06 | *31:36 |
| 6 | 470 bp | 1070 bp | *23:07N | *01:04N, 03:21N, 11:21N, 24:11N |
| 75,10 | 95 bp, 205 bp | 800 bp | *23:08N, 23:22 | *02:82N |
| 87,11 | 135 bp, 215 bp | 1070 bp | *23:09, 23:26 | *01:02, 01:20, 24:129 |
| 9 | 235 bp | 1070 bp | *23:05 | *24:25 |
| 1012 | 135 bp, 235 bp | 800 bp | *23:10, 23:23, 23:43 | *24:10w, 24:46, B*18:27 |
| 11 | 200 bp | 800 bp | *23:11N |  |
| 12 | 190 bp | 1070 bp | *23:12 | *24:30, 24:42, 25:11, 32:08, B*13:39w, 38:16w, 40:13w, 40:19w, 40:37w, 40:109w, 44:02:19w, 44:05:03w, 44:18w, 44:25w, 44:50w, 44:75w, 44:95w, 49:01:01w-49:01:03w, 49:04w-49:20w, 51:103w, 51:119w, 57:51w |
| 135,13 | 90 bp, 210 bp | 800 bp | *23:02, 23:24, 23:30 | *24:06, 24:87, 24:138, 24:167 |
| 14 | 245 bp | 1070 bp | *23:04 | *02:17:01-02:17:02, 02:108, 02:110, 02:268, 02:300, 02:303, 24:03:01-24:03:02, 24:10, 24:18, 24:22, 24:33, 24:94, 24:125, 24:138, 24:167, 29:07, 31:29, B*18:27 |
| 15 | 210 bp | 1070 bp | *23:14 | *24:13:02, B*18:27 |
| 1614 | 175 bp, 205 bp | 800 bp | *23:14 | *02:17:01w-02:17:02w, 24:02:01:01-24:11N, 24:13:01-24:13:02, 24:17-24:50, 24:54-24:56, 24:58-24:63, 24:66-24:91, 24:93, 24:95-24:113, 24:115-24:137, 24:139-24:182, 26:16, 33:19, 68:45 |
| 1715 | 125 bp, 225 bp | 1070 bp | *23:13, 23:33 | *03:72, 11:88, 24:07, 24:19, 24:24, 24:131, 30:01:01-30:01:05, 30:11:01-30:11:02, 30:14L-30:20, 30:23-30:26, 30:30-30:31, 30:35-30:43, 30:48-30:49, 30:52-30:54, 68:45 |
| 185 | 110 bp | 1070 bp | *23:01:01-23:01:07, 23:02w, 23:04-23:13, 23:14w, 23:15-23:23, 23:25-23:33, 23:35-23:46 | *02:40, 02:51, 02:130, 24:24, 32:28, 33:32, 68:51w |
| 195,16 | 120 bp, 260 bp | 800 bp | *23:15, 23:27 |  |
| 2017 | 130 bp, 230 bp | 800 bp | *23:16, 23:29 | *24:128 |
| 215 | 90 bp | 800 bp | *23:01:01-23:01:07, 23:02?-23:04?, 23:06-23:07N, 23:08N?, 23:09, 23:10?-23:16?, 23:18?-23:25?, 23:26, 23:27?-23:37?, 23:38N, 23:39?-23:46? |  |
| 225,6,18 | 90 bp, 290 bp | 1070 bp | *23:19Q, 23:31, 23:45 | *24:17, 24:41, 24:62, 24:106, 29:07, 31:29 |
| 235,7,19 | 80 bp, 170 bp | 1070 bp | *23:20, 23:45 | *02:41, 02:80, 02:117, 02:289, 02:304, 24:62, 26:10, 32:28, 33:32 |
| 2420 | 180 bp, 240 bp | 800 bp | *23:21, 23:40 |  |
| 255,21 | 95 bp, 205 bp | 1070 bp | *23:41-23:42 | *02:221, 29:15 |
| 266,22 | 145 bp, 245 bp | 1070 bp | *23:36, 23:39 | *24:32, 30:22, 32:07 |
| 2723 | 205 bp, 285 bp | 1070 bp | *23:34-23:35 |  |
| 28 | 270 bp | 1070 bp | *23:32 |  |
| 2924 | 200 bp, 240 bp | 1070 bp | *23:37, 23:40 |  |
| 30 | 245 bp | 1070 bp | *23:38N | *24:61 |
| 31 | 185 bp | 1070 bp | *23:44 |  |
| 32 | 195 bp | 1070 bp | *23:46 | *24:66 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-A*23 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-A*23 subtyping.

In addition, wells number 3, 5, 7, 10, 11, 13, 16, 19 to 21 and 24 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

alleles. Specific In the presence of a specific amplification the intensity of the control band often decreases.

3For several HLA-A alleles 1st or 4th exon nucleotide sequences are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in these regions are conserved within allelic groups.

The A*23:08N and 23:22 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 7.

The A*23:09 and 23:26 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 8.

The A*23:10 and 23:23 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 10.

The A*23:13 and 23:33 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 17.

The A*23:15 and 23:27 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 19.

The A*23:16 and 23:29 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 20.

The A*23:18 and 23:28 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 4.

The A*23:19Q and 23:31 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 22.

The A*23:36 and 23:39 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 26.

The A*23:41 and 23:42 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 25.

4Due to the sharing of sequence motifs between HLA-A alleles non-HLA-A*23 alleles will be amplified by primer mixes 1 to 10, 12 to 18, 20, 22, 23, 25, 26, 30 and 32. In addition, the B*18:27 allele will be amplified by primer mixes 1, 3, 10, 14 and 15, and primer mix 12 weakly amplifies the B*13:39, 38:16, 40:13, 40:19, 40:37, 40:109, 44:02:19, 44:05:03, 44:18, 44:25, 44:50, 44:75, 44:95, 49:01:01-49:01:03, 49:04-49:20, 51:103, 51:119 and 57:51 alleles.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6Primer mixes 1, 22 and 26 may yield less PCR product than the other A*23 primer mixes.

7Primer mix 8 and 23 may give rise to nonspecific amplifications.

8Primer mix 3: Specific PCR fragment of 125 bp in the A*23:03:01-23:03:02 and the A*24:21:01, 29:07 and 31:29 and the B*18:27 PCR fragment of 270 bp in the A*23:25 allele.

9Primer mix 4: Specific PCR fragment of 90 bp in the A*23:18 and 23:28 and the A*24:77 alleles. Specific PCR fragment of 200 bp in the A*23:28 and the A*24:77 alleles.

10Primer mix 7: Specific PCR fragment of 95 bp in the A*23:08N and the A*02:82N alleles. Specific PCR fragment of 205 bp in the A*23:22 allele.

11Primer mix 8: Specific PCR fragment of 135 bp in the A*23:26 allele. Specific PCR fragment of 215 bp in the A*23:09 and the A*01:02, 01:20 and 24:129 alleles.

12Primer mix 10: Specific PCR fragment of 135 bp in the A*23:23 and in the B*18:27 alleles. Specific PCR fragment of 235 bp in the A*23:10 and 23:43 and in the A*24:10w and 24:46 alleles.

13Primer mix 13: Specific PCR fragment of 90 bp in the A*23:30 allele. Specific PCR fragment of 210 bp in the A*23:02 and 23:24 and in the A*24:06, 24:87, 24:138 and 24:167 alleles.

14Primer mix 16: Specific PCR fragment of 175 bp in the A*23:14 and the A*24:02:16, 24:06, 24:13:01-24:13:02, 24:18, 24:22, 24:54, 24:87, 24:88, 24:91, 24:107, 24:133 and 24:167 alleles. Specific PCR fragment of 205 bp in the A*24:05, 24:24, 24:67, 24:130, 24:168, 26:16 and 68:45 alleles. Specific PCR fragment of 175 and 205 bp in the A*24:02:01:01-24:02:15, 24:02.17-24:04, 24:07-24:11N, 24:17, 24:19-24:21:02, 24:23, 24:25-24:50, 24:55-24:56, 24:58-24:63, 24:66-24:86N, 24:88-24:90N, 24:93, 24:95-24:106, 24:108-24:113, 24:115-24:129, 24:131-24:132N, 24:134-24:137, 24:139-24:166, 24:169-24:182 and 33:19 alleles. Both fragments may not always be visible.

15Primer mix 17: Specific PCR fragment of 125 bp in the A*23:33 allele. Specific PCR fragment of 225 bp in the A*23:13 and the A*03:72, 11:88, 24:07, 24:19, 24:24, 24:131, 30:01:01-30:01:05, 30:11:01-30:11:02, 30:14L-30:20, 30:23-30:26, 30:30-30:31, 30:35-30:43, 30:48-30:49, 30:52-30:54 and 68:45 alleles.

16Primer mix 19: Specific PCR fragment of 120 bp in the A*23:15 allele. Specific PCR fragment of 260 bp in the A*23:27 allele.

17Primer mix 20: Specific PCR fragment of 130 bp in the A*23:29 and in the A* 24:128 alleles. Specific PCR fragment of 230 bp in the A*23:16 allele.

18Primer mix 22: Specific PCR fragment of 90 bp in the A*23:31 and 23:45 and the A*24:17, 24:41, 24:62, 24:106, 29:07 and 31:29 alleles. Specific PCR fragment of 290 bp in the A*23:19Q allele.

19Primer mix 23: Specific PCR fragment of 80 bp in the A*23:45 and the A*02:41, 02:80, 02:117, 02:289, 02:304, 24:62, 26:10, 32:28 and 33:32 alleles. Specific PCR fragment of 170 bp in the A*23:20 allele.

20Primer mix 24: Specific PCR fragment of 180 bp in the A*23:21 allele. Specific PCR fragment of 240 bp in the A*23:40 allele.

21Primer mix 25: Specific PCR fragment of 95 bp in the A*23:41 and the A*02:221 and 29:15 alleles. Specific PCR fragment of 205 bp in the A*23:42 allele.

22Primer mix 26: Specific PCR fragment of 145 bp in the A*23:39 and the A*30:22 alleles. Specific PCR fragment of 245 bp in the A*23:36 and the A*24:32 and 32:07 alleles.

23Primer mix 27: Specific PCR fragment of 205 bp in the A*23:34 allele. Specific PCR fragment of 285 bp in the A*23:35 allele.

24Primer mix 29: Specific PCR fragment of 200 bp in the A*23:37 allele.  Specific PCR fragment of 240 bp in the A*23:40 allele.

‘w’, may be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.

1The A*23:08N and 23:22 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 7.

The A*23:09 and 23:26 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 8.

The A*23:10 and 23:23 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 10.

The A*23:13 and 23:33 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 17.

The A*23:15 and 23:27 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 19.

The A*23:16 and 23:29 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 20.

The A*23:18 and 23:28 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 4.

The A*23:19Q and 23:31 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 22.

The A*23:36 and 23:39 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 26.

The A*23:41 and 23:42 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 25.

2Primer mix 3: Specific PCR fragment of 125 bp in the A*23:03:01-23:03:02 and the A*24:21:01, 29:07 and 31:29 and the B*18:27 alleles. Specific PCR fragment of 270 bp in the A*23:25 allele.

Primer mix 4: Specific PCR fragment of 90 bp in the A*23:18 and 23:28 and the A*24:77 alleles. Specific PCR fragment of 200 bp in the A*23:28 and the A*24:77 alleles.

Primer mix 7: Specific PCR fragment of 95 bp in the A*23:08N and the A*02:82N alleles. Specific PCR fragment of 205 bp in the A*23:22 allele.

Primer mix 8: Specific PCR fragment of 135 bp in the A*23:26 allele. Specific PCR fragment of 215 bp in the A*23:09 and the A*01:02, 01:20 and 24:129 alleles.

Primer mix 10: Specific PCR fragment of 135 bp in the A*23:23 and in the B*18:27 alleles. Specific PCR fragment of 235 bp in the A*23:10 and 23:43 and in the A*24:10w and 24:46 alleles.

Primer mix 13: Specific PCR fragment of 90 bp in the A*23:30 allele. Specific PCR fragment of 210 bp in the A*23:02 and 23:24 and in the A*24:06, 24:87, 24:138 and 24:167 alleles.

Primer mix 16: Specific PCR fragment of 175 bp in the A*23:14 and the A*24:02:16, 24:06, 24:13:01-24:13:02, 24:18, 24:22, 24:54, 24:87, 24:88, 24:91, 24:107, 24:133 and 24:167 alleles. Specific PCR fragment of 205 bp in the A*24:05, 24:24, 24:67, 24:130, 24:168, 26:16 and 68:45 alleles. Specific PCR fragment of 175 and 205 bp in the A*24:02:01:01-24:02:15, 24:02.17-24:04, 24:07-24:11N, 24:17, 24:19-24:21:02, 24:23, 24:25-24:50, 24:55-24:56, 24:58-24:63, 24:66-24:86N, 24:88-24:90N, 24:93, 24:95-24:106, 24:108-24:113, 24:115-24:129, 24:131-24:132N, 24:134-24:137, 24:139-24:166, 24:169-24:182 and 33:19 alleles. Both fragments may not always be visible.

Primer mix 17: Specific PCR fragment of 125 bp in the A*23:33 allele. Specific PCR fragment of 225 bp in the A*23:13 and the A*03:72, 11:88, 24:07, 24:19, 24:24, 24:131, 30:01:01-30:01:05, 30:11:01-30:11:02, 30:14L-30:20, 30:23-30:26, 30:30-30:31, 30:35-30:43, 30:48-30:49, 30:52-30:54 and 68:45 alleles.

Primer mix 19: Specific PCR fragment of 120 bp in the A*23:15 allele. Specific PCR fragment of 260 bp in the A*23:27 allele.

Primer mix 20: Specific PCR fragment of 130 bp in the A*23:29 and in the A* 24:128 alleles. Specific PCR fragment of 230 bp in the A*23:16 allele.

Primer mix 22: Specific PCR fragment of 90 bp in the A*23:31 and 23:45 and the A*24:17, 24:41, 24:62, 24:106, 29:07 and 31:29 alleles. Specific PCR fragment of 290 bp in the A*23:19Q allele.

Primer mix 23: Specific PCR fragment of 80 bp in the A*23:45 and the A*02:41, 02:80, 02:117, 02:289, 02:304, 24:62, 26:10, 32:28 and 33:32 alleles. Specific PCR fragment of 170 bp in the A*23:20 allele.

Primer mix 24: Specific PCR fragment of 180 bp in the A*23:21 allele. Specific PCR fragment of 240 bp in the A*23:40 allele.

Primer mix 25: Specific PCR fragment of 95 bp in the A*23:41 and the A*02:221 and 29:15 alleles. Specific PCR fragment of 205 bp in the A*23:42 allele.

Primer mix 26: Specific PCR fragment of 145 bp in the A*23:39 and the A*30:22 alleles. Specific PCR fragment of 245 bp in the A*23:36 and the A*24:32 and 32:07 alleles.

Primer mix 27: Specific PCR fragment of 205 bp in the A*23:34 allele. Specific PCR fragment of 285 bp in the A*23:35 allele.

Primer mix 29: Specific PCR fragment of 200 bp in the A*23:37 allele.  Specific PCR fragment of 240 bp in the A*23:40 allele.

‘w’, may be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.

Change in revision R01 compared to R00:

- Primer mix 21 does not amplify the A*23:05 allele. Furthermore, for many A*23 alleles it is not known whether they are amplified by this primer mix due to lack of nucleotide sequence information. This has been changed in the specificity and amplification tables.

Change in revision R02 compared to R01:

- Primer mix 12 weakly amplifies the following HLA-B alleles: B*13:39, 38:16, 40:13, 40:19, 40:37, 40:109, 44:02:19, 44:05:03, 44:18, 44:25, 44:50, 44:75, 44:95, 49:01:01-49:01:03, 49:04-49:20, 51:103, 51:119 and 57:51. This has been corrected in the Specificity and Interpretation Tables.