PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-A*24

Prod. No:	101.422-24/24u

101.422-03/03u

Lot No:    	12G

Expiry Date:    	2011-September-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 82 primer mixes used for HLA-A*24 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-A*24 alleles | Other amplified HLA Class I alleles3 |
| --- | --- | --- | --- | --- |
| 17 | 210 bp | 800 bp | *24020101-240212, 240213w, 240214-240217, 240220-2411N, 241301-2415, 2417-2432, 2434-2464, 2466-2475, 2477-2499 | *230101-2321, 3319, 8001w |
| 2 | 245 bp | 1070 bp | *240301, 240302, 2410, 2418, 2422, 2433, 2494 | *021701, 021702, 9208, 9210, 2304, 2907, B*1827 |
| 3 | 210 bp | 800 bp | *24020101-240217, 240220-2405, 2407-2411N, 2417, 2419-2421, 2423, 2425-2450, 2455, 2456, 2458-2463, 2466-2486N, 2488-2490N, 2493, 2495-2499 | *3319 |
| 45 | 220 bp | 1070 bp | *2406, 241301, 2418, 2422, 2424, 2494 | *021701, 021702, 9208, 9210, 230101-2313, 2315-2321, 2907 |
| 5 | 175 bp | 1070 bp | *24020101-240217, 240220-2404, 2406-2411N, 241301, 241302, 2417-2423, 2425-2450, 2454-2456, 2458-2463, 2466-2491, 2493, 2495-2499 | *021701w, 021702w, 2314, 3319 |
| 65 | 175 bp | 1070 bp | *2405, 2424 | *230101-2313, 2315-2321, 2907, B*1827 |
| 7 | 335 bp | 1070 bp | *24020101-240217, 240220-240302, 2405-2411N, 241301, 241302, 2417, 2418, 2420-2427, 2429-2443, 2445N-2450, 2452, 2454-2456, 2458-2464, 2466-2488, 2490N, 2491, 2493-2499 | *230101-2321 |
| 84 | 75 bp | 1070 bp | *2404 |  |
| 9 | 225 bp | 800 bp | *2407, 2419, 2424 | *2313, 300101, 300102, 301101, 301102, 3014L-3020, 3023-3026, 6845 |
| 10 | 370 bp | 1070 bp | *24020101-240217, 240220-2406, 2408-2411N, 241301, 241302, 2417, 2418, 2420-2423, 2425-2450, 2452, 2454-2456, 2458-2464, 2466-2491, 2493-2499 | *0210, 021701, 021702, 0239, 9208, 9210, 9248, 230101-2312, 2314-2321, 3319 |
| 118 | 200 bp, 245 bp | 1070 bp | *2408, 2442, 2461, 2489 | *0276, 3022 |
| 12 | 235 bp | 1070 bp | *2425 | *2305 |
| 13 | 160 bp | 1070 bp | *24020101-240217, 240220, 2404-2409N, 2411N, 241301-2415, 2417, 2419, 2420, 2423-2432, 2434-2464, 2466-2474, 2476-2493, 2495-2499 | *0219, 0236, 0237, 0254, 230101, 2302, 2305-2321, 3319, 6826 |
| 144 | 105 bp | 1070 bp | *2409N |  |
| 15 | 385 bp | 800 bp | *2414, 2415, 2451, 2453, 2457, 2492 | *0246, 0248, 0270, 9229, 0330, 3007, 3108, 3205, 3321 |
| 164 | 85 bp | 1070 bp | *2417, 2441 | *2907 |
| 17 | 230 bp | 1070 bp | *2410, 2446 | *2310 |
| 18 | 275 bp | 1070 bp | *24020102L |  |
| 197 | 195 bp | 1070 bp | *24020101-240209, 240211-240217, 240220-2411N, 241301-2415, 2417-2432, 2434-2464, 2466-2499 | *230101-2321, 3319 |
| 206,7 | 470 bp | 1070 bp | *2411N | *0104N, 0321N, 1121N, 2307N |
| 21 | 155 bp | 800 bp | *2431 |  |
| 224 | 125 bp | 800 bp | *2427 |  |
| 23 | 190 bp | 800 bp | *2428, 2430, 2442, 2489 | *020109, 0250, 9222, 0309, 1106, 1118, 2312, 2603, 2606, 2621, 2630, 2919, 3208, 3324, 6805, 6815, 6820, 7406 |
| 24 | 240 bp | 800 bp | *2419, 2428, 2444, 2489 | *0276, 300101, 300102, 301101, 301102, 3013-3020, 3023, 3024, 3026, 6845 |
| 25 | 220 bp | 1070 bp | *241301, 241302, 2418, 2424, 2456, 2494 | *021701, 021702, 9208, 9210, 230101, 230301-2321, 2907, B*1827 |
| 264,9 | 90 bp, 220 bp | 800 bp | *2422, 2496 |  |
| 274, 7,10 | 80 bp, 370 bp | 800 bp | *2414, 2432 | *0246, 0248, 0270, 9229, 3205 |
| 28 | 155 bp | 800 bp | *2435 |  |
| 29 | 210 bp | 800 bp | *2408, 2429, 2442, 2489 | *0276, 3022 |
| 304, 11 | 125 bp, 200 bp | 800 bp | *2421, 2459 | *230301, 230302, 2907, B*1827 |
| 31 | 155 bp | 800 bp | *2437 |  |
| 32 | 225 bp | 1070 bp | *2415, 2441, 2451, 2492 | *01010101-0104N, 0106-0135, 0137, 1127, 1138, 1139, 2629, 3213, 6610, B*0764w, B*1512w, B*1519w |
| 334 | 100 bp | 1070 bp | *2439 |  |
| 34 | 195 bp | 800 bp | *2436N |  |
| 35 | 200 bp | 800 bp | *2445N, 2488 |  |
| 364,7 | 115 bp | 1070 bp | *2447 |  |
| 37 | 210 bp | 1070 bp | *2448N, 2454 |  |
| 38 | 145 bp | 800 bp | *2449 |  |
| 39 | 210 bp | 800 bp | *2450 | *9229 |
| 40 | 225 bp | 1070 bp | *2408, 2420, 2488 |  |
| 41 | 200 bp | 1070 bp | *2426, 2462 | *2629, 3105, 3213, 3310, 6610 |
| 42 | 200 bp | 1070 bp | *2424, 2467 | *2616, 6845 |
| 43 | 160 bp | 800 bp | *2443 |  |
| 44 | 250 bp | 800 bp | *2451, 2457, 2492 | *01010101-0104N, 0106-0119, 0121-0135, 0137, 0318, 1127, 1138, 1139, 2629, 2903, 3105, 3213, 3310, 6610, 6826, 8001 |
| 45 | 250 bp | 1070 bp | *2414, 2452 | *0120, 0219, 0236, 0237, 0254, 2629, 6610, B*0764, B*1512, B*1519 |
| 464,5 | 110 bp | 1070 bp | *2415, 2441, 2451, 2492 | *0250, 0273, 0293, 9222, 9256, 2610, 68020101-680202, 6815, 6818N, 6825, 6827, 6828, 6831, 6834, 6840, 6844, 6848 |
| 4712 | 200 bp, 410 bp | 800 bp | *2418, 2426, 2456 | *0330, 3007, 3108, 3205 |
| 48 | 195 bp | 1070 bp | *2424, 2471 | *230101-2321, 2907, B*1827 |
| 4913 | 215 bp, 245 bp | 1070 bp | *2423, 2491 |  |
| 50 | 235 bp | 800 bp | *2434 |  |
| 51 | 215 bp | 800 bp | *2438 |  |
| 527 | 240 bp | 800 bp | *2440N |  |
| 53 | 230 bp | 1070 bp | *2455 |  |
| 54 | 165 bp | 1070 bp | *2458 |  |
| 55 | 240 bp | 1070 bp | *2460N |  |
| 56 | 270 bp | 1070 bp | *2463 |  |
| 57 | 135 bp | 1070 bp | *2464 |  |
| 58 | 195 bp | 1070 bp | *2466 |  |
| 59 | 255 bp | 1070 bp | *2468 |  |
| 60 | 275 bp | 800 bp | *2469 |  |
| 614 | 105 bp | 800 bp | *2470 |  |
| 624 | 125 bp | 800 bp | *2472 | *9206, 9245 |
| 63 | 135 bp | 1070 bp | *2473 |  |
| 64 | 170 bp | 1070 bp | *2474 |  |
| 654,14 | 80 bp, 235 bp | 1070 bp | *2475, 2490N | *0288N |
| 66 | 200 bp | 800 bp | *2477 |  |
| 67 | 230 bp | 1070 bp | *2479 |  |
| 68 | 285 bp | 800 bp | *2478 |  |
| 694 | 105 bp | 1070 bp | *2480 |  |
| 70 | 250 bp | 1070 bp | *2481 |  |
| 71 | 260 bp | 800 bp | *2482 | *2913, 3107, 3108, 3110 |
| 724 | 120 bp | 1070 bp | *2483N |  |
| 734 | 100 bp | 1070 bp | *2484N |  |
| 74 | 200 bp | 1070 bp | *2485 |  |
| 75 | 290 bp | 1070 bp | *2486N |  |
| 767,15 | 170 bp, 260 bp | 1070 bp | *2476, 2498 |  |
| 77 | 210 bp | 800 bp | *2406, 2487 | *2302 |
| 78 | 140 bp | 800 bp | *2457, 2492 | *0250, 0273, 9222, 9256, 0317, 2610, 680101-6843, 6845-6848 |
| 79 | 255 bp | 1070 bp | *2414, 2493 | *0120, 0219, 0236, 0237, 0254 |
| 80 | 220 bp | 1070 bp | *2495 |  |
| 81 | 210 bp | 1070 bp | *2497 |  |
| 82 | 190 bp | 1070 bp | *2499 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-A*24 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-A*24 subtyping.

In addition, wells number 3, 9, 15, 21, 22, 23, 24, 26, 27, 28, 29, 30, 31, 34, 35, 38, 39, 43, 44, 47, 50, 51, 52, 60, 61, 62, 66, 68, 71, 77 and 78 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3Due to the sharing of sequence motifs between HLA-A alleles some non-HLA-A*24 alleles will be amplified by primer mixes 1 to 7, 9 to 13, 15 to 17, 19, 20, 23 to 25, 27, 29, 30, 32, 39, 41, 42, 44 to 48, 62, 65, 71 and 77 to 79. In addition, the B*0764, B*1512 and B*1519 alleles will be amplified by primer mixes 32 and 45, and the B*1827 allele will be amplified by mixes 2, 6, 25, 30 and 48.

We assume that unknown 4th exon A*23 and A*24 nucleotide sequences are conserved within the A*23/A*24 allele group.

4Short specific PCR fragments are less intense and not as sharp as longer specific bands.

5Primer mixes 4, 6,  46 and 48 may yield less specific PCR products than the other A*24 primer mixes.

6Primer mix 20 may give rise to a primer oligomer artefact.

7Primer mixes 1, 19, 20, 27, 36, 52 and 76 may give rise to nonspecific amplifications.

8Primer mix 11: Specific PCR fragment of 200 bp in the A*2408, A*2442 and 2489 and the A*0276 and A*3002 alleles. Specific PCR fragment of 245 bp in the A*2461 allele.

9Primer mix 26: Specific PCR fragment of 90 bp in the A*2496 allele. Specific PCR fragment of  220 bp in the A*2422 allele.

10Primer mix 27: Specific PCR fragment of 80 bp in the A*2432 and A*3205 alleles. Specific PCR fragment of 370 bp in the A*2414, A*0246, A*0248, A*0270 and A*9229 alleles.

11Primer mix 30: Specific PCR fragment of 125 bp in the A*2421 and the A*230301-230302, A*2907 and B*1827 alleles. Specific PCR fragment of 200 bp in the A*2459 allele.

12Primer mix 47: Specific PCR fragment of 200 bp in the A*2418 and 2456 alleles. Specific PCR fragment of 410 bp in the A*2426 and the A*0330, 3007, 3108 and 3205 alleles.

13Primer mix 49: Specific PCR fragment of 215 bp in the A*2491 allele. Specific PCR fragment of 245 bp in the A*2423 allele.

14Primer mix 65: Specific PCR fragment of 80 bp in the A*2475 allele. Specific PCR fragment of 235 bp in the A*2490N and the A*0288N alleles.

15Primer mix 76: Specific PCR fragment of 170 bp in the A*2476 allele. Specific PCR fragment of 260 bp in the A*2498 allele.

‘w’, might be weakly amplified.

1The sequence of the A*2401 has been shown to be in error.

The sequence of the A*2412 allele has been shown to be identical to A*2408.

The A*2416 allele has been renamed to A*3108.

The A*2465 allele has been renamed to A*242202.

2Primer mix 11: Specific PCR fragment of 200 bp in the A*2408 and A*2442 and the A*0276 and A*3002 alleles. Specific PCR fragment of 245 bp in the A*2461 allele.

Primer mix 26: Specific PCR fragment of 90 bp in the A*2496 allele. Specific PCR fragment of  220 bp in the A*2422 allele.

Primer mix 27: Specific PCR fragment of 80 bp in the A*2432 and A*3205 alleles. Specific PCR fragment of 370 bp in the A*2414, A*0246, A*0248, A*0270 and A*9229 alleles.

Primer mix 30: Specific PCR fragment of 125 bp in the A*2421 and the A*230301-230302, A*2907 and B*1827 alleles. Specific PCR fragment of 200 bp in the A*2459 allele.

Primer mix 47: Specific PCR fragment of 200 bp in the A*2418 and 2456 alleles. Specific PCR fragment of 410 bp in the A*2426 and the A*0330, 3007, 3108 and 3205 alleles.

Primer mix 49: Specific PCR fragment of 215 bp in the A*2491 allele. Specific PCR fragment of 245 bp in the A*2423 allele.

Primer mix 65: Specific PCR fragment of 80 bp in the A*2475 allele. Specific PCR fragment of 235 bp in the A*2490N and the A*0288N alleles.

Primer mix 76: Specific PCR fragment of 170 bp in the A*2476 allele. Specific PCR fragment of 260 bp in the A*2498 allele.

‘w’, might be weakly amplified.