PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-A*68

Prod. No:	101.418-12/12u

101.418-04/04u

Lot No:    	70K

Expiry Date:    	2013-July-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for HLA-A*68 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-A*68 alleles3 | Other amplified HLA-A alleles4 |
| --- | --- | --- | --- | --- |
| 16 | 195 bp | 800 bp | *68:01:01-68:02:04, 68:06-68:14, 68:16-68:19, 68:21-68:30, 68:32-68:35, 68:37-68:45, 68:46w, 68:47-68:54 | *01:13, 02:34-02:35:03, 02:56:01-02:56:02, 02:62, 02:78, 02:103, 03:01:01:01-03:01:08, 03:01:10-03:07, 03:09-03:31, 03:33-03:35, 03:37-03:40, 03:42-03:56, 03:58-03:82, 11:01:01-11:01:22, 11:03-11:13, 11:15:01-11:15:02, 11:20-11:27, 11:29-11:37, 11:39, 11:41-11:44, 11:46-11:50Q, 11:52Q, 11:54-11:56, 11:58-11:64, 24:19, 30:18, 34:01:01-34:08, 66:01-66:02, 66:04, 66:06-66:10, 66:12-66:14, 69:01, 74:13, C*03:82 |
| 2 | 435 bp | 1070 bp | *68:01:01-68:01:07, 68:03:01-68:05, 68:08:01-68:09, 68:11N-68:12, 68:16-68:17, 68:19-68:26, 68:29, 68:32-68:33, 68:35-68:39, 68:41-68:43, 68:45-68:47, 68:50, 68:52 | *01:51, 03:24, 11:10, 33:18, 34:02-34:04, 34:07-34:08 |
| 3 | 195 bp | 1070 bp | *68:02:01:01-68:02:04, 68:15, 68:18N, 68:28, 68:31, 68:34, 68:39-68:40, 68:44, 68:48-68:49N, 68:51, 68:53-68:54 |  |
| 49 | 180 bp, 225 bp | 1070 bp | *68:03:01-68:03:02, 68:05, 68:20, 68:30 | *02:06:05 |
| 510 | 140 bp, 235 bp | 800 bp | *68:04, 68:25 | *66:15 |
| 6 | 225 bp | 1070 bp | *68:05, 68:15, 68:20 | *02:06:05, 02:122, 02:143 |
| 711 | 135 bp, 155 bp | 1070 bp | *68:06, 68:32 | *02:52 |
| 812 | 160 bp, 240 bp | 800 bp | *68:07, 68:46 |  |
| 97,13 | 150 bp, 195 bp, 250 bp | 800 bp | *68:08:01-68:08:02, 68:18N, 68:47 | *26:43:01-26:43:02, 34:03?-34:04?, 34:06?-34:08?, 66:06 |
| 10 | 165 bp | 800 bp | *68:09, 68:26 | *01:12, 01:19, 03:10, 11:01:01-11:07, 11:10-11:21N, 11:26-11:27, 11:29-11:30, 11:32-11:34, 11:36-11:43, 11:45-11:49, 11:51-11:58, 11:60-11:64, 24:17, 24:41, 29:05 |
| 1114 | 160 bp, 200 bp | 800 bp | *68:10, 68:14, 68:17 |  |
| 1215 | 205 bp, 405 bp | 1070 bp | *68:11N, 68:38 |  |
| 1316 | 210 bp, 240 bp | 800 bp | *68:12, 68:50-68:51 | *26:18 |
| 1417 | 150 bp, 195 bp | 800 bp | *68:13, 68:41 |  |
| 158,18 | 145 bp, 205 bp | 1070 bp | *68:14, 68:19 | *02:121, 02:237, 03:17, 24:18, C*12:37 |
| 1619 | 150 bp, 215 bp | 1070 bp | *68:15-68:16, 68:31, 68:40 | *02:122, 02:143 |
| 1720 | 165 bp, 185 bp | 1070 bp | *68:02:01:01-68:02:04, 68:15, 68:18N, 68:20, 68:27-68:28, 68:31, 68:34, 68:40, 68:44, 68:48-68:49N, 68:51, 68:53-68:54 | *02:02w, 02:03:01-02:03:03, 02:05:01w-02:05:03w, 02:08w, 02:22:01-02:22:02, 02:47w, 02:49-02:50, 02:63w, 02:102w, 02:104, 02:115w, 02:117, 02:122, 02:135-02:136, 02:148, 02:154w-02:155w, 02:172w, 02:179w, 02:186w, 02:191, 02:209w, 02:230, 02:232w, 02:253, 02:258, 02:264, 23:02, 24:06, 24:87, 24:138, 25:01:01-25:03, 25:05-25:11, 25:13, 26:01:01-26:01:04, 26:01:07-26:07:02, 26:09-26:26, 26:28-26:39, 26:41-26:42, 26:45-26:47, 26:49-26:50, 31:30, 32:10, 34:01:01-34:01:02, 34:05, 43:01, 66:01-66:05, 66:07-66:15, B*27:25, B*27:45, C*02:07 |
| 187,21 | 200 bp, 225 bp | 800 bp | *68:21, 68:26 | *01:01:01:01-01:04N, 01:06-01:29, 01:31N-01:66, 03:04, 03:18, 11:27, 11:38-11:39, 24:17, 24:41, 29:03, 80:01-80:02 |
| 198 | 325 bp | 1070 bp | *68:22 |  |
| 205,8 | 90 bp | 1070 bp | *68:23 | *01:20, 01:66, 02:114, 02:246, 29:22 |
| 2122 | 165 bp, 215 bp | 1070 bp | *68:24, 68:28 | *02:49, 24:87, B*27:45 |
| 226 | 165 bp | 800 bp | *68:01:01-68:01:07, 68:03:01-68:05, 68:07, 68:10-68:14, 68:16-68:17, 68:19-68:25, 68:29-68:30, 68:32-68:33, 68:35-68:39, 68:41-68:43, 68:45-68:47, 68:50, 68:52 | *01:01:01:01w-01:04Nw, 01:07w-01:11Nw, 01:13w-01:18Nw, 01:20w-01:24w, 01:26w-01:29w, 01:31Nw-01:52Nw, 01:54w-01:64w, 01:66w, 02:229, 03:18w, 03:50, 03:66, 11:08, 11:44, 36:01w, 36:02, 36:03w-36:05w |
| 23 | 185 bp | 1070 bp | *68:01:01-68:01:07, 68:03:01-68:05, 68:07-68:14, 68:16-68:17, 68:19-68:25, 68:29-68:30, 68:32-68:33, 68:35-68:39, 68:41-68:43, 68:45-68:47, 68:50, 68:52 | *02:114, 02:229, 02:246, 03:01:01:01-03:17, 03:20-03:39, 03:41-03:42, 03:44-03:52, 03:54-03:81, 11:04, 11:35, 29:01:01:01-29:02:01:01, 29:02:03-29:02:05, 29:04-29:22, 30:26, 31:03-31:04, 31:06, 32:04, 33:18, 34:02-34:04, 34:07-34:08, 36:01-36:03, 36:05 |
| 247 | 375 bp | 1070 bp |  | *02:55, 26:22, 33:22, 66:09, 69:01 |
| 255,23 | 110 bp, 240 bp | 1070 bp | *68:29, 68:52 | *02:243, 24:82 |
| 265,7,24 | 100 bp, 185 bp | 1070 bp | *68:33, 68:49N |  |
| 2725 | 185 bp, 235 bp | 1070 bp | *68:34, 68:43 |  |
| 2826 | 200 bp, 230 bp | 1070 bp | *68:35, 68:38, 68:44 |  |
| 295-7,27 | 80 bp, 250 bp | 800 bp | *68:36, 68:42, 68:54 | *02:03:01-02:03:03, 02:26w, 02:99w, 02:117, 02:148, 02:171:02w, 02:253, 02:258, 02:264, 11:25w |
| 307,28 | 145 bp, 245 bp | 1070 bp | *68:37 | *02:117, 02:135, 25:01:01-25:07, 25:10-25:13, 26:01:01-26:01:14, 26:01:16-26:10, 26:12-26:13, 26:15-26:17, 26:19-26:27, 26:29-26:39, 26:41-26:43:02, 26:45-26:46, 26:48-26:50, 34:01:01-34:01:02, 34:05, 43:01, 66:01-66:15 |
| 317 | 220 bp | 1070 bp | *68:48, 68:50 | *25:01:01-25:04, 25:06-25:07, 25:09-25:13, 26:01:01-26:10, 26:12-26:43:02, 26:45-26:46, 26:48-26:50, 34:01:01-34:01:02, 34:03?-34:08?, 43:01, 66:01-66:15 |
| 3229 | 165 bp, 195 bp | 1070 bp | *68:21, 68:45, 68:53 | *02:74:02, 02:159, 23:25, 24:24, 24:67, 26:16 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-A*68 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-A*68 subtyping.

In addition, wells number 5, 8 to 11, 13, 14, 18, 22 and 29 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3The A*68:29 and A*68:52 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 25.

4Due to the sharing of sequence motifs between HLA-A alleles non-HLA-A*68 alleles will be amplified by primer mixes 1, 2, 4 to 7, 9, 10, 13, 15 to 18, 20 to 25 and 29 to 32. In addition, the B*27:25, B*27:45 and C*02:07 alleles will be amplified by primer mix 17, the B*27:45 allele will be amplified by primer mix 21, the C*03:82 allele will be amplified by primer mix 1 and the C*12:37 allele will be amplified by primer mix 15.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6Primer mixes 1, 22 and 29 may yield less specific PCR product than the other A*68 primer mixes.

7Primer mix 9, 18, 24, 26, 29, 30 and 31 may give rise to non-specific amplifications.

8Primer mixes 15, 19 and 20 have a tendency of giving rise to a primer oligomer artifact.

9Primer mix 4: Specific PCR fragment of 180 bp in the A*68:30 allele. Specific PCR fragment of 225 bp in the A*68:03:01-68:03:02, A*68:05 and A*68:20 alleles. Specific PCR fragment of 180 and 225 bp in the A*02:06:05 allele.

10Primer mix 5: Specific PCR fragment of 140 bp in the A*68:25 allele. Specific PCR fragment of 235 bp in the A*68:04 and the A*66:15 alleles.

11Primer mix 7: Specific PCR fragment of 135 bp in the A*68:06 and A*02:52 alleles. Specific PCR fragment of 155 bp in the A*68:32 allele.

12Primer mix 8: Specific PCR fragment of 160 bp in the A*68:07 allele. Specific PCR fragment of 240 bp in the A*68:46 allele.

13Primer mix 9: Specific PCR fragment of 150 bp in the A*68:18N allele. Specific PCR fragment of 195 bp in the A*68:47 allele. Specific PCR fragment of 250 bp in the A*68:08:01-68:08:02 and in the A*26:43:01-26:43:02, 34:03?-34:04?, 34:06?-34:08? and 66:06 alleles.

14Primer mix 11: Specific PCR fragment of 160 bp in the A*68:17 allele. Specific PCR fragment of 200 bp in the A*68:10 and A*68:14 alleles.

15Primer mix 12: Specific PCR fragment of 205 bp in the A*68:38 allele. Specific PCR fragment of 405 bp in the A*68:11N allele.

16Primer mix 13: Specific PCR fragment of 210 bp in the A*68:12 and A*68:50 alleles. Specific PCR fragment of 240 bp in the A*68:51 and 26:18 alleles.

17Primer mix 14: Specific PCR fragment of 150 bp in the A*68:41 allele. Specific PCR fragment of 195 bp in the A*68:13 allele.

18Primer mix 15: Specific PCR fragment of 145 bp in the A*68:19 and in the A*02:237, 03:17 and 24:18 alleles. Specific PCR fragment of 205 bp in the A*68:14 and in the A*02:121 and in the C*12:37 alleles.

19Primer mix 16: Specific PCR fragment of 150 bp in the A*68:16 allele. Specific PCR fragment of 215 bp in the A*68:15, 68:31 and 68:40 and in the A*02:122 and 02:143 alleles.

20Primer mix 17: Specific PCR fragment of 165 bp in the A*68:02:01:01-68:02:04, 68:15, 68:18N, 68:27-68:28, 68:31, 68:34, 68:40, 68:44, 68:48-68:49N, 68:51 and 68:53-68:54 and in the A*02:02w, 02:03:01-02:03:03, 02:05:01w-02:05:03w, 02:08w, 02:22:01-02:22:02, 02:47w, 02:49-02:50, 02:63w, 02:102w, 02:104, 02:115w, 02:117, 02:122, 02:135-02:136, 02:148, 02:154w-02:155w, 02:172w, 02:179w, 02:186w, 02:191, 02:209w, 02:230, 02:232w, 02:253, 02:258, 02:264, 23:02, 24:06, 24:87, 24:138, 25:01:01-25:03, 25:05-25:11, 25:13, 26:01:01-26:01:04, 26:01:07-26:07:02, 26:09-26:26, 26:28-26:39, 26:42, 26:45-26:47, 26:49-26:50, 31:30, 32:10, 34:01:01-34:01:02, 34:05, 43:01, 66:01-66:05, 66:07-66:15 and in the B*27:25, B*27:45 and C*02:07 alleles. Specific PCR fragment of 185 bp in the A*68:20 allele. Specific PCR fragment of 165 and 185 bp in the A*26:41 allele.

21Primer mix 18: Specific PCR fragment of 200 bp in the A*68:26 and in the A*01:01:01:01-01:04N, 01:06-01:29, 01:31N-01:66, 03:18, 11:27, 11:38-11:39, 24:17, 24:41, 29:03 and 80:01-80:02 alleles. Specific PCR fragment of 225 bp in the A*68:21 and A*03:04 alleles.

22Primer mix 21: Specific PCR fragment of 165 bp in the A*68:28 and in the A*02:49, 24:87 and in the B*27:45 alleles. Specific PCR fragment of 215 bp in the A*68:24 allele.

23Primer mix 25: Specific PCR fragment of 110 bp in the A*68:52 allele. Specific PCR fragment of 240 bp in the A*68:29 and in the A*02:243 and 24:82 alleles.

24Primer mix 26: Specific PCR fragment of 100 bp in the A*68:49N allele. Specific PCR fragment of 185 bp in the A*68:33 allele.

25Primer mix 27: Specific PCR fragment of 185 bp in the A*68:34 allele. Specific PCR fragment of 235 bp in the A*68:43 allele.

26Primer mix 28: Specific PCR fragment of 200 bp in the A*68:35 and 68:38 alleles. Specific PCR fragment of 230 bp in the A*68:44 allele.

27Primer mix 29: Specific PCR fragment of 80 bp in the A*68:42, 68:54, 02:03:01-02:03:03, 02:26w, 02:99w, 02:117, 02:148, 02:171:02w, 02:253, 02:258, 02:264, 11:25w alleles. Specific PCR fragment of 250 bp in the A*68:36 allele.

28Primer mix 30: Specific PCR fragment of 145 bp in the A*02:117, 02:135, 25:01:01-25:07, 25:10-25:13, 26:01:01-26:01:14, 26:01:16-26:10, 26:12-26:13, 26:15-26:17, 26:19-26:27, 26:29-26:39, 26:41-26:43:02, 26:45-26:46, 26:48-26:50, 34:01:01-34:01:02, 34:05, 43:01 and 66:01-66:15 alleles. Specific PCR fragment of 245 bp in the A*68:37 allele.

29Primer mix 32: Specific PCR fragment of 165 bp in the A*68:53 and 02:159 alleles. Specific PCR fragment of 195 bp in the A*68:21 and 68:45 and in the A*02:74:02, 23:25, 24:24, 24:67 and 26:16 alleles.

‘w, may be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.

1The A*68:29 and A*68:52 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 25.

2Primer mix 4: Specific PCR fragment of 180 bp in the A*68:30 allele. Specific PCR fragment of 225 bp in the A*68:03:01-68:03:02, A*68:05 and A*68:20 alleles. Specific PCR fragment of 180 and 225 bp in the A*02:06:05 allele.

Primer mix 5: Specific PCR fragment of 140 bp in the A*68:25 allele. Specific PCR fragment of 235 bp in the A*68:04 and the A*66:15 alleles.

Primer mix 7: Specific PCR fragment of 135 bp in the A*68:06 and A*02:52 alleles. Specific PCR fragment of 155 bp in the A*68:32 allele.

Primer mix 8: Specific PCR fragment of 160 bp in the A*68:07 allele. Specific PCR fragment of 240 bp in the A*68:46 allele.

Primer mix 9: Specific PCR fragment of 150 bp in the A*68:18N allele. Specific PCR fragment of 195 bp in the A*68:47 allele. Specific PCR fragment of 250 bp in the A*68:08:01-68:08:02 and in the A*26:43:01-26:43:02, 34:03?-34:04?, 34:06?-34:08? and 66:06 alleles.

Primer mix 11: Specific PCR fragment of 160 bp in the A*68:17 allele. Specific PCR fragment of 200 bp in the A*68:10 and A*68:14 alleles.

Primer mix 12: Specific PCR fragment of 205 bp in the A*68:38 allele. Specific PCR fragment of 405 bp in the A*68:11N allele.

Primer mix 13: Specific PCR fragment of 210 bp in the A*68:12 and A*68:50 alleles. Specific PCR fragment of 240 bp in the A*68:51 and 26:18 alleles.

Primer mix 14: Specific PCR fragment of 150 bp in the A*68:41 allele. Specific PCR fragment of 195 bp in the A*68:13 allele.

Primer mix 15: Specific PCR fragment of 145 bp in the A*68:19 and in the A*02:237, 03:17 and 24:18 alleles. Specific PCR fragment of 205 bp in the A*68:14 and in the A*02:121 and in the C*12:37 alleles.

Primer mix 16: Specific PCR fragment of 150 bp in the A*68:16 allele. Specific PCR fragment of 215 bp in the A*68:15, 68:31 and 68:40 and in the A*02:122 and 02:143 alleles.

Primer mix 17: Specific PCR fragment of 165 bp in the A*68:02:01:01-68:02:04, 68:15, 68:18N, 68:27-68:28, 68:31, 68:34, 68:40, 68:44, 68:48-68:49N, 68:51 and 68:53-68:54 and in the A*02:02w, 02:03:01-02:03:03, 02:05:01w-02:05:03w, 02:08w, 02:22:01-02:22:02, 02:47w, 02:49-02:50, 02:63w, 02:102w, 02:104, 02:115w, 02:117, 02:122, 02:135-02:136, 02:148, 02:154w-02:155w, 02:172w, 02:179w, 02:186w, 02:191, 02:209w, 02:230, 02:232w, 02:253, 02:258, 02:264, 23:02, 24:06, 24:87, 24:138, 25:01:01-25:03, 25:05-25:11, 25:13, 26:01:01-26:01:04, 26:01:07-26:07:02, 26:09-26:26, 26:28-26:39, 26:42, 26:45-26:47, 26:49-26:50, 31:30, 32:10, 34:01:01-34:01:02, 34:05, 43:01, 66:01-66:05, 66:07-66:15 and in the B*27:25, B*27:45 and C*02:07 alleles. Specific PCR fragment of 185 bp in the A*68:20 allele. Specific PCR fragment of 165 and 185 bp in the A*26:41 allele.

Primer mix 18: Specific PCR fragment of 200 bp in the A*68:26 and in the A*01:01:01:01-01:04N, 01:06-01:29, 01:31N-01:66, 03:18, 11:27, 11:38-11:39, 24:17, 24:41, 29:03 and 80:01-80:02 alleles. Specific PCR fragment of 225 bp in the A*68:21 and A*03:04 alleles.

Primer mix 21: Specific PCR fragment of 165 bp in the A*68:28 and in the A*02:49, 24:87 and in the B*27:45 alleles. Specific PCR fragment of 215 bp in the A*68:24 allele.

Primer mix 25: Specific PCR fragment of 110 bp in the A*68:52 allele. Specific PCR fragment of 240 bp in the A*68:29 and in the A*02:243 and 24:82 alleles.

Primer mix 26: Specific PCR fragment of 100 bp in the A*68:49N allele. Specific PCR fragment of 185 bp in the A*68:33 allele.

Primer mix 27: Specific PCR fragment of 185 bp in the A*68:34 allele. Specific PCR fragment of 235 bp in the A*68:43 allele.

Primer mix 28: Specific PCR fragment of 200 bp in the A*68:35 and 68:38 alleles. Specific PCR fragment of 230 bp in the A*68:44 allele.

Primer mix 29: Specific PCR fragment of 80 bp in the A*68:42, 68:54, 02:03:01-02:03:03, 02:26w, 02:99w, 02:117, 02:148, 02:171:02w, 02:253, 02:258, 02:264, 11:25w alleles. Specific PCR fragment of 250 bp in the A*68:36 allele.

Primer mix 30: Specific PCR fragment of 145 bp in the A*02:117, 02:135, 25:01:01-25:07, 25:10-25:13, 26:01:01-26:01:14, 26:01:16-26:10, 26:12-26:13, 26:15-26:17, 26:19-26:27, 26:29-26:39, 26:41-26:43:02, 26:45-26:46, 26:48-26:50, 34:01:01-34:01:02, 34:05, 43:01 and 66:01-66:15 alleles. Specific PCR fragment of 245 bp in the A*68:37 allele.

Primer mix 32: Specific PCR fragment of 165 bp in the A*68:53 and 02:159 alleles. Specific PCR fragment of 195 bp in the A*68:21 and 68:45 and in the A*02:74:02, 23:25, 24:24, 24:67 and 26:16 alleles.

‘w, may be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.

Change in revision R01 compared to R00:

- Primer mix 29 does not amplify the A*68:37 allele. This has been corrected in the specificity and amplification tables.