PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B low resolution

Prod. No:	101.501-48/48u

101.501-12/12u

Lot No:    	20K

Expiry Date:    	2012-May-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 48 primer mixes used for HLA-B low resolution SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | HLA-B serol.3 | Amplified HLA Class I4,5 alleles |
| --- | --- | --- | --- | --- |
| 16,7 | 110 bp | 800 bp | 7, 703, 40, 41, 42, 48, 61 | *07:02:01-07:18:02, 07:20-07:32, 07:34-07:39, 07:41-07:47, 07:49N-07:50, 07:52, 07:54-07:59, 07:61-07:99, 15:138, 37:07, 40:15-40:16, 40:23, 40:32, 40:98, 41:08, 42:05:01-42:05:02, 48:05, 48:08, 48:15, C*02:23 |
| 2 | 215 bp | 1070 bp | 8, 44 | *08:01:01-08:25, 08:27-08:49, 08:51-08:61, 15:142, 15:180, 44:49, 51:68 |
| 3 | 140 bp, 235 bp | 1070 bp | 7, 8, 13, 15, 35, 4005, 44, 49, 61, 62, 77 | *07:20, 07:24, 07:60, 08:21, 08:25, 13:01:01-13:04, 13:06-13:08Q, 13:10-13:23, 13:25-13:37, 15:07, 15:36w, 15:45, 15:55, 15:68, 15:89w, 15:126, 35:05:01-35:05:02, 35:16-35:17, 35:22, 35:30, 35:51, 35:58, 35:72, 35:89, 35:97, 40:05, 40:71, 44:08w, 44:54, 44:57w, 44:60, 46:12, 46:20, 51:64, 53:14, 58:18, C*03:05, C*03:25, C*03:27 |
| 48 | 130 bp, 265 bp | 1070 bp | 12, 13, 14, 17, 21, 35, 40, 41, 44, 45, 47, 49, 50, 60, 61, 64, 65 | *13:01:01-13:04, 13:06-13:13, 13:15-13:23, 13:25-13:37, 14:01-14:04, 14:07N, 14:09, 14:11-14:12, 14:14-14:18, 15:46, 15:53, 15:106, 18:44, 35:46-35:47, 35:63, 40:01:01-40:01:10, 40:07, 40:10, 40:14:01-40:16, 40:22N-40:23, 40:25, 40:30-40:34, 40:36, 40:38, 40:42-40:43, 40:45, 40:47-40:49, 40:51-40:55, 40:58-40:63, 40:65-40:67, 40:69, 40:72:01-40:73, 40:76-40:77, 40:79-40:81, 40:84, 40:87-40:88, 40:92, 41:01-41:12, 44:02:01:01-44:03:06, 44:03:08-44:05:02, 44:09-44:39, 44:41-44:43, 44:45-44:56N, 44:58N-44:80, 44:82, 44:84-44:99, 45:01-45:11, 47:01:01:01-47:07, 49:01:01-49:02, 49:04-49:10, 50:01:01-50:02, 50:04-50:06, 50:08-50:09, C*01:30 |
| 59 | 185 bp, 235 bp | 800 bp | 7, 16, 17, 27, 2708, 37, 38, 3901, 3902, 39, 64, 67 | *14:01, 14:07N-14:08, 14:10, 14:12, 14:14, 27:01-27:06, 27:08-27:10, 27:12-27:13, 27:16-27:18, 27:20, 27:23, 27:26-27:27, 27:29, 27:31, 27:35-27:37, 27:39-27:42, 27:44-27:46, 27:48-27:61, 27:64N-27:65N, 37:02, 38:01:01-38:03, 38:07-38:22, 39:01:01:01-39:01:01:02L, 39:01:03-39:01:08, 39:01:10-39:02:01, 39:03, 39:05:01-39:06:02, 39:07?, 39:08-39:09, 39:11, 39:14-39:15, 39:18, 39:19:02, 39:22, 39:24-39:44, 39:46-39:48, 39:50-39:57, 47:04-47:05, 48:21, 67:01:01 |
| 6 | 190 bp | 800 bp | 14, 35, 38, 39, 65 | *07:28, 14:02:01-14:02:02, 14:02:04-14:06:02, 14:09, 14:11, 14:13, 14:15-14:18, 15:77, 15:189, 35:26, 38:05, 39:04, 44:16, 44:37, 44:64:01-44:64:02, 44:91, 57:04, C*16:10 |
| 710 | 290 bp | 1070 bp | 15, 22, 46, 62, 63, 71, 72, 75, 76, 77 | *15:01:01:01-15:01:03, 15:01:06-15:02:04, 15:03:03-15:08, 15:10:02-15:11:03, 15:12-15:15, 15:17:01:01-15:17:02, 15:19-15:21, 15:24-15:28, 15:30-15:36, 15:38:01-15:40, 15:42-15:46, 15:48, 15:50, 15:55-15:58, 15:60, 15:63, 15:65-15:66, 15:70-15:71, 15:73, 15:75-15:79N, 15:81-15:89, 15:92, 15:94N, 15:96-15:97, 15:101-15:102, 15:104-15:107, 15:109-15:113, 15:116-15:118, 15:120-15:122, 15:125-15:126, 15:128-15:129, 15:135-15:150, 15:152, 15:154-15:155, 15:157, 15:159-15:160, 15:162-15:172, 15:174-15:175, 15:177-15:179, 15:181N-15:185, 15:187-15:191, 46:01:01-46:22 |
| 8 | 165 bp, 220 bp, 330 bp | 1070 bp | 5, 8, 12, 21, 22, 37, 41, 42, 44, 45, 48, 51, 56, 57, 60, 62, 70, 71, 72, 82 | *08:01:01-08:05, 08:08N-08:12:03, 08:15-08:19N, 08:21-08:24, 08:26-08:27, 08:29-08:36, 08:38-08:39, 08:41-08:48, 08:50-08:54, 08:56-08:61, 15:03:01-15:03:03, 15:09-15:10:02, 15:18:01-15:18:04, 15:23, 15:29, 15:37, 15:46-15:47, 15:49, 15:51-15:54, 15:61-15:62, 15:64, 15:69, 15:72, 15:74, 15:80, 15:83, 15:90-15:91, 15:93, 15:98-15:99, 15:103, 15:106, 15:108, 15:114-15:115, 15:119, 15:123-15:124, 15:127, 15:131-15:134, 15:143, 15:151, 15:153, 15:156, 15:158, 15:161, 15:173, 15:176, 15:180, 15:186, 35:87, 37:12, 40:12, 41:01-41:03:02, 41:05-41:09, 41:11-41:12, 42:01:01-42:02, 42:04-42:08, 42:10-42:13, 44:14-44:15, 44:18, 44:20, 44:62, 45:01-45:11, 51:08, 51:20, 51:36, 51:44N, 52:19, 55:20, 56:13, 57:09, 82:01-82:03, C*07:46 |
| 911 | 165 bp, 190 bp, 390 bp | 1070 bp | 5, 17, 21, 35, 51, 5102, 5103, 52, 56, 62, 63, 70, 78 | *15:01:02, 15:09, 15:16-15:17:02, 15:67, 15:95, 15:162, 15:168, 15:177, 35:01:10, 35:04:02, 40:26, 40:28, 44:62, 51:01:01-51:01:03, 51:01:05-51:02:03, 51:03-51:09:02, 51:11N-51:12, 51:13:02-51:14, 51:16-51:23, 51:24:03, 51:26-51:33, 51:37-51:41N, 51:43-51:44N, 51:46, 51:48-51:61, 51:63-51:80, 51:82-51:91, 51:94-51:95, 52:01:01-52:01:04, 52:02-52:13, 52:15-52:20, 56:05:01-56:06, 56:21, 58:08, 78:01-78:07 |
| 1010 | 180 bp | 800 bp | 13, 22, 55, 60 | *07:78, 13:01:01-13:02:07, 13:07N-13:09, 13:11, 13:14-13:20, 13:22:01-13:23, 13:25, 13:27-13:34, 13:36-13:37, 40:48, 45:10, 49:07, 55:09, 55:22, 55:24 |
| 116 | 105 bp, 195 bp | 1070 bp | 8, 12, 27, 38, 39, 3902, 40, 44, 45, 48, 60, 70, 71, 72, 82 | *07:27, 07:50, 08:04, 08:17, 08:54, 15:03:01-15:03:03, 15:47, 15:49, 15:54, 15:61-15:62, 15:64, 15:68-15:69, 15:91, 15:98, 15:103, 15:123, 15:127, 15:131-15:132, 15:151, 15:156, 15:158, 15:173, 18:37, 27:18, 27:29, 38:03, 39:02:01-39:02:02, 39:08, 39:13:01-39:13:02, 39:23, 39:39, 39:49, 40:12, 40:46, 40:93, 42:11, 44:10, 44:15, 44:18, 44:40, 44:44, 45:01, 45:05-45:07, 45:11, 48:01:01-48:05, 48:07-48:22, 50:02, 52:16, 55:18, 82:01-82:03 |
| 12 | 280 bp | 1070 bp | 5, 7, 8, 13, 15, 16, 17, 18, 22, 35, 40, 42, 44, 46, 48, 49, 51, 53, 55, 56, 57, 58, 60, 61, 62, 63, 70, 71, 72, 75, 76, 77, 78 | *07:09, 07:11, 07:17, 08:28, 08:35, 08:37, 13:04, 13:10, 13:26, 15:01:01:01-15:01:04, 15:01:06-15:08, 15:11:01-15:16, 15:18:01-15:21, 15:23-15:29, 15:31-15:36, 15:38:01-15:40, 15:43-15:44, 15:46-15:47, 15:49-15:57, 15:60-15:62, 15:64-15:72, 15:74-15:76, 15:78:01-15:82, 15:84-15:85, 15:87-15:89, 15:91-15:98, 15:101-15:129, 15:131-15:132, 15:134-15:136, 15:138-15:149N, 15:151-15:161, 15:163-15:167, 15:169-15:176, 15:178-15:187, 15:189-15:191, 18:01:01-18:15, 18:17N-18:25, 18:27-18:40, 18:42-18:49, 27:41, 35:01:01-35:01:19, 35:05:01-35:05:02, 35:07-35:08:04, 35:10-35:11, 35:14:01-35:17, 35:19-35:21, 35:23-35:30, 35:32, 35:35, 35:37, 35:40N-35:43, 35:45-35:54, 35:57-35:58, 35:61-35:64, 35:66-35:69, 35:71-35:72, 35:76-35:80, 35:82, 35:86, 35:89-35:94, 35:97, 35:99, 39:07, 39:43, 40:03, 40:20, 40:38, 40:52, 40:59-40:60, 42:09, 44:17, 44:43, 45:09, 46:01:01-46:10, 46:12-46:17, 46:19-46:22, 48:02:01-48:02:02, 48:14, 49:04-49:05, 51:37, 51:45, 51:63, 53:01:01-53:03, 53:05-53:06, 53:08:01-53:18, 53:20-53:23, 54:06, 54:09, 54:14, 55:14, 55:23, 55:32, 56:03, 56:09, 56:18, 57:01:01-57:01:07, 57:06, 57:08, 57:10-57:11, 57:13-57:16, 57:18-57:27, 57:29-57:31, 58:01:01-58:02, 58:04-58:07, 58:09-58:19, 58:21-58:26 |
| 13 | 195 bp | 1070 bp | 27, 35, 37, 44, 58, 76 | *15:12, 15:14, 15:19, 15:91, 15:131, 15:161, 35:45, 35:71, 37:01:01-37:09, 37:12-37:13, 37:15-37:21, 38:17, 44:17, 44:43, 45:09, 46:17, 53:22, 58:07 |
| 146 | 105 bp, 395 bp, 435 bp | 1070 bp | 5, 7, 15, 41, 42, 62, 63, 70, 71, 75, 77 | *07:04, 07:25, 15:09-15:10:02, 15:13, 15:16-15:18:04, 15:21, 15:23-15:24, 15:37, 15:44, 15:51-15:52, 15:66-15:67, 15:72, 15:80, 15:87, 15:90, 15:93, 15:95, 15:99, 15:108, 15:114-15:115, 15:119, 15:124, 15:133-15:134, 15:153, 15:157, 15:161-15:162, 15:168, 15:176-15:177, 15:186, 15:189, 41:08, 42:05:01-42:05:02 |
| 156 | 115 bp, 150 bp | 1070 bp | 18 | *18:01:01-18:15, 18:17N-18:28, 18:30-18:36, 18:38-18:47, 18:49 |
| 166 | 80 bp | 1070 bp | 7, 27, 2708, 44, 60 | *07:73, 27:01-27:21, 27:23-27:51, 27:53-27:65N, 38:22, 40:46, 40:93, 44:40, 44:44 |
| 17 | 150 bp | 800 bp | 12, 13, 17, 18, 22, 27, 35, 37, 39, 44, 45, 47, 48, 51, 53, 56, 57, 58, 62, 70, 75, 77, 78 | *08:49, 13:01:01-13:01:03, 13:06-13:07N, 13:12-13:13, 13:17, 13:20, 13:22:01-13:23, 13:25-13:26, 13:28-13:29, 13:36, 14:10, 15:02:01-15:02:04, 15:13, 15:20-15:21, 15:25:01-15:25:02, 15:36, 15:44, 15:62, 15:77, 15:80, 15:85, 15:88-15:89, 15:106, 15:112, 15:121, 15:139, 15:144, 15:154, 15:165, 15:170, 18:22, 27:19, 27:30, 35:01:01-35:04:03, 35:06-35:08:04, 35:10-35:17, 35:19-35:21, 35:23-35:30, 35:33-35:36, 35:38-35:42:02, 35:45-35:50, 35:52, 35:54-35:57, 35:59, 35:61-35:63, 35:65Q, 35:69-35:71, 35:74, 35:76-35:78, 35:80-35:85, 35:90-35:96, 35:98, 37:01:01-37:01:07, 37:03N-37:06, 37:08, 37:10-37:11, 37:13-37:22, 38:20, 39:42, 40:28, 44:02:01:01-44:14, 44:16-44:17, 44:19N, 44:21-44:30, 44:32-44:40, 44:42-44:46, 44:48-44:52N, 44:55-44:64:02, 44:66-44:98, 48:02:01-48:02:02, 51:04, 51:42, 51:46, 51:56, 53:01:01-53:13, 53:15-53:23, 55:14, 56:09, 56:11-56:12, 57:01:01-57:01:04, 57:01:06-57:10, 57:12, 57:14-57:20, 57:22-57:30, 58:01:01-58:01:02, 58:01:04, 58:04-58:05, 58:09-58:15, 58:17N, 58:19, 58:21-58:24, 58:28, 83:01 |
| 18 | 135 bp | 1070 bp | 8, 18, 22, 35, 39, 78 | *07:65, 08:32, 18:01:01-18:08, 18:10-18:15, 18:17N-18:36, 18:38-18:47, 35:01:01-35:03:02, 35:03:04-35:18, 35:20:01-35:24:02, 35:28-35:45, 35:48, 35:50-35:55, 35:57-35:62, 35:64-35:72, 35:74-35:99, 37:11, 39:19:01-39:19:02, 56:06, 78:01-78:05, 78:07 |
| 196,7 | 60 bp, 245 bp, 400 bp | 1070 bp | 5, 15, 44, 48, 60, 62, 63, 70, 71, 72, 75, 76, 77, 82 | *15:01:01:01-15:01:04, 15:01:06-15:21, 15:23-15:40, 15:42-15:58, 15:60-15:67, 15:69-15:99, 15:101-15:129, 15:131-15:191, 40:12, 44:10, 82:01-82:03 |
| 20 | 210 bp | 800 bp | 27, 37 | *07:27, 08:49, 37:01:01-37:22, 38:17 |
| 21 | 170 bp | 800 bp | 16, 35, 38, 39, 3901, 3902, 67, 72 | *08:55, 15:69, 15:186, 35:35, 38:01:01-38:09, 38:11-38:21, 39:01:01:01-39:01:01:02L, 39:01:03-39:20, 39:22-39:24, 39:26-39:29, 39:31, 39:35, 39:37-39:42, 39:44-39:46, 39:48-39:49, 39:51-39:57, 58:20, 67:01:01-67:02 |
| 226 | 110 bp | 1070 bp | 38 | *38:01:01-38:03, 38:05, 38:08-38:22 |
| 23 | 395 bp | 1070 bp | 14, 16, 38, 39, 3901, 64, 65 | *07:69, 07:85, 14:01-14:18, 38:01:01-38:02:02, 38:04-38:05, 38:08-38:22, 39:01:01:01-39:01:01:02L, 39:01:03-39:01:11, 39:03-39:07, 39:09, 39:11-39:12, 39:14-39:15, 39:18-39:19:02, 39:22, 39:24-39:38Q, 39:40N-39:48, 39:50-39:57 |
| 24 | 425 bp | 1070 bp | 7, 703, 8, 14, 15, 16, 21, 39, 3901, 3902, 40, 41, 42, 45, 48, 50, 60, 61, 64, 65, 67, 70, 73, 81 | *07:02:01-07:26, 07:28-07:35, 07:37, 07:39-07:64, 07:66-07:80, 07:82-07:99, 08:01:01-08:01:10, 08:04-08:35, 08:37-08:51, 08:53-08:61, 14:01-14:02:04, 14:03-14:18, 39:01:01:01-39:01:01:02L, 39:01:03-39:20, 39:22-39:57, 40:01:01-40:01:10, 40:07, 40:09?-40:11?, 40:14:01?-40:15?, 40:16, 40:18?, 40:21?-40:22N?, 40:23, 40:24?-40:38?, 40:42?-40:46?, 40:48?-40:50?, 40:51, 40:52?-40:58?, 40:59-40:60, 40:61?-40:65?, 40:66, 40:67?-40:69?, 40:71?, 40:72:01-40:73, 40:74?-40:75?, 40:77, 40:78?, 40:79, 40:80?-40:88?, 40:90?-40:93?, 40:95?, 40:98?-40:99?, 41:01-41:12, 42:01:01-42:02, 42:04-42:13, 45:01-45:11, 48:01:01-48:17, 48:19-48:22, 50:01:01-50:02, 50:04-50:09, 67:01:01-67:02, 73:01, 81:02 |
| 257 | 175 bp | 1070 bp | 15, 40, 44, 48, 60, 62, 71 | *15:116, 15:124, 40:01:01-40:01:06, 40:01:08-40:01:10, 40:07, 40:10, 40:12, 40:21-40:23, 40:25, 40:33, 40:36, 40:38, 40:42-40:43, 40:46-40:49, 40:51-40:52, 40:54-40:55, 40:60-40:63, 40:65-40:67, 40:69, 40:73-40:74, 40:76, 40:79, 40:81, 40:84, 40:87-40:88, 40:92, 44:31, 46:06, 48:03:01-48:03:02 |
| 2610 | 130 bp | 1070 bp | 21, 4005, 41, 50, 60, 61 | *18:48, 40:02:01-40:06:02, 40:08-40:09, 40:11, 40:13, 40:18-40:20, 40:24, 40:26-40:29, 40:35, 40:37, 40:39-40:40, 40:44, 40:50, 40:56-40:57, 40:64, 40:68, 40:70-40:71, 40:74-40:75, 40:78, 40:82, 40:85-40:86, 40:89-40:91, 40:94-40:99 |
| 276 | 105 bp | 1070 bp | 7, 8, 22, 41, 42 | *07:04, 07:25, 08:01:01-08:05, 08:07-08:12:03, 08:14-08:19N, 08:21-08:24, 08:26-08:39, 08:41-08:54, 08:56-08:61, 35:87, 41:01-41:08, 41:10-41:12, 42:01:01-42:02, 42:04-42:07, 42:09-42:13, 55:20 |
| 28 | 325 bp | 1070 bp | 7, 22, 27, 2708, 35, 42, 45, 46, 54, 55, 56, 67, 73, 78, 81, 82 | *07:02:01-07:02:19, 07:04-07:07, 07:09-07:15, 07:17-07:26, 07:28-07:31, 07:33-07:36, 07:39-07:46, 07:47w, 07:48-07:49N, 07:51-07:68, 07:70-07:84, 07:86-07:99, 15:76, 15:101, 27:01-27:11, 27:13-27:15, 27:17, 27:19-27:21, 27:24-27:28, 27:30-27:38, 27:40-27:58, 27:60-27:65N, 35:76, 42:01:01-42:02, 42:04-42:06, 42:08-42:10, 42:12-42:13, 44:90, 44:97, 45:06, 46:01:01-46:01:04, 46:02w, 46:03-46:22, 54:01-54:22, 55:01:01-55:05, 55:07-55:17, 55:19-55:40, 56:01:01-56:16, 56:18-56:22, 56:24-56:29, 67:01:01-67:02, 73:01, 81:01-81:04N, 82:01-82:03, 83:01 |
| 296,12 | 115 bp, 195 bp, 225 bp, 260 bp | 1070 bp | 35, 37, 44, 47, 57 | *08:49, 08:60, 35:38, 35:45, 35:71, 37:01:01-37:01:07, 37:03N-37:06, 37:08, 37:10-37:22, 42:13, 44:02:01:01-44:14, 44:16-44:17, 44:19N-44:36, 44:38-44:63, 44:65-44:99, 51:42, 53:22, 57:07, 57:09, 57:24, 83:01, C*15:25 |
| 30 | 215 bp | 800 bp | 5, 8, 12, 17, 21, 22, 41, 42, 44, 45, 51, 5102, 5103, 52, 53, 56, 62 | *08:09, 15:83, 41:01, 41:05-41:07, 41:09, 41:12, 42:04, 44:06, 44:15, 44:18, 44:20, 45:01-45:11, 51:01:01, 51:01:03-51:01:08, 51:01:10-51:02:01, 51:02:03-51:04, 51:06-51:07:01, 51:08-51:09:01, 51:10-51:14, 51:16-51:24:03, 51:26-51:46, 51:48-51:53, 51:55-51:77, 51:79-51:88, 51:90-51:92, 51:94-51:95, 52:01:02, 52:01:04, 52:02-52:03, 52:06:01-52:06:02, 52:09, 52:19, 53:06, 55:20, 56:13, 58:08 |
| 31 | 130 bp, 270 bp | 1070 bp | 17, 18, 22, 35, 37, 46, 51, 53, 62, 78 | *14:10, 15:57w, 18:22, 35:21, 35:24:01-35:24:02, 35:81, 35:96, 37:04:01-37:04:02, 40:28, 46:01:01-46:22, 51:04, 51:46, 51:56, 53:02, 53:06, 57:14, 58:09 |
| 326,12 | 90 bp, 410 bp | 1070 bp | 15, 22, 27, 35, 47, 54, 55, 56, 78, 81, 82 | *07:65, 27:01w, 27:02-27:11, 27:13-27:15, 27:17, 27:19-27:21, 27:24-27:28, 27:30-27:38, 27:40-27:58, 27:60-27:65N, 35:76, 44:90, 44:97, 47:01:01:01-47:03, 47:06-47:07, 54:01-54:22, 55:01:01-55:05, 55:07-55:17, 55:19-55:40, 56:01:01-56:16, 56:18-56:22, 56:24-56:29, 81:01, 82:01-82:03, 83:01 |
| 336 | 90 bp, 175 bp | 1070 bp | 15, 27, 35, 48, 60, 62, 75, 77, 81 | *13:36, 15:02:01-15:02:04, 15:08, 15:11:01-15:11:04, 15:13, 15:15, 15:21, 15:31, 15:44, 15:55, 15:76w, 15:88-15:89, 15:112, 15:121, 15:139, 15:144, 15:148, 15:170, 15:189, 15:191, 27:24, 35:46, 40:31, 40:45, 40:80, 48:01:01-48:01:02, 48:04, 48:06-48:07, 48:09, 48:11, 48:15-48:16, 48:18-48:20, 48:22, 55:35w, 81:01-81:04N |
| 34 | 145 bp, 430 bp | 1070 bp | 44, 49, 59, 61 | *40:13, 40:19, 44:18, 44:25, 44:50, 44:95, 49:01:01-49:01:02, 49:04-49:10, 54:12, 56:21, 59:01-59:05 |
| 356 | 120 bp, 210 bp | 800 bp | 5, 13, 15, 17, 22, 35, 45, 49, 50, 51, 5102, 5103, 52, 55, 56, 62, 63, 78 | *07:78, 07:84, 13:16, 13:31w, 15:04w, 15:16, 15:42, 15:67, 15:95, 15:137w, 40:95, 49:01:01, 49:02-49:10, 50:01:01-50:02, 50:04-50:09, 51:01:01-51:03, 51:05, 51:07:01-51:09:02, 51:11N-51:14, 51:16-51:24:03, 51:26-51:41N, 51:43-51:44N, 51:48-51:55, 51:57-51:58, 51:60, 51:61w, 51:63, 51:65-51:80, 51:82-51:95, 52:01:01-52:20, 54:20, 55:01:01-55:01:06, 55:03, 55:05, 55:09, 55:11, 55:15, 55:17, 55:21w, 55:24-55:25, 55:28-55:29, 55:31, 55:33, 55:36, 55:38, 55:40, 56:05:01-56:06, 56:21, 56:25, 58:08, 78:01-78:07 |
| 36 | 430 bp | 1070 bp | 5, 17, 27, 44, 51, 5102, 5103, 52, 53, 57, 58, 61 | *27:02, 27:30, 27:53, 27:57, 27:62, 27:65N, 40:13, 40:19, 44:06, 44:25, 44:50, 44:95, 51:01:01-51:24:03, 51:26-51:46, 51:48-51:53, 51:55-51:77, 51:79-51:95, 52:01:01-52:19, 53:01:01-53:02, 53:04-53:08:02, 53:10, 53:14-53:23, 57:01:01-57:11, 57:13-57:31, 58:01:01-58:02, 58:04-58:16, 58:18-58:28 |
| 37 | 145 bp | 1070 bp | 12, 21, 35, 40, 4005, 41, 45, 47, 50, 60, 61 | *15:46, 15:53, 15:106, 15:143, 18:48, 35:19, 35:47, 35:63, 40:01:01-40:11, 40:14:01-40:16, 40:18, 40:20, 40:22N-40:40, 40:42-40:45, 40:48-40:75, 40:77-40:92, 40:94-40:95, 40:97-40:99, 41:01-41:04, 41:05?, 41:06-41:12, 44:09, 44:46, 44:75, 44:90, 45:01-45:11, 47:02, 47:03w, 50:01:01-50:02, 50:04-50:05, 50:07-50:09 |
| 38 | 300 bp | 1070 bp | 7, 12, 13, 15, 17, 18, 21, 27, 2708, 35, 37, 38, 39, 3902, 40, 4005, 41, 44, 45, 47, 48, 49, 50, 52, 60, 61, 62, 70, 72, 76 | *07:54, 08:17, 08:38, 08:54, 13:01:01-13:04, 13:06, 13:08Q-13:23, 13:25-13:35, 13:37, 15:01:01:01-15:01:04, 15:01:06-15:01:16, 15:03:01-15:07, 15:12, 15:14, 15:19-15:20, 15:24-15:27:03, 15:30, 15:32-15:36, 15:38:01-15:40, 15:42-15:43, 15:45-15:50, 15:53-15:54, 15:56-15:58, 15:60-15:63, 15:65-15:66, 15:68-15:71, 15:73-15:75, 15:77-15:79N, 15:81-15:87, 15:91-15:92, 15:94N, 15:96-15:98, 15:101-15:107, 15:109-15:111N, 15:113, 15:116-15:118, 15:122-15:123, 15:125-15:129, 15:131-15:132, 15:135-15:138, 15:140-15:142, 15:145-15:147, 15:150-15:152, 15:154-15:160, 15:163-15:167, 15:169, 15:171-15:175, 15:178-15:179, 15:181N-15:185, 15:187-15:188, 15:190N, 18:12, 27:01-27:21, 27:24-27:65N, 35:10, 35:13, 35:16, 35:28, 35:63, 35:69, 35:80, 37:01:01-37:07, 37:09-37:22, 38:03-38:04, 39:02:01-39:02:02, 39:08, 39:13:01-39:13:02, 39:22-39:23, 39:49, 40:01:01-40:07, 40:09-40:16, 40:18-40:24, 40:26-40:40, 40:42-40:67, 40:70-40:99, 41:01-41:12, 42:11, 44:02:01:01-44:05:02, 44:07-44:11, 44:13-44:99, 45:01-45:11, 47:01:01:01-47:07, 48:01:01-48:05, 48:07-48:15, 48:17-48:22, 49:01:01-49:10, 50:01:01-50:02, 50:04-50:09, 52:01:01-52:20, 53:17, 55:18, 55:34, 55:40, 78:05-78:06 |
| 39 | 160 bp, 330 bp | 1070 bp | 22, 44, 45, 47, 54 | *44:02:01:01-44:02:13, 44:06, 44:08-44:09, 44:11-44:12, 44:16, 44:19N-44:24, 44:27, 44:33-44:34, 44:41, 44:44, 44:48-44:49, 44:52N-44:53, 44:55, 44:59, 44:63, 44:66-44:68, 44:71-44:74, 44:80, 44:83-44:84, 44:86-44:87, 44:89-44:91, 44:93, 44:95, 44:97, 44:99, 54:01-54:22, 83:01 |
| 40 | 180 bp, 210 bp | 1070 bp | 13, 15, 18, 35, 39, 40, 54, 55, 56, 59, 78 | *07:65, 13:06, 15:42, 15:86, 18:04, 35:42:02, 35:60, 39:17, 40:58, 45:08, 46:18, 54:01-54:02, 54:05N, 54:07-54:08N, 54:10, 54:12-54:13, 54:16-54:22, 55:01:01-55:03, 55:05, 55:07, 55:10-55:12, 55:15-55:16, 55:18-55:19, 55:21, 55:25-55:26, 55:29-55:31, 55:33-55:40, 56:05:01, 56:06, 56:10, 56:23, 59:01, 59:05, 78:01, 78:02:02-78:03, 78:07, C*15:02:04 |
| 41 | 180 bp | 1070 bp | 12, 15, 21, 22, 44, 45, 49, 50, 51, 56, 61, 62, 82 | *13:03, 15:73, 40:71, 44:10, 44:15, 44:18, 45:01, 45:04-45:07, 45:11, 46:11, 49:01:01-49:03, 49:06, 49:08-49:10, 50:01:01-50:02, 50:04-50:08, 51:15, 51:62, 54:03, 56:01:01-56:02, 56:04, 56:07-56:08, 56:13-56:14, 56:16-56:17, 56:20, 56:24-56:29, 59:04, 82:01-82:03, C*03:12, C*03:19 |
| 426,7 | 90 bp, 240 bp | 800 bp | 57 | *55:14, 57:01:01-57:31 |
| 436,12 | 90 bp | 1070 bp | 5, 13, 15, 17, 39, 55, 56, 58, 60, 61, 62, 71 | *13:11, 15:18:03, 15:73, 39:17, 40:48, 40:71, 51:62, 56:02, 56:04, 56:10, 58:01:01-58:02, 58:04-58:28, C*02:06w |
| 446 | 95 bp | 1070 bp | 8, 18, 22, 35, 37, 38, 39, 44, 51, 5102, 5103, 53, 78 | *07:65w, 08:32, 18:01:01-18:11, 18:13-18:15, 18:17N-18:36, 18:38-18:47, 18:49, 35:01:01-35:09:02, 35:11-35:12:02, 35:14:01-35:15, 35:17-35:18, 35:20:01-35:24:02, 35:27, 35:29-35:45, 35:48, 35:50-35:62, 35:64-35:68:02, 35:70-35:72, 35:74-35:75, 35:76w, 35:77-35:79, 35:81-35:99, 37:08, 38:06-38:07, 39:19:01-39:19:02, 44:06, 51:01:01-51:24:03, 51:26-51:46, 51:48-51:95, 53:01:01-53:16, 53:18-53:23, 56:06w, 78:01-78:04, 78:07 |
| 456,7 | 115 bp, 150 bp | 1070 bp | 15, 18,22, 27, 35, 39, 46, 55, 62, 72, 73, 75, 76 | *13:31, 15:01:01:01-15:01:04, 15:01:06-15:01:16, 15:04, 15:07-15:08, 15:11:01-15:12, 15:14-15:15, 15:19, 15:24, 15:26N-15:28, 15:30, 15:32, 15:34-15:35, 15:38:01-15:38:02, 15:43, 15:45-15:46, 15:50, 15:53-15:54, 15:56-15:58, 15:60, 15:63, 15:66, 15:68, 15:70-15:71, 15:73, 15:75-15:77, 15:79N, 15:81-15:82, 15:85, 15:87, 15:92, 15:94N, 15:96-15:97, 15:101-15:102, 15:104-15:105, 15:109-15:111N, 15:113, 15:117-15:118, 15:120, 15:122, 15:125-15:126, 15:128-15:129, 15:135, 15:137, 15:140, 15:142-15:149N, 15:152, 15:154, 15:157, 15:159-15:160, 15:163-15:167, 15:169, 15:171-15:172, 15:174-15:175, 15:178, 15:180-15:184, 15:187, 15:189-15:191, 18:19, 27:25, 35:14:01-35:14:02, 35:43-35:44, 35:62, 35:67, 35:79, 35:86, 39:18, 39:36, 46:01:01-46:02, 46:04-46:05, 46:07N, 46:09-46:10, 46:12, 46:14-46:17, 46:20, 46:22, 51:61, 54:06, 55:21, 56:03, 73:01, C*06:20 |
| 46 | 360 bp | 1070 bp | Bw412 |  |
| 47 | 350 bp | 1070 bp | Bw6 |  |
| 4814 | - | - |  | Negative Control |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-B low resolution SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-B low resolution typing.

In addition, wells number 5, 6, 10, 17, 20, 21, 30, 35 and 42 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification. In the presence of a specific amplification the intensity of the control band often decreases.

3The serological reactivity of all HLA-B alleles is not known. In this table we use the information in the HLA Dictionary 2004 on the www.ebi.ac.uk/imgt/hla web site, the information available at the www.worldmarrow.org web site and the expert-assigned serological grouping in Tissue Antigens (2009) 73:95-170.

4For several HLA-B alleles only partial nucleotide sequences are available, especially for the 1st exon. In these instances it is not known whether some of the primers of the HLA-B low resolution SSP set are completely matched with the target sequences or not. We assume that unknown sequences are conserved within allelic groups.

The B*08:26, B*08:50 and the B*42:07 alleles give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

The B*14:08 and the B*39:25N, B*39:30, B*39:32 to 39:34, 39:47 and 39:50 alleles give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

The B*18:07:02, B*18:29 and the B*35:32, B*35:37, B*35:53N, B*35:64, B*35:66, B*35:68:01-35:68:02 and B*35:99 alleles give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

The B*41:09 and the B*45:02 and B*45:03 alleles give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

The B*55:04, B*55:08, B*55:13, B*55:27 and the B*56:15, B*56:19N and B*56:22 give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

The B*55:23, B*55:32 and the B*56:18 give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

5Due to sharing of sequence motifs, non-HLA-B alleles will be amplified by a few primer mixes; primer mix 1 will amplify the C*02:23 allele, primer mix 3 will amplify the HLA-C*03:05, C*03:25 and C*03:27 alleles, primer mix 4 will amplify the C*01:30 allele, primer mix 6 will amplify the C*16:10 allele, the C*07:46 allele will be amplified by primer mix 8, primer mix 29 will amplify the C*15:25 allele, primer mix 40 will amplify the C*15:02:04 allele, primer mix 41 will amplify the C*03:12 and C*03:19 alleles, primer mix 43 will weakly amplify the C*02:06 allele and primer mix 45 will amplify the C*06:20 allele. Furthermore, the C*17:01 and C*17:02 alleles might be faintly amplified by primer mix 25.

6Specific PCR fragments shorter than 125 base pairs have a lower intensity and are less sharp than longer PCR bands.

7Primer mixes 1, 19, 25, 42 and 45 may give rise to a primer oligomer artifact.

8Primer mix 4 may yield less specific PCR product than the other HLA-B low resolution primer mixes in B*40, B*41, B*45, B*49 and B*50 alleles.

9Primer mix 5 yields notably less specific PCR product than the other HLA-B low resolution primer mixes.

10Primer mixes 7, 10 and 26 might give rise to non-specific amplification products.

11Primer 9 may yield less specific PCR product than the other HLA-B low resolution primer mixes. This primer mix may also give rise to non-specific amplification products, and may furthermore faintly amplify the B*57 and B*58 alleles.

12Primer mix 29, 32 and 43 might generate a false band of about 500 base pairs. This band should be disregarded when interpreting HLA-B low resolution typings.

13The Bw4-associated HLA-A specificities A23, A24, A2403, A25 and A32 are not amplified by the primer pair in primer mix 46.

14Primer mix 48 contains a negative control, which will amplify more than 95% of HLA amplicons as well as the amplicons generated by control primer pairs. PCR product sizes range from 75 to 200 base pairs. The PCR product generated by the control primer pair is 430 base pairs.

‘?’, nucleotide sequence information not available for the primer matching sequence.

‘w’, might be weakly amplified.

1The sequence of the B*07:01 allele has been shown to be in error. The sequence of the B*13:05 allele has been shown to be identical to B*13:04. The B*13:24 allele has been renamed B*13:22:02.  The sequence of the B*15:01:05 allele has been corrected and renamed B*15:120. The B*15:22 allele has been renamed B*35:43. The sequence of the B*15:41 allele has been shown to be identical to B*15:39. The B*15:59 allele has been renamed B*35:44. The B*9530 allele has been renamed B*15:27:02. The sequence of the B*18:16 allele has been shown to be identical to B*18:14. The sequence of the B*27:05:01 allele has been shown to be identical to B*27:05:02. The sequence of the B*27:22 allele has been shown to be identical to the corrected B*27:06 sequence. The B*35:73 allele has been renamed B*35:08:03. The sequence of the B*39:01:02 allele has been shown to be identical to B*39:01:01:01. The sequence of the B*39:21 allele has been shown to be identical to B*39:24. The sequence of the B*40:17 allele has been shown to be identical to B*40:16. The sequence of the B*40:41 allele has been shown to be identical to B*40:40. The sequence of the B*42:03 allele has never been assigned. The sequence of the B*44:01 allele has been shown to be identical to B*44:02:01:01. The sequence of the B*50:03 allele has been shown to be identical to B*50:02. The sequence of the B*51:25 allele has been shown to be identical to B*51:22. The B*51:47 allele has been renamed B*51:09:02. The sequence of the B*55:06 allele has been shown to be identical to B*55:04. The sequence of the B*58:03 allele has never been assigned.The B*79:01 allele has been renamed B*15:18.The B*9530 allele has been renamed B*15:27:02.

The B*08:26, B*08:50 and the B*42:07 alleles give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

The B*14:08 and the B*39:25N, B*39:30, B*39:32 to 39:34, 39:47 and 39:50 alleles give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

The B*18:07:02, B*18:29 and the B*35:32, B*35:37, B*35:53N, B*35:64, B*35:66, B*35:68:01-35:68:02 and B*35:99 alleles give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

The B*41:09 and the B*45:02 and B*45:03 alleles give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

The B*55:04, B*55:08, B*55:13, B*55:27 and the B*56:15, B*56:19N and B*56:22 give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

The B*55:23, B*55:32 and the B*56:18 give rise to identical amplification patterns with the HLA-B low resolution primer set. These alleles can be separated by the respective high resolution primer sets.

2The serological reactivity of all HLA-B alleles is not known. In this table we use the information in the HLA Dictionary 2004 on the www.ebi.ac.uk/imgt/hla web site, the information available at the www.worldmarrow.org web site and the expert-assigned serological grouping in Tissue Antigens (2009) 73:95-170.

‘ser’, serological HLA specificity.

‘w’, might be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.

Change in revision R01 compared to R00:

- The HLA-B*51:50 allele is amplified in primer mix 36.

Change in revision R02 compared to R01:

- The HLA-C*03:12 and 03:19 alleles are amplified in primer mix 41.