PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*08

Prod. No:	101.513-24/24u

101.513-04/04u

Lot No:    	51F

Expiry Date:    	2011-February-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for HLA-B*08 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*08 alleles | Other amplified HLA Class I alleles3 |
| --- | --- | --- | --- | --- |
| 1 | 215 bp | 800 bp | 080101-0805, 0807, 0808N, 0810, 0811, 0814, 0815, 0817-0819N, 0821-0824, 0826-0838 | 0704, 0719, 0725, 3587, 3709, 4102, 4104, 4201, 4202, 420501-4209 |
| 2 | 215 bp | 800 bp | 080101-0803, 0805-0816, 0818-0825, 0827-0838 |  |
| 3 | 245 bp | 1070 bp | 080101-080106, 0804-0814, 0816, 0818-0825, 0827-0838 | 0729, 9542, 3907?, 3912 |
| 4 | 255 bp | 1070 bp | 0802 | 4449 |
| 5 | 245 bp | 1070 bp | 0803, 0823 | 9542 |
| 6 | 205 bp | 800 bp | 0804, 0817, 0824 | 9542, 4449 |
| 76 | 215, 250 bp | 1070 bp | 0805, 0836 |  |
| 8 | 170 bp | 1070 bp | 0806, 0820 | 070501-0706, 0732, 0740, 0753, 1318, 1530, 1558, 1573, 9550, 3518, 3544, 3908, 3911, 3918, 3933, 3936, 4015, 4016, 4023, 4805, 4819, 5105, 5129, 5154, 5161, 5410, 5509, 5521, 5702, 5712 |
| 9 | 165 bp | 1070 bp | 0807, 0837 | 0704, 0719, 0725, 1551, 3538, 3709, 4104, 4209, 4417, 4451, 4509 |
| 10 | 175 bp | 800 bp | 0808N |  |
| 11 | 295 bp | 800 bp | 0809, 0827 | 4101, 4105-4107, 4204, 5520 |
| 12 | 385 bp | 1070 bp | 0810 |  |
| 135 | 90 bp | 1070 bp | 0811 |  |
| 14 | 290 bp | 1070 bp | 0812, 0816 | 410301-410302, 5315 |
| 15 | 215 bp | 1070 bp | 0813, 0825 | 0726, 0734, 0743, 0748, 1405, 1555, 1814, 1822, 2707, 2711, 2724, 2732-2734, 2743, 3505, 3516, 3517, 3522, 3530, 3531, 3551, 3558, 3572, 3589, 3903, 3914, 3924, 3929, 400201-4003, 4005, 4008, 4009, 4013, 4018, 4019, 4024, 4027, 4029, 4031, 4035, 4037, 4039, 4040, 4045, 4050, 4056-4058, 4071, 4078, 4080, 4082, 4085, 4089, 4090, 4091, 4094, 4454, 480101-480102, 4804, 4806, 4807, 4809-4816, 4818, 5314, 5504, 5818, 8101-8104N, Cw*0305, Cw*0325, Cw*0327, Cw*0808 |
| 165 | 110 bp | 800 bp | 0813, 0825 | 5315 |
| 175 | 95 bp | 1070 bp | 0814 | 0728, 2732, 4454 |
| 18 | 425 bp | 800 bp | 0815 | 0713, 0715, 3927, 4073, 6702, 7301 |
| 19 | 415 bp | 800 bp | 0816 | 0713, 0715, 6702 |
| 205,7 | 140, 205 bp | 1070 bp | 0817, 0822, 0838 | 9542, 4449 |
| 21 | 465 bp | 1070 bp | 0818 | 7301 |
| 225 | 130 bp | 800 bp | 0819N |  |
| 235,8 | 90, 235 bp | 800 bp | 0806, 0817, 0821, 0825 | 1557, 9535, 3527, 3556, 5315, 5512, 7806 |
| 24 | 215 bp | 1070 bp | 0826 | 0708, 0732, 0738, 1508, 1529, 1556, 350101-3519, 3521-3525, 3527, 3527, 3529-3549, 3551-3562, 3564-3571, 3574, 3575, 3577, 3579-3581, 3583, 3586-3594, 3806, 3807, 4406, 4806, 510101-5106, 5108-5121, 5123-512402, 5126-5132, 5134-5146, 5148-5163, 520601-520602, 530101-5308, 5310-5316, 5901-5904, 7801-780202, 7804 |
| 25 | 160 bp | 1070 bp | 0828, 0835, 0837 | 1551, 4209, 4417, 4509 |
| 264 | 385 bp | 1070 bp | 0829 |  |
| 275,9 | 105, 140 bp | 1070 bp | 0822, 0830N |  |
| 285 | 85 bp | 1070 bp | 0831 |  |
| 2910 | 150, 250 bp | 1070 bp | 0832, 0836 |  |
| 30 | 285 bp | 1070 bp | 0833 |  |
| 31 | 375 bp | 1070 bp | 0834 |  |
| 32 | 230 bp | 1070 bp | 0835, 0837 | 4209, 5315 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-B*08 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-B*08 subtyping.

In addition, wells number 2, 6, 10, 11, 16, 18, 22 and 23 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3Due to the sharing of sequence motifs between HLA-B alleles some non-HLA-B*08 alleles will be amplified by primer mixes 1, 3, 4 to 6, 8, 9, 11, 14 to 21, 23 to 25 and 32. In addition, the Cw*0305, Cw*0325, Cw*0327 and Cw*0808 alleles will be amplified by the primer mix 15.

4Primer mix 26 may have a tendency of giving rise to nonspecific amplifications.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6Primer mix 7: Specific PCR fragment of 215 bp in the B*0805 allele. Specific PCR fragment of 250 bp in the B*0836 alleles.

7Primer mix 20: Specific PCR fragment of 140 bp in the B*0822 allele. Specific PCR fragment of 205 bp in B*0817 and B*0838 and in the B*9542 and B*4449 alleles.

8Primer mix 23: Specific PCR fragment of 90 bp in the B*0821 and B* 0825 and B*5315 alleles. Specific PCR fragment of 235 bp in the B*0806, 0817 and in the B*1557, B*9535, B*3527, B*3556, B*5512 and B*7806 alleles.

Specific PCR fragment of 90 bp in the B*0821 and B* 0825 and B*5315 alleles. Specific PCR fragment of 235 bp in the B*0806, 0817 and the B*1557, 9535, 7806 alleles.

9Primer mix 27: Specific PCR fragment of 105 bp in the B*0830N allele. Specific PCR fragment of 140 bp in the B*0822 allele.

10Primer mix 29: Specific PCR fragment of 150 bp in the B*0832 allele. Specific fragment of 250 bp in the B*0836 allele.

1Primer mix 7: Specific PCR fragment of 215 bp in the B*0805 allele. Specific PCR fragment of 250 bp in the B*0836 alleles.

Primer mix 20: Specific PCR fragment of 140 bp in the B*0822 allele. Specific PCR fragment of 205 bp in B*0817 and B*0838 and in the B*9542 and B*4449 alleles.

Primer mix 23: Specific PCR fragment of 90 bp in the B*0821 and B* 0825 and B*5315 alleles. Specific PCR fragment of 235 bp in the B*0806, 0817 and in the B*1557, B*9535, B*3527, B*3556, B*5512 and B*7806 alleles.

Primer mix 27: Specific PCR fragment of 105 bp in the B*0830N allele. Specific PCR fragment of 140 bp in the B*0822 allele.

Primer mix 29: Specific PCR fragment of 150 bp in the B*0832 allele. Specific fragment of 250 bp in the B*0836 allele.