PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*18

Prod. No:	101.519-12/12u

Lot No:    	87F

Expiry Date:    	2011-June-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 24 primer mixes used for HLA-B*18 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*18 alleles | Other amplified HLA Class I alleles3 |
| --- | --- | --- | --- | --- |
| 1 | 170 bp | 800 bp | 180101-1802, 1804-1808, 1810-1815, 1817N-1828, 1830-1833 |  |
| 24 | 260 bp | 800 bp | 180101-180103, 1803-1809, 1812, 1813, 1815, 1817N-1820, 1823N-1826, 1828-1833 | 140601-140602, 1408, 1537, 1538, 3932, 3943, 3948, 4051, 5106, 5145, 5162 |
| 3 | 260 bp | 800 bp | 1802 | 2728 |
| 45, 7 | 100 bp | 800 bp | 1803, 1828 |  |
| 57 | 140 bp | 1070 bp | 1804, 1824 |  |
| 67 | 130 bp | 1070 bp | 1805 |  |
| 7 | 150 bp | 1070 bp | 1807 |  |
| 8 | 190 bp | 1070 bp | 1810, 1821 | 070201-0704, 0707-0713, 0715, 0716, 071801-071802, 0721-0723, 0725-0727, 0729, 0730, 0733, 0735-0739, 0741, 0742, 0744-0752, 0754-0759, 0761-0768, 0770-0772, 0775, 0776, 1540, 1547, 1549, 1552, 9514, 9517, 9524, 9538, 2734, 2741, 3515, 3533, 3566, 3586, 3707, 4003, 4018, 4020, 4024, 4031-4033, 4044, 4052, 4059, 4606, 4808, 5713, Cw*0206, Cw*0223 |
| 95 | 255 bp | 1070 bp | 1808, 1827 |  |
| 106,7 | 85 bp | 800 bp | 1823N |  |
| 115,7,8 | 125, 630 bp | 1070 bp | 1809-1811, 1821 | 350202, 352002 |
| 127 | 140 bp | 1070 bp | 1812 |  |
| 137 | 85 bp | 1070 bp | 1813, 1819, 1830 | 1403, 1538, 5129, 5161, A*6604weakly |
| 149 | 170, 260 bp | 1070 bp | 1804, 1814, 1825 | 1405, 350202, 352002, 5164 |
| 157 | 100 bp | 1070 bp | 1815, 1819, 1830, 1831 | 1401-1410, 1537, 1538, 3521, 4028, 4051, 510101-510109, 5103, 5104, 5106, 5107, 5111N-5114, 5116-5118, 5121, 5122, 512401-512402, 5126-5130, 5132, 5133, 5135, 5137-5139, 5141N, 5143, 5145, 5146, 5148-5152, 5155-5158, 5160-5165, 520101-5202, 5204-5209, 5212-5214, 5306, 560501-5606, 5621, 5808, 7801-7803, 7805, 7806 |
| 167,10 | 95, 365 bp | 1070 bp | 1817N, 1819 | 152703, 351401, 3562, 3936, 5521, Cw*0109, Cw*0722 |
| 177,11 | 100, 255 bp | 1070 bp | 1818, 1831 |  |
| 186,7,12 | 85, 125, 150 bp | 1070 bp | 1815, 1821weakly, 1829, 1830weakly, 1832 | 0709weakly, 0711weakly, 1503, 1516, 1518, 1523, 1529, 1539, 1540, 1547weakly, 1549weakly, 1561, 1562, 1564, 1565weakly, 1567, 1569, 1571, 1572, 1574, 1580, 1593, 1595, 1598, 9503, 9508, 9515, 9519, 9527, 9531, 9532, 9534, 9538, 9553, 9558, 3511, 3521, 3550, 3558, 3591, 3599weakly, 4603weakly, 4608, 4614, 4903, 4904, 5137, 5145, 5306, 5308, 5402, 5514, 5516, 5713weakly, 5806, 5819 Cw*1509, Cw*1519, Cw*1520 |
| 197 | 105 bp | 1070 bp | 1806 |  |
| 205 | 290 bp | 1070 bp | 1820 | 0714, 0717, 0728, 0814, 0828, 1310, 1401-1410, 1502, 1506, 1513, 15170101-151702, 1521, 1525, 1531, 1536, 1544, 1555, 1577, 1588, 1589, 9506, 9512, 9521, 9528, 9537, 9539, 9544, 9556, 2701-270402, 270502-2706, 2708-2710, 2712-2719, 2721, 2723, 2725, 2726, 2728-2732, 2735-2740, 2742, 2744-2746, 2750, 370101-3706, 3708, 3710, 3711, 3713, 3714, 3917, 4009, 4042, 4060, 4089, 44020101-4409, 4411-4413, 4415, 4416, 4418-4430, 4432-4442, 4444, 4446-4450, 4452N-4461N, 4463-4467, 4469, 4501-4508, 47010101-4705, 4817, 490101-4903, 4905, 5001, 5002, 5004, 5142, 5307, 5415, 5704, 5705, 8301 |
| 21 | 215 bp | 1070 bp | 180101-1809, 1812-1815, 1817N-1819, 1822-1833 | 1315, 1537, 1538, 3521, 3524, 3581, 3932, 3943, 3948, 4028, 4051, 510101-510109, 5103, 5104, 5106-510902, 5111N-5114, 5116, 5119-5122, 512401-512402, 5126-5133, 5135, 5137-5139, 5141N, 5143-5146, 5148-5153, 5155-5158, 5160-5165, 520101-5202, 5204-5210, 5212-5214, 5302, 5306, 560501-5606, 5621, 5714, 5808, 5809, 7801-7803, 7805, 7806 |
| 2213 | 150, 270 bp | 800 bp | 1822, 1833 | 1410, 3521, 3524, 3581, 4028, 5104, 5146, 5156, 5302, 5306, 5714, 5809 |
| 237 | 100 bp | 800 bp | 1821 | 0709, 0711, 1533, 9507, 9516, 9541, 2741, 3564, 4003, 4020, 4052, 4059, 4606, 5713, Cw*1509, Cw*1519, Cw*1520 |
| 24 | 190 bp | 1070 bp | 1826 | 0734, 080101-0806, 0808N-0810, 0812, 0813, 0815-0820, 0822-0824, 0826, 0827, 0829-0836, 0838, 1306, 1542, 1583, 1586, 3560, 3587, 3712, 380101-3807, 3809-3819, 39010101-39010102L, 390103-390602, 3908-3914, 3916, 3918-3920, 3922-3924, 3926-3928, 3930, 3931, 3934-3937, 3939, 3941, 3942, 3944-3946, 3948, 4039, 4051, 4101-410302, 4105-4108, 4201, 4202, 4204-4208, 4210, 4618, 5121, 5136, 5401, 5402, 5404, 5405N, 5407, 5408N, 5410-5413, 5417, 550101-5505, 5507, 5510-5513, 5515-5521, 5525, 5526, 5528-5534, 5610, 5612, 5623, 5820, 5901-5903, 670101-6702 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-B*18 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-B*18 subtyping. In addition, wells number 2, 3, 4, 10, 22 and 23 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification. In the presence of a specific amplification the intensity of the control band often decreases.

3Due to the sharing of sequence motifs between HLA-B alleles non-HLA-B*18 alleles will be amplified by primer mixes 2, 3, 8, 11, 13 to 16, 18 and 20 to 24. In addition, the A*6604 allele might be weakly amplified by primer mix 13, the Cw*0206 and Cw*0223 will be amplified by primer mix 8, Cw*0109 and Cw*0722 will be amplified by primer mix 16 and Cw*1509, Cw*1519 and Cw*1520 alleles will be amplified by primer mixes 18 and 23.

4The B*1401 to 1404, 1407N and 1409 alleles might be faintly amplified by primer mix 2.

5Primer mixes 4, 9, 11 and 20 have a tendency of giving rise to non-specific amplifications.

6Primer mix 18 may rise to primer oligomer formation.

7Short specific PCR fragments are less intense and not as sharp as longer specific bands.

8Primer mix 11: Specific PCR fragment of 125 bp in the B*1809 allele. Specific PCR fragment of 630 bp in the B*1810, 1811, 1821 and the B*350202 and 352002 alleles.

9Primer mix 14: Specific PCR fragment of 170 bp in the B*1804, B*1825 and the B*350202 and 352002 alleles. Specific PCR fragment of 260 bp in the B*1814 and the B*1405 and 5164 alleles.

10Primer mix 16: Specific PCR fragment of 95 bp in the B*1819 and the B*152703, 351401, 3562, 3936, 5521, Cw*0109 and Cw*0722 alleles. Specific PCR fragment of 365 bp in the B*1817N allele.

11Primer mix 17: Specific PCR fragment of 100 bp in the B*1831 allele. Specific PCR fragment of 255 bp in the B*1818 allele.

12Primer mix 18: Specific PCR fragment of 85 bp in the B*1829 and B*1571, 3550, 4614, 4903, 5402 and 5516 alleles. Specific PCR fragment of 125 bp in the B*1832 and B*3591 alleles. Specific PCR fragment of 150 bp in the B*1815, 1821weakly, 1830weakly and the B*0709weakly, 0711weakly, 1503, 1516, 1518, 1523, 1529, 1539, 1540, 1547weakly, 1549weakly, 1561, 1562, 1564, 1565weakly, 1567, 1569, 1572, 1574, 1580, 1593, 1595, 1598, 9503, 9508, 9515, 9519, 9527, 9531, 9532, 9534, 9538, 9553, 9558, 3511, 3521, 3558, 3599weakly, 4603weakly, 4608, 4904, 5137, 5145, 5306, 5308, 5514, 5713weakly, 5806, 5819, Cw*1509, Cw*1519 and Cw*1520 alleles.

13Primer mix 22: Specific PCR fragment of 150 bp in the B*1833 allele. Specific PCR fragment of 270 bp in the B*1822 and in B*1410, 3521, 3524, 2581, 4028, 5104. 5146, 5156, 5302, 5306, 5714 and 5809 alleles.

1The sequence of the B*1816 allele has been found to be identical to B*1814.

2Primer mix 11: Specific PCR fragment of 125 bp in the B*1809 allele. Specific PCR fragment of 630 bp in the B*1810, 1811, 1821 and the B*350202 and 352002 alleles.

Primer mix 14: Specific PCR fragment of 170 bp in the B*1804, B*1825 and the B*350202 and 352002 alleles. Specific PCR fragment of 260 bp in the B*1814 and the B*1405 and 5164 alleles.

Primer mix 16: Specific PCR fragment of 95 bp in the B*1819 and the B*152703, 351401, 3562, 3936, 5521, Cw*0109 and Cw*0722 alleles. Specific PCR fragment of 365 bp in the B*1817N allele.

Primer mix 17: Specific PCR fragment of 100 bp in the B*1831 allele. Specific PCR fragment of 255 bp in the B*1818 allele.

Primer mix 18: Specific PCR fragment of 85 bp in the B*1829 and B*1571, 3550, 4614, 4903, 5402 and 5516 alleles. Specific PCR fragment of 125 bp in the B*1832 and B*3591 alleles. Specific PCR fragment of 150 bp in the B*1815, 1821weakly, 1830weakly and the B*0709weakly, 0711weakly, 1503, 1516, 1518, 1523, 1529, 1539, 1540, 1547weakly, 1549weakly, 1561, 1562, 1564, 1565weakly, 1567, 1569, 1572, 1574, 1580, 1593, 1595, 1598, 9503, 9508, 9515, 9519, 9527, 9531, 9532, 9534, 9538, 9553, 9558, 3511, 3521, 3558, 3599weakly, 4603weakly, 4608, 4904, 5137, 5145, 5306, 5308, 5514, 5713weakly, 5806, 5819, Cw*1509, Cw*1519 and Cw*1520 alleles.

Primer mix 22: Specific PCR fragment of 150 bp in the B*1833 allele. Specific PCR fragment of 270 bp in the B*1822 and in B*1410, 3521, 3524, 2581, 4028, 5104. 5146, 5156, 5302, 5306, 5714 and 5809 alleles.

‘w’, might be weakly amplified.

Change in revision R01 compared to R00:

Primer mix 10 may give rise to primer oligomer formation.