PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*18

Prod. No:	101.519-12/12u

Lot No:    	33K

Expiry Date:    	2012-August-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for HLA-B*18 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*18 alleles3 | Other amplified HLA Class I alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 170 bp | 800 bp | *18:01:01-18:02, 18:04-18:08, 18:10-18:15, 18:17N-18:28, 18:30-18:49 |  |
| 2 | 260 bp | 800 bp | *18:01:01-18:01:08, 18:03-18:09, 18:12-18:13, 18:15, 18:17N-18:20, 18:23N-18:26, 18:28-18:34, 18:36-18:38, 18:40-18:43, 18:45-18:49 | *14:06:01-14:06:02, 14:08, 15:37-15:38:02, 15:185, 39:32, 39:43, 39:48, 40:51, 51:06, 51:45, 51:62 |
| 3 | 260 bp | 800 bp | *18:02 | *27:28, 27:62 |
| 45 | 100 bp | 800 bp | *18:03 |  |
| 55 | 140 bp | 1070 bp | *18:04, 18:24 |  |
| 65 | 130 bp | 1070 bp | *18:05 |  |
| 75,8 | 90 bp, 150 bp | 1070 bp | *18:07:01-18:07:02, 18:41 |  |
| 8 | 190 bp | 1070 bp | *18:10, 18:21, 18:35 | *07:02:01-07:04, 07:07-07:13, 07:15-07:16, 07:18:01-07:18:02, 07:21-07:23, 07:25-07:27, 07:29-07:30, 07:33, 07:35-07:39, 07:41-07:42, 07:44-07:52, 07:54-07:59, 07:61-07:68, 07:70-07:77, 07:79, 07:81-07:89, 07:91-07:95, 07:98-07:99, 13:26, 13:35, 15:40, 15:47, 15:49, 15:52, 15:114, 15:117, 15:124, 15:138, 27:34, 27:41, 35:15, 35:33, 35:66, 35:86, 37:07, 40:03, 40:18, 40:20, 40:24, 40:31-40:33, 40:44, 40:52, 40:59, 40:98, 46:06, 48:08, 57:13, 57:25, C*02:06, C*02:23, C*02:36 |
| 9 | 255 bp | 1070 bp | *18:08, 18:27 |  |
| 105 | 85 bp | 800 bp | *18:23N |  |
| 115,9 | 125 bp, 610 bp, 635 bp | 1070 bp | *18:09-18:11, 18:21, 18:35-18:36 | *35:02:02, 35:20:02 |
| 125,10 | 90 bp, 140 bp | 1070 bp | *18:12, 18:41 |  |
| 135 | 85 bp | 1070 bp | *18:13, 18:19, 18:30 | *14:03, 15:38:01-15:38:02, 51:29, 51:61, 51:82, A*66:04w, C*01:30 |
| 1411 | 170 bp, 260 bp | 1070 bp | *18:04, 18:14, 18:25 | *14:05, 14:13, 35:02:02, 35:20:02, 51:64 |
| 155,12 | 100 bp, 265 bp | 1070 bp | *18:15, 18:19, 18:30-18:31, 18:44 | *14:01-14:18, 15:37-15:38:02, 35:21, 35:96, 40:28, 40:51, 49:09, 51:01:01-51:01:17, 51:03-51:04, 51:06-51:07:02, 51:11N-51:14, 51:16-51:18, 51:21-51:22, 51:24:01-51:24:03, 51:26-51:30, 51:32-51:33, 51:35, 51:37-51:39, 51:41N, 51:43, 51:45-51:46, 51:48-51:52, 51:55-51:58, 51:60-51:72, 51:74-51:80, 51:82-51:92, 51:94-51:95, 52:01:01-52:02, 52:04-52:09, 52:12-52:18, 52:20, 53:06, 56:05:01-56:06, 56:21, 58:08, 78:01-78:03, 78:05-78:07, C*01:30 |
| 165,13 | 95 bp, 360 bp | 1070 bp | *18:17N, 18:19 | *13:31, 15:27:03, 15:38:02, 35:14:01, 35:62, 39:36, 46:01:03, 55:21, C*01:09, C*07:22 |
| 175,14 | 110 bp, 255 bp | 1070 bp | *18:18, 18:31, 18:47 |  |
| 185,15 | 85 bp, 555 bp, 580 bp | 1070 bp | *18:15, 18:21w, 18:29, 18:30w, 18:32 | *15:71, 15:175, 35:50, 37:22, 41:12, 46:14, 49:03, 54:02, 55:16 |
| 195,16 | 105 bp, 405 bp | 1070 bp | *18:06, 18:39 |  |
| 206 | 290 bp | 1070 bp | *18:20 | *07:14, 07:17, 07:28, 07:96, 08:14, 08:28, 08:49, 13:10, 14:01-14:12, 14:14-14:18, 15:02:01-15:02:04, 15:06, 15:13, 15:17:01:01-15:17:02, 15:21, 15:25:01-15:25:02, 15:31, 15:36, 15:44, 15:55, 15:77, 15:88-15:89, 15:106, 15:112, 15:121, 15:128, 15:137, 15:139, 15:144, 15:156, 15:162, 15:168, 15:170, 15:177, 27:01-27:06, 27:08-27:10, 27:12-27:19, 27:21, 27:23, 27:25-27:26, 27:28-27:32, 27:35-27:40, 27:42, 27:44-27:65N, 37:01:01-37:06, 37:08, 37:10-37:11, 37:13-37:22, 38:22, 39:17, 40:09, 40:42, 40:60, 40:89, 44:02:01:01-44:09, 44:11-44:13, 44:15-44:16, 44:18-44:30, 44:32-44:42, 44:44, 44:46-44:50, 44:52N-44:61N, 44:63-44:76, 44:78-44:81, 44:83-44:99, 45:01-45:08, 45:10-45:11, 47:01:01:01-47:07, 48:17, 49:01:01-49:03, 49:05-49:10, 50:01:01-50:02, 50:04-50:09, 51:42, 51:85, 53:07, 54:15, 57:04-57:05, 83:01 |
| 21 | 215 bp | 1070 bp | *18:01:01-18:09, 18:12-18:15, 18:17N-18:19, 18:22-18:34, 18:36-18:49 | *13:15, 14:13, 15:37-15:38:02, 15:185, 35:21, 35:24:01-35:24:02, 35:81, 35:96, 39:32, 39:43, 39:48, 40:28, 40:51, 51:01:01-51:01:17, 51:03-51:04, 51:06-51:09:02, 51:11N-51:14, 51:16, 51:19-51:22, 51:24:01-51:24:03, 51:26-51:33, 51:35, 51:37-51:39, 51:41N, 51:43-51:46, 51:48-51:53, 51:55-51:58, 51:60-51:80, 51:82-51:84, 51:86-51:92, 51:94-51:95, 52:01:01-52:02, 52:04-52:10, 52:12-52:20, 53:02, 53:06, 56:05:01-56:06, 56:21, 57:14, 58:08-58:09, 78:01-78:03, 78:05-78:07 |
| 2217 | 150 bp, 270 bp | 800 bp | *18:22, 18:33 | *14:10, 35:21, 35:24:01-35:24:02, 35:81, 35:96, 37:04:01-37:04:02, 40:28, 51:04, 51:46, 51:56, 53:02, 53:06, 57:14, 58:09 |
| 23 | 515 bp | 1070 bp | *18:21, 18:40 |  |
| 24 | 190 bp | 1070 bp | *18:26 | *07:34, 08:01:01-08:06, 08:08N-08:10, 08:12:01-08:13, 08:15-08:20, 08:22-08:24, 08:26-08:27, 08:29-08:36, 08:38-08:39, 08:41-08:48, 08:50-08:61, 13:06, 14:13, 15:42, 15:83, 15:86, 15:188, 35:60, 35:87, 37:12, 38:01:01, 38:01:03-38:07, 38:09-38:21, 39:01:01:01-39:01:01:02L, 39:01:03-39:06:02, 39:08-39:14, 39:16, 39:18-39:20, 39:22-39:24, 39:26-39:28, 39:30-39:31, 39:34-39:37, 39:39, 39:41-39:42, 39:44-39:46, 39:48, 39:51-39:54, 39:56-39:57, 40:39, 40:51, 41:01-41:03:02, 41:05-41:09, 41:11-41:12, 42:01:01-42:02, 42:04-42:08, 42:10-42:13, 46:18, 51:21, 51:36, 54:01-54:02, 54:04-54:05N, 54:07-54:08N, 54:10-54:13, 54:17-54:22, 55:01:01-55:05, 55:07, 55:10-55:13, 55:15-55:21, 55:25-55:26, 55:28-55:40, 56:10, 56:12, 56:23, 58:20, 59:01-59:03, 59:05, 67:01:01-67:02, 78:07, C*15:24 |
| 255,18 | 75 bp, 185 bp | 1070 bp | *18:35, 18:48 | *07:68, 15:138, 35:66, 40:77, 40:87, 48:12, 48:14 |
| 26 | 180 bp | 1070 bp | *18:04, 18:25, 18:43 | *35:02:02, 35:20:02 |
| 275,19 | 85 bp, 140 bp | 800 bp | *18:37, 18:46 |  |
| 285,20 | 100 bp, 175 bp | 800 bp | *18:38, 18:45 |  |
| 295 | 90 bp | 1070 bp | *18:42 |  |
| 305 | 145 bp | 1070 bp | *18:34 |  |
| 315 | 135 bp | 1070 bp | *18:49 | *35:27, 35:56, 37:05, 78:06 |
| 325,7 | 100 bp | 1070 bp | *18:28 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-B*18 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-B*18 subtyping.

In addition, wells number 2 to 4, 10, 22, 27 and 28 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3The B*18:18 and 18:47 alleles may can be distinguished by the different sizes of the specific PCR products generated by primer mix 17. The B*18:37 and 18:46 alleles may can be distinguished by the different sizes of the specific PCR products generated by primer mix 27. The B*18:38 and 18:45 alleles may can be distinguished by the different sizes of the specific PCR products generated by primer mix 28.

4Due to the sharing of sequence motifs between HLA-B alleles non-HLA-B*18 alleles will be amplified by primer mixes 2, 3, 8, 11, 13 to 16, 18,  20 to 22, 24 to 26 and 31. In addition, the A*66:04 allele will be weakly amplified by primer mix 13, C*02:06 C*02:23 and C*02:36 will be amplified by primer mix 8, C*01:30 will be amplified by primer mixes 13 and 15, C*01:09 and C*07:22 will be amplified by primer mix 16 and the C*15:24 allele will be amplified by primer mix 24

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6Primer mix 20 may have a tendency of giving rise to non-specific amplifications.

7Primer mix 32 may give rise to primer oligomer formation.

8Primer mix 7: Specific PCR fragment of 90 bp in the B*18:41 allele. Specific PCR fragment of 150 bp in the B*18:07:01-18:07:02 alleles.

9Primer mix 11: Specific PCR fragment of 125 bp in the B*18:09 allele. Specific PCR fragment of 610 bp in the B*18:36 allele. Specific PCR fragment of 635 bp in the B*18:10-18:11, 18:21 and 18:35 alleles. Specific PCR fragment of 610 and 635 bp in the B*35:02:02 and 35:20:02 alleles.

10Primer mix 12: Specific PCR fragment of 90 bp in the B* 18:41 allele. Specific PCR fragment of 140 bp in the B*18:12 allele.

11Primer mix 14: Specific PCR fragment of 170 bp in the B*18:04 and 18:25 and in the B*35:02:02 and 35:20:02 alleles. Specific PCR fragment of 260 bp in the B*18:14 and in the B*14:05, 14:13 and 51:64 alleles.

12Primer mix 15: Specific PCR fragment of 100 bp in the B*18:15, 18:19, 18:30 and 18:31 and in the B*14:05-14:06:02, 14:08, 14:10, 14:13, 15:37-15:38:02, 35:21, 35:96, 40:28, 40:51, 49:09, 51:01:01-51:01:17, 51:03-51:04, 51:06-51:07:02, 51:11N-51:14, 51:16-51:18, 51:21-51:22, 51:24:01-51:24:03, 51:26-51:30, 51:32-51:33, 51:35, 51:37-51:39, 51:41N, 51:43, 51:45-51:46, 51:48-51:52, 51:55-51:58, 51:60-51:72, 51:74-51:80, 51:82-51:92, 51:94-51:95, 52:01:01-52:02, 52:04-52:09, 52:12-52:18, 52:20, 53:06, 56:05:01-56:06, 56:21, 58:08, 78:01-78:03 and  78:05-78:07 and in the C*01:30 alleles. Specific PCR fragment of 265 bp in the B*18:44 and in the C*01:30 alleles. Specific PCR fragments of 100 and 265 bp in the B*14:01-14:04, 14:07N, 14:09, 14:11-14:12 and 14:14-14:18 alleles. Both specific fragments may not always be visible.

13Primer mix 16: Specific PCR fragment of 95 bp in the B*18:19 and in the B*13:31, 15:27:03, 15:38:02, 35:14:01, 35:62, 39:36, 46:01:03 and 55:21 and in the C*01:09 and C*07:22 alleles. Specific PCR fragment of 360 bp in the B*18:17N allele.

14Primer mix 17: Specific PCR fragment of 110 bp in the B*18:31 and 18:47 alleles. Specific PCR fragment of 255 bp in the B*18:18 allele.

15Primer mix 18: Specific PCR fragment of 85 bp in the B*18:29 and in the B*15:71, 15:175, 35:50, 37:22, 41:12, 46:14, 49:03, 54:02 and 55:16 alleles. Specific PCR fragment of 555 bp in the B*18:32 allele. Specific PCR fragment of 580 bp in the B*18:15, 18:21w and 18:30w alleles.

16Primer mix 19: Specific PCR fragment of 105 bp in the B*18:06 allele. Specific PCR fragment of 405 bp in the B*18:39 allele.

17Primer mix 22: Specific PCR fragment of 150 bp in the B*18:33 allele. Specific PCR fragment of 270 bp in the B*18:22 and in the B*14:10 and in the B*35:21, 35:24:01-35:24:02, 35:81, 35:96, 37:04:01-37:04:02, 40:28, 51:04, 51:46, 51:56, 53:02, 53:06, 57:14 and 58:09 alleles.

18Primer mix 25: Specific PCR fragment of 75 bp in the B*18:48 allele. Specific PCR fragment of 185 bp in the B*18:35 and in the B*07:68, 15:138, 35:66, 40:77, 40:87, 48:12 and 48:14 alleles.

19Primer mix 27: Specific PCR fragment of 85 bp in the B*18:37 allele. Specific PCR fragment of 140 bp in the B*18:46 allele.

20Primer mix 28: Specific PCR fragment of 100 bp in the B*18:45 allele. Specific PCR fragment of 175 bp in the B*18:38 allele.

‘w’, might be weakly amplified.

1The sequence of the B*18:16 allele has been found to be identical to B*18:14.

The B*18:18 and 18:47 alleles may can be distinguished by the different sizes of the specific PCR products generated by primer mix 17.

The B*18:37 and 18:46 alleles may can be distinguished by the different sizes of the specific PCR products generated by primer mix 27.

The B*18:38 and 18:45 alleles may can be distinguished by the different sizes of the specific PCR products generated by primer mix 28.

2Primer mix 7: Specific PCR fragment of 90 bp in the B*18:41 allele. Specific PCR fragment of 150 bp in the B*18:07:01-18:07:02 alleles.

Primer mix 11: Specific PCR fragment of 125 bp in the B*18:09 allele. Specific PCR fragment of 610 bp in the B*18:36 allele. Specific PCR fragment of 635 bp in the B*18:10-18:11, 18:21 and 18:35 alleles. Specific PCR fragment of 610 and 635 bp in the B*35:02:02 and 35:20:02 alleles.

Primer mix 12: Specific PCR fragment of 90 bp in the B* 18:41 allele. Specific PCR fragment of 140 bp in the B*18:12 allele.

Primer mix 14: Specific PCR fragment of 170 bp in the B*18:04 and 18:25 and in the B*35:02:02 and 35:20:02 alleles. Specific PCR fragment of 260 bp in the B*18:14 and in the B*14:05, 14:13 and 51:64 alleles.

Primer mix 15: Specific PCR fragment of 100 bp in the B*18:15, 18:19, 18:30 and 18:31 and in the B*14:05-14:06:02, 14:08, 14:10, 14:13, 15:37-15:38:02, 35:21, 35:96, 40:28, 40:51, 49:09, 51:01:01-51:01:17, 51:03-51:04, 51:06-51:07:02, 51:11N-51:14, 51:16-51:18, 51:21-51:22, 51:24:01-51:24:03, 51:26-51:30, 51:32-51:33, 51:35, 51:37-51:39, 51:41N, 51:43, 51:45-51:46, 51:48-51:52, 51:55-51:58, 51:60-51:72, 51:74-51:80, 51:82-51:92, 51:94-51:95, 52:01:01-52:02, 52:04-52:09, 52:12-52:18, 52:20, 53:06, 56:05:01-56:06, 56:21, 58:08, 78:01-78:03 and  78:05-78:07 and in the C*01:30 alleles. Specific PCR fragment of 265 bp in the B*18:44 and in the C*01:30 alleles. Specific PCR fragments of 100 and 265 bp in the B*14:01-14:04, 14:07N, 14:09, 14:11-14:12 and 14:14-14:18 alleles. Both specific fragments may not always be visible.

Primer mix 16: Specific PCR fragment of 95 bp in the B*18:19 and in the B*13:31, 15:27:03, 15:38:02, 35:14:01, 35:62, 39:36, 46:01:03 and 55:21 and in the C*01:09 and C*07:22 alleles. Specific PCR fragment of 360 bp in the B*18:17N allele.

Primer mix 17: Specific PCR fragment of 110 bp in the B*18:31 and 18:47 alleles. Specific PCR fragment of 255 bp in the B*18:18 allele.

Primer mix 18: Specific PCR fragment of 85 bp in the B*18:29 and in the B*15:71, 15:175, 35:50, 37:22, 41:12, 46:14, 49:03, 54:02 and 55:16 alleles. Specific PCR fragment of 555 bp in the B*18:32 allele. Specific PCR fragment of 580 bp in the B*18:15, 18:21w and 18:30w alleles.

Primer mix 19: Specific PCR fragment of 105 bp in the B*18:06 allele. Specific PCR fragment of 405 bp in the B*18:39 allele.

Primer mix 22: Specific PCR fragment of 150 bp in the B*18:33 allele. Specific PCR fragment of 270 bp in the B*18:22 and in the B*14:10 and in the B*35:21, 35:24:01-35:24:02, 35:81, 35:96, 37:04:01-37:04:02, 40:28, 51:04, 51:46, 51:56, 53:02, 53:06, 57:14 and 58:09 alleles.

Primer mix 25: Specific PCR fragment of 75 bp in the B*18:48 allele. Specific PCR fragment of 185 bp in the B*18:35 and in the B*07:68, 15:138, 35:66, 40:77, 40:87, 48:12 and 48:14 alleles.

Primer mix 27: Specific PCR fragment of 85 bp in the B*18:37 allele. Specific PCR fragment of 140 bp in the B*18:46 allele.

Primer mix 28: Specific PCR fragment of 100 bp in the B*18:45 allele. Specific PCR fragment of 175 bp in the B*18:38 allele.

‘w’, might be weakly amplified.