PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*18

Prod. No:	101.519-12/12u

Lot No:    	31R

Expiry Date:    	2015-April-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for HLA-B*18 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*18 alleles3 | Other amplified HLA Class I alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 170 bp | 800 bp | *18:01:01:01-18:02, 18:04-18:08, 18:10-18:15, 18:17N-18:28, 18:30-18:53, 18:55-18:71, 18:73-18:76 | *48:28 |
| 2 | 260 bp | 800 bp | *18:01:01:01-18:01:17, 18:03-18:09, 18:12-18:13, 18:15, 18:17N-18:20, 18:23N-18:26, 18:28-18:34, 18:36-18:38, 18:40-18:43, 18:45-18:55, 18:57, 18:59-18:68, 18:70-18:76 | *14:06:01-14:06:02, 14:08, 15:37-15:38:02, 15:185, 39:32, 39:43, 39:48, 40:51, 40:113, 40:163, 51:06:01-51:06:02, 51:45, 51:62, 51:135, 56:31, C*08:51 |
| 3 | 260 bp | 800 bp | *18:02 | *27:28, 27:62 |
| 45 | 100 bp | 800 bp | *18:03 | *39:39:02 |
| 5 | 140 bp | 1070 bp | *18:04, 18:24 |  |
| 6 | 130 bp | 1070 bp | *18:05 |  |
| 75,9 | 90 bp, 150 bp | 1070 bp | *18:07:01-18:07:02, 18:41 |  |
| 8 | 190 bp | 1070 bp | *18:10, 18:21, 18:35, 18:50 | *07:02:01-07:04, 07:07-07:13, 07:15-07:16, 07:18:01-07:18:02, 07:21-07:23, 07:25-07:27, 07:29-07:30, 07:33, 07:35-07:39, 07:41-07:42, 07:44-07:52, 07:54-07:59, 07:61-07:68:03, 07:70-07:77, 07:79, 07:81-07:89, 07:91-07:95, 07:98-07:99, 07:101-07:104, 07:106-07:111N, 07:113-07:114, 07:116-07:122, 07:124-07:130, 07:132-07:136, 07:139, 07:141-07:162, 13:26, 13:35, 15:40, 15:47:01-15:47:02, 15:49, 15:52, 15:114, 15:117, 15:124, 15:138, 15:238, 15:241, 27:34, 27:41, 35:15, 35:33, 35:66, 35:86, 37:07, 40:03, 40:18, 40:20, 40:24, 40:31-40:33, 40:44, 40:52, 40:59, 40:98, 40:120, 40:159, 46:06, 46:30, 48:08, 48:23, 57:13, 57:25, 58:37, C*02:02:19, C*02:06, C*02:23, C*02:36, C*15:42 |
| 95,10 | 125 bp, 255 bp | 1070 bp | *18:08, 18:27, 18:75 |  |
| 105,7 | 85 bp | 800 bp | *18:23N | *44:108N |
| 115,11 | 125 bp, 610 bp, 635 bp | 1070 bp | *18:09-18:11, 18:21, 18:35-18:36, 18:54, 18:56-18:58, 18:67 | *35:02:02, 35:20:02, 44:03:12 |
| 125,12 | 85 bp, 140 bp | 1070 bp | *18:12, 18:41, 18:73 | *48:28 |
| 135,13 | 85 bp, 265 bp | 1070 bp | *18:13, 18:19, 18:30, 18:44:01-18:44:02 | *14:01:01-14:04, 14:07N, 14:09, 14:11-14:12, 14:14-14:32, 15:38:01-15:38:02, 51:29, 51:61:01-51:61:02, 51:82, 52:21, 52:24, A*66:04w, C*01:30, C*08:51 |
| 1414 | 170 bp, 260 bp | 1070 bp | *18:04, 18:14, 18:25, 18:68 | *14:05, 14:13, 35:02:02, 35:20:02, 40:174, 44:03:12, 51:64 |
| 155,6 | 100 bp | 1070 bp | *18:15, 18:19, 18:30-18:31, 18:57 | *14:01:01-14:32, 15:37-15:38:02, 35:21, 35:96, 35:188, 40:28, 40:51, 40:174, 49:09, 51:01:01-51:01:34, 51:03-51:04, 51:06:01-51:07:02, 51:11N-51:14, 51:16-51:18, 51:21-51:22, 51:24:01-51:24:04, 51:26-51:30, 51:32-51:33, 51:35, 51:37-51:39, 51:41N, 51:43, 51:45-51:46, 51:48-51:52, 51:55-51:58, 51:60-51:72, 51:74-51:80, 51:82-51:92, 51:94-51:96, 51:98N-51:107, 51:109-51:114, 51:116-51:119, 51:121, 51:123-51:137, 52:01:01:01-52:02, 52:04-52:09, 52:12-52:18, 52:20-52:28, 52:30, 53:06, 53:28, 56:05:01-56:06, 56:21, 58:08:01-58:08:02, 78:01:01-78:03, 78:05-78:07, C*01:30, C*08:51, C*15:39 |
| 165,15 | 95 bp, 360 bp | 1070 bp | *18:17N, 18:19 | *08:70, 13:31, 13:41, 15:27:03, 15:38:02, 35:14:01, 35:62, 35:163, 39:36, 44:146, 46:01:03, 51:61:02, 52:21, 55:21, A*26:68, C*01:09, C*02:02:14, C*07:22, C*07:138, C*12:03:16 |
| 175,16 | 100 bp, 255 bp | 1070 bp | *18:18, 18:31 | *52:28 |
| 185,7,17 | 85 bp, 555 bp, 580 bp | 1070 bp | *18:15, 18:21w, 18:29, 18:30w, 18:32, 18:57 | *15:71, 15:175, 15:204, 15:225, 35:50, 37:22, 41:12, 46:14, 49:03, 54:02, 55:16, 56:35, 57:39 |
| 195,18 | 105 bp, 160 bp, 405 bp | 1070 bp | *18:06, 18:39, 18:53 |  |
| 206 | 290 bp | 1070 bp | *18:20 | *07:14, 07:17, 07:28, 07:96:01-07:96:02, 07:115, 08:14, 08:28, 08:49, 08:74, 08:87, 13:10, 13:46, 13:51, 14:01:01-14:12, 14:14-14:22, 14:24-14:32, 15:02:01-15:02:06, 15:06, 15:13:01-15:13:02, 15:17:01:01-15:17:02, 15:21, 15:25:01-15:25:03, 15:31, 15:36, 15:44, 15:55, 15:77, 15:88-15:89, 15:106, 15:112, 15:121, 15:128, 15:137, 15:139, 15:144, 15:156, 15:162, 15:168, 15:170, 15:177, 15:196, 15:204, 15:208, 15:213-15:214, 15:216, 15:230, 15:233, 15:240, 15:250, 27:01-27:06, 27:08-27:10, 27:12-27:19, 27:21, 27:23, 27:25-27:26, 27:28-27:32, 27:35-27:40, 27:42, 27:44-27:92, 35:164, 37:01:01-37:06, 37:08, 37:10-37:11, 37:13-37:34, 38:22, 39:17, 40:09, 40:42, 40:60, 40:89, 40:124:01-40:124:02, 40:172, 40:180, 44:02:01:01-44:09, 44:11-44:13, 44:15-44:16, 44:18-44:30, 44:32-44:42, 44:44, 44:46-44:50, 44:52N-44:61N, 44:63-44:76, 44:78-44:81, 44:83-44:106, 44:108N-44:121, 44:124-44:134, 44:136-44:155, 45:01-45:08, 45:10-45:13, 47:01:01:01-47:08, 48:17, 48:26, 49:01:01-49:03, 49:05-49:22, 50:01:01-50:02, 50:04-50:17, 51:42, 51:85, 52:26, 53:07, 54:15, 55:41, 57:04-57:05, 57:32, 57:41, 83:01 |
| 21 | 215 bp | 1070 bp | *18:01:01:01-18:09, 18:12-18:15, 18:17N-18:19, 18:22-18:34, 18:36-18:55, 18:57, 18:59-18:76 | *13:15, 14:13, 14:23, 15:37-15:38:02, 15:185, 35:21, 35:24:01-35:24:02, 35:81, 35:96, 35:109, 35:157, 35:188, 35:190, 39:32, 39:43, 39:48, 40:28, 40:51, 40:113, 40:163, 40:174, 51:01:01-51:01:34, 51:03-51:04, 51:06:01-51:09:02, 51:11N-51:14, 51:16, 51:19-51:22, 51:24:01-51:24:04, 51:26-51:33, 51:35, 51:37-51:39, 51:41N, 51:43-51:46, 51:48-51:53, 51:55-51:58, 51:60-51:80, 51:82-51:84, 51:86-51:92, 51:94-51:107, 51:109-51:137, 52:01:01:01-52:02, 52:04-52:10:02, 52:12-52:25, 52:27-52:30, 53:02, 53:06, 53:28, 56:05:01-56:06, 56:21, 56:31, 56:34, 57:14, 58:08:01-58:09, 78:01:01-78:03, 78:05-78:07, C*15:39 |
| 225,19 | 125 bp, 150 bp, 270 bp | 800 bp | *18:22, 18:33, 18:69w, 18:75 | *14:10, 35:21, 35:24:01-35:24:02, 35:81, 35:96, 35:109, 35:157, 35:188, 35:190, 37:04:01w-37:04:02w, 40:28, 51:04, 51:46, 51:56:01-51:56:02, 53:02, 53:06, 53:28, 57:14, 58:09, C*15:39 |
| 2320 | 150 bp, 515 bp | 1070 bp | *18:21, 18:40, 18:51, 18:53, 18:61 |  |
| 24 | 190 bp | 1070 bp | *18:26, 18:61 | *07:34, 08:01:01-08:05, 08:08N-08:10, 08:12:01-08:13, 08:15-08:20, 08:22-08:24, 08:26-08:27, 08:29-08:36, 08:38-08:39, 08:41-08:48, 08:50-08:73, 08:75-08:76, 08:78, 08:80-08:86N, 08:88, 08:90-08:94, 13:06, 13:53, 14:13, 15:42, 15:83, 15:86, 15:188, 15:224, 15:252, 35:60, 35:87, 37:12, 38:01:01, 38:01:03-38:01:05, 38:01:07-38:07, 38:09-38:21, 38:23-38:28, 38:31-38:40, 39:01:01:01-39:01:01:03, 39:01:03-39:06:02, 39:08-39:14, 39:16, 39:18-39:20, 39:22-39:24:02, 39:26-39:28, 39:30-39:31, 39:34-39:37, 39:39:01-39:39:02, 39:41-39:42, 39:44-39:46, 39:48, 39:51-39:54, 39:56-39:66, 39:68-39:73, 39:75, 40:39, 40:51, 40:163, 40:184, 40:199, 41:01-41:03:02, 41:05-41:09, 41:11-41:16, 41:20, 42:01:01-42:02, 42:04-42:08, 42:10-42:15, 42:17, 46:18, 51:21, 51:36, 51:101, 54:01:01-54:02, 54:04-54:05N, 54:07-54:08N, 54:10-54:13, 54:17-54:25, 54:27, 55:01:01-55:05, 55:07, 55:10-55:13, 55:15-55:21, 55:25-55:26, 55:28-55:40, 55:42-55:45, 55:47-55:50, 55:52-55:56, 56:10, 56:12, 56:23, 58:20, 59:01:01:01-59:03, 59:05, 67:01:01-67:03, 78:07, C*15:24 |
| 255,21 | 75 bp, 185 bp | 1070 bp | *18:35, 18:48 | *07:68:01-07:68:03, 15:138, 15:230, 15:241, 35:66, 40:77, 40:87:01-40:87:02, 40:121, 40:158, 44:150, 48:12, 48:14, 48:26 |
| 265,7,22 | 90 bp, 180 bp | 1070 bp | *18:04, 18:25, 18:42-18:43 | *35:02:02, 35:20:02, 39:39:02, 44:03:12, A*24:02:37, A*26:01:16 |
| 275,23 | 80 bp, 135 bp | 800 bp | *18:37, 18:46, 18:73-18:74N | *07:109, 13:10, 13:26, 48:28 |
| 285,24 | 100 bp, 180 bp | 800 bp | *18:38, 18:45, 18:74N | *08:83, 13:10-13:11, 38:38, 40:91, 40:197 |
| 295,8,25 | 65 bp, 120 bp | 1070 bp | *18:47, 18:50 | *13:15, 40:113, 51:16, 51:31, 51:82, 52:08, 73:01 |
| 306,7,26 | 145 bp, 420 bp | 800 bp | *18:34, 18:52 |  |
| 31 | 135 bp | 1070 bp | *18:49 | *35:27, 35:56, 35:185, 35:203, 37:05, 78:06 |
| 32 | 175 bp | 1070 bp | *18:28 | *15:250 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-B*18 SSP typings.

When the primers in a primer mix can give rise to HLA-specific PCR products of more than one length this is indicated if the size difference is more than 20 base pairs. Size differences of 20 base pairs or less are not given. For high resolution SSP kits the respective lengths of the HLA-specific PCR product(s) are given for the alleles amplified by these primer mixes.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-B*18 subtyping.

In addition, wells number 2 to 4, 10, 22, 27, 28 and 30 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several HLA-B alleles 1st and/or 4th exon(s) and beyond, as well as intron nucleotide sequences, are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in these regions are conserved within allelic groups.

4Due to the sharing of sequence motifs between HLA-B alleles non-HLA-B*18 alleles will be amplified by primer mixes 1 to 4, 8, 10 to 18,  20 to 22, 24 to 29, 31 and 32. In addition, the A*24:02:37 and A*26:01:16 alleles will be amplified by primer mix 26, the A*26:68, C*01:09, C*02:02:14, C*07:22, C*07:138 and C*12:03:16 alleles will be amplified by primer mix 16, the A*66:04 allele will be weakly amplified by primer mix 13, the C*01:30 allele will be amplified by primer mixes 13 and 15, the C*02:02:19, C*02:06, C*02:23, C*02:36 and C*15:42 alleles will be amplified by primer mix 8, the C*08:51 allele will be amplified by primer mixes 2, 13 and 15, the C*15:24 allele will be amplified by primer mix 24 and the C*15:39 allele will be amplified by primer mixes 15, 21 and 22.

5HLA-specific PCR products shorter than 125 base pairs have a lower intensity and are less sharp than longer PCR products.

6Primer mixes 15, 20 and 30 may have tendencies of unspecific amplifications.

7Primer mixes 10, 18, 26 and 30 have a tendency to giving rise to primer oligomer formation.

8Primer mix 29 may give rise to a lower yield of HLA-specific PCR product than the other B*18 primer mixes.

9Primer mix 7: Specific PCR fragment of 90 bp in the B*18:41 allele. Specific PCR fragment of 150 bp in the B*18:07:01-18:07:02 alleles.

10Primer mix 9: Specific PCR fragment of 125 bp in the B*18:75 allele. Specific PCR fragment of 255 bp in the B*18:08 and18:27 alleles.

11Primer mix 11: Specific PCR fragment of 125 bp in the B*18:09, 18:54 and 18:67 alleles. Specific PCR fragment of 610 bp in the B*18:36 and 18:57 alleles. Specific PCR fragment of 635 bp in the B*18:10-18:11, 18:21 and 18:35 and the B*39:39:02 alleles. Specific PCR fragment of 610 and 635 bp in the B*18:56 and 18:58 and the A*26:01:16, B*35:02:02 and 35:20:02 alleles. Specific PCR fragment of 125 and 635 bp in the the A*24:02:37 allele. Specific PCR fragment of 125, 610 and 635 bp in the B*44:03:12 allele

12Primer mix 12: Specific PCR fragment of 90 bp in the B*18:73 and 18:41 alleles. Specific PCR fragment of 140 bp in the B*18:12 and the B*48:28 alleles.

13Primer mix 13: Specific PCR fragment of 85 bp in the B*18:13, 18:19 and 18:30 and the 15:38:01-15:38:02, 51:29, 51:61:01-51:61:02, 51:82, 52:21, 52:24 and in the *A*66:04w and C*08:51 alleles. Specific PCR fragment of 265 bp in the B*18:44:01-18:44:02 and in the B*14:01:01-14:02, 14:04, 14:07N, 14:09, 14:11-14:12 and 14:14-14:32 alleles. Specific PCR fragment of 85 and 265 bp in the B*14:03 and C*01:30 alleles.

14Primer mix 14: Specific PCR fragment of 170 bp in the B*18:04, 18:25 and 18:68 and the B*35:02:02, 35:20:02 and 44:03:12 alleles. Specific PCR fragment of 260 bp in the B*18:14 and the B*14:05, 14:13, 40:174 and 51:64 alleles.

15Primer mix 16: Specific PCR fragment of 95 bp in the B*18:19 and in the B*08:70, 13:31, 13:41, 15:27:03, 15:38:02, 35:14:01, 35:62, 35:163, 39:36, 44:146, 46:01:03, 51:61:02, 52:21 and 55:21 and the A*26:68, C*01:09, C*02:02:14, C*07:22, C*07:138 and C*12:03:16 alleles. Specific PCR fragment of 360 bp in the B*18:17N allele.

16Primer mix 17: Specific PCR fragment of 100 bp in the B*18:31 and the B*52:28 alleles. Specific PCR fragment of 255 bp in the B*18:18 allele.

17Primer mix 18: Specific PCR fragment of 85 bp in the B*18:29 and the B*15:71, 15:175, 15:204, 15:225, 35:50, 37:22, 41:12, 46:14, 49:03, 54:02, 55:16, 56:35 and 57:39 alleles. Specific PCR fragment of 555 bp in the B*18:32 allele. Specific PCR fragment of 580 bp in the B*18:15, 18:21w, 18:30w and 18:57 alleles.

18Primer mix 19: Specific PCR fragment of 105 bp in the B*18:06 allele. Specific PCR fragment of 160 bp in the B*18:53 allele. Specific PCR fragment of 405 bp in the B*18:39 allele.

19Primer mix 22: Specific PCR fragment of 125 bp in the B*18:75 allele. Specific PCR fragment of 150 bp in the B*18:33 allele. Specific PCR fragment of 270 bp in the B*18:22 and 18:69w and the B*14:10, 35:21, 35:24:01-35:24:02, 35:81, 35:96, 35:109, 35:157, 35:188, 35:190, 37:04:01w-37:04:02w, 40:28, 51:04, 51:46, 51:56:01-51:56:02, 53:02, 53:06, 53:28, 57:14 and 58:09 and the C*15:39 alleles.

20Primer mix 23: Specific PCR fragment of 150 bp in the B*18:51 and 18:53 alleles. Specific PCR fragment of 515 bp in the B*18:21, 18:40 and 18:61 alleles.

21Primer mix 25: Specific PCR fragment of 75 bp in the B*18:48 allele. Specific PCR fragment of 185 bp in the B*18:35 and the B*07:68:01-07:68:03, 15:138, 15:230, 15:241, 35:66, 40:77, 40:87:01-40:87:02, 40:121, 40:158, 44:150, 48:12, 48:14 and 48:26 alleles.

22Primer mix 26: Specific PCR fragment of 90 bp in the B*18:42 allele. Specific PCR fragment of 180 bp in the B*18:04, 18:25 and 18:43 and the B*35:02:02, 35:20:02, 39:39:02 and 44:03:12 and the A*24:02:37 and A*26:01:16 alleles.

23Primer mix 27: Specific PCR fragment of 80 bp in the B*18:37 and 18:73 and the B*07:109 and 48:28 alleles. Specific PCR fragment of 135 bp in the B*18:46 and 18:74N and the B*13:10 and 13:26 alleles.

24Primer mix 28: Specific PCR fragment of 100 bp in the B*18:45 allele. Specific PCR fragment of 180 bp in the B*18:38 and 18:74N and the B*08:83, 13:10-13:11, 38:38, 40:91 and 40:197 alleles.

25Primer mix 29: Specific PCR fragment of 65 bp in the B*18:50 and the B*13:15, 40:113, 51:16, 51:31, 51:82, 52:08 and 73:01 alleles. Specific PCR fragment of 120 bp in the B*18:47 allele.

26Primer mix 30: Specific PCR fragment of 145 bp in the B*18:34 allele. Specific PCR fragment of 420 bp in the B*18:52 allele.

‘w’, might be weakly amplified.

1The sequence of the B*1816 allele has been found to be identical to B*18:14.

2HLA-B*18 alleles in bold lettering are listed as confirmed alleles on the on the IMGT/HLA web page www.ebi.ac.uk/imgt/hla, release 3.9.0, July 2012.

3The B*18:34 and 18:52 alleles may be distinguished by the different sizes of the specific PCR products generated by primer mix 30.

4The B*18:36 and 18:67 alleles may be distinguished by the different sizes of the specific PCR products generated by primer mix 11.

5The B*18:37 and 18:46 alleles may be distinguished by the different sizes of the specific PCR products generated by primer mix 27.

6The B*18:38 and 18:45 alleles may be distinguished by the different sizes of the specific PCR products generated by primer mix 28.

7The B*18:40 and 18:51 alleles may be distinguished by the different sizes of the specific PCR products generated by primer mix 23.

8The B*18:42 and 18:43 alleles may be distinguished by the different sizes of the specific PCR products generated by primer mix 26.

9The HLA-B*18 primer set cannot separate the B*18:72 and the B*15:185, 39:32, 39:43 and 56:31 alleles. These alleles can be distinguished by the HLA-B low resolution kit and/or the HLA-B*15, HLA-B*39 and HLA-B*56 high resolution kits.

10Primer mix 7: Specific PCR fragment of 90 bp in the B*18:41 allele. Specific PCR fragment of 150 bp in the B*18:07:01-18:07:02 alleles.

Primer mix 9: Specific PCR fragment of 125 bp in the B*18:75 allele. Specific PCR fragment of 255 bp in the B*18:08 and18:27 alleles.

Primer mix 11: Specific PCR fragment of 125 bp in the B*18:09, 18:54 and 18:67 alleles. Specific PCR fragment of 610 bp in the B*18:36 and 18:57 alleles. Specific PCR fragment of 635 bp in the B*18:10-18:11, 18:21 and 18:35 and the A*26:01:16 and B*39:39:02 alleles. Specific PCR fragment of 610 and 635 bp in the B*18:56 and 18:58 and the B*35:02:02 and 35:20:02 alleles. Specific PCR fragment of 125 and 635 bp in the the A*24:02:37 allele. Specific PCR fragment of 125, 610 and 635 bp in the B*44:03:12 allele

Primer mix 12: Specific PCR fragment of 90 bp in the B*18:73 and 18:41 alleles. Specific PCR fragment of 140 bp in the B*18:12 and the B*48:28 alleles.

Primer mix 13: Specific PCR fragment of 85 bp in the B*18:13, 18:19 and 18:30 and the B*14:03, 15:38:01-15:38:02, 51:29, 51:61:01-51:61:02, 51:82, 52:21, 52:24 and in the *A*66:04w, C*01:30 and C*08:51 alleles. Specific PCR fragment of 265 bp in the B*18:44:01-18:44:02 and in the B*14:01:01-14:04, 14:07N, 14:09, 14:11-14:12 and 14:14-14:32 and the C*01:30 alleles.

Primer mix 14: Specific PCR fragment of 170 bp in the B*18:04, 18:25 and 18:68 and the B*35:02:02, 35:20:02 and 44:03:12 alleles. Specific PCR fragment of 260 bp in the B*18:14 and the B*14:05, 14:13, 40:174 and 51:64 alleles.

Primer mix 16: Specific PCR fragment of 95 bp in the B*18:19 and in the B*08:70, 13:31, 13:41, 15:27:03, 15:38:02, 35:14:01, 35:62, 35:163, 39:36, 44:146, 46:01:03, 51:61:02, 52:21 and 55:21 and the A*26:68, C*01:09, C*02:02:14, C*07:22, C*07:138 and C*12:03:16 alleles. Specific PCR fragment of 360 bp in the B*18:17N allele.

Primer mix 17: Specific PCR fragment of 100 bp in the B*18:31 and the B*52:28 alleles. Specific PCR fragment of 255 bp in the B*18:18 allele.

Primer mix 18: Specific PCR fragment of 85 bp in the B*18:29 and the B*15:71, 15:175, 15:204, 15:225, 35:50, 37:22, 41:12, 46:14, 49:03, 54:02, 55:16, 56:35 and 57:39 alleles. Specific PCR fragment of 555 bp in the B*18:32 allele. Specific PCR fragment of 580 bp in the B*18:15, 18:21w, 18:30w and 18:57 alleles.

Primer mix 19: Specific PCR fragment of 105 bp in the B*18:06 allele. Specific PCR fragment of 160 bp in the B*18:53 allele. Specific PCR fragment of 405 bp in the B*18:39 allele.

Primer mix 22: Specific PCR fragment of 125 bp in the B*18:75 allele. Specific PCR fragment of 150 bp in the B*18:33 allele. Specific PCR fragment of 270 bp in the B*18:22 and 18:69w and the B*14:10, 35:21, 35:24:01-35:24:02, 35:81, 35:96, 35:109, 35:157, 35:188, 35:190, 37:04:01w-37:04:02w, 40:28, 51:04, 51:46, 51:56:01-51:56:02, 53:02, 53:06, 53:28, 57:14 and 58:09 and the C*15:39 alleles.

Primer mix 23: Specific PCR fragment of 150 bp in the B*18:51 and 18:53 alleles. Specific PCR fragment of 515 bp in the B*18:21, 18:40 and 18:61 alleles.

Primer mix 25: Specific PCR fragment of 75 bp in the B*18:48 allele. Specific PCR fragment of 185 bp in the B*18:35 and the B*07:68:01-07:68:03, 15:138, 15:230, 15:241, 35:66, 40:77, 40:87:01-40:87:02, 40:121, 40:158, 44:150, 48:12, 48:14 and 48:26 alleles.

Primer mix 26: Specific PCR fragment of 90 bp in the B*18:42 allele. Specific PCR fragment of 180 bp in the B*18:04, 18:25 and 18:43 and the B*35:02:02, 35:20:02, 39:39:02 and 44:03:12 and the A*24:02:37 and A*26:01:16 alleles.

Primer mix 27: Specific PCR fragment of 80 bp in the B*18:37 and 18:73 and the B*07:109 and 48:28 alleles. Specific PCR fragment of 135 bp in the B*18:46 and 18:74N and the B*13:10 and 13:26 alleles.

Primer mix 28: Specific PCR fragment of 100 bp in the B*18:45 allele. Specific PCR fragment of 180 bp in the B*18:38 and 18:74N and the B*08:83, 13:10-13:11, 38:38, 40:91 and 40:197 alleles.

Primer mix 29: Specific PCR fragment of 65 bp in the B*18:50 and the B*13:15, 40:113, 51:16, 51:31, 51:82, 52:08 and 73:01 alleles. Specific PCR fragment of 120 bp in the B*18:47 allele.

Primer mix 30: Specific PCR fragment of 145 bp in the B*18:34 allele. Specific PCR fragment of 420 bp in the B*18:52 allele.

‘w’, might be weakly amplified.