PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*27

Prod. No:	101.521-24/24u

101.521-04/04u

Lot No:    	09F

Expiry Date:    	2010-September-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 24 primer mixes used for HLA-B*27 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*27 alleles3 | Other amplified HLA Class I alleles3,4 |
| --- | --- | --- | --- | --- |
| 1 | 390 bp | 800 bp | 2701, 2718, 2723, 2729 | 180101, 180103, 1802, 1804-1815, 1817N-1824, 1826-1829, 3542, 370101-3714, 400201, 400202-400203?, 4003-40060102, 400602?, 4008, 4009-4011?, 4013, 401401-4015?, 4018-4022N?, 4024-4038?, 4039, 4040?, 4042?, 4043, 4044-4049?, 4050, 4052-4058?, 4061-4065?, 4067-4069?, 4070, 4071?, 407202?, 4074-4076?, 4078?, 4080-4088?, 4089, 4090-4092?, 47010101-4705 |
| 27 | 385, 405 bp | 800 bp | 2702, 2730, 2739 | 4013, 4019? |
| 35 | 120 bp | 1070 bp | 2703 |  |
| 4 | 245 bp | 1070 bp | 2703, 270502-270510, 2707, 2709, 2710, 2713, 2714, 2716, 2717, 2719, 2727-2729, 2732, 2734, 2735, 2738, 2739, 2741, 2743 | 370101-3704, 3706-3709, 3712, 3713 |
| 5 | 400 bp | 1070 bp | 270401-270402, 2706, 2708, 2711, 2712, 2715, 2718, 2720, 2721, 2723-2726, 2731, 2733, 2736, 2740 | 180101-1808, 1810-1815, 1817N-1824, 1826-1829, 3542, 3711, 3714, 400201-400602, 4008, 4009-4011?, 401401-4015?, 4018?, 4020-4022N?, 4024-4036?, 4038?, 4039, 4040?, 4042-4046?, 4048-4050?, 4052-4058?, 4061-4065?, 4067-4069?, 4070, 4071?, 407202?, 4074-4076?, 4078?, 4080-4088?, 4089, 4090-4092?, 4702, 4703, 8201, 8202 |
| 6 | 415 bp | 800 bp | 2701-270402, 270502-270503, 270505-2707, 2709-2711, 2713-2717, 2719-2721, 2723-2725, 2727-2732, 2734-2739, 2741, 2743 | 1809, 370101-3704, 3706-3710, 3712- 3714, 4013, 4019?, 4047?, 47010101-47010102, 4703-4705 |
| 7 | 410 bp | 1070 bp | 2708, 2712, 2718, 2726, 2733, 2740, 2742 | 180101-1808, 1810-1815, 1817N-1824, 1826-1829, 3542, 3705, 3711, 3714, 400201-400602, 4008, 4009-4011?, 401401-4015?, 4018?, 4020-4022N?, 4024-4038?, 4039, 4040?, 4042-4046?, 4048-4050?, 4052-4058?, 4061-4065?, 4067-4069?, 4070, 4071?, 407202?, 4074?, 4075?, 4078?, 4080-4088?, 4089, 4090-4092?, 4702, 4703weakly, 8201, 8202 |
| 85 | 95 bp | 1070 bp | 2701-270402, 270502-270510, 2708, 2710, 2712, 2713, 2715-2718, 2723, 2725, 2726, 2728, 2729, 2731, 2736-2740, 2742 | 3702, 4704, 4705 |
| 9 | 205 bp | 1070 bp | 270401-270402, 2706, 2710, 2715, 2718, 2720, 2740 |  |
| 105 | 90 bp | 800 bp | 2706, 2735, 2741 | 9529, 1802, Cw*0705weakly |
| 11 | 190 bp | 1070 bp | 2707, 2711, 2720, 2724, 2727, 2733, 2743 | 070501-0706, 0732, 0740, 0753, 1301-130204, 1307N-1309, 1311, 1313-1322, 3531, 3588, 400101-400203, 4004, 40060101-4008, 4010-4016, 4019, 4021-4023, 4025, 4027, 4029, 4030, 4034-4038, 4040, 4043, 4045-4050, 4053-4058, 4061, 4062, 4064-4070, 407201-4088, 4090, 4091, 4431, 480101-480102, 480301-4807, 4809-4816, 4818, 4819, 5110, 5116, 5131, 5134, 5208, 5509, 5522, 5524, 8101-8104N |
| 128 | 270, 430 bp | 1070 bp | 2713, 2743 |  |
| 13 | 370 bp | 800 bp | 2712, 2716 | 4075weakly |
| 145,9 | 120, 345 bp | 800 bp | 2717, 2734 | 400602 |
| 15 | 370 bp | 1070 bp | 2718, 2729 | 180101-1806, 1808-1815, 1817N-1824, 1826-1828, 370101-3714, 400201, 400202?, 4003-40060102, 400602?, 4009-4011?, 401401-4015?, 4018-4022N?, 4024-4038?, 4039, 4040?, 4042-4050?, 4052-4058?, 4062-4065?, 4067?, 4069?, 4070, 4071?, 407202?, 4074?, 4076?, 4078?, 4080-4088?, 4089, 4090-4092?, 47010101-4705 |
| 166 | 245 bp | 1070 bp | 2719, 2730 | 0712, 0714, 071801-071802, 1301, 1307N, 1313, 1317, 1320-1322, 3515, 3533, 3588, 4004, 4030, 4034, 4059, 4064, 4068, 4416, 4421, 446401-446402, 4817, 5713, Cw*0334 |
| 175 | 100 bp | 1070 bp | 2714 | 4420, 4447 |
| 185,10 | 95, 175 bp | 800 bp | 2724, 2732 | 0728, 0814, 4031, 4045, 4080, 4454, 480101-480102, 4804, 4806, 4807, 4809, 4811, 4815, 4816, 4818, 4819, 8101-8104N |
| 195,11 | 95, 235 bp | 800 bp | 2725, 2735, 2738 | 9529 |
| 205,12 | 95, 175 bp | 800 bp | 2709, 2736 |  |
| 215 | 110 bp | 800 bp | 270401, 270402?, 2706 |  |
| 2213 | 195, 380 bp | 800 bp | 2726, 2731, 2737 | 8201, 8202 |
| 23 | 235 bp | 800 bp | 2701-270402, 270502-2706, 2708-2710, 2712, 2713, 2716-2718, 2720, 2723, 2726, 2727, 2729, 2731, 2735-2737, 2739-2742 | 3702, 4704, 4705 |
| 245,14 | 105, 260 bp | 1070 bp | 2718, 2728, 2729 | 0727, 0750, 0804, 0817, 1503, 1547, 1549, 1554, 1561, 1562, 1564, 1568, 1569, 1591, 1598, 9503, 9523, 9527, 9531, 9532, 1802, 3803, 390201-390202, 3908, 391301-391302, 3923, 3939, 4012, 4046, 4440, 4444, 480101-4805, 4807-4819, 5518 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-B*27 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-B*27 subtyping.

In addition, wells number 2, 6, 10, 13, 14, 18 to 23 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several HLA-B alleles 1st exon nucleotide sequences are not available. In these instances it is not known whether some of the primers of the HLA-B*27 SSP subtyping kit are completely matched with the target sequences or not. We assume that unknown sequences in the 1st exon are conserved within allelic groups.

4Due to the sharing of sequence motifs between HLA-B alleles non-HLA-B*27 alleles will be amplified by primer mixes 1, 2, 4 to 8, 10, 11, 13 to 19, 22 to 24. In addition, the primers in vial 10 will weakly amplify the Cw*0705 allele and the Cw*0334 allele will be amplified by primer mix 16.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6Primer mix 16 has a tendency of giving rise to nonspecific amplifications.

7Primer mix 2: Specific PCR product of 385 bp in the B*2739 allele. Specific PCR product of 405 bp in the B*2702 and B*2730 and the B*4012 and B*4019? alleles.

8Primer mix 12: Specific PCR product of 270 bp in the B*2743 allele. Specific PCR product of 430 bp in the B*2713 allele.

9Primer mix 14: Specific PCR product of 120 bp in the B*2734 and B*400602 alleles. Specific PCR product of 345 bp in the B*2717 allele.

10Primer mix 18: Specific PCR product or 95 bp in the B*2732 and B*0728, 0814 and 4454 alleles. Specific PCR product of 175 bp in the B*2724 and B*4031, 4045, 4080, 480101-480102, 4804, 4806, 4807, 4809, 4811, 4815, 4816, 4818, 4819 and 8101- 8104N alleles.

11Primer mix 19: Specific PCR fragment of 95 bp in the B*2735 allele. Specific PCR fragment of 235 bp in the B*2725, 2738 and B*9529 alleles.

12Primer mix 20: Specific PCR fragment of 95 bp in the B*2709 allele. Specific PCR fragment of 175 bp in the B*2736 allele.

13Primer mix 22: Specific PCR fragment of 195 bp in the B*2737 allele. Specific PCR fragment of 380 bp in the B*2726, 2731 and B*8201-8202 alleles.

14Primer mix 24: Specific PCR fragment of 105 bp in the B*2718, 2729 and the B*0727, 0750, 0804, 0817, 1503, 1547, 1549, 1554, 1561, 1562, 1564, 1568, 1569, 1591, 1598, 9503, 9523, 9527, 9531, 9532, 3803, 390201-390202, 3908, 391301-391302, 3923, 3939, 4012, 4046, 4440, 4444, 480101-4805, 4807-4819 and 5518 alleles. Specific PCR fragment of 260 bp in the B*2728 and B*1802 alleles.

‘?’, nucleotide sequence information not available for the primer matching sequence.

1The sequence of the B*27051 allele has been shown to be identical to B*270502.

The sequence of the B*2722 allele has been shown to be identical to the corrected B*2706 nucleotide sequence.

2Primer mix 2: Specific PCR product of 385 bp in the B*2739 allele. Specific PCR product of 405 bp in the B*2702 and B*2730 and the B*4012 and B*4019? alleles.

Primer mix 12: Specific PCR product of 270 bp in the B*2743 allele. Specific PCR product of 430 bp in the B*2713 allele.

Primer mix 14: Specific PCR product of 120 bp in the B*2734 and B*400602 alleles. Specific PCR product of 345 bp in the B*2717 allele.

Primer mix 18: Specific PCR product or 95 bp in the B*2732 and B*0728, 0814 and 4454 alleles. Specific PCR product of 175 bp in the B*2724 and B*4031, 4045, 4080, 480101-480102, 4804, 4806, 4807, 4809, 4811, 4815, 4816, 4818, 4819 and 8101- 8104N alleles.

Primer mix 19: Specific PCR fragment of 95 bp in the B*2735 allele. Specific PCR fragment of 235 bp in the B*2725, 2738 and B*9529 alleles.

Primer mix 20: Specific PCR fragment of 95 bp in the B*2709 allele. Specific PCR fragment of 175 bp in the B*2736 allele.

Primer mix 22: Specific PCR fragment of 195 bp in the B*2737 allele. Specific PCR fragment of 380 bp in the B*2726, 2731 and B*8201-8202 alleles.

Primer mix 24: Specific PCR fragment of 105 bp in the B*2718, 2729 and the B*0727, 0750, 0804, 0817, 1503, 1547, 1549, 1554, 1561, 1562, 1564, 1568, 1569, 1591, 1598, 9503, 9523, 9527, 9531, 9532, 3803, 390201-390202, 3908, 391301-391302, 3923, 3939, 4012, 4046, 4440, 4444, 480101-4805, 4807-4819 and 5518 alleles. Specific PCR fragment of 260 bp in the B*2728 and B*1802 alleles.

‘w’, might be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.