PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*27

Prod. No:	101.521-24/24u

101.521-04/04u

Lot No:    	22L

Expiry Date:    	2013-September-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for HLA-B*27 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*27 alleles3 | Other amplified HLA Class I alleles3,4 |
| --- | --- | --- | --- | --- |
| 1 | 390 bp | 800 bp | *27:01, 27:18, 27:23, 27:29, 27:44 | *18:01:01, 18:01:03-18:02, 18:04-18:15, 18:17N-18:24, 18:26-18:32, 18:34-18:52, 35:42:01-35:42:02, 37:01:01-37:25, 40:02:01-40:06:03, 40:08, 40:09?-40:11:02?, 40:14:01?-40:15?, 40:18?, 40:20, 40:21?-40:22N?, 40:24?-40:38?, 40:39, 40:42?, 40:43, 40:44?-40:49?, 40:50, 40:52?-40:58?, 40:61?-40:65?, 40:67?-40:69?, 40:70, 40:71?, 40:72:02?, 40:74?-40:76?, 40:78?, 40:80?-40:88?, 40:89, 40:90?-40:93?, 40:94, 40:95?-40:96?, 40:97, 40:98?-40:116?, 40:118N?-40:121?, 40:122, 40:123?, 40:124:02?-40:137?, 40:141?, 40:142N-40:144N, 40:145?, 40:148?-40:149?, 40:151?, 40:154?, 40:156?-40:158?, 47:01:01:01-47:07 |
| 2 | 405 bp | 800 bp | *27:02, 27:30, 27:53, 27:57, 27:62, 27:65N | *40:13, 40:19?, 40:109?, 40:117? |
| 35 | 120 bp | 1070 bp | *27:03 |  |
| 4 | 245 bp | 1070 bp | *27:03, 27:05:02-27:05:15, 27:07, 27:09-27:10, 27:13-27:14, 27:16-27:17, 27:19, 27:27-27:29, 27:32, 27:34-27:35, 27:38-27:39, 27:41, 27:43, 27:45-27:52, 27:54-27:56, 27:58-27:60, 27:64N, 27:67, 27:70-27:73 | *37:01:01-37:04:02, 37:06-37:09, 37:12-37:13, 37:15-37:25 |
| 5 | 400 bp | 1070 bp | *27:04:01-27:04:03, 27:06, 27:08, 27:11-27:12, 27:15, 27:18, 27:20-27:21, 27:23-27:26, 27:31, 27:33, 27:36, 27:40, 27:44, 27:61, 27:63, 27:66N, 27:68-27:69 | *18:01:01-18:08, 18:10-18:15, 18:17N-18:24, 18:26-18:32, 18:34-18:48, 18:50-18:52, 35:42:01-35:42:02, 37:11, 37:14, 40:02:01-40:06:03, 40:08, 40:09?-40:11:02?, 40:14:01?-40:15?, 40:18?, 40:20, 40:21?-40:22N?, 40:24?-40:36?, 40:38?, 40:39, 40:42?-40:46?, 40:48?-40:50?, 40:52?-40:58?, 40:61?-40:65?, 40:67?-40:69?, 40:70, 40:71?, 40:72:02?, 40:74?-40:76?, 40:78?, 40:80?-40:88?, 40:89, 40:90?-40:93?, 40:94, 40:95?, 40:97, 40:98?-40:108?, 40:111?-40:116?, 40:118N?-40:121?, 40:122, 40:123?, 40:124:02?-40:134?, 40:136?-40:137?, 40:141?, 40:142N-40:144N, 40:145?, 40:148?-40:149?, 40:151?, 40:154?, 40:156?, 40:158?, 47:02-47:03, 82:01-82:03 |
| 6 | 415 bp | 800 bp | *27:01-27:05:03, 27:05:05-27:07, 27:09-27:11, 27:13-27:17, 27:19-27:21, 27:23-27:25, 27:27-27:32, 27:34-27:39, 27:41, 27:43, 27:45-27:73 | *18:09, 37:01:01-37:04:02, 37:06-37:10, 37:12-37:25, 40:13, 40:19?, 40:47?, 40:96?, 40:109?-40:110?, 40:117?, 40:157?, 47:01:01:01-47:01:01:02, 47:03-47:07 |
| 7 | 410 bp | 1070 bp | *27:08, 27:12, 27:18, 27:26, 27:33, 27:40, 27:42, 27:44 | *18:01:01-18:08, 18:10-18:15, 18:17N-18:24, 18:26-18:32, 18:34-18:52, 35:42:01-35:42:02, 37:05, 37:11, 40:02:01-40:06:03, 40:08, 40:09?-40:11:02?, 40:14:01?-40:15?, 40:18?, 40:20, 40:21?-40:22N?, 40:24?-40:38?, 40:39, 40:42?-40:46?, 40:48?-40:50?, 40:52?-40:58?, 40:61?-40:65?, 40:67?-40:69?, 40:70, 40:71?, 40:72:02?, 40:74?-40:75?, 40:78?, 40:80?-40:88?, 40:89, 40:90?-40:93?, 40:94, 40:95?, 40:97, 40:98?-40:108?, 40:111?-40:116?, 40:118N?-40:121?, 40:122, 40:123?, 40:124:02?-40:137?, 40:141?, 40:142N-40:144N, 40:145?, 40:148?-40:149?, 40:151?, 40:154?, 40:156?, 40:158?, 47:02, 82:01-82:03 |
| 85 | 95 bp | 1070 bp | *27:01-27:05:15, 27:08, 27:10, 27:12-27:13, 27:15-27:18, 27:23, 27:25-27:26, 27:28-27:29, 27:31, 27:36-27:40, 27:42, 27:44-27:45, 27:47-27:69, 27:71-27:73 | *37:02, 47:04-47:05 |
| 9 | 205 bp | 1070 bp | *27:04:01-27:04:03, 27:06, 27:10, 27:15, 27:18, 27:20, 27:25w, 27:40, 27:54, 27:63, 27:66N, 27:68-27:69 | *15:129w |
| 105,8 | 90 bp, 185 bp | 800 bp | *27:06, 27:35, 27:41, 27:60 | *15:129, 18:02, 38:22, C*07:05 |
| 11 | 190 bp | 1070 bp | *27:07, 27:11, 27:20, 27:24, 27:27, 27:33, 27:43 | *07:05:01-07:06, 07:32, 07:40, 07:53, 07:69, 07:78, 07:80, 07:90, 07:97, 07:105, 07:112, 08:40, 13:01:01-13:01:02, 13:01:04-13:02:09, 13:07N-13:09, 13:11, 13:13-13:23, 13:25, 13:27-13:33, 13:36-13:40, 35:31, 35:88, 39:47, 39:50, 40:01:01-40:02:09, 40:02:11, 40:04, 40:06:01:01-40:08, 40:10:01-40:16, 40:19, 40:21-40:23, 40:25, 40:27:01, 40:29-40:30, 40:34-40:38, 40:40, 40:43, 40:45-40:50, 40:53-40:58, 40:61-40:62, 40:64-40:70, 40:72:01-40:88, 40:90-40:91, 40:93-40:97, 40:99-40:119, 40:121-40:123, 40:125-40:130, 40:132, 40:134-40:158, 44:31, 48:01:01-48:01:03, 48:03:01-48:07, 48:09-48:16, 48:18-48:22, 48:24, 51:10, 51:16, 51:31, 51:34, 51:81-51:82, 51:93, 52:08, 55:09, 55:22, 55:24, 58:27, 81:01-81:05 |
| 126,9 | 310 bp, 425 bp | 1070 bp | *27:13, 27:43 | *35:113, 39:62, 44:98 |
| 1310 | 215 bp, 370 bp, 400 bp | 800 bp | *27:12, 27:16, 27:47, 27:53 | *40:75? |
| 145,11 | 120 bp, 345 bp, | 800 bp | *27:17, 27:34 | *40:02:07, 40:06:02, 57:03:02, C*02:23, C*02:36 |
| 1512 | 250 bp, 370 bp | 1070 bp | *27:18, 27:29, 27:73 | *18:01:01-18:06, 18:08-18:15, 18:17N-18:24, 18:26-18:28, 18:30-18:32, 18:34-18:52, 37:01:01-37:20, 37:22-37:25, 40:02:01-40:02:02, 40:02:04-40:06:03, 40:09?-40:11:02?, 40:14:01?-40:15?, 40:18?-40:19?, 40:20, 40:21?-40:22N?, 40:24?-40:38?, 40:39, 40:42?-40:50?, 40:52?-40:58?, 40:62?-40:65?, 40:67?, 40:69?, 40:70, 40:71?, 40:72:02?, 40:74?, 40:76?, 40:78?, 40:80?-40:88?, 40:89, 40:90?-40:93?, 40:94, 40:95?-40:96?, 40:97, 40:98?-40:102?, 40:104?-40:105?, 40:107?-40:121?, 40:122, 40:123?, 40:124:02?-40:137?, 40:141?, 40:142N-40:144N, 40:145?, 40:148?-40:149?, 40:151?, 40:154?, 40:156?-40:158?, 47:01:01:01-47:07 |
| 1613 | 155 bp, 245 bp | 1070 bp | *27:19, 27:30, 27:68 | *07:12, 07:14, 07:18:01-07:18:02, 13:01:01-13:01:05, 13:07N, 13:13, 13:17, 13:20-13:23, 13:25-13:26, 13:28-13:29, 13:36, 13:39, 15:201, 35:15, 35:33, 35:88, 40:04, 40:30, 40:34, 40:59, 40:64, 40:68, 40:99, 40:120, 40:129, 40:137, 44:16, 44:21, 44:64:01-44:64:02, 48:17, 57:13, 57:25, C*03:34, C*15:42 |
| 175,14 | 100 bp, 310 bp | 800 bp | *27:14, 27:51 | *44:20, 44:47, 44:100, 51:85 |
| 185,15 | 95 bp, 175 bp, 415 bp | 800 bp | *27:24, 27:32, 27:49 | *07:28, 08:14, 40:31, 40:45, 40:80, 44:54, 44:106, 48:01:01-48:01:03, 48:04, 48:06-48:07, 48:09, 48:11, 48:15-48:16, 48:18-48:20, 48:22, 48:24, 81:01-81:05 |
| 195,16 | 95 bp, 240 bp | 800 bp | *27:25, 27:35, 27:38, 27:47, 27:50, 27:63 | *15:129, 38:22 |
| 205,17 | 95 bp, 175 bp, 215 bp, 345 bp | 800 bp | *27:09, 27:25, 27:36, 27:45, 27:69 | *15:129, 37:23, 48:21, 51:32 |
| 215,18 | 110 bp, 160 bp | 1070 bp | *27:04:01, 27:04:02?-27:04:03?, 27:06, 27:24-27:25, 27:39, 27:66N, 27:68-27:69 |  |
| 2219 | 165 bp, 195 bp, 235 bp, 375 bp | 800 bp | *27:15, 27:26, 27:28, 27:31, 27:37, 27:55, 27:62, 27:71 | *18:02, 18:43, 82:01-82:03, C*07:05 |
| 23 | 235 bp | 800 bp | *27:01-27:06, 27:08-27:10, 27:12-27:13, 27:16-27:18, 27:20, 27:23, 27:26-27:27, 27:29, 27:31, 27:35-27:37, 27:39-27:42, 27:44-27:46, 27:48-27:61, 27:64N-27:69, 27:72-27:73 | *37:02, 47:04-47:05, 48:21 |
| 245,20 | 105 bp, 260 bp | 1070 bp | *27:18, 27:28-27:29, 27:62 | *07:27, 07:50, 08:04, 08:17, 08:54, 15:03:01-15:03:03, 15:47, 15:54, 15:61-15:62, 15:64, 15:68-15:69, 15:91, 15:98, 15:103, 15:123, 15:127, 15:131-15:132, 15:151, 15:156, 15:158, 15:173, 18:02, 18:37, 38:03, 39:02:01-39:02:02, 39:08, 39:13:01-39:13:02, 39:23, 39:39, 39:49, 40:12, 40:46, 40:93, 42:11, 44:40, 44:44, 48:01:01-48:05, 48:07-48:24, 52:16, 55:18 |
| 255 | 85 bp | 1070 bp | *27:46 | A*23:23 |
| 265,21 | 105 bp, 145 bp, 235 bp | 1070 bp | *27:52, 27:64N, 27:72 |  |
| 2722 | 225 bp, 290 bp, 320 bp | 1070 bp | *27:57-27:58, 27:66N |  |
| 286,23 | 145 bp, 325 bp | 1070 bp | *27:48, 27:64N | *40:118N |
| 295,24 | 70 bp, 105 bp | 1070 bp | *27:54, 27:67 |  |
| 307,25 | 160 bp, 240 bp | 800 bp | *27:59N, 27:72-27:73 |  |
| 315,6,26 | 125 bp, 160 bp | 1070 bp | *27:56, 27:65N |  |
| 325,6 | 90 bp | 1070 bp | *27:32, 27:70 | *07:28, 08:14, 15:17:01:01-15:17:02, 15:162, 15:168, 15:177, 15:196, 15:208, 40:124:02, 44:41:01, 44:54, 44:65, 44:106, C*02:07 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-B*27 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-B*27 subtyping.

In addition, wells number 2, 6, 10, 13, 14, 17 to 20, 22, 23 and 30 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several HLA-B alleles 1st or 4th exon nucleotide sequences are not available. In these instances it is not known whether some of the primers of the HLA-B*27 SSP subtyping kit are completely matched with the target sequences or not. We assume that unknown sequences in the 1st or 4th exon are conserved within allelic groups.

4Due to the sharing of sequence motifs between HLA-B alleles non-HLA-B*27 alleles will be amplified by primer mixes 1, 2, 4 to 20, 22 to 24, 28 and 32. In addition, the A*23:23 will be amplified by primer mix 25, the C*02:07 will be amplified by primer mix 32, the C*02:23 and C*02:36 will be amplified by primer mix 14, the C*03:34 and C*15:42 alleles will be amplified by primer mix 16 and the C*07:05 allele will be amplified by primer mixes 10 and 22.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6Primer mixes 12, 28, 31 and 32 have a tendency of giving rise to nonspecific amplifications.

7Primer mix 30 may give rise to a long unspecific amplification product. This band should be disregarded when interpreting the typing results.

8Primer mix 10: Specific PCR product of 90 bp in the B*27:06, 27:35 and 27:41 and the B*15:129, 18:02 and 38:22 and in the C*07:05 alleles. Specific PCR product of 185 bp in the B*27:60 allele.

9Primer mix 12: Specific PCR product of 310 bp in the B*27:43 and the B*35:113, 39:62 and 44:98 alleles. Specific PCR product of 425 bp in the B*27:13 allele.

10Primer mix 13: Specific PCR product of 215 bp in the B*27:47 allele. Specific PCR product of 370 bp in the B*27:12 and 27:16 and in the B*40:75? alleles. Specific PCR product of 400 bp in the B*27:16 and B*27:53 alleles.

11Primer mix 14: Specific PCR product of 120 bp in the B*27:34 and the B*40:02:07, 40:06:02 and 57:03:02 and in the C*02:23 and C*02:36 alleles. Specific PCR product of 345 bp in the B*27:17 allele.

12Primer mix 15: Specific PCR product of 250 bp in the B*27:73 allele. Specific PCR product of 370 bp in the B*27:18 and 27:29 and in the B*18:01:01-18:06, 18:08-18:15, 18:17N-18:24, 18:26-18:28, 18:30-18:32, 18:34-18:52, 37:01:01-37:20, 37:22-37:25, 40:02:01-40:02:02, 40:02:04-40:06:03, 40:09?-40:11:02?, 40:14:01?-40:15?, 40:18?-40:19?, 40:20, 40:21?-40:22N?, 40:24?-40:38?, 40:39, 40:42?-40:50?, 40:52?-40:58?, 40:62?-40:65?, 40:67?, 40:69?, 40:70, 40:71?, 40:72:02?, 40:74?, 40:76?, 40:78?, 40:80?-40:88?, 40:89, 40:90?-40:93?, 40:94, 40:95?-40:96?, 40:97, 40:98?-40:102?, 40:104?-40:105?, 40:107?-40:121?, 40:122, 40:123?, 40:124:02?-40:137?, 40:141?, 40:142N-40:144N, 40:145?, 40:148?-40:149?, 40:151?, 40:154?, 40:156?-40:158? and 47:01:01:01-47:07 allele.

13Primer mix 16: Specific PCR product of 155 bp in the B*27:68 and the B*15:201 alleles. Specific PCR product of 245 bp in the B*27:19, 27:30, 07:12, 07:14, 07:18:01-07:18:02, 13:01:01-13:01:05, 13:07N, 13:13, 13:17, 13:20-13:23, 13:25-13:26, 13:28-13:29, 13:36, 13:39, 35:15, 35:33, 35:88, 40:04, 40:30, 40:34, 40:59, 40:64, 40:68, 40:99, 40:120, 40:129, 40:137, 44:16, 44:21, 44:64:01-44:64:02, 48:17, 57:13, 57:25, C*03:34, C*15:42 allele.

14Primer mix 17: Specific PCR product of 100 bp in the B*27:14 and the B*44:20, 44:47, 44:100 and 51:85 alleles. Specific PCR product of 310 bp in the B*27:51 allele.

15Primer mix 18: Specific PCR product of 95 bp in the B*27:32 and the B*07:28, 08:14, 44:54 and 44:106 alleles. Specific PCR product of 175 bp in the B*27:24 and the B*40:31, 40:45, 40:80, 48:01:01-48:01:03, 48:04, 48:06-48:07, 48:09, 48:11, 48:15-48:16, 48:18-48:20, 48:22, 48:24 and 81:01-81:05 alleles. Specific PCR product of 415 bp in the B*27:49 allele.

16Primer mix 19: Specific PCR fragment of 95 bp in the B*27:35 and the B*38:22 alleles. Specific PCR fragment of 240 bp in the B*27:25, 27:38, 27:47, 27:50 and 27:63 and the B*15:129 alleles.

17Primer mix 20: Specific PCR fragment of 95 bp in the B*27:09 allele. Specific PCR fragment of 175 bp in the B*27:36 and the B*48:21 alleles. Specific PCR fragment of 215 bp in the B*27:25 and 27:45 and the B*15:129 alleles. Specific PCR fragment of 345 bp in the B*27:69 and the B*37:23 and 51:32 alleles.

18Primer mix 21: Specific PCR fragment of 110 bp in the B*27:04:01, 27:04:02?-27:04:03?, 27:06, 27:24-27:25, 27:39, 27:66N and 27:68-27:69 alleles. Specific PCR fragment of 160 bp in the B*27:39 allele.

19Primer mix 22: Specific PCR fragment of 165 bp in the B*27:55 allele Specific PCR fragment of 195 bp in the B*27:37 and the B*18:43 alleles. Specific PCR fragment of 235 bp in the B*27:15, 27:28, 27:62 and 27:71 and the B*18:02 and in the C*07:05 alleles. Specific PCR fragment of 375 bp in the B*27:26 and 27:31 and the B*82:01-82:03 alleles.

20Primer mix 24: Specific PCR fragment of 105 bp in the B*27:18 and 27:29 and the B*07:27, 07:50, 08:04, 08:17, 08:54, 15:03:01-15:03:03, 15:47, 15:54, 15:61-15:62, 15:64, 15:68-15:69, 15:91, 15:98, 15:103, 15:123, 15:127, 15:131-15:132, 15:151, 15:156, 15:158, 15:173, 18:37, 38:03, 39:02:01-39:02:02, 39:08, 39:13:01-39:13:02, 39:23, 39:39, 39:49, 40:12, 40:46, 40:93, 42:11, 44:40, 44:44, 48:01:01-48:05, 48:07-48:24, 52:16 and 55:18 alleles. Specific PCR fragment of 260 bp in the B*27:28 and 27:62 and the B*18:02 alleles.

21Primer mix 26: Specific PCR fragment of 105 bp in the B*27:52 allele. Specific PCR fragment of 145 bp in the B*27:64N allele. Specific PCR fragment of 235 bp in the B*27:72 allele.

22Primer mix 27: Specific PCR fragment of 225 bp in the B*27:66N allele. Specific PCR fragment of 290 bp in the B*27:58 allele. Specific PCR fragment of 320 bp in the B*27:57 allele.

23Primer mix 28: Specific PCR fragment of 145 bp in the B*27:64N and the B*40:118N alleles. Specific PCR fragment of 325 bp in the B*27:48 allele.

24Primer mix 29: Specific PCR fragment of 70 bp in the B*27:54 allele. Specific PCR fragment of 105 bp in the B*27:67 allele.

25Primer mix 30: Specific PCR fragment of 160 bp in the B*27:59N allele. Specific PCR fragment of 240 bp in the B*27:72 and 27:73 allele.

26Primer mix 31: Specific PCR fragment of 125 bp in the B*27:65N allele. Specific PCR fragment of 160 bp in the B*27:56 allele.

‘w’, might be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.

1The sequence of the B*27051 allele has been shown to be identical to B*27:05:02.

The sequence of the B*2722 allele has been shown to be identical to the corrected B*27:06 nucleotide sequence.

2Primer mix 10: Specific PCR product of 90 bp in the B*27:06, 27:35 and 27:41 and the B*15:129, 18:02 and 38:22 and in the C*07:05 alleles. Specific PCR product of 185 bp in the B*27:60 allele.

Primer mix 12: Specific PCR product of 310 bp in the B*27:43 and the B*35:113, 39:62 and 44:98 alleles. Specific PCR product of 425 bp in the B*27:13 allele.

Primer mix 13: Specific PCR product of 215 bp in the B*27:47 allele. Specific PCR product of 370 bp in the B*27:12 and 27:16 and in the B*40:75? alleles. Specific PCR product of 400 bp in the B*27:16 and B*27:53 alleles.

Primer mix 14: Specific PCR product of 120 bp in the B*27:34 and the B*40:02:07, 40:06:02 and 57:03:02 and in the C*02:23 and C*02:36 alleles. Specific PCR product of 345 bp in the B*27:17 allele.

Primer mix 15: Specific PCR product of 250 bp in the B*27:73 allele. Specific PCR product of 370 bp in the B*27:18 and 27:29 and in the B*18:01:01-18:06, 18:08-18:15, 18:17N-18:24, 18:26-18:28, 18:30-18:32, 18:34-18:52, 37:01:01-37:20, 37:22-37:25, 40:02:01-40:02:02, 40:02:04-40:06:03, 40:09?-40:11:02?, 40:14:01?-40:15?, 40:18?-40:19?, 40:20, 40:21?-40:22N?, 40:24?-40:38?, 40:39, 40:42?-40:50?, 40:52?-40:58?, 40:62?-40:65?, 40:67?, 40:69?, 40:70, 40:71?, 40:72:02?, 40:74?, 40:76?, 40:78?, 40:80?-40:88?, 40:89, 40:90?-40:93?, 40:94, 40:95?-40:96?, 40:97, 40:98?-40:102?, 40:104?-40:105?, 40:107?-40:121?, 40:122, 40:123?, 40:124:02?-40:137?, 40:141?, 40:142N-40:144N, 40:145?, 40:148?-40:149?, 40:151?, 40:154?, 40:156?-40:158? and 47:01:01:01-47:07 allele.

Primer mix 16: Specific PCR product of 155 bp in the B*27:68 and the B*15:201 alleles. Specific PCR product of 245 bp in the B*27:19, 27:30, 07:12, 07:14, 07:18:01-07:18:02, 13:01:01-13:01:05, 13:07N, 13:13, 13:17, 13:20-13:23, 13:25-13:26, 13:28-13:29, 13:36, 13:39, 35:15, 35:33, 35:88, 40:04, 40:30, 40:34, 40:59, 40:64, 40:68, 40:99, 40:120, 40:129, 40:137, 44:16, 44:21, 44:64:01-44:64:02, 48:17, 57:13, 57:25, C*03:34, C*15:42 allele.

Primer mix 17: Specific PCR product of 100 bp in the B*27:14 and the B*44:20, 44:47, 44:100 and 51:85 alleles. Specific PCR product of 310 bp in the B*27:51 allele.

Primer mix 18: Specific PCR product of 95 bp in the B*27:32 and the B*07:28, 08:14, 44:54 and 44:106 alleles. Specific PCR product of 175 bp in the B*27:24 and the B*40:31, 40:45, 40:80, 48:01:01-48:01:03, 48:04, 48:06-48:07, 48:09, 48:11, 48:15-48:16, 48:18-48:20, 48:22, 48:24 and 81:01-81:05 alleles. Specific PCR product of 415 bp in the B*27:49 allele.

Primer mix 19: Specific PCR fragment of 95 bp in the B*27:35 and the B*38:22 alleles. Specific PCR fragment of 240 bp in the B*27:25, 27:38, 27:47, 27:50 and 27:63 and the B*15:129 alleles.

Primer mix 20: Specific PCR fragment of 95 bp in the B*27:09 allele. Specific PCR fragment of 175 bp in the B*27:36 and the B*48:21 alleles. Specific PCR fragment of 215 bp in the B*27:25 and 27:45 and the B*15:129 alleles. Specific PCR fragment of 345 bp in the B*27:69 and the B*37:23 and 51:32 alleles.

Primer mix 21: Specific PCR fragment of 110 bp in the B*27:04:01, 27:04:02?-27:04:03?, 27:06, 27:24-27:25, 27:39, 27:66N and 27:68-27:69 alleles. Specific PCR fragment of 160 bp in the B*27:39 allele.

Primer mix 22: Specific PCR fragment of 165 bp in the B*27:55 allele Specific PCR fragment of 195 bp in the B*27:37 and the B*18:43 alleles. Specific PCR fragment of 235 bp in the B*27:15, 27:28, 27:62 and 27:71 and the B*18:02 and in the C*07:05 alleles. Specific PCR fragment of 375 bp in the B*27:26 and 27:31 and the B*82:01-82:03 alleles.

Primer mix 24: Specific PCR fragment of 105 bp in the B*27:18 and 27:29 and the B*07:27, 07:50, 08:04, 08:17, 08:54, 15:03:01-15:03:03, 15:47, 15:54, 15:61-15:62, 15:64, 15:68-15:69, 15:91, 15:98, 15:103, 15:123, 15:127, 15:131-15:132, 15:151, 15:156, 15:158, 15:173, 18:37, 38:03, 39:02:01-39:02:02, 39:08, 39:13:01-39:13:02, 39:23, 39:39, 39:49, 40:12, 40:46, 40:93, 42:11, 44:40, 44:44, 48:01:01-48:05, 48:07-48:24, 52:16 and 55:18 alleles. Specific PCR fragment of 260 bp in the B*27:28 and 27:62 and the B*18:02 alleles.

Primer mix 26: Specific PCR fragment of 105 bp in the B*27:52 allele. Specific PCR fragment of 145 bp in the B*27:64N allele. Specific PCR fragment of 235 bp in the B*27:72 allele.

Primer mix 27: Specific PCR fragment of 225 bp in the B*27:66N allele. Specific PCR fragment of 290 bp in the B*27:58 allele. Specific PCR fragment of 320 bp in the B*27:57 allele.

Primer mix 28: Specific PCR fragment of 145 bp in the B*27:64N and the B*40:118N alleles. Specific PCR fragment of 325 bp in the B*27:48 allele.

Primer mix 29: Specific PCR fragment of 70 bp in the B*27:54 allele. Specific PCR fragment of 105 bp in the B*27:67 allele.

Primer mix 30: Specific PCR fragment of 160 bp in the B*27:59N allele. Specific PCR fragment of 240 bp in the B*27:72 and 27:73 allele.

Primer mix 31: Specific PCR fragment of 125 bp in the B*27:65N allele. Specific PCR fragment of 160 bp in the B*27:56 allele.

‘w’, might be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.