PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*48

Prod. No:	101.546-06/06u

Lot No:    	16G

Expiry Date:    	2011-September-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 16 primer mixes used for HLA-B*48 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*48 alleles3 | Other amplified HLA-B alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 385 bp | 800 bp | *480101-4805, 4807-4815, 4817-4819 | *0817, 0838, 3803, 3804, 390201, 390202, 3908, 391301, 391302, 3922, 3923, 3949, 400101-400106, 4007, 4009?-4011?, 401401?-4015?, 4016, 4018?, 4019?, 4021?, 4022N?, 4023, 4024?, 4026?-4038?, 4042?-4050?, 4051, 4052?-4058?, 4059, 4060, 4061?-4065?, 4066, 4067?, 4071?, 407201-4073, 4074?-4076?, 4077, 4078?, 4079, 4080?-4088?, 4090?-4093?, 4095?, 4096?, 4098?, 4101-4108, 4211, 4418, 4501-4505, 4507-4509, 490101-4905, 5001, 5002, 5004 |
| 25,6 | 145 bp | 800 bp | *480101, 480102, 480301, 480302, 4806, 4807, 4809, 4811, 4815-4819 | *2736, 400101-400106, 4007, 4010, 4012, 4021-4023, 4025, 4030, 4031, 4033, 4034, 4036, 4038, 4042, 4043, 4045-4049, 4052, 4054, 4055, 4059-4061, 4063, 4066, 4067, 4069, 4073, 4074, 4076, 4079-4081, 4084, 4087, 4088, 4431, 4606, 8101-8104N |
| 3 | 175 bp | 800 bp | *480101, 480102, 4804, 4806, 4807, 4809, 4811, 4815, 4816, 4818, 4819 | *2724, 4031, 4045, 4080, 8101-8104N |
| 4 | 150 bp | 800 bp | *4802 | *130101, 130102, 1306, 1307N, 1312, 1313, 1317, 1320, 132201-1323, 1325, 1326, 1410, 1502, 1513, 1520, 1521, 152501, 1536, 1544, 1562, 1577, 1580, 1585, 1588, 1589, 9506, 9512, 9521, 9539, 9544, 9554, 1822, 2719, 2730, 350101-350403, 3506-350803, 3510-3517, 3519-3521, 3523-3530, 3533-3536, 3538-3542, 3545-3550, 3552, 3554-3557, 3559, 3561-3563, 3565Q, 3569-3571, 3574, 3576-3578, 3580-3585, 3590-3595, 370101-370105, 3703N-3706, 3708, 3710, 3711, 3713, 3714, 3942, 4028, 44020101-440205, 440208-4414, 4416, 4417, 4419N, 4421-4430, 4432-4440, 4442-4446, 4448-4452N, 4455-446402, 4466, 4467, 4469, 5104, 5142, 5146, 5156, 530101-5306, 5308-5313, 5315-5318, 5514, 5609, 5611, 5612, 570101-5710, 5712, 5714-5719, 580101, 580102, 5804, 5805, 5809-5815, 5817N, 5819, 5821, 8301 |
| 5 | 285 bp | 1070 bp | *480301, 480302, 4817 | *0707, 0712, 0714, 071801, 071802, 0777, 9538,1835, 400101-400106, 4007, 4010, 4012, 401401-401403, 4021-4023, 4025, 4033, 4036, 4038, 4042, 4043, 4046-4049, 4052, 4054, 4055, 4059-4063, 4065-4067, 4069, 407201-4074, 4076, 4077, 4079, 4081, 4084, 4087, 4088, 4108, 4431, 4606, Cw*0223, Cw*0738 |
| 6 | 170 bp | 1070 bp | *4805 |  |
| 7 | 385 bp | 1070 bp | *4806 | *070201-070207, 070209-0712, 0714-0753, 0755-0764, 0766-0772, 0775-0777, 080101-0809, 0811-0816, 0818-0837, 0840, 1401-1403, 1405-1410, 380101-380202, 3805-3819, 39010101, 39010102L, 390103-390106, 3903-3907, 3909-3912, 3914-3920, 3924-3948, 3950, 4201, 4202, 4204-4210, 4212, 670101, 670102, 7301, 8102 |
| 85,6,7 | 85, 225 bp | 1070 bp | *4807, 4816, 4817 | *4036, 4048, 4077 |
| 9 | 215 bp | 1070 bp | *4805, 4808, 4819 | *070201-070207, 070209, 0703, 070501-0706, 0708-0711, 0713, 0715-0717, 0720-0724, 0727-0733, 0735-0742, 0744, 0746, 0747, 0749N-0751, 0753-0765, 0767N-0772, 0775, 0776, 0806, 0820, 0840, 1507, 1545, 1568, 9526, 3566, 3707, 4015, 4016, 4032, 4098, 4612 |
| 10 | 240 bp | 800 bp | *4804, 4813 | *0753, 130101-1303, 1306-1309, 1311-1323, 1325, 1509, 1530, 1542, 1548, 1558, 1573, 1583, 1586, 9550, 1826, 2707, 2711, 2720, 2724, 2727, 2733, 2743, 350201w-350203w, 350401-350403, 3506, 350901, 350902, 3512, 3518, 3522, 3531, 3544, 3559, 3560, 3581w, 3583w, 3588, 3595w, 3712, 380101, 380201-3819, 39010101, 39010102L, 390103-390602, 3908-3914, 3916, 3918-3920, 3922-3924, 3926-3928, 3930-3942, 3944-3948, 3950, 400201-400205, 4004-400602, 4008, 4011, 4013, 4019, 4026-4029, 4035, 4037, 4039, 4040, 4050, 4051, 4053, 4056-4058, 4064, 4068, 4070, 4071, 4075, 4078, 4082, 4083, 4085, 4086, 4090-4097, 4106, 4208, 4410, 4414, 4462, 4611, 4618, 510101-510202, 510204-5116, 5119-512402, 5126-5136, 5138-5141N, 5143, 5144N, 5146, 5148-5165, 520101-5211, 5213, 5214, 5401-5405N, 5407, 5408N, 5410-5413, 5417-5419, 550101-5505, 5507-5513, 5515-5519, 5521, 5522, 5524-5526, 5528-5535, 5601, 5602, 5604-5608, 5610, 5612-5617, 5619N-5624, 5702-570302, 5707, 5709, 5712, 5717, 5808, 5820, 5901-5905, 670101-6702, 7801-7806, 8201, 8202 |
| 11 | 170 bp | 800 bp | *480101-4805, 4807-4819 | *0727, 0750, 0804, 0817, 150301, 1547, 1554, 1561, 1562, 1564, 1568, 1569, 1591, 1598, 9503, 9523, 9527, 9531, 9532, 9551, 9556, 9558, 180101-1803, 1805, 1806, 1808-1815, 1817N-1828, 1830-1832, 1835, 370101-3714, 3803, 390201, 390202, 3908, 391301, 391302, 3923, 3939, 3949, 4012, 4211 |
| 125,6 | 105 bp | 1070 bp | *4809 |  |
| 135,6,8 | 130 bp | 1070 bp | *4805, 4810, 4812, 4813, 4814w | *070501-0706, 0732, 0734, 0740, 0753, 0769, 080101-0806, 0808N-0813, 0815-0827, 0829-0836, 0838, 0840, 1303, 132201, 132202, 1509, 1530, 1542, 1548, 1558, 1573, 1583, 1586, 9550, 1826, 2707, 2711, 2720, 2727, 2733, 2743, 350201w-350203w, 350401-350403, 3506, 350901, 350902, 3512, 3518, 3522, 3531, 3544, 3559, 3560, 3581w, 3583w, 3587, 3588, 3595w, 3712, 380101, 380201-3819, 39010101, 39010102L, 390103-390602, 3908-3914, 3916, 3918-3920, 3922, 3924, 3926-3928, 3930-3942, 3945-3948, 3950, 400201-400205, 4004-400602, 4008, 4011, 4013-4016, 4019, 4026-4029, 4035, 4037, 4039, 4040, 4050, 4053, 4056-4058, 4064, 4068, 4070, 4071, 407201w, 407202w, 4075, 4077w, 4078, 4082, 4083, 4086, 4090, 4093-4097, 4101-410302, 4105-4108, 4201, 4202, 4204-4208, 4210-4212, 4410, 4414, 4462, 4611, 4618, 510101-510202, 510204-5116, 5119-512402, 5126, 5128-5136, 5138-5141N, 5143, 5144N, 5146, 5148-5165, 520101-5211, 5213, 5214, 5401-5405N, 5407, 5408N, 5410, 5412, 5413, 5417-5419, 550101-5505, 5507-5513, 5515-5522, 5524-5526, 5528-5535, 5601, 5602, 5604-5608, 5610, 5612-5617, 5619N-5624, 5702-570302, 5707, 5709, 5712, 5717, 5808, 5820, 5901-5905, 670101-6702, 7801-7806, 8201, 8202 |
| 146,9 | 95, 250 bp | 1070 bp | *4811, 4814 | *0709, 0711, 0717, 0828, 0835, 0837, 1507, 1555, 1568, 9526, 1814, 3505, 3551, 3558, 3566, 3572, 3589, 3597, 4003, 4209, 4612, 5314, 5818 |
| 155,6,10 | 140, 435 bp | 800 bp | *4812, 4814, 4818 | *0736, 0738, 0768, 0803, 1405, 1507, 1545, 1555, 1568, 9526, 1814, 2732, 3505, 3522, 3551, 3558, 3566, 3572, 3589, 3597, 380101, 380102, 3805-3807, 3809-3814, 3816, 3819, 3903, 3914, 3924, 3929, 3937, 4035, 4071, 4210, 4418, 4454, 4612, 490101, 490102, 4903-4905, 5164, 5314, 5818 |
| 165,6 | 120 bp | 1070 bp | *4805, 4808, 4815 | *070201-070207, 070209-071802, 0720-0724, 0726-0732, 0734-0739, 0741-0747, 0749N, 0750, 0752, 0754-0759, 0761-0772, 0775-0777, 9538, 3707, 4015, 4016, 4023, 4032, 4098, Cw*0223 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-B*48 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-B*48 SSP subtyping.

In addition, wells number 2, 3, 4, 10, 11 and 15 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band.

In the presence of a specific amplification the intensity of the control band often decreases.

3The B*4806 and B*8102 alleles give rise to identical amplification patterns. These two alleles can be separated by e.g. the HLA-B low resolution SSP kit.

The B*4810, B*0817 and B*4211 alleles give rise to identical amplification patterns. These alleles can be separated by e.g. the HLA-B low resolution SSP kit.

The B*4813 and B*3803, 390201-390202, 3908 and 391301-391302 give rise to identical amplification patterns. These alleles can be separated by e.g. the HLA-B low resolution SSP kit.

4Due to the sharing of sequence motifs between HLA-B alleles non-HLA-B*48 alleles will be amplified by primer mixes 1 to 5, 7 to 11 and 13 to 16. In addition, the Cw*0223 allele will be amplified by primer mixes 5 and 16, and the Cw*0738 allele will be amplified by primer mix 5.

5Primer mixes 2, 8, 12, 13, 15 and 16 have a tendency of giving rise to nonspecific amplifications.

6Short specific PCR fragments are less intense and not as sharp as longer specific bands.

7Primer mix 8: Specific PCR fragment of 85 bp in the B*4816 allele. Specific PCR fragment of 225 bp in the B*4807, 4817 and B*4036, 4048 and 4077 alleles.

8Primer mix 13 might faintly amplify the B*13xx alleles.

9Primer mix 14: Specific PCR fragment of 95 bp in the B*4814 and the B* 0709, 0711, 0717, 0828, 0835, 0837, 1507, 1555, 1568, 9526, 1814, 3505, 3551, 3558, 3566, 3572, 3589, 3597, 4003, 4209, 4612, 5314 and 5818 alleles. Specific PCR fragment of 250 bp in the B*4811 allele.

10Primer mix 15: Specific PCR fragment of 140 bp in the B*4812, 4814 and the B*0768, 1405, 1507, 1545, 1555, 1568, 9526, 1814, 2732, 3505, 3522, 3551, 3558, 3566, 3572, 3589, 3597, 3819, 3903, 3914, 3924, 3929, 3937, 4035, 4071, 4210, 4454, 4612, 5164, 5314 and 5818 alleles. Specific PCR fragment of 435 bp in the B*4818 and the B* 0736, 0738, 0803, 380101, 380102, 3805-3807, 3809-3814, 3816, 3819, 4418, 490101, 490102 and 4903-4905 alleles.

‘w’, might be weakly amplified.

‘?’, nucleotide sequence information not available for the primer matching sequence.

1The B*4806 and B*8102 alleles give rise to identical amplification patterns. These two alleles can be separated by e.g. the HLA-B low resolution SSP kit.

2The B*4810, B*0817 and B*4211 alleles give rise to identical amplification patterns. These alleles can be separated by e.g. the HLA-B low resolution SSP kit.

3The B*4813 and B*3803, 390201-390202, 3908 and 391301-391302 give rise to identical amplification patterns. These alleles can be separated by e.g. the HLA-B low resolution SSP kit.

4Primer mix 8: Specific PCR fragment of 85 bp in the B*4816 allele. Specific PCR fragment of 225 bp in the B*4807, 4817 and B*4036, 4048 and 4077 alleles.

Primer mix 13 might faintly amplify the B*13xx alleles.

Primer mix 14: Specific PCR fragment of 95 bp in the B*4814 and the B* 0709, 0711, 0717, 0828, 0835, 0837, 1507, 1555, 1568, 9526, 1814, 3505, 3551, 3558, 3566, 3572, 3589, 3597, 4003, 4209, 4612, 5314 and 5818 alleles. Specific PCR fragment of 250 bp in the B*4811 allele.

Primer mix 15: Specific PCR fragment of 140 bp in the B*4812, 4814 and the B*0768, 1405, 1507, 1545, 1555, 1568, 9526, 1814, 2732, 3505, 3522, 3551, 3558, 3566, 3572, 3589, 3597, 3819, 3903, 3914, 3924, 3929, 3937, 4035, 4071, 4210, 4454, 4612, 5164, 5314 and 5818 alleles. Specific PCR fragment of 435 bp in the B*4818 and the B* 0736, 0738, 0803, 380101, 380102, 3805-3807, 3809-3814, 3816, 3819, 4418, 490101, 490102 and 4903-4905 alleles.

‘?’, nucleotide sequence information not available for the primer matching sequence.

‘w’, may be weakly amplified.