PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*51

Prod. No:	101.561-24/03 – including Taq pol.

101.561-24u/03u – without Taq pol.

Lot No:    	30E

Expiry Date:    	2010-February-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ug/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 45 primer mixes used for HLA-B*51 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*51 alleles3 | Other amplified HLA-B alleles4 |
| --- | --- | --- | --- | --- |
| 15 | 105 bp | 800 bp | 510101-5106, 5108-5121, 5123, 5124, 5126-5146, 5148-5152 | 0832, 1807, 350101-350801, 350803-3518, 3521-3524, 3527, 3529-3545, 3548, 3550-3562, 3564-3571, 3574, 3575, 3577, 3579, 3580, 3581, 3583, 3584, 3806, 3807, 4406, 520601-520602, 530101-5308, 5310-5314, 7801-780202, 7804 |
| 25,6 | 95 bp | 800 bp | 510101-510108, 5103, 5104, 5106, 5107, 5111N-5114, 5116-5118, 5121, 5122, 5124, 5126-5130, 5132, 5133, 5135, 5137-5139, 5141N, 5143, 5145, 5146, 5148-5152 | 1401-1407N, 1537, 1538, 1815, 1819, 3521, 4028, 4051, 520101-5202, 5204-5209, 5306, 560501-5606, 5621, 5808, 7801-7803, 7805 |
| 3 | 265 bp | 1070 bp | 510201-510203, 5105, 5110, 5115, 5123, 5134, 5136, 5140 | 0809, 130201-1304, 1308Q, 1309, 1314, 1316, 1318, 1319, 1504, 1516, 1542, 1567, 1583, 1595, 9537, 2714, 3537, 3560, 390601-390602, 3933, 3934, 40060101-400602, 4044, 4053, 4070, 4075, 4101, 4105-4107, 4204, 4415, 4418, 4420, 4447, 4501-4507, 4611, 4901-4905, 5001, 5002, 5004, 5203, 5211, 5401-5405N, 5407, 5408N, 5410-5413, 550101-5503, 5505, 5507, 5509-5513, 5515-5529, 5601, 5607, 5608, 5613-5617, 5619N, 5620, 5901, 5902, 7804 |
| 46 | 255 bp | 1070 bp | 5103 |  |
| 56 | 270 bp | 1070 bp | 5104, 5146 | 1822, 3521, 3524, 3581, 3704, 4028, 5302, 5306, 5714, 5809 |
| 66 | 210 bp | 1070 bp | 5105weakly, 510901-5110, 5115, 5119, 5131, 5140 | 130201-1304, 1308Q, 1309, 1314, 1315, 1318, 1319, 2714, 3537, 3560, 390601-390602, 3933weakly, 3934, 40060101-400602, 4044, 4053, 4070, 4075, 4447, 4611, 5203, 5210, 5401-5405N, 5407, 5408N, 5410weakly, 5411-5413, 550201-550202, 5507, 5510, 5512, 5513, 5516, 5518, 5519, 5522, 5523, 5526, 5527, 5601, 5607, 5608, 5614-5617, 5619N, 5620, 5901, 5902, 7301, 7804 |
| 76 | 270 bp | 1070 bp | 5106, 5145 | 1401-1407N, 1537, 1538, 180101-1809, 1812-1815, 1817N-1820, 1823N-1828, 2728, 3932, 3943, 4051 |
| 85,6 | 105 bp | 800 bp | 5107 | 180101-1806, 1808-1815, 1817N-1828, 352001-352002, 3528, 3572, 370101-3705, 3707-3713, 4903, 520101-520104, 5203-5205, 5207-5211, 5309, 7805 |
| 95,6,7 | 85, 195, 215 bp | 1070 bp | 5108, 5117, 5120, 5135, 5144N | 3704 |
| 108 | 160, 245 bp | 1070 bp | 5110, 5121, 5136 | 0809, 1542, 1583, 2714, 3560, 390601-390602, 3934, 40060101-400602, 4044, 4053, 4070, 4075, 4101, 4105-4107, 4204, 5401, 5402, 5404, 5405N, 5407, 5408N, 5410, 5411-5413, 550101-5503, 5505, 5507, 5510-5513, 5515-5521, 5523, 5525-5529, 5901, 5902, 7301 |
| 11 | 250 bp | 1070 bp | 5110, 5116, 5131, 5134 | 130201-130204, 1308Q, 1309, 1314-1316, 1318, 1319, 2714, 40060101-400602, 4044, 4053, 4070, 4075, 5208, 5509, 5522, 5524, 7301 |
| 12 | 495 bp | 1070 bp | 5111N |  |
| 139 | 200 bp | 1070 bp | 5112 |  |
| 145,10 | 105, 125 bp | 800 bp | 511301-511302, 5120 | 0832, 9537, 1803, 3529, 3569, 3574-3576, 3584, 3585, 3713, 390601-390602, 3919, 3933, 3934, 4502, 5513, 5606, 7301, 7801, 7803 |
| 155,6,11 | 100, 230 bp | 800 bp | 5114, 5119 | 390601-390602 |
| 16 | 190 bp | 1070 bp | 5115, 5118, 5135 | 1303, 1573, 4071, 4410, 4415, 4418, 4501, 4504-4507, 4611, 4901-4903, 5001, 5002, 5004, 5403, 5601, 5602, 5604, 5607, 5608, 5613, 5614, 5616, 5617, 5620, 8201, 8202 |
| 175,6 | 105 bp | 1070 bp | 5122 | 3582, 3585, 3919, 7803 |
| 185,6,12 | 140, 220 bp | 800 bp | 5108, 5120, 5128, 5136, 5144N | 0809, 1583, 4101, 4105-4107, 4204, 4415, 4418, 4420, 4501-4507, 5520, 5613 |
| 195,6 | 145 bp | 800 bp | 5110, 5124 | 0809, 40060101-400602, 4044, 4053, 4070, 4075, 4101, 4105-4107, 4204, 5411, 5520, 5620, 5902, 7301 |
| 205 | 110 bp | 1070 bp | 5126 |  |
| 215,13 | 130, 185 bp | 1070 bp | 5127N, 5138 |  |
| 22 | 160 bp | 1070 bp | 510101, 510103-510201, 510203-5104, 5106-510901, 5110-5114, 5116-5124, 5126-5146, 5148-5152 | 1804, 4406, 5306, 7801, 780202, 7803 |
| 23 | 210 bp | 800 bp |  | 1804, 4058, 560501, 5606, 7801, 780202, 7803 |
| 24 | 210 bp | 1070 bp | 510101, 510103-510201, 510203-5104, 5106-510901, 5110-5114, 5116-5124, 5126-5146, 5148, 5149, 5151, 5152 | 4406, 4903, 520102, 520104-5203, 520601-520602, 5209, 5306, 5808 |
| 255,14 | 130, 175 bp | 1070 bp | 5130, 5138 |  |
| 265,15 | 105, 155 bp | 800 bp | 511301-511302, 5132, 5137 | 1304, 1504, 1516, 1567, 1595, 9537, 3537, 390601-390602, 3933, 3934, 4502, 4904, 4905, 5513, 5523, 7301 |
| 2716 | 205, 270, 350 bp | 800 bp | 5104, 5133, 5139, 5146 | 1822, 3521, 3524, 3581, 3704, 4028, 5302, 5306, 5714, 5809 |
| 2817 | 205, 255 bp | 1070 bp | 5123, 5133 | 4415, 4418, 4420, 4447, 4501-4503, 4505-4507, 5002 |
| 29 | 245 bp | 1070 bp | 510101-5103, 5105, 5107-510902, 5111N-5115, 5117-5120, 5122-5124, 5126-5130, 5132, 5133, 5135, 5137-5141N, 5143, 5144N, 5148-5152 | 1303, 1304, 1504, 1516, 1567, 1595, 9537, 3537, 3933, 4415, 4418, 4420, 4447, 4501-4507, 4611, 4901-4905, 5001, 5002, 5004, 520101-5207, 5209-5211, 5403, 5601, 560501-5608, 5613-5617, 5620, 5621, 5808, 7801-7805 |
| 305 | 105 bp | 800 bp | 5106 | 070503weakly, 150102, 1509, 400106, 4026 |
| 315,18 | 105, 225 bp | 800 bp | 5105, 511301-511302, 5129, 5137 | 1304, 1318, 1504, 1516, 1567, 1595, 9537, 3537, 390601-390602, 3933, 3934, 4502, 4904, 4905, 5410, 5509, 5513, 5521, 5523, 7301 |
| 32 | 165 bp | 1070 bp | 5116, 5131, 5134 | 070503, 400106, 5208 |
| 33 | 195 bp | 1070 bp | 5141N |  |
| 34 | 260 bp | 1070 bp | 5142 | 3545, 3571, 44020101-4414, 4417, 4419N, 4421-4430, 4432-4436, 4438-4440, 4443-4446, 4448-4453, 4455-4459, 5707, 8301 |
| 35 | 225 bp | 1070 bp |  | 3538, 370101-370104, 3703N-3706, 3708, 3710-3713, 44020101-440204, 4405, 4406, 4408, 4409, 4411, 4412, 4414, 4416, 4417, 4419N, 4421-4425, 4427, 4433, 4434, 4442, 4444, 4448, 4449, 4451-4453, 4455, 4458N, 4459, 5709, 8301 |
| 36 | 215 bp | 1070 bp | 5143 |  |
| 37 | 165 bp | 1070 bp | 5144N |  |
| 38 | 205 bp | 1070 bp | 5137, 5145 | 1538, 180101-1809, 1812-1815, 1817N-1820, 1822-1825, 1827, 1828, 3521, 3524, 3943, 5302, 5306, 5714, 5809 |
| 39 | 260 bp | 1070 bp | 5146 |  |
| 40 | 185 bp | 1070 bp | 510101-5124, 5126-5146, 5148, 5149, 5151, 5152 | 0736, 0738, 1513, 15170101-151702, 1524, 1587, 4406, 4818, 4903, 520101-5211, 530101-5302, 5304-5308, 5310, 5314, 570101-5711, 5713-5716, 5801, 5802, 5804-5816 |
| 41 | 220 bp | 1070 bp | 5148 |  |
| 425 | 135 bp | 800 bp | 5149 |  |
| 43 | 215 bp | 800 bp | 5150 |  |
| 44 | 290 bp | 800 bp | 5151 |  |
| 45 | 190 bp | 1070 bp | 5152 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-B*49 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers, e.g. the primers in wells number 4, 5, 6, 7, 8, 9, 15, 17, 18 and 19 have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Wells number 1 and 2 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-B*51 subtyping.

In addition, wells number 8, 14, 15, 18, 19, 23, 26, 27, 30, 31, 42 to 44 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several HLA-B alleles fourth exon nucleotide sequences are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in the fourth exon are conserved within allelic groups.

4Due to the sharing of sequence motifs between HLA-B alleles many non-HLA-B*51 alleles will be amplified by many the HLA-B*51 primer mixes.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6Primer mixes 2, 4, 5, 6, 7, 8, 9, 15, 17, 18 and 19 have a tendency to giving rise to nonspecific amplifications.

7Primer mix 9: Specific PCR fragment of 85 bp in the B*5108, 5120, 5144N and B*3704 alleles. Specific PCR fragment of 195 bp in the B*5135 allele. Specific PCR fragment of 215 bp in the B*5117 allele.

8Primer mix 10: Specific PCR fragment of 160 bp in the B*5110 and B*2714, 40060101-400602, 4044, 4053, 4070, 4075 and 7301 alleles. Specific PCR fragment of 245 bp in the B*5121, 5136 and B*0809, 1542, 1583, 3560, 390601-390602, 3934, 4101, 4105-4107, 4204, 5401, 5402, 5404, 5405N, 5407, 5408N, 5410-5413, 550101-5503, 5505, 5507, 5510-5513, 5515-5521, 5523, 5525-5529 and 5901-5902 alleles.

9Primer mix 13 has a tendency of primer oligomer formation.

10Primer mix 14: Specific PCR fragment of 105 bp in the B*511301-511302 and B*390601-390602, 3933, 3934, 4502 and 7301 alleles. Specific PCR fragment of 125 bp in the B*5120 and B*0832, 9537, 1803, 3529, 3569, 3574-3576, 3584, 3585, 3713, 3919, 5513, 5606, 7801 and 7803 alleles.

11Primer mix 15: Specific PCR fragment of 100 bp in the B*5114 allele. Specific PCR fragment of 230 bp in the B*5119 and B*390601-390602 alleles.

12Primer mix 18: Specific PCR fragment of 140 bp in the B*5128 allele. Specific PCR fragment of 220 bp in the B*5108, 5120, 5136, 5144N and B*0809, 1583, 4101, 4105-4107, 4204, 4415, 4418, 4420, 4501-4507, 5520 and 5613 alleles.

13Primer mix 21: Specific PCR fragment of 130 bp in the B*5138 allele. Specific PCR fragment of 185 bp in the B*5127N allele.

14Primer mix 25: Specific PCR fragment of 130 bp in the B*5138 allele. Specific PCR fragment of 175 bp in the B*5130 allele.

Primer mix 25 has a tendency of giving rise to primer dimer formation.

15Primer mix 26: Specific PCR fragment of 105 bp in the B*511301-511302, 5137 and B*1304, 1504, 1516, 1567, 1595, 9537, 3537, 390601-390602, 3933, 3934, 4502, 4904, 4905, 5513, 5523 and 7301 alleles. Specific PCR fragment of 155 bp in the B*5132 allele.

16Primer mix 27: Specific PCR fragment of 205 bp in the B*5133 allele. Specific PCR fragment of 270 bp in the B*5104, 5146 and B*1822, 3521, 3524, 3581, 3704, 4028, 5302, 5306, 5714 and 5809 alleles. Specific PCR fragment of 350 bp in the B*5139 allele.

17Primer mix 28: Specific PCR fragment of 205 bp in the B*5133 allele. Specific PCR fragment of 255 bp in the B*5123 and B*4415, 4418, 4420, 4447, 4501-4503, 4505-4507, 5002.

18Primer mix 31: Specific PCR fragment of 105 bp in the B*511301-511302, 5137 and B*1304, 1516, 1567, 1595, 3537, 390601-390602, 3934, 4502, 4904, 4905, 5513, 5523 and 7301 alleles. Specific PCR fragment of 225 bp in the B*5105, 5129 and B*1318, 1504, 9537, 3933, 5410, 5509 and 5521 alleles.

1The B*5125 nucleotide sequence has been shown to be identical to B*5122.

The B*5147 nucleotide sequence has been renamed to B*510902.

2Primer mix 9: Specific PCR fragment of 85 bp in the B*5108, 5120, 5144N and B*3704 alleles. Specific PCR fragment of 195 bp in the B*5135 allele. Specific PCR fragment of 215 bp in the B*5117 allele.

Primer mix 10: Specific PCR fragment of 160 bp in the B*5110 and B*2714, 40060101-400602, 4044, 4053, 4070, 4075 and 7301 alleles. Specific PCR fragment of 245 bp in the B*5121, 5136 and B*0809, 1542, 1583, 3560, 390601-390602, 3934, 4101, 4105-4107, 4204, 5401, 5402, 5404, 5405N, 5407, 5408N, 5410-5413, 550101-5503, 5505, 5507, 5510-5513, 5515-5521, 5523, 5525-5529 and 5901-5902 alleles.

Primer mix 14: Specific PCR fragment of 105 bp in the B*511301-511302 and B*390601-390602, 3933, 3934, 4502 and 7301 alleles. Specific PCR fragment of 125 bp in the B*5120 and B*0832, 9537, 1803, 3529, 3569, 3574-3576, 3584, 3585, 3713, 3919, 5513, 5606, 7801 and 7803 alleles.

Primer mix 15: Specific PCR fragment of 100 bp in the B*5114 allele. Specific PCR fragment of 230 bp in the B*5119 and B*390601-390602 alleles.

Primer mix 18: Specific PCR fragment of 140 bp in the B*5128 allele. Specific PCR fragment of 220 bp in the B*5108, 5120, 5136, 5144N and B*0809, 1583, 4101, 4105-4107, 4204, 4415, 4418, 4420, 4501-4507, 5520 and 5613 alleles.

Primer mix 21: Specific PCR fragment of 130 bp in the B*5138 allele. Specific PCR fragment of 185 bp in the B*5127N allele.

Primer mix 25: Specific PCR fragment of 130 bp in the B*5138 allele. Specific PCR fragment of 175 bp in the B*5130 allele.

Primer mix 26: Specific PCR fragment of 105 bp in the B*511301-511302, 5137 and B*1304, 1504, 1516, 1567, 1595, 9537, 3537, 390601-390602, 3933, 3934, 4502, 4904, 4905, 5513, 5523 and 7301 alleles. Specific PCR fragment of 155 bp in the B*5132 allele.

Primer mix 27: Specific PCR fragment of 205 bp in the B*5133 allele. Specific PCR fragment of 270 bp in the B*5104, 5146 and B*1822, 3521, 3524, 3581, 3704, 4028, 5302, 5306, 5714 and 5809 alleles. Specific PCR fragment of 350 bp in the B*5139 allele.

Primer mix 28: Specific PCR fragment of 205 bp in the B*5133 allele. Specific PCR fragment of 255 bp in the B*5123 and B*4415, 4418, 4420, 4447, 4501-4503, 4505-4507, 5002.

Primer mix 31: Specific PCR fragment of 105 bp in the B*511301-511302, 5137 and B*1304, 1516, 1567, 1595, 3537, 390601-390602, 3934, 4502, 4904, 4905, 5513, 5523 and 7301 alleles. Specific PCR fragment of 225 bp in the B*5105, 5129 and B*1318, 1504, 9537, 3933, 5410, 5509 and 5521 alleles.

‘w’, might be weakly amplified.