PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*55

Prod. No:	101.570-06/06u

Lot No:    	55E

Expiry Date:    	2010-May-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ug/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 24 primer mixes used for HLA-B*55 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*55 alleles | Other amplified HLA Class I alleles3 |
| --- | --- | --- | --- | --- |
| 15 | 400 bp | 800 bp | 550101-5505, 5507-5517, 5519-5530 | 3576, 5401-5406, 5408N-5413, 5601-5607, 5608weakly, 5609-5613, 5615, 5616, 5618-5622, 8101, 8103?, 8104?, 8201, 8202, 8301 |
| 24 | 125 bp | 1070 bp | 550101-5503, 5505, 5507, 5509-5513, 5515, 5516, 5518, 5519, 5521-5530 | 1301-1304, 1306-1309, 1311-1320, 1516, 1520, 1534, 1542, 1562, 1567, 1585, 1586, 1595, 9537, 1822, 2714, 350101-350803, 3510, 3511, 3513-3515, 3519-3521, 3523-3530, 3533-3538, 3540N-3542, 3545-3550, 3552, 3954-3558, 3560, 3562, 3563, 3565Q, 3566, 356801-3572, 3574-3578, 3580-3585, 4028, 4410, 4415, 4418, 4448, 4501-4508, 4611, 4802, 4901-4905, 5001, 5002, 5115, 530101-5306, 5308-5316, 5401-5405N, 5407, 5408N, 5410, 5412, 55413, 5601, 5602, 5607-5611, 5613-5617, 5619N, 5622, 5623, 5705, 580101-5802, 5804-5807, 5809-5817N, 5901, 8201, 8202 |
| 3 | 150 bp | 1070 bp | 550101-550104, 5503, 5505, 5509weakly, 5511, 5515, 5524, 5525, 5529 | 1316, 1320, 1542 |
| 4 | 235 bp | 1070 bp | 5503 | 0815, 3574, 4073, 460101-4604, 4606-4614 |
| 5 | 235 bp | 800 bp | 5504 | 0719, 0731, 0734, 0743, 080101-0808N, 0810, 0813-0815, 0817-0820, 0822-0824, 0826-0836, 1405, 1814, 1822weakly, 3587, 3709, 3903, 3914, 3924, 3929, 3937, 4039, 4102, 4104, 4201, 4202, 420501-4209, Cw*0808 |
| 64,6 | 100 bp | 1070 bp | 5505 |  |
| 7 | 180 bp | 1070 bp | 5508 | 0720, 0724, 0760, 0821, 0825, 1509, 1510, 1530, 1537, 1545, 1548, 1563, 1590, 1599, 350201-350202, 350401-350402, 350901-350902, 3512, 3518, 3522, 3534, 3539, 3544, 3581, 3583, 4005, 4026, 4028, 4063, 510101-510902, 5111N, 5112, 5118-5120, 5122-512402, 5126-5130, 5132, 5133, 5135, 5138-5141N, 5143, 5144N, 5146, 5148-5155, 520101-5207, 5209-5212, 560501-5606, 5615, 5621, 5702-570302, 5705, 5707, 5709, 5712, 5808, 7801-7805 |
| 84,5,7 | 105, 425 bp | 800 bp | 5512, 5513 | 9537, 390601-390602, 3933, 3934, 4086, 4502, 511301-511302, 5622, 7301 |
| 98 | 215, 325 bp | 1070 bp | 5511, 5514, 5516 | 4030, 4034, 4202, 4209, 4506, 5402, 5712 |
| 10 | 140 bp | 1070 bp | 5507 | 5401, 5403, 5404, 5406-5413 |
| 114,9 | 125, 180 bp | 1070 bp | 5509, 5515, 5522, 5524 | 1301-130204, 1307N-1309, 1311, 1314-1320, 4048 |
| 12 | 210 bp | 1070 bp | 5510 | 070201-070207, 0704-0707, 0709, 0711, 0712, 0714, 0715, 0717-0726, 0728, 0730, 0731, 0733-0736, 0739-0749N, 0751-0764, 4201, 4202, 4204-4206, 4208, 670101-670102, 8101-8104N |
| 13 | 150 bp | 1070 bp | 550201-550202, 5507, 5510, 5512, 5516, 5518, 5519, 5522, 5526, 5530 | 1301-1303, 1306-1309, 1311, 1312, 1314, 1315, 1317, 1318weakly, 1319, 1586, 3560, 4048, 4071, 4410, 4611, 5115, 5401-5403, 5405N, 5407, 5408N, 5410weakly,5412, 5413, 5601, 5602, 5604, 5607, 5608, 5610, 5614, 5616, 5617, 5619N, 5620, 5623, 5901 |
| 14 | 215 bp | 800 bp |  | 150104, 370104, 5401-5413 |
| 15 | 245 bp | 1070 bp | 550101-5503, 5505, 5507, 5510-5513, 5515-5521, 5523, 5525-5530 | 0809, 1542, 1583, 3560, 390601-390602, 3934, 4101, 4105-4107, 4204, 4508, 5121, 5136, 5401, 5402, 5404, 5405N, 5407, 5408N, 5410-5413, 5623, 5901, 5902 |
| 16 | 245 bp | 1070 bp |  | 1303, 1304, 1504, 1516, 1567, 1595, 9537, 3537, 3933, 4415, 4418, 4420, 4447, 4501-4507, 4611, 4901-4905, 5001, 5002, 5004, 510101-5103, 5105, 5107-510902, 5111N-5115, 5117-5120, 5122-512402, 5126-5130, 5132, 5133, 5135, 5137-5141N, 5143, 5144N, 5148-5155, 520101-5207, 5209-5212, 5403, 5601, 560501-5608, 5613-5617, 5620-5622, 5808, 7801-7805 |
| 174 | 105 bp | 1070 bp | 5517, 5520, 5527, 5528 | 0809, 1583, 2714, 40060101-400602, 4044, 4053, 4070, 4075, 4083, 4101, 4105-4107, 4204, 4420, 4447, 510101-5103, 5105, 5107-5112, 5114, 5116-5124, 5126-5136, 5138-5141N, 5143, 5144N,, 5148-5155, 520101-5212, 5404, 5411, 560501-5606, 5615, 5621, 5808, 5902, 7801-7805 |
| 1810 | 215, 310, 395 bp | 800 bp | 5518, 5519, 5525 |  |
| 194 | 205 bp | 800 bp | 5530 |  |
| 205,11 | 95, 220 bp | 1070 bp | 5520, 5526 | 0809, 1583, 4101, 4105-4107, 4204, 4415, 4418, 4420, 4501-4508, 5108, 5120, 5136, 5144N, 5613 |
| 21 | 270 bp | 800 bp | 5510 | 180101-1803, 1805-1815, 1818-1828, 3525, 370101-3713, 5616, 5812, 8101, 8103?, 8104?, 8201, 8202, 8301 |
| 22 | 225 bp | 1070 bp | 5509, 5521 | 1318, 1504, 9537, 3933, 5105, 5129, 5154, 5410 |
| 2312 | 165, 220 bp | 800 bp | 5521, 5529 | 1504, 9537 |
| 244 | 100 bp | 1070 bp | 5513, 5523, 5527 | 1304, 1504, 1516, 1567, 1595, 9537, 3537, 390601-390602, 3933, 3934, 4044, 4086, 4420, 4447, 4502, 4904, 4905, 511301-511302, 5137, 5212, 5622, 7301 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-B*55 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the HLA-B*55 subtyping.

In addition, wells number 5, 8, 14, 18, 19, 21 and 23 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

## 3Due to the sharing of sequence motifs between HLA-B alleles non-HLA-B*55 alleles will be amplified by primer mixes 1 to 5, 7 to 17 and 20 to 24. In addition, the Cw*0808 allele will be amplified by primer mix 5.

4Specific PCR fragments shorter than 125 base pairs have a lower intensity than longer PCR bands.

5Primer mixes 1 and 8 might have a tendency of giving rise to primer oligomer formation.

6Primer mix 6 has a tendency of giving rise to non-specific amplifications.

7Primer mix 8: Specific PCR fragment of 105 bp in the B*5513 and B*9537, 390601-390602, 3933, 3934, 4086, 4502, 511301-511302, 5622 and 7301 alleles. Specific PCR fragment of 425 bp in the B*5512 allele.

8Primer mix 9: Specific PCR fragment of 215 bp in the B*5516 and B*4202, 4209, 4506 and 5402 alleles. Specific PCR fragment of 325 bp in the B*5511, 5514  and B*4030, 4034 and 5712 alleles.

9Primer mix 11: Specific PCR fragment of 125 bp in the B*5515 allele. Specific PCR fragment of 180 bp in the B*5509, 5522, 5524 and B*1301-130204, 1307N-1309, 1311, 1314-1320 and 4048 alleles.

10Primer mix 18: Specific PCR fragment of 215 bp in the B*5525 allele. Specific PCR fragment of 310 bp in the B*5519 allele. Specific PCR fragment of 395 bp in the B*5518 allele.

11Primer mix 20: Specific PCR fragment of 220 bp in the B*5520 and B*0809, 1583, 4101, 4105-4107, 4204, 4415, 4418, 4420, 4501-4508, 5108, 5120, 5136, 5144N and 5613 alleles. Specific PCR fragment of 95 bp in the B*5526 allele.

12Primer mix 23: Specific PCR fragment of 165 bp in the B*5529 allele. Specific PCR fragment of 220 bp in the B*5521 and B*1504 and 9537 alleles.

*?*, nucleotide sequence of the primer matching region is not known.

1The B*5506 sequence shown to contain errors and be identical to B*5504.

1Primer mix 8: Specific PCR fragment of 105 bp in the B*5513 and B*9537, 390601-390602, 3933, 3934, 4086, 4502, 511301-511302, 5622 and 7301 alleles. Specific PCR fragment of 425 bp in the B*5512 allele.

Primer mix 9: Specific PCR fragment of 215 bp in the B*5516 and B*4202, 4209, 4506 and 5402 alleles. Specific PCR fragment of 325 bp in the B*5511, 5514  and B*4030, 4034 and 5712 alleles.

Primer mix 11: Specific PCR fragment of 125 bp in the B*5515 allele. Specific PCR fragment of 180 bp in the B*5509, 5522, 5524 and B*1301-130204, 1307N-1309, 1311, 1314-1320 and 4048 alleles.

Primer mix 18: Specific PCR fragment of 215 bp in the B*5525 allele. Specific PCR fragment of 310 bp in the B*5519 allele. Specific PCR fragment of 395 bp in the B*5518 allele.

Primer mix 20: Specific PCR fragment of 220 bp in the B*5520 and B*0809, 1583, 4101, 4105-4107, 4204, 4415, 4418, 4420, 4501-4508, 5108, 5120, 5136, 5144N and 5613 alleles. Specific PCR fragment of 95 bp in the B*5526 allele.

Primer mix 23: Specific PCR fragment of 165 bp in the B*5529 allele. Specific PCR fragment of 220 bp in the B*5521 and B*1504 and 9537 alleles.

‘w’, may be weakly amplified.

‘?’, the nucleotide sequence of the primer matching region is not know.