PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*55

Prod. No:	101.570-06/06u

Lot No:    	78K

Expiry Date:    	2013-July-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 30 primer mixes used for HLA-B*55 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*55 alleles | Other amplified HLA Class I alleles3 |
| --- | --- | --- | --- | --- |
| 15 | 400 bp | 800 bp | *55:01:01-55:05, 55:07-55:17, 55:19-55:33, 55:35-55:46, 55:48 | *07:65, 35:76, 44:90, 54:01-54:06, 54:08N-54:23, 56:01:01-56:07, 56:08w, 56:09-56:13, 56:15-56:16, 56:18-56:22, 56:24-56:30, 81:01, 81:03?-81:04N?, 82:01-82:03, 83:01 |
| 24 | 125 bp | 1070 bp | *55:01:01-55:03, 55:05, 55:07, 55:09-55:13, 55:15-55:16, 55:18-55:19, 55:21-55:37, 55:39-55:48 | *13:01:01-13:04, 13:06-13:09, 13:11-13:20, 13:22:01-13:23, 13:25-13:34, 13:36-13:40, 15:16, 15:20, 15:34, 15:42, 15:62, 15:67, 15:85-15:86, 15:95, 15:137, 15:194, 18:22, 18:52, 27:14, 35:01:01:01-35:08:04, 35:10-35:11:02, 35:13-35:15, 35:19-35:21, 35:23-35:30, 35:33-35:38, 35:40N-35:42:02, 35:45-35:50, 35:52, 35:54-35:58, 35:60, 35:62-35:63, 35:65Q-35:66, 35:68:01-35:72, 35:74-35:78, 35:80-35:85, 35:89-35:98, 35:100-35:101:02, 35:103-35:112, 35:115-35:116, 35:119-35:124, 35:126-35:134N, 35:136-35:148, 35:150-35:151, 40:28, 44:10, 44:15, 44:18, 44:48, 45:01-45:13, 46:11, 46:18, 48:02:01-48:02:02, 49:01:01-49:15, 50:01:01, 50:02, 50:05-50:12, 51:15, 51:56, 53:01:01-53:06, 53:08:01-53:24, 54:01-54:05N, 54:07-54:08N, 54:10, 54:12-54:14, 54:16-54:23, 56:01:01-56:01:03, 56:02, 56:07-56:11, 56:13-56:17, 56:19N, 56:22-56:26, 56:28N-56:30, 57:05, 58:01:01-58:01:02, 58:01:04-58:02, 58:04-58:07, 58:09, 58:11-58:13, 58:15-58:19, 58:21-58:26, 58:28-58:31N, 59:01, 59:03-59:05, 82:01-82:03, C*06:20, C*07:81 |
| 3 | 150 bp | 1070 bp | *55:01:01-55:01:06, 55:03, 55:05, 55:09w, 55:11, 55:15, 55:24-55:25, 55:29, 55:31, 55:33, 55:36, 55:38, 55:40, 55:44-55:45 | *07:78w, 13:16, 13:20, 15:42, 51:62, 51:106, 54:20w, 56:25 |
| 4 | 235 bp | 1070 bp | *55:03 | *08:15, 35:74, 40:73, 46:01:01-46:04, 46:06-46:26 |
| 5 | 235 bp | 800 bp | *55:04 | *07:19, 07:31, 07:34, 07:43, 08:01:01-08:05, 08:07-08:08N, 08:10, 08:13-08:15, 08:17-08:20, 08:22-08:24, 08:26-08:39, 08:41-08:48, 08:50-08:59, 08:61-08:66, 14:05, 14:13, 18:14, 18:22w, 35:87, 37:09, 38:19, 39:03, 39:14, 39:24, 39:29, 39:37, 40:39, 41:02:01-41:02:03, 41:04, 41:10-41:11, 41:13, 41:15, 42:01:01-42:02, 42:05:01-42:12, 42:14, C*08:08 |
| 64,6 | 100 bp | 1070 bp | *55:05 |  |
| 7 | 180 bp | 1070 bp | *55:08 | *07:20, 07:24, 07:60, 07:100, 08:21, 08:25, 15:09-15:10:02, 15:30, 15:37, 15:45, 15:48, 15:63, 15:90, 15:99, 15:150, 35:02:01-35:02:04, 35:04:01-35:04:03, 35:09:01-35:09:02, 35:12:01-35:12:02, 35:18, 35:22, 35:34, 35:39, 35:44, 35:81, 35:83, 35:95, 35:129N, 35:149, 40:05, 40:26, 40:28, 40:63, 40:92, 44:62, 44:77, 44:82, 44:107, 51:01:01-51:01:14, 51:01:16-51:09:02, 51:11N-51:12, 51:18-51:20, 51:22-51:24:04, 51:26-51:30, 51:32-51:33, 51:35, 51:38-51:41N, 51:43-51:44N, 51:46, 51:48-51:61, 51:64-51:80, 51:83-51:84, 51:86-51:91, 51:94-51:96, 51:98N-51:100, 51:102-51:105, 52:01:01-52:07, 52:09-52:13, 52:15-52:22, 53:19, 56:05:01-56:06, 56:15, 56:21, 57:02:01-57:03:02, 57:05, 57:07, 57:09, 57:12, 57:17, 57:28N, 58:08, 58:28, 78:01-78:06, C*03:81 |
| 84,8 | 105 bp, 170 bp, 425 bp | 800 bp | *55:12-55:13, 55:43 | *15:137, 39:06:01-39:06:02, 39:33-39:34, 39:50, 39:57, 39:62, 40:86, 45:02, 50:09, 51:13:01-51:13:02, 51:92, 52:14, 56:22, 59:03, 73:01-73:02 |
| 95,9 | 215 bp, 375 bp | 1070 bp | *55:11, 55:14, 55:25w |  |
| 10 | 140 bp | 1070 bp | *55:07 | *54:01, 54:03-54:04, 54:06-54:23, C*05:30 |
| 114,10 | 90 bp, 125 bp, 180 bp | 1070 bp | *55:09, 55:15, 55:22, 55:24, 55:48 | *07:78, 13:01:01-13:02:09, 13:07N-13:09, 13:11, 13:14-13:20, 13:22:01-13:23, 13:25, 13:27-13:34, 13:36-13:40, 40:48, 45:10, 49:07 |
| 12 | 210 bp | 1070 bp | *55:10 | *07:02:01-07:02:20, 07:04-07:07, 07:09, 07:11-07:12, 07:14-07:15, 07:17-07:26, 07:28, 07:30-07:31, 07:33-07:36, 07:39-07:49N, 07:51-07:64, 07:66-07:68:02, 07:73-07:82, 07:84, 07:87-07:117, 38:26, 42:01:01-42:01:02, 42:04-42:06, 42:08, 42:10, 42:12-42:14, 67:01:01-67:01:02, 67:03, 81:01-81:04N |
| 13 | 150 bp | 1070 bp | *55:02:01-55:02:06, 55:07, 55:10, 55:12, 55:16, 55:18-55:19, 55:22, 55:26, 55:30, 55:34-55:35, 55:37w, 55:39, 55:41-55:43, 55:47-55:48 | *13:01:01-13:03, 13:06-13:09, 13:11-13:12, 13:14-13:15, 13:17, 13:18w, 13:19, 13:22:01-13:23, 13:25, 13:27-13:30, 13:32-13:34, 13:36-13:40, 15:86, 35:60, 40:48, 40:71, 44:10, 46:11, 46:18, 49:11, 51:15, 54:01-54:03, 54:05N, 54:07-54:08N, 54:10w, 54:12-54:13, 54:17-54:19, 54:21-54:23, 56:01:01-56:02, 56:04, 56:07-56:08, 56:10, 56:14, 56:16-56:17, 56:19N-56:20, 56:23-56:24, 56:26-56:29, 59:01, 59:04-59:05 |
| 14 | 215 bp | 800 bp |  | *07:02:19, 15:01:04, 37:01:04, 40:94, 51:01:18, 54:01-54:23, 58:01:08 |
| 15 | 245 bp | 1070 bp | *55:01:01-55:03, 55:05, 55:07, 55:10-55:13, 55:15-55:21, 55:23, 55:25-55:48 | *08:09, 15:42, 15:83, 35:60, 39:06:01-39:06:02, 39:34, 39:57, 39:62, 41:01, 41:05-41:07, 41:09, 41:12, 41:14, 41:16, 42:04, 45:08, 46:18, 51:21, 51:36, 51:101, 54:01-54:02, 54:04-54:05N, 54:07-54:08N, 54:10-54:23, 56:23, 59:01-59:03, 59:05, 78:07 |
| 16 | 245 bp | 1070 bp |  | *13:03-13:04, 15:04, 15:16, 15:67, 15:95, 15:137, 15:155, 35:37, 39:33, 44:15, 44:18, 44:20, 44:47, 44:100, 45:01-45:07, 45:09, 45:11-45:13, 46:11, 49:01:01-49:06, 49:08-49:15, 50:01:01-50:02, 50:04-50:11, 51:01:01-51:03, 51:05, 51:07:01-51:09:02, 51:11N-51:15, 51:17-51:20, 51:22-51:24:04, 51:26-51:30, 51:32-51:33, 51:35, 51:37-51:41N, 51:43-51:44N, 51:48-51:55, 51:57-51:58, 51:60-51:61, 51:63, 51:65-51:80, 51:83-51:92, 51:94-51:100, 51:102-51:106, 52:01:01-52:07, 52:09-52:22, 54:03, 56:01:01-56:01:04, 56:05:01-56:08, 56:13-56:17, 56:20-56:22, 56:24-56:30, 58:08, 59:04, 78:01-78:06 |
| 174 | 105 bp | 1070 bp | *55:17, 55:20, 55:27-55:28 | *07:84, 08:09, 13:35, 15:83, 27:14, 40:06:01:01-40:06:03, 40:44, 40:53, 40:70, 40:75, 40:83, 40:93, 40:95-40:96, 40:103, 40:109-40:110, 40:127, 40:131, 40:148, 41:01, 41:05-41:07, 41:09, 41:12, 41:14, 41:16, 42:04, 44:20, 44:47, 44:100, 51:01:01-51:03, 51:05, 51:07:01-51:12, 51:14, 51:16-51:24:04, 51:26-51:34, 51:36, 51:38-51:41N, 51:43-51:44N, 51:48-51:55, 51:57-51:58, 51:60-51:61, 51:65-51:80, 51:82-51:91, 51:93-51:96, 51:98N, 51:100-51:105, 52:01:01-52:13, 52:15-52:22, 54:04, 54:11, 54:15, 56:05:01-56:06, 56:15, 56:21, 58:08, 59:02, 78:01-78:07 |
| 185,6,11 | 215 bp, 310 bp, 415 bp | 800 bp | *55:18-55:19, 55:25w, 55:31 | *56:23, 59:01-59:05 |
| 19 | 205 bp | 1070 bp | *55:30, 55:36 | *39:54, C*03:70 |
| 204,12 | 95 bp, 220 bp | 1070 bp | *55:20, 55:26 | *08:09, 15:83, 35:143, 41:01, 41:05-41:07, 41:09, 41:12, 41:14, 41:16, 42:04, 44:15, 44:18, 44:20, 44:100, 45:01-45:13, 51:08, 51:20, 51:36, 51:44N, 51:73, 51:97, 52:19, 56:13 |
| 21 | 270 bp | 800 bp | *55:10 | *18:01:01-18:03, 18:05-18:15, 18:18-18:28, 18:30-18:52, 35:25, 35:124-35:125, 35:142, 37:01:01-37:21, 37:23-37:25, 40:149?, 52:16, 54:21, 56:16, 58:12, 81:01, 81:03?-81:05?, 82:01-82:03, 83:01 |
| 224,13 | 95 bp, 225 bp | 800 bp | *55:09, 55:21, 55:23, 55:27, 55:37 | *07:78, 07:84, 13:04, 13:18, 13:31, 13:35, 15:04, 15:16, 15:67, 15:95, 15:137, 15:155, 35:37, 39:33, 40:44, 44:20, 44:47, 44:100, 45:09, 49:04-49:05, 51:05, 51:29, 51:37, 51:54, 51:61, 51:82, 51:90, 51:92, 52:12, 52:21, 54:10, 54:14-54:15, 54:20 |
| 2314 | 165 bp, 220 bp | 1070 bp | *55:16, 55:21, 55:29 | *13:31, 15:04, 15:137, 42:02, 42:09, 45:06, 51:61, 52:21, 54:02 |
| 244,15 | 100 bp, 235 bp | 1070 bp | *55:13, 55:23, 55:27, 55:32-55:33 | *07:84, 13:04, 13:35, 15:04, 15:16, 15:67, 15:95, 15:137, 15:155, 35:37, 39:06:01-39:06:02, 39:33-39:34, 39:50, 39:57, 39:62, 40:44, 40:86, 44:20, 44:47, 44:100, 45:02, 45:09, 49:04-49:05, 50:09, 51:13:01-51:13:02, 51:37, 51:63, 51:90, 51:92, 51:97, 52:12, 52:14, 54:14-54:15, 56:22, 59:03, 73:01-73:02 |
| 2516 | 285 bp, 380 bp | 1070 bp | *55:18, 55:34-55:35, 55:40 | *56:03, 56:06 |
| 264,6,17 | 75 bp, 310 bp, 400 bp | 1070 bp | *55:34, 55:42, 55:45, 55:47 |  |
| 274,18 | 95 bp, 170 bp | 1070 bp | *55:43, 55:46 | *54:16 |
| 284,7,19 | 95 bp, 110 bp | 800 bp | *55:41, 55:44 | *44:15, 44:18, 45:01, 45:04-45:08, 45:10-45:13, 49:01:01-49:03, 49:06-49:15, 50:01:01-50:02, 50:04-50:08, 50:10-50:11 |
| 294 | 110 bp | 1070 bp | *55:39 |  |
| 304 | 80 bp | 1070 bp | *55:38 | *56:27 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-B*55 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 430 base pairs, for most wells, or a band of 515 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the longer, 515 bp, internal positive control band in order to help in the correct orientation of the HLA-B*55 subtyping.

In addition, wells number 5, 8, 14, 18, 21, 22 and 28 contain the primer pair giving rise to the longer, 515 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3Due to the sharing of sequence motifs between HLA-B alleles non-HLA-B*55 alleles will be amplified by primer mixes 1 to 5, 7, 8, 10 to 25, 27, 28 and 30. In addition, the C*03:70 allele will be amplified by primer mix 19, the C*03:81 allele will be amplified by primer mix 7, the C*05:30 allele will be amplified by primer mix 10, the C*06:20 and C*07:81 alleles will be amplified by primer mix 2 and the C*08:08 allele will be amplified by primer mix 5.

4Specific PCR fragments shorter than 125 base pairs have a lower intensity than longer PCR bands.

5Primer mixes 1, 9 and 18 might have a tendency of giving rise to primer oligomer formation.

6Primer mixes 6, 18 and 26 have a tendency of giving rise to non-specific amplifications.

7Primer mix 28 might give a lower yield of specific PCR product than the other B*55 primer mixes.

8Primer mix 8: Specific PCR fragment of 105 bp in the B*55:13 and in the B*15:137, 39:06:01-39:06:02, 39:33-39:34, 39:50, 39:57, 39:62, 40:86, 45:02, 50:09, 51:13:01-51:13:02, 51:92, 52:14, 56:22, 59:03 and 73:01-73:02 alleles. PCR fragment of 170 bp in the *55:43 allele.  Specific PCR fragment of 425 bp in the B*55:12 allele.

9Primer mix 9: Specific PCR fragment of 215 bp in the B*55:25w allele. Specific PCR fragment of 375 bp in the B*55:11 and 55:14  alleles.

10Primer mix 11: Specific PCR fragment of 90 bp in the B*55:48 allele. Specific PCR fragment of 125 bp in the B*55:15 allele. Specific PCR fragment of 180 bp in the B*55:09, 55:22 and 55:24 and in the B*07:78, 13:01:01-13:02:09, 13:07N-13:09, 13:11, 13:14-13:20, 13:22:01-13:23, 13:25, 13:27-13:34, 13:36-13:40, 40:48, 45:10 and 49:07 alleles.

11Primer mix 18: Specific PCR fragment of 215 bp in the B*55:25w allele. Specific PCR fragment of 310 bp in the B*55:19 allele. Specific PCR fragment of 415 bp in the B*55:18 and 55:31 and in the B*56:23 and 59:01-59:05 alleles.

12Primer mix 20: Specific PCR fragment of 95 bp in the B*55:26 and in the B*35:143 and 51:73 alleles. Specific PCR fragment of 220 bp in the B*55:20 and in the B*08:09, 15:83, 41:01, 41:05-41:07, 41:09, 41:12, 41:14, 41:16, 42:04, 44:15, 44:18, 44:20, 44:100, 45:01-45:13, 51:08, 51:20, 51:36, 51:44N, 51:97, 52:19 and 56:13 alleles.

13Primer mix 22: Specific PCR fragment of 95 bp in the B*55:23 and 55:27 and in the B*13:04, 13:35, 15:16, 15:67, 15:95, 15:155, 35:37, 40:44, 44:20, 44:47, 44:100, 45:09, 49:04-49:05, 51:37, 51:90, 51:92, 52:12 and 54:14-54:15 alleles. Specific PCR fragment of 225 bp in the B*55:09, 55:21 and 55:37 and in the B*07:78, 13:18, 13:31, 15:137, 39:33, 51:05, 51:29, 51:54, 51:61, 51:82, 52:21, 54:10 and 54:20 alleles. Specific PCR fragment of 95 and 225 bp in the B*07:84 and 15:04 alleles.

14Primer mix 23: Specific PCR fragment of 165 bp in the B*55:29 allele. Specific PCR fragment of 220 bp in the B*55:16 and 55:21 and in the B*13:31, 15:04, 15:137, 51:61 and 52:21 alleles.

15Primer mix 24: Specific PCR fragment of 100 bp in the B*55:13, 55:23, 55:27 and 55:32 and in the B*07:84, 13:04, 13:35, 15:04, 15:16, 15:67, 15:95, 15:137, 15:155, 35:37, 39:06:01-39:06:02, 39:33-39:34, 39:50, 39:57, 39:62, 40:44, 40:86, 44:20, 44:47, 44:100, 45:02, 45:09, 49:04-49:05, 50:09, 51:13:01-51:13:02, 51:37, 51:63, 51:90, 51:92, 51:97, 52:12, 52:14, 54:14-54:15, 56:22, 59:03 and 73:01-73:02 alleles. Specific PCR fragment of 235 bp in the B*55:33 allele.

16Primer mix 25: Specific PCR fragment of 285 bp in the B*55:35 and in the B*56:03 and 56:06 alleles. Specific PCR fragment of 380 bp in the B*55:18, 55:34 and 55:40 alleles.

17Primer mix 26: Specific PCR fragment of 75 bp in the B*55:42 allele. Specific PCR fragment of 310 bp in the B*55:45 allele. Specific PCR fragment of 400 bp in the B*55:34 and 55:47 alleles.

18Primer mix 27: Specific PCR fragment of 95 bp in the B*55:46 and in the B*54:16 alleles. Specific PCR fragment of 170 bp in the B*55:43 allele.

19Primer mix 28: Specific PCR fragment of 95 bp in the B*55:41 and in the B*44:15, 44:18, 45:01, 45:04-45:08, 45:10-45:13, 49:01:01-49:03, 49:06-49:15, 50:01:01-50:02, 50:04-50:08 and 50:10-50:11 alleles. Specific PCR fragment of 110 bp in the B*55:44 allele.

*?*, nucleotide sequence of the primer matching region is not known.

‘w’, may be weakly amplified.

1The B*5506 sequence shown to contain errors and be identical to B*55:04.

2Primer mix 8: Specific PCR fragment of 105 bp in the B*55:13 and in the B*15:137, 39:06:01-39:06:02, 39:33-39:34, 39:50, 39:57, 39:62, 40:86, 45:02, 50:09, 51:13:01-51:13:02, 51:92, 52:14, 56:22, 59:03 and 73:01-73:02 alleles. PCR fragment of 170 bp in the *55:43 allele.  Specific PCR fragment of 425 bp in the B*55:12 allele.

Primer mix 9: Specific PCR fragment of 215 bp in the B*55:25w allele. Specific PCR fragment of 375 bp in the B*55:11 and 55:14  alleles.

Primer mix 11: Specific PCR fragment of 90 bp in the B*55:48 allele. Specific PCR fragment of 125 bp in the B*55:15 allele. Specific PCR fragment of 180 bp in the B*55:09, 55:22 and 55:24 and in the B*07:78, 13:01:01-13:02:09, 13:07N-13:09, 13:11, 13:14-13:20, 13:22:01-13:23, 13:25, 13:27-13:34, 13:36-13:40, 40:48, 45:10 and 49:07 alleles.

Primer mix 18: Specific PCR fragment of 215 bp in the B*55:25w allele. Specific PCR fragment of 310 bp in the B*55:19 allele. Specific PCR fragment of 415 bp in the B*55:18 and 55:31 and in the B*56:23 and 59:01-59:05 alleles.

Primer mix 20: Specific PCR fragment of 95 bp in the B*55:26 and in the B*35:143 and 51:73 alleles. Specific PCR fragment of 220 bp in the B*55:20 and in the B*08:09, 15:83, 41:01, 41:05-41:07, 41:09, 41:12, 41:14, 41:16, 42:04, 44:15, 44:18, 44:20, 44:100, 45:01-45:13, 51:08, 51:20, 51:36, 51:44N, 51:97, 52:19 and 56:13 alleles.

Primer mix 22: Specific PCR fragment of 95 bp in the B*55:23 and 55:27 and in the B*13:04, 13:35, 15:16, 15:67, 15:95, 15:155, 35:37, 40:44, 44:20, 44:47, 44:100, 45:09, 49:04-49:05, 51:37, 51:90, 51:92, 52:12 and 54:14-54:15 alleles. Specific PCR fragment of 225 bp in the B*55:09, 55:21 and 55:37 and in the B*07:78, 13:18, 13:31, 15:137, 39:33, 51:05, 51:29, 51:54, 51:61, 51:82, 52:21, 54:10 and 54:20 alleles. Specific PCR fragment of 95 and 225 bp in the B*07:84 and 15:04 alleles.

Primer mix 23: Specific PCR fragment of 165 bp in the B*55:29 allele. Specific PCR fragment of 220 bp in the B*55:16 and 55:21 and in the B*13:31, 15:04, 15:137, 51:61 and 52:21 alleles.

Primer mix 24: Specific PCR fragment of 100 bp in the B*55:13, 55:23, 55:27 and 55:32 and in the B*07:84, 13:04, 13:35, 15:04, 15:16, 15:67, 15:95, 15:137, 15:155, 35:37, 39:06:01-39:06:02, 39:33-39:34, 39:50, 39:57, 39:62, 40:44, 40:86, 44:20, 44:47, 44:100, 45:02, 45:09, 49:04-49:05, 50:09, 51:13:01-51:13:02, 51:37, 51:63, 51:90, 51:92, 51:97, 52:12, 52:14, 54:14-54:15, 56:22, 59:03 and 73:01-73:02 alleles. Specific PCR fragment of 235 bp in the B*55:33 allele.

Primer mix 25: Specific PCR fragment of 285 bp in the B*55:35 and in the B*56:03 and 56:06 alleles. Specific PCR fragment of 380 bp in the B*55:18, 55:34 and 55:40 alleles.

Primer mix 26: Specific PCR fragment of 75 bp in the B*55:42 allele. Specific PCR fragment of 310 bp in the B*55:45 allele. Specific PCR fragment of 400 bp in the B*55:34 and 55:47 alleles.

Primer mix 27: Specific PCR fragment of 95 bp in the B*55:46 and in the B*54:16 alleles. Specific PCR fragment of 170 bp in the B*55:43 allele.

Primer mix 28: Specific PCR fragment of 95 bp in the B*55:41 and in the B*44:15, 44:18, 45:01, 45:04-45:08, 45:10-45:13, 49:01:01-49:03, 49:06-49:15, 50:01:01-50:02, 50:04-50:08 and 50:10-50:11 alleles. Specific PCR fragment of 110 bp in the B*55:44 allele.

‘w’, may be weakly amplified.

‘?’, the nucleotide sequence of the primer matching region is not known.

Change in revision R01 compared to R00:

- The B*55:25 allele is weakly amplified by primer mixes 9 and 18. This has been revised in the Specificity and Interpretation Tables.