PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*56

Prod. No:	101.571-06 – including Taq polymerase

101.571-06u – without Taq polymerase

Lot No:    	08E

Expiry Date:    	2010-January-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ug/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 24 primer mixes used for HLA-B*56 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*56 alleles3 | Other amplified HLA Class I alleles4 |
| --- | --- | --- | --- | --- |
| 15 | 125 bp | 800 bp | 5601, 5602, 5607-5611, 5613-5617, 5619N | 1301-1304, 1306-1309, 1311-1320, 1516, 1520, 1534, 1542, 1562, 1567, 1585, 1586, 1595, 9537, 1822, 2714, 350101-350803, 3510, 3511, 3513-3515, 3519-3521, 3523-3530, 3533-3538, 3540N-3542, 3545-3550, 3552, 3554-3558, 3560, 3562, 3563, 3565Q, 3566, 3568-3572, 3574-3578, 3580-3585, 4028, 4410, 4415, 4418, 4448, 4501-4507, 4611, 4802, 4901-4905, 5001, 5002, 5115, 530101-5306, 5308-5314, 5401-5405N, 5407, 5408N, 5410, 5412, 5413, 550101-5503, 5505, 5507, 5509-5513, 5515, 5516, 5518, 5519, 5521-5529, 5705, 5801, 5802, 5804-5807, 5809, 5811-5816, 5901, 8201, 8202 |
| 2 | 400 bp | 1070 bp | 5601-5613, 5615-5621 | 3576, 3578, 5401-5406, 5408N-5413, 550101-5505, 5507-5517, 5519-5529, 8101, 8201, 8202, 8301 |
| 3 | 180 bp | 1070 bp | 5601, 5602, 5604, 5607, 5608, 5613, 5614, 5616, 5617, 5619N, 5620 | 1303, 1573, 4071, 4410, 4415, 4418, 4501, 4504-4507, 4611, 4901-4903, 5001, 5002, 5004, 5115, 5403, 8201, 8202 |
| 45 | 105 bp | 800 bp | 5602, 5604, 5610 | 1311, 1573, 1586, 3917, 4048, 4071, 8201, 8202, Cw*0206, Cw*1215 |
| 56 | 285, 400 bp | 1070 bp | 5603, 5606, 5614 |  |
| 65 | 105 bp | 1070 bp | 560501 |  |
| 75,7 | 120 bp | 800 bp | 560501-5606, 5621 | 510101-510103, 510105-5103, 5105, 5107-510902, 5111N, 5112, 511302, 5114, 5116-5123, 5126-5137, 5139-5141N, 5143, 5144N, 5148-5152, 520101-5211, 550104, 5808, 7801-7805 |
| 8 | 400 bp | 1070 bp | 5608, 5614 |  |
| 9 | 145 bp | 1070 bp | 5607 | 0802, 9515, 2701, 380201-3804, 3808, 3815, 4440, 4444 |
| 10 | 150 bp | 1070 bp | 5609, 5611, 5612 | 1301, 1306, 1307N, 1312, 1313, 1317, 1320, 1502, 1513, 1520, 1521, 1525, 1536, 1544, 1562, 1577, 1580, 1585, 1588, 1589, 9506, 9512, 9521, 9539, 1822, 2719, 2730, 350101-350402, 3506-350803, 3510-3517, 3519-3521, 3523-3530, 3533-3536, 3538-3542, 3545-3550, 3552, 3554-3557, 3559, 3561-3563, 3565Q, 3569-3571, 3574, 3576-3578, 3580-3585, 370101-370104, 3703N-3706, 3708, 3710, 3711, 3713, 3942, 4028, 44020101-4414, 4416, 4417, 4419N, 4421-4430, 4432-4440, 4442-4446, 4448-4452N, 4455-4459, 4802, 5104, 5142, 5146, 530101-5306, 5308-5313, 5514, 570101-5710, 5712, 5714-5716, 5801, 5804, 5805, 5809-5815, 8301 |
| 115 | 105 bp | 800 bp | 5601, 5607, 5608, 5613, 5614, 5616, 5617, 5619N, 5620 | 130201-1303, 1308Q, 1309, 1314-1316, 1318, 1319, 1542, 3560, 4415, 4418, 4501, 4503-4507, 4611, 4901-4903, 5001, 5002, 5004, 5115, 5401-5403, 5405N, 5407, 5408N, 5410, 5412, 5413, 550101-5503, 5505, 5507, 5509-5512, 5515, 5516, 5518, 5519, 5521, 5522, 5524-5526, 5529, 5901 |
| 12 | 180 bp | 800 bp | 5610 | 1306, 1542, 1586, 3560, 3917weakly, 5401, 5402, 5405N, 5407, 5408N, 5410, 5412, 5413, 550101-5503, 5505, 5507, 5510-5512, 5515, 5516, 5518, 5519, 5521, 5525, 5526, 5529, 5901 |
| 134 | 180 bp | 1070 bp | 5611 | 1558 weakly, 9533, 3503, 3506 weakly, 3513, 3536, 3538, 3555, 3556, 3559 weakly, 3570, 3574, 3575, 3584, 3585, 3932 weakly, 3933 weakly, 511301-511302 weakly, 5304 |
| 145 | 80 bp | 1070 bp | 5604 | 1573, 3917, 4048, 4071, 5004, Cw*0312 weakly, Cw*0319 weakly |
| 15 | 160 bp | 1070 bp | 5613 | 4415, 4418, 4501, 4504-4507, 8201, 8202 |
| 16 | 160 bp | 1070 bp |  | 44020101-440204, 4406, 4408, 4409, 4411, 4412, 4416, 4419N-4424, 4427, 4433, 4434, 4441, 4444, 4448, 4449, 4452N, 4453, 4455, 4459, 8301 |
| 175 | 105 bp | 800 bp | 560501-5606, 5615, 5621 | 0809, 1583, 2714, 40060101-400602, 4044, 4053, 4070, 4075, 4101, 4105-4107, 4204, 4420, 4447, 510101-5103, 5105, 5107-5112, 5114, 5116-5124, 5126-5136, 5138-5141N, 5143, 5144N, 5148-5152, 520101-5211, 5404, 5411, 5517, 5520, 5527, 5528, 5808, 5902, 7801-7805 |
| 18 | 295 bp | 800 bp | 5616 | 5510, 8201, 8202 |
| 19 | 185 bp | 800 bp | 5619N | 1407N, 3940N |
| 20 | 160 bp | 1070 bp |  | 4424, 5139, 5401, 5403, 5404, 5406-5413 |
| 215,7 | 110 bp | 1070 bp | 5617 | 0737 |
| 22 | 180 bp | 1070 bp | 5618 | 1550, 1569, 1593, 180101-1809, 1811-1815, 1817N-1819, 1822-1824, 1828, 3535, 3907, 4209, 4603, 5409, 5514, 5523, 5805 Cw*1509, Cw*1519, Cw*1520 |
| 235 | 85 bp |  | 5620 | 4048 |
| 245 | 70 bp |  | 5621 | 0736, 5412 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DR low resolution SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1 070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-B*56 subtyping.

In addition, wells number 4, 7, 11, 12, 17 to 19 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3The HLA-B56 primer set cannot separate the B*5609, B*3576 and B*3578 alleles. These alleles can be distinguished by the HLA-B low resolution and/or B*35 kits.

The HLA-B56 primer set cannot separate the B*5615, B*5528 and B*5529 alleles. These alleles can be distinguished by the HLA-B low resolution and/or B*55 kits.

## 4Due to the sharing of sequence motifs between HLA-B alleles non-HLA-B*56 alleles will be amplified by primer mixes 1 to 4, 7 and 9 to 24. In addition, the Cw*0206 and Cw*1215 alleles will be amplified by primer mix 4, the C*0312 and Cw*0319 alleles weakly by primer mix 14 and the Cw*1509, Cw*1519 and Cw*1520 alleles by primer mix 22.

## 5Specific PCR fragments shorter than 125 base pairs have a lower intensity than longer PCR bands.

6Primer mix 5 has a tendency of giving rise to nonspecific amplifications.

Primer mix 5: Specific PCR fragment of 285 bp in the B*5603 and B*5606 alleles. Specific PCR fragment of 400 bp in the B*5614 allele.

7Primer mixes 7 and 21 may give rise to less specific PCR products than the other HLA-B*56 primer mixes.

1Primer mix 5: Specific PCR fragment of 285 bp in the B*5603 and B*5606 alleles. Specific PCR fragment of 400 bp in the B*5614 allele.

2The HLA-B56 primer set cannot separate the B*5609, B*3576 and B*3578 alleles. These alleles can be distinguished by the HLA-B low resolution and/or B*35 kits.

The HLA-B56 primer set cannot separate the B*5615, B*5528 and B*5529 alleles. These alleles can be distinguished by the HLA-B low resolution and/or B*55 kits.

‘w’, may be weakly amplified.