PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-B*56

Prod. No:	101.571-06/06u

Lot No:    	35K

Expiry Date:    	2012-September-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 24 primer mixes used for HLA-B*56 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-B*56 alleles3 | Other amplified HLA Class I alleles4 |
| --- | --- | --- | --- | --- |
| 15 | 125 bp | 800 bp | *56:01:01-56:02, 56:07-56:11, 56:13-56:17, 56:19N, 56:22-56:26, 56:28N-56:29 | *13:01:01-13:04, 13:06-13:09, 13:11-13:20, 13:22:01-13:23, 13:25-13:34, 13:36-13:39, 15:16, 15:20, 15:34, 15:42, 15:62, 15:67, 15:85-15:86, 15:95, 15:137, 15:194, 18:22, 27:14, 35:01:01:01-35:08:04, 35:10-35:11:02, 35:13-35:15, 35:19-35:21, 35:23-35:30, 35:33-35:38, 35:40N-35:42:02, 35:45-35:50, 35:52, 35:54-35:58, 35:60, 35:62-35:63, 35:65Q-35:66, 35:68:01-35:72, 35:74-35:78, 35:80-35:85, 35:89-35:98, 35:100-35:101:02, 35:103-35:112, 35:115-35:116, 35:119-35:124, 35:126-35:134N, 35:136-35:145N, 40:28, 44:10, 44:15, 44:18, 44:48, 45:01-45:12, 46:11, 46:18, 48:02:01-48:02:02, 49:01:01-49:10, 50:01:01, 50:02, 50:05-50:09, 51:15, 51:56, 53:01:01-53:06, 53:08:01-53:23, 54:01-54:05N, 54:07-54:08N, 54:10, 54:12-54:23, 55:01:01-55:01:05, 55:02:01-55:02:03, 55:02:05-55:03, 55:05, 55:07, 55:09-55:13, 55:15-55:16, 55:18-55:19, 55:21-55:37, 55:39-55:43, 57:05, 58:01:01-58:01:02, 58:01:04-58:02, 58:04-58:07, 58:09, 58:11-58:19, 58:21-58:26, 58:28-58:30, 59:01, 59:03-59:05, 82:01-82:03, C*06:20, C*07:81 |
| 2 | 400 bp | 1070 bp | *56:01:01-56:13, 56:15-56:29 | *07:65, 35:76, 35:78, 44:90, 54:01-54:06, 54:08N-54:23, 55:01:01-55:05, 55:07-55:17, 55:19-55:33, 55:35-55:43, 81:01, 81:03?-81:04N?, 82:01-82:03, 83:01 |
| 3 | 180 bp | 1070 bp | *56:01:01-56:02, 56:04, 56:07-56:08, 56:13-56:14, 56:16-56:17, 56:19N-56:20, 56:24-56:29 | *13:03, 15:73, 40:71, 44:10, 44:15, 44:18, 45:01, 45:04-45:07, 45:11-45:12, 46:11, 49:01:01-49:03, 49:06, 49:08-49:10, 50:01:01-50:02, 50:04-50:08, 51:15, 51:62, 54:03, 59:04, 82:01-82:03 |
| 45 | 105 bp | 800 bp | *56:02, 56:04, 56:10 | *13:11, 15:18:03, 15:73, 15:86, 39:17, 40:48, 40:71, 51:62, 82:01-82:03, C*02:06, C*12:15 |
| 5 | 285 bp | 1070 bp | *56:03 | *55:35 |
| 65 | 105 bp | 1070 bp | *56:05:01 |  |
| 75,6,8 | 120 bp, 210 bp | 800 bp | *56:05:01-56:06, 56:21, 56:25 | *07:78w, 07:84w, 13:16, 15:16, 15:42, 15:67, 15:95, 40:95, 49:01:01, 49:02-49:10, 50:01:01-50:02, 50:04-50:09, 51:01:01-51:03, 51:05, 51:07:01-51:09:02, 51:11N-51:14, 51:16-51:24:03, 51:26-51:41N, 51:43-51:44N, 51:48-51:55, 51:57-51:58, 51:60-51:61, 51:63, 51:65-51:80, 51:82-51:96, 52:01:01-52:21, 54:20w, 55:01:01-55:01:06, 55:03, 55:05, 55:09w, 55:11, 55:15, 55:17, 55:24-55:25, 55:28-55:29, 55:31, 55:33, 55:36, 55:38, 55:40, 58:08, 78:01-78:07 |
| 8 | 395 bp | 1070 bp | *56:08, 56:14 |  |
| 9 | 145 bp | 1070 bp | *56:07 | *08:02, 15:115, 27:01, 38:02:01-38:04, 38:08, 38:15, 38:18, 38:23, 44:40, 44:44 |
| 107 | 150 bp | 800 bp | *56:09, 56:11-56:12 | *08:49, 13:01:01-13:01:05, 13:06-13:07N, 13:12-13:13, 13:17, 13:20, 13:22:01-13:23, 13:25-13:26, 13:28-13:29, 13:36, 13:39, 14:10, 15:02:01-15:02:04, 15:13, 15:20-15:21, 15:25:01-15:25:02, 15:36, 15:44, 15:62, 15:77, 15:80, 15:85, 15:88-15:89, 15:106, 15:112, 15:121, 15:139, 15:144, 15:154, 15:165, 15:170, 15:194, 18:22, 27:19, 27:30, 35:01:01:01-35:04:03, 35:06-35:08:04, 35:10-35:17, 35:19-35:21, 35:23-35:30, 35:33-35:36, 35:38-35:42:02, 35:45-35:50, 35:52, 35:54-35:57, 35:59, 35:61-35:63, 35:65Q, 35:69-35:71, 35:74, 35:76-35:78, 35:80-35:85, 35:90-35:96, 35:98, 35:100-35:101:02, 35:103-35:113, 35:115-35:116, 35:120-35:126, 35:128-35:134N, 35:136-35:145N, 37:01:01-37:01:07, 37:03N-37:06, 37:08, 37:10-37:11, 37:13-37:23, 38:20, 39:42, 40:28, 44:02:01:01-44:14, 44:16-44:17, 44:19N, 44:21-44:30, 44:32-44:40, 44:42-44:46, 44:48-44:52N, 44:55-44:64:02, 44:66-44:98, 44:101-44:105, 44:107-44:110, 48:02:01-48:02:02, 51:04, 51:42, 51:46, 51:56, 53:01:01-53:13, 53:15-53:23, 55:14, 57:01:01-57:01:04, 57:01:06-57:10, 57:12, 57:14-57:20, 57:22-57:30, 57:32, 58:01:01-58:01:02, 58:01:04-58:01:07, 58:04-58:05, 58:09-58:15, 58:17N, 58:19, 58:21-58:24, 58:28-58:30, 83:01 |
| 115 | 105 bp | 800 bp | *56:01:01-56:01:04, 56:07-56:08, 56:13-56:14, 56:16-56:17, 56:19N-56:20, 56:23-56:29 | *07:78, 13:02:01-13:03, 13:08Q-13:09, 13:14-13:16, 13:18-13:19, 13:27, 13:30-13:34, 13:37-13:38, 15:42, 35:60, 44:15, 44:18, 45:01, 45:03-45:08, 45:10-45:12, 46:11, 46:18, 49:01:01-49:03, 49:06-49:10, 50:01:01-50:02, 50:04-50:08, 51:15, 54:01-54:03, 54:05N, 54:07-54:08N, 54:10, 54:12-54:13, 54:16-54:23, 55:01:01-55:01:03, 55:01:05-55:03, 55:05, 55:07, 55:09-55:12, 55:15-55:16, 55:18-55:19, 55:21-55:22, 55:24-55:26, 55:29-55:31, 55:33-55:38, 55:40-55:41, 55:43, 59:01, 59:04-59:05 |
| 127 | 180 bp | 800 bp | *56:10, 56:23 | *13:06, 15:42, 15:86, 35:60, 39:17w, 45:08w, 46:18, 54:01-54:02, 54:05N, 54:07-54:08N, 54:10, 54:12-54:13, 54:17-54:23, 55:01:01-55:03, 55:05, 55:07, 55:10-55:12, 55:15-55:16, 55:18-55:19, 55:21, 55:25-55:26, 55:29-55:31, 55:33-55:43, 59:01, 59:05 |
| 137 | 180 bp | 1070 bp | *56:11, 56:22 | *15:58, 15:133, 35:03:01-35:03:04, 35:06, 35:13, 35:36, 35:38, 35:55-35:56, 35:59, 35:70, 35:74-35:75, 35:84-35:85, 35:98, 35:106, 35:109, 35:127-35:128, 35:136, 39:32-39:33, 51:13:01-51:13:02, 51:92, 52:14, 53:04 |
| 145 | 80 bp | 1070 bp | *56:04, 56:27 | *15:18:03, 15:73, 39:17, 40:48, 40:71, 50:04, 51:62, 55:38, C*03:12w, C*03:19w, C*15:26w |
| 159 | 160 bp, 380 bp | 1070 bp | *56:13, 56:28N | *44:15, 44:18, 45:01, 45:04-45:08, 45:10-45:12, 82:01-82:03 |
| 16 | 160 bp | 1070 bp |  | *44:02:01:01-44:02:13, 44:06, 44:08-44:09, 44:11-44:12, 44:16, 44:19N-44:24, 44:27, 44:33-44:34, 44:41, 44:44, 44:48-44:49, 44:52N-44:53, 44:55, 44:59, 44:63, 44:66-44:68, 44:71-44:74, 44:80, 44:83-44:84, 44:86-44:87, 44:89-44:91, 44:93, 44:95, 44:97, 44:99-44:102, 44:104, 44:106, 83:01 |
| 177 | 180 bp | 800 bp | *56:05:01-56:06, 56:15, 56:21 | *07:20, 07:24, 07:60, 07:100, 08:21, 08:25, 15:09-15:10:02, 15:30, 15:37, 15:45, 15:48, 15:63, 15:90, 15:99, 15:150, 35:02:01-35:02:04, 35:04:01-35:04:03, 35:09:01-35:09:02, 35:12:01-35:12:02, 35:18, 35:22, 35:34, 35:39, 35:44, 35:81, 35:83, 35:95, 35:129N, 40:05, 40:26, 40:28, 40:63, 40:92, 44:62, 44:77, 44:82, 44:107, 51:01:01-51:01:14, 51:01:16-51:09:02, 51:11N-51:12, 51:18-51:20, 51:22-51:24:03, 51:26-51:30, 51:32-51:33, 51:35, 51:38-51:41N, 51:43-51:44N, 51:46, 51:48-51:61, 51:64-51:80, 51:83-51:84, 51:86-51:91, 51:94-51:96, 52:01:01-52:07, 52:09-52:13, 52:15-52:21, 53:19, 55:08, 57:02:01-57:03:02, 57:05, 57:07, 57:09, 57:12, 57:17, 57:28N, 58:08, 58:28, 78:01-78:06, C*03:81 |
| 186 | 295 bp | 800 bp | *56:16 | *54:21, 55:10, 82:01-82:03 |
| 195,10 | 75 bp, 185 bp | 800 bp | *56:19N, 56:29 | *14:07N, 39:40N |
| 20 | 215 bp | 1070 bp |  | *07:02:19, 15:01:04, 37:01:04, 40:94, 54:01-54:23 |
| 215,11 | 110 bp, 170 bp | 1070 bp | *56:17, 56:23, 56:26 | *07:37 |
| 22 | 180 bp | 1070 bp | *56:18 | *08:37, 15:50, 15:69, 15:93, 15:186, 15:199, 18:01:01-18:09, 18:11-18:15, 18:17N-18:19, 18:22-18:25, 18:27-18:34, 18:37-18:40, 18:42-18:49, 35:35, 35:93, 39:07, 39:43, 42:09, 46:03, 46:21, 54:09, 54:14, 55:14, 55:23, 57:26, 58:05, C*07:123, C*15:09, C*15:19-15:20, C*15:27, C*16:20 |
| 235,12 | 85 bp, 350 bp | 1070 bp | *56:20, 56:24 | *07:78, 40:48 |
| 24 | 380 bp | 1070 bp | *56:21 | *08:03, 08:52, 40:13, 40:19, 40:109, 40:117, 48:18, 51:01:01-51:01:07, 51:01:09-51:01:14, 51:01:16-51:12, 51:16-51:24:03, 51:26-51:36, 51:38-51:41N, 51:43-51:44N, 51:46, 51:48-51:49, 51:51-51:53, 51:55-51:61, 51:64-51:77, 51:79-51:84, 51:86-51:89, 51:91, 51:93-51:96, 52:01:01-52:11, 52:13, 52:15-52:19, 52:21, 53:19, 57:02:01-57:03:02, 57:05, 57:07, 57:09, 57:17, 58:08, 58:27-58:28, 59:02 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA B*56 high resolution SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1 070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-B*56 subtyping.

In addition, wells number 4, 7, 10 to 12 and 17 to 19 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several HLA-B alleles first exon nucleotide sequences are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in the first exon are conserved within allelic groups.

The HLA-B*56 primer set cannot separate the B*56:05:02 and B*56:06 alleles. These two alleles can be distinguished by the HLA-B low resolution kit.

The HLA-B*56 primer set cannot separate the B*56:09, B*35:76 and B*35:78 alleles. These alleles can be distinguished by the HLA-B low resolution and/or B*35 kits.

The B*56:13 and 56:28N alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 15.

The B*56:17 and 56:26 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 21.

The B*56:19N and 56:29 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 19.

4Due to the sharing of sequence motifs between HLA-B alleles non-HLA-B*56 alleles will be amplified by primer mixes 1 to 5, 7 and 9 to 24. In addition, the C*02:06 and C*12:15 alleles will be amplified by primer mix 4, the C*03:12, C*03:19 and 15:26 alleles weakly by primer mix 14, the C*03:81 by primer mix 17, the C*06:20 and C*07:81 by primer mix 1 and the C*07:123, C*15:09, C*15:19, C*15:20, C*15:27 and C*16:20 alleles by primer mix 22.

5Specific PCR fragments shorter than 125 base pairs have a lower intensity than longer PCR bands.

6Primer mix 7 and 18 may give rise to less specific PCR products than the other HLA-B*56 primer mixes.

7Primer mixes 10, 12, 13 and 17 may give rise to unspecific amplification products.

8Primer mix 7: Specific PCR fragment of 120 bp in the B*51:05, 51:08-51:09:02, 51:13:02-51:14, 51.19, 51:20, 51:31, 51:40, 51:44N, 51:54, 51:73, 51:91, 51:93, 52:03, 52:10, 52:19 and 78:04 alleles. Specific PCR fragment of 210 bp in the B*56:25 and in the B*07:78w, 07:84w, 13:16, 15:16, 15:42, 15:67, 15:95, 49:01:01, 49:02-49:10, 50:01:01-50:02, 50:04-50:09, 51:01:04, 51:01:13, 51:02:04 51:13:01, 51:24:01-51:24:02, 51:38, 51:92, 52:01:05, 52:14, 54:20w, 55:01:01-55:01:03, 55:01:05-55:01:06, 55:03, 55:05, 55:09w, 55:11, 55:15, 55:17, 55:24-55:25, 55:28-55:29, 55:31, 55:33, 55:36, 55:38 and 55:40  alleles. Specific PCR fragment of 120 and 210 bp in the B*56:05:01-56:06 and 56:21 and in the B*40:95, 51:01:01-51:01:03, 51:01:05-51:01:12, 51:01:14-51:02:03, 51:03,  51:07:01-51:07:02, 51:11N-51:12, 51:16-51:18, 51:21-51:23, 51:24:03, 51:26-51:30, 51:32-51:37, 51:39, 51:41N, 51:43, 51:48-51:53, 51:55, 51:57-51:58, 51:60-51:61, 51:63, 51:65-51:72, 51:74-51:80, 51:82-51:90, 51:94-51:96, 52:01:01-52:01:04, 52:02, 52:04-52:09, 52:11-52:13, 52:15-52:18, 52:20-52:21, 55:01:04, 58:08, 78:01-78:03 and 78:05-78:07 alleles.

9Primer mix 15: Specific PCR fragment of 160 bp in the B*56:13 and in the B*44:15, 44:18, 45:01, 45:04-45:08, 45:10-45:12 and 82:01-82:03 alleles. Specific PCR fragment of 380 bp in the B* 56:28N allele.

10Primer mix 19: Specific PCR fragment of 75 bp in the B* 56:29 allele. Specific PCR fragment of 185 bp in the B*56:19N and in the B*14:07N and 39:40N alleles.

11Primer mix 21: Specific PCR fragment of 110 bp in the B* *56:17 and 56:23 and in the B*07:37 alleles. Specific PCR fragment of 170 bp in the B*56:26 allele.

12Primer mix 23: Specific PCR fragment of 85 bp in the B*56:20 and in the B*07:78 and 40:48 alleles. Specific PCR fragment of 350 bp in the B*56:24 allele.

’w’, might be weakly amplified.

1The HLA-B*56 primer set cannot separate the B*56:05:02 and B*56:06 alleles. These two alleles can be distinguished by the HLA-B low resolution kit.

The HLA-B*56 primer set cannot separate the B*56:09, B*35:76 and B*35:78 alleles. These alleles can be distinguished by the HLA-B low resolution and/or B*35 kits.

The B*56:13 and 56:28N alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 15.

The B*56:17 and 56:26 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 21.

The B*56:19N and 56:29 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 19.

2Primer mix 7: Specific PCR fragment of 120 bp in the B*51:05, 51:08-51:09:02, 51:13:02-51:14, 51.19, 51:20, 51:31, 51:40, 51:44N, 51:54, 51:73, 51:91, 51:93, 52:03, 52:10, 52:19 and 78:04 alleles. Specific PCR fragment of 210 bp in the B*56:25 and in the B*07:78w, 07:84w, 13:16, 15:16, 15:42, 15:67, 15:95, 49:01:01, 49:02-49:10, 50:01:01-50:02, 50:04-50:09, 51:01:04, 51:01:13, 51:02:04 51:13:01, 51:24:01-51:24:02, 51:38, 51:92, 52:01:05, 52:14, 54:20w, 55:01:01-55:01:03, 55:01:05-55:01:06, 55:03, 55:05, 55:09w, 55:11, 55:15, 55:17, 55:24-55:25, 55:28-55:29, 55:31, 55:33, 55:36, 55:38 and 55:40  alleles. Specific PCR fragment of 120 and 210 bp in the B*56:05:01-56:06 and 56:21 and in the B*40:95, 51:01:01-51:01:03, 51:01:05-51:01:12, 51:01:14-51:02:03, 51:03,  51:07:01-51:07:02, 51:11N-51:12, 51:16-51:18, 51:21-51:23, 51:24:03, 51:26-51:30, 51:32-51:37, 51:39, 51:41N, 51:43, 51:48-51:53, 51:55, 51:57-51:58, 51:60-51:61, 51:63, 51:65-51:72, 51:74-51:80, 51:82-51:90, 51:94-51:96, 52:01:01-52:01:04, 52:02, 52:04-52:09, 52:11-52:13, 52:15-52:18, 52:20-52:21, 55:01:04, 58:08, 78:01-78:03 and 78:05-78:07 alleles.

Primer mix 15: Specific PCR fragment of 160 bp in the B*56:13 and in the B*44:15, 44:18, 45:01, 45:04-45:08, 45:10-45:12 and 82:01-82:03 alleles. Specific PCR fragment of 380 bp in the B* 56:28N allele.

Primer mix 19: Specific PCR fragment of 75 bp in the B* 56:29 allele. Specific PCR fragment of 185 bp in the B*56:19N and in the B*14:07N and 39:40N alleles.

Primer mix 21: Specific PCR fragment of 110 bp in the B* *56:17 and 56:23 and in the B*07:37 alleles. Specific PCR fragment of 170 bp in the B*56:26 allele.

Primer mix 23: Specific PCR fragment of 85 bp in the B*56:20 and in the B*07:78 and 40:48 alleles. Specific PCR fragment of 350 bp in the B*56:24 allele.

‘w’, may be weakly amplified.

Change in revision R01 compared to R00:

- The B*56:06 allele is not amplified by primer mix 5. This has been revised in the specificity and interpretation tables.