PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-C*05

Prod. No:	101.613-12/12u

Lot No:    	47N

Expiry Date:    	2014-September-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for HLA-C*05 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-C*05 alleles3,4 | Other amplified HLA Class I alleles5 |
| --- | --- | --- | --- | --- |
| 1 | 155 bp | 800 bp | *05:01:01:01-05:01:18, 05:03-05:08, 05:10-05:11, 05:13-05:16, 05:19-05:51Q, 05:53-05:72 | *07:41, 08:02:01-08:02:07, 08:04-08:05, 08:07, 08:12-08:13, 08:17-08:19, 08:23, 08:25, 08:28-08:32, 08:34, 08:37, 08:43, 08:45, 08:47-08:49, 08:52N-08:53, 08:55N |
| 2 | 165 bp | 1070 bp | *05:01:01:01-05:01:18, 05:03-05:28, 05:30-05:47, 05:49-05:72 | *06:05, 06:67, 08:10, 12:21, 12:33, 17:05 |
| 3 | 150 bp | 1070 bp | *05:09:01-05:09:02, 05:17, 05:44, 05:52 | *01:13, 02:51, 03:87, 07:130, 08:15:01-08:15:02, 08:51, 16:27, B*15:33 |
| 46 | 120 bp | 800 bp | *05:03 | *07:52 |
| 58 | 225 bp, 285 bp | 1070 bp | *05:04, 05:31 | *07:68, 08:09, 08:11 |
| 6 | 270 bp | 1070 bp | *05:05, 05:16 | *08:12, A*29:10, A*68:69 |
| 7 | 265 bp | 1070 bp | *05:01:01:01-05:01:18, 05:03-05:04, 05:06-05:08, 05:10-05:16, 05:18:01-05:51Q, 05:53-05:60, 05:62-05:72 | *07:04:01-07:04:07, 07:11-07:12, 07:41, 07:63, 07:68, 07:101, 07:139, 07:142, 07:181, 07:199, 08:01:01-08:14, 08:16-08:50, 08:52N-08:56 |
| 86,9 | 85 bp, 210 bp | 800 bp | *05:06, 05:55 |  |
| 9 | 285 bp | 1070 bp | *05:07N |  |
| 106,10 | 95 bp, 195 bp | 1070 bp | *05:08, 05:30, 05:52 | *02:51, 08:29, 08:31, B*15:33 |
| 116,11 | 115 bp, 205 bp | 1070 bp | *05:25, 05:33, 05:42 | *06:05, 06:67, 07:101, 07:148, 07:161, 08:28, A*80:01w-80:02w |
| 1212 | 225 bp, 285 bp | 1070 bp | *05:10, 05:38 | *08:44 |
| 136 | 95 bp | 1070 bp | *05:11, 05:17, 05:27, 05:68, 05:70 | *03:87, 07:130, 08:04, 08:13 |
| 146 | 120 bp | 1070 bp | *05:12, 05:15 |  |
| 1513 | 185 bp, 240 bp | 1070 bp | *05:13, 05:34 | *06:13 |
| 16 | 195 bp | 1070 bp | *05:14 |  |
| 17 | 155 bp | 1070 bp | *05:12, 05:18:01 | *08:01:01-08:01:05, 08:03:01-08:03:02, 08:06, 08:08-08:11, 08:14, 08:16, 08:20-08:22, 08:24, 08:26N-08:27, 08:33:02, 08:35-08:36N, 08:38-08:42, 08:44, 08:46, 08:50, 08:54, 08:56 |
| 18 | 235 bp | 1070 bp | *05:19 |  |
| 19 | 175 bp | 800 bp | *05:20 | *01:43, 07:101, 07:148, 07:161, 08:01:01-08:09, 08:11-08:12, 08:14-08:15:02, 08:17, 08:19-08:24, 08:26N-08:54, 08:56 |
| 2014 | 205 bp, 390 bp | 1070 bp | *05:21, 05:26 |  |
| 21 | 230 bp | 1070 bp | *05:04, 05:22:01-05:22:02 | *07:04:01-07:04:07, 07:11-07:12, 07:63, 07:68, 07:101, 07:139, 07:142, 07:181, 07:199, 08:09, 08:11 |
| 226 | 100 bp | 800 bp | *05:23, 05:62 | *08:07, 08:47 |
| 236,15 | 85 bp, 135 bp | 1070 bp | *05:24, 05:36 | *07:148 |
| 2416 | 185 bp, 265 bp | 1070 bp | *05:29, 05:43 | *08:13, 08:16, 08:25, 08:37 |
| 256,17 | 105 bp, 205 bp | 1070 bp | *05:35, 05:40 |  |
| 266,18 | 115 bp, 185 bp | 1070 bp | *05:27-05:28, 05:39 | *03:87, 06:64, B*15:33 |
| 27 | 155 bp | 1070 bp | *05:42, 05:46 | *06:67, 07:101, 07:148, 07:161, 08:05, 08:21, 17:05 |
| 287 | 200 bp | 800 bp | *05:45 |  |
| 2919 | 140 bp, 185 bp, 260 bp | 1070 bp | *05:34, 05:37, 05:41 | *04:78, 06:13 |
| 306,20 | 70 bp, 175 bp | 1070 bp | *05:32, 05:53 |  |
| 31 | 155 bp | 1070 bp | *05:18:02-05:18:03 | *07:04:01-07:04:07, 07:11-07:12, 07:63, 07:68, 07:101, 07:139, 07:142, 07:181, 07:199, 08:33:01 |
| 326,21 | 105 bp, 175 bp | 1070 bp | *05:48N, 05:51Q |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-C*05 SSP subtypings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-C*05 subtyping.

In addition, wells number 4, 8 19, 22 and 28 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3The C*05:18:01 and C*08:10 and the C*05:29 and C*08:25 alleles will give rise to identical amplification patterns with the HLA-C*05 subtyping kit. These alleles can be distinguished by the HLA-C low resolution kit and/or the C*08 subtyping kit.

4For several HLA-C*05 alleles nucleotide sequences are only available from the 2nd and 3rd exon. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in the 4th exon and in the introns are conserved within allelic groups.

5Due to the sharing of sequence motifs between HLA-C alleles non-HLA-C*05 alleles will be amplified by primer mixes 1 to 7, 10 to 13, 15, 17, 19, 21 to 24, 26, 27, 29 and 31. In addition, the A*29:10 and A*68:69 alleles will be amplified by primer mix 6, the A*80 will be weakly amplified by primer mix 11 and the B*15:33 allele will be amplified by primer mixes 3, 10 and 26.

6Specific PCR fragments shorter than 125 base pairs have a lower intensity than longer PCR bands.

7Primer mix 28 may give rise to primer oligomer formation.

8Primer mix 5: Specific PCR fragment of 225 bp in the C*05:04 and in the C*07:68, 08:09 and 08:11 alleles. Specific PCR fragment of 285 bp in the C*05:31 allele.

9Primer mix 8: Specific PCR fragment of 85 bp in the C*05:06 allele. Specific PCR fragment of 210 bp in the C*05:55 allele.

10Primer mix 10: Specific PCR fragment of 95 bp in the C*05:08 and 05:52 and the C*02:51, 08:29 and 08:31 and in the B*15:33 alleles. Specific PCR fragment of 195 bp in the C*05:30 allele.

11Primer mix 11: Specific PCR fragment of 115 bp in the C*05:33 allele. Specific PCR fragment of 205 bp in the C*05:25 and 05:42 and the C*06:05, 06:67, 07:101, 07:148, 07:161 and 08:28 and in the A*80:01w-80:02w alleles.

12Primer mix 12: Specific PCR fragment of 225 bp in the C*05:38 allele. Specific PCR fragment of 285 bp in the C*05:10 and the C*08:44 alleles.

13Primer mix 15: Specific PCR fragment of 185 bp in the C*05:34 and in the C*06:13 alleles. Specific PCR fragment of 240 bp in the C*05:13 allele.

14Primer mix 20: Specific PCR fragment of 205 bp in the C*05:26 allele. Specific PCR fragment of 390 bp in the C*05:21 allele.

15Primer mix 23: Specific PCR fragment of 85 bp in the C*05:24 allele. Specific PCR fragment of 135 bp in the C*05:36 and in the C*07:148 alleles.

16Primer mix 24: Specific PCR fragment of 185 bp in the C*05:43 and the C*08:37 alleles. Specific PCR fragment of 265 bp in the C*05:29 and in the C*08:13, 08:16 and 08:25 alleles.

17Primer mix 25: Specific PCR fragment of 105 bp in the C*05:40 allele. Specific PCR fragment of 205 bp in the C*05:35 allele.

18Primer mix 26: Specific PCR fragment of 115 bp in the C*05:27 and 05:39 and in the C*03:87 and in the B*15:33 alleles. Specific PCR fragment of 185 bp in the C*05:28 and the C*06:64 alleles.

19Primer mix 29: Specific PCR fragment of 140 bp in the C*05:41 and the C*04:78 alleles. Specific PCR fragment of 185 bp in the C*05:34 and in the C*06:13 alleles. Specific PCR fragment of 260 bp in the C*05:37 allele.

20Primer mix 30: Specific PCR fragment of 70 bp in the C05:53 allele. Specific PCR fragment of 175 bp in the C*05:32 allele.

21Primer mix 32: Specific PCR fragment of 105 bp in the C*05:51Q allele. Specific PCR fragment of 175 bp in the C*05:48N allele.

’w’, might be weakly amplified.

1The A-Cw*0502 nucleotide sequence has been deleted as it is identical to C*05:09.

2The C*05:18:01 and C*08:10 and the C*05:29 and C*08:25 alleles will give rise to identical amplification patterns with the HLA-C*05 subtyping kit. These alleles can be distinguished by the HLA-C low resolution kit and/or the C*08 subtyping kit.

3HLA-C*05 alleles in bold lettering are listed as confirmed alleles on the IMGT/HLA web page www.ebi.ac.uk/imgt/hla, release 3.7.0, January 2012.

4The C*05:06 and C*05:55 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 8.

5The C*05:08 and C*05:30 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 10.

6The C*05:10 and C*05:38 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 12.

7The C*05:21 and C*05:26 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 20.

8The C*05:24 and C*05:36 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 23.

9The C*05:25 and C*05:33 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 11.

10The C*05:28 and C*05:39 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 26.

11The C*05:35 and C*05:40 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 25.

12The C*05:37 and C*05:41 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 29.

13Primer mix 5: Specific PCR fragment of 225 bp in the C*05:04 and in the C*07:68, 08:09 and 08:11 alleles. Specific PCR fragment of 285 bp in the C*05:31 allele.

Primer mix 8: Specific PCR fragment of 85 bp in the C*05:06 allele. Specific PCR fragment of 210 bp in the C*05:55 allele.

Primer mix 10: Specific PCR fragment of 95 bp in the C*05:08 and 05:52 and the C*02:51, 08:29 and 08:31 and in the B*15:33 alleles. Specific PCR fragment of 195 bp in the C*05:30 allele.

Primer mix 11: Specific PCR fragment of 115 bp in the C*05:33 allele. Specific PCR fragment of 205 bp in the C*05:25 and 05:42 and the C*06:05, 06:67, 07:101, 07:148, 07:161 and 08:28 and in the A*80:01w-80:02w alleles.

Primer mix 12: Specific PCR fragment of 225 bp in the C*05:38 allele. Specific PCR fragment of 285 bp in the C*05:10 and the C*08:44 alleles.

Primer mix 15: Specific PCR fragment of 185 bp in the C*05:34 and in the C*06:13 alleles. Specific PCR fragment of 240 bp in the C*05:13 allele.

Primer mix 20: Specific PCR fragment of 205 bp in the C*05:26 allele. Specific PCR fragment of 390 bp in the C*05:21 allele.

Primer mix 23: Specific PCR fragment of 85 bp in the C*05:24 allele. Specific PCR fragment of 135 bp in the C*05:36 and in the C*07:148 alleles.

Primer mix 24: Specific PCR fragment of 185 bp in the C*05:43 and the C*08:37 alleles. Specific PCR fragment of 265 bp in the C*05:29 and in the C*08:13, 08:16 and 08:25 alleles.

Primer mix 25: Specific PCR fragment of 105 bp in the C*05:40 allele. Specific PCR fragment of 205 bp in the C*05:35 allele.

Primer mix 26: Specific PCR fragment of 115 bp in the C*05:27 and 05:39 and in the C*03:87 and in the B*15:33 alleles. Specific PCR fragment of 185 bp in the C*05:28 and the C*06:64 alleles.

Primer mix 29: Specific PCR fragment of 140 bp in the C*05:41 and the C*04:78 alleles. Specific PCR fragment of 185 bp in the C*05:34 and in the C*06:13 alleles. Specific PCR fragment of 260 bp in the C*05:37 allele.

Primer mix 30: Specific PCR fragment of 70 bp in the C05:53 allele. Specific PCR fragment of 175 bp in the C*05:32 allele.

Primer mix 32: Specific PCR fragment of 105 bp in the C*05:51Q allele. Specific PCR fragment of 175 bp in the C*05:48N allele.

’w’, might be weakly amplified.