PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-C*06

Prod. No:	101.614-12/12u

Lot No:    	76N

Expiry Date:    	2015-January-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 41 primer mixes used for HLA-C*06 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-C*06 alleles3 | Other amplified HLA Class I alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 240 bp | 800 bp | *06:02:01:01-06:02:01:02, 06:02:03-06:02:19, 06:04-06:16N, 06:18-06:75 | *03:39, 03:67, 04:42, 05:43, 08:37, 12:16, 16:21 |
| 2 | 220 bp | 800 bp | *06:02:01:01-06:02:01:02, 06:02:03-06:03:02, 06:07-06:13, 06:15-06:34, 06:36-06:39, 06:41-06:71, 06:73-06:76 | *01:04, 01:09, 02:05, 02:17, 12:03:01:01-12:07, 12:11-12:13, 12:15, 12:23, 12:25-12:26, 12:28-12:29, 12:31-12:35, 12:37-12:39N, 12:42Q-12:43, 12:45-12:48, 12:50-12:55, 12:57-12:63, 12:65-12:66, 12:70-12:71, 12:75-12:76, 14:16, 16:04, 16:29, 16:33, 16:42 |
| 3 | 135 bp | 1070 bp | *06:03:01, 06:18 | *02:02:13, 03:02:01-03:04:14, 03:04:16-03:04:24, 03:05-03:17, 03:19-03:38:02, 03:40:01-03:66, 03:67w, 03:68-03:98, 03:100-03:117, 03:119-03:136, 03:138-03:143, 03:146, 07:96, 15:02:10, 15:43 |
| 4 | 250 bp | 1070 bp | *06:04 | *01:22, 01:35, 05:11, 05:17, 05:27, 05:68, 08:01:01-08:01:05, 08:03:01-08:04:02, 08:06, 08:08-08:11, 08:13-08:14, 08:16:01-08:16:02, 08:20-08:22, 08:24, 08:26N, 08:36N, 08:38-08:42, 08:44, 08:46, 08:50, 08:54, 08:56-08:60, 12:14:01-12:14:02, 12:18:01-12:18:02, 12:20, 14:06, 14:15, 15:02:01-15:07, 15:09-15:13, 15:15-15:24, 15:26-15:50, 15:52-15:60, 16:35, 16:40, 17:01:01:01-17:11, B*58:02 |
| 57 | 165 bp, 220 bp | 800 bp | *06:05, 06:18, 06:23, 06:67 | *01:04, 01:09, 02:21, 05:01:01:01-05:01:18, 05:03-05:28, 05:30-05:47, 05:49-05:74, 08:10, 12:21, 12:33, 17:05 |
| 6 | 250 bp | 1070 bp | *06:05-06:06 | *01:02:01-01:03, 01:05-01:08, 01:10-01:20, 01:23-01:34, 01:36-01:66, 05:01:01:01-05:01:18, 05:03-05:07N, 05:09:01-05:10, 05:12-05:16, 05:18:01-05:26, 05:28-05:50, 05:53-05:61, 05:63-05:67, 05:69, 05:71-05:74, 08:02:01-08:02:07, 08:05, 08:07, 08:12, 08:15:01-08:15:02, 08:17-08:19, 08:23, 08:25, 08:28, 08:30, 08:32-08:35, 08:37, 08:43, 08:45, 08:47-08:49, 08:51-08:53, 08:55N, 12:09, 12:24, 14:02:01-14:05, 14:07N-14:14, 14:17-14:37, 15:08, 18:01-18:02, 18:04-18:05 |
| 75,8 | 110 bp, 185 bp, 235 bp | 1070 bp | *06:07, 06:19, 06:33 |  |
| 8 | 240 bp | 1070 bp | *06:08 | *01:10, 02:05, 02:17, 14:25, 16:29 |
| 99 | 165 bp, 210 bp, 435 bp | 1070 bp | *06:09, 06:17, 06:23 | *01:04, 01:09, 02:22, 04:94:01-04:94:02, 05:08, 05:52, 07:07, 07:09, 07:76, 08:27, 08:29, 08:31, 12:31, 18:01-18:05, B*15:137 |
| 10 | 190 bp | 800 bp | *06:10, 06:22 | *07:107, 07:224, 16:31, B*15:193 |
| 1110 | 130 bp, 185 bp | 1070 bp | *06:11, 06:22 | *07:01:13, 07:04:01-07:04:07, 07:11-07:12, 07:45, 07:63, 07:68, 07:101, 07:107, 07:139, 07:142, 07:181, 07:199, 07:224, 12:03:09, 16:31, B*15:193 |
| 126,11 | 205 bp, 275 bp | 1070 bp | *06:12, 06:20 | *01:32, 02:56, 03:102, 07:81, 07:168, 12:50 |
| 1312 | 155 bp, 210 bp | 1070 bp | *06:13, 06:59 |  |
| 1413 | 225 bp, 305 bp | 1070 bp | *06:14, 06:55 | *03:32, 03:45, 03:136, 04:80, 04:100, 07:10, 07:43, 07:196, 15:25, B*35:178 |
| 15 | 360 bp | 800 bp | *06:15 |  |
| 166,14 | 235 bp, 340 bp | 1070 bp | *06:16N, 06:21 |  |
| 176,15 | 160 bp, 220 bp | 1070 bp | *06:24, 06:37, 06:59 | *01:20 |
| 18 | 220 bp | 1070 bp | *06:26 |  |
| 195,16 | 85 bp, 160 bp | 800 bp | *06:28, 06:32 | *02:14, 03:67, 04:42, 05:43, 07:20, 07:73, 07:172, 08:37, 15:23, 16:21, 18:04, B*08:56, B*15:142, B*51:68, B*57:49 |
| 205,17 | 115 bp, 275 bp | 1070 bp | *06:27, 06:29 | *07:134 |
| 2118 | 190 bp, 380 bp | 1070 bp | *06:25, 06:36 | *04:81, 12:56 |
| 22 | 170 bp | 1070 bp | *06:30 | *02:02:13, 07:181, 12:03:09 |
| 23 | 205 bp | 1070 bp | *06:31 | *16:04, 16:29, 16:33, 16:42 |
| 2419 | 160 bp, 210 bp | 1070 bp | *06:09, 06:34-06:35 | *02:22, 02:47, 04:94:01-04:94:02, 05:08, 05:52, 08:27, 08:29, 08:31, 12:31, 18:03, B*13:31, B*13:41, B*15:58, B*15:73, B*15:137, B*39:36, B*55:21 |
| 255 | 85 bp | 1070 bp | *06:38 |  |
| 26 | 130 bp | 1070 bp | *06:39 |  |
| 276,20 | 190 bp, 225 bp | 1070 bp | *06:40, 06:42 | *14:29 |
| 285,21 | 90 bp, 210 bp | 1070 bp | *06:41, 06:47 | *12:11, 12:32 |
| 2922 | 175 bp, 210 bp | 1070 bp | *06:43, 06:47 | *12:11, B*15:207 |
| 305 | 100 bp | 1070 bp | *06:44 | *07:01:13 |
| 31 | 155 bp | 1070 bp | *06:45 |  |
| 3223 | 185 bp, 205 bp | 1070 bp | *06:19, 06:66 |  |
| 335,24 | 105 bp, 245 bp | 1070 bp | *06:60, 06:69 |  |
| 34 | 275 bp | 1070 bp | *06:20 | *01:32, 02:56, 03:102, 07:81, 07:168, 12:50 |
| 3525 | 230 bp, 380 bp | 1070 bp | *06:46N, 06:65 |  |
| 365,26 | 120 bp, 215 bp | 1070 bp | *06:57-06:58 |  |
| 37 | 205 bp | 1070 bp | *06:49N |  |
| 385,27 | 120 bp, 470 bp | 1070 bp | *06:70, 06:73 | *02:02:13, 08:20, 08:40 |
| 39 | 290 bp | 1070 bp | *06:50 | *02:20, 12:53 |
| 40 | 275 bp | 1070 bp | *06:54 |  |
| 41 | 155 bp | 1070 bp | *06:03:01-06:03:02, 06:76 | *02:02:13, 12:03:09, B*51:39 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-C*06 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells. Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-C*06 subtyping. In addition, wells number 2, 5, 10, 15 and 19 contain the primer pair giving rise to the shorter, 800 bp, internal positive control in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several HLA-C*06 alleles 1st, 4th and 5th exon or intron nucleotide sequences are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in these regions are conserved within allelic groups.

4Due to the sharing of sequence motifs between HLA-C alleles non-HLA-C*06 alleles will be amplified by primer mixes 1 to 6, 8 to 12, 14, 17, 19 to 24, 27 to 30, 34, 38, 39 and  41. In addition, the B*58:02 allele will be amplified by primer mix 4, the B*15:137 allele will be amplified by the primer mix 9, the B*15:193 allele will be amplified by the primer mix 10 and 11, the B*35:178 allele will be amplified by the primer mix 14, the B*08:56, B*15:142, B*51:68 and B*57:49 alleles will be amplified by primer mix 19, the B*13:31, B*13:41, B*15:58, B*15:73, B*15:137, B*39:36 and B*55:21 alleles will be amplified by primer mix 24, the B B*15:207 allele will be amplified by the primer mix 29 and the B*51:39 allele will be amplified by the primer mix 41.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6Primer mixes 12, 16, 17 and 27 have a tendency of giving rise to primer oligomer formation.

7Primer mix 5: Specific PCR fragment of 165 bp in the C*06:05 and 06:67 and in the C*05:01:01:01-05:01:18, 05:03-05:28, 05:30-05:47, 05:49-05:74, 08:10, 12:21, 12:33 and 17:05 alleles. Specific PCR fragment of 220 bp in the C*06:18 and 06:23 and the C*01:04, 01:09 and 02:21 alleles.

8Primer mix 7: Specific PCR fragment of 110 bp in the C*06:07 allele. Specific PCR fragment of 185 bp in the C*06:19 allele. Specific PCR fragment of 235 bp in the C*06:33 allele.

9Primer mix 9: Specific PCR fragment of 165 bp in the C*06:09 and the C*02:22, 04:94:01-04:94:02, 05:08, 05:52, 08:27, 08:29, 08:31, 12:31 and 18:03 alleles and in addition the B*15:137 allele. Specific PCR fragment of 210 bp in the C*06:23 and the C*01:04 and 01:09 alleles. Specific PCR fragment of 435 bp in the C*06:17 and the C*07:07, 07:09, 07:76, 18:01, 18:02, 18:04 and 18:05 alleles. Specific PCR fragments of 165 and 435 bp in the C*18:03 allele.

10Primer mix 11: Specific PCR fragment of 130 bp in the C*06:11 and the C*07:01:13, 07:04:01-07:04:07, 07:11-07:12, 07:45, 07:63, 07:68, 07:101, 07:139, 07:142, 07:181, 07:199 and 12:03:09 alleles. Specific PCR fragment of 185 bp in the C*06:22 and the C*07:107, 07:224 and 16:31 alleles and in addition in the B*15:193 allele.

11Primer mix 12: Specific PCR fragment of 205 bp in the C*06:12 allele. Specific PCR fragment of 275 bp in the C*06:20 and in the C*01:32, 02:56, 03:102, 07:81, 07:168 and 12:50 alleles.

12Primer mix 13: Specific PCR fragment of 155 bp in the C*06:13 allele. Specific PCR fragment of 210 bp in the C*06:59 allele.

13Primer mix 14: Specific PCR fragment of 225 bp in the C*06:55 allele. Specific PCR fragment of 305 bp in the C*06:14 and in the C*03:32, 03:45, 03:136, 04:80, 04:100, 07:10, 07:43, 07:196 and 15:25 alleles and in addition in the B*35:178 allele.

14Primer mix 16: Specific PCR fragment of 235 bp in the C*06:16N allele. Specific PCR fragment of 340 bp in the C*06:21 allele.

15Primer mix 17: Specific PCR fragment of 160 bp in the C*06:37 and the C*01:20 alleles. Specific PCR fragment of 220 bp in the C*06:24 and 06:59 alleles.

16Primer mix 19: Specific PCR fragment of 85 bp in the C*06:28 and the C*02:14, 03:67, 04:42, 05:43, 07:20, 07:73, 07:172, 08:37, 15:23, 16:21 and 18:04 alleles and in addition in the B*08:56, B*15:142, B*51:68 and B*57:49 alleles. Specific PCR fragment of 160 bp in the C*06:32 allele.

17Primer mix 20: Specific PCR fragment of 115 bp in the C*06:29 and the C*07:134 alleles. Specific PCR fragment of 275 bp in the C*06:27 allele.

18Primer mix 21: Specific PCR fragment of 190 bp in the C*06:36 and the C*12:56 alleles. Specific PCR fragment of 380 bp in the C*06:25 and the C*04:81 alleles.

19Primer mix 24: Specific PCR fragment of 160 bp in the C*06:09 and 06:34 and the C*02:22, 02:47, 04:94:01-04:94:02, 05:08, 05:52, 08:27, 08:29, 08:31, 12:31 and 18:03 alleles, and in addition in the B*13:31, B*13:41, B*15:58, B*15:73, B*15:137, B*39:36 and B*55:21 alleles. Specific PCR fragment of 210 bp in the C*06:35 allele.

20Primer mix 27: Specific PCR fragment of 190 bp in the C*06:42 and the C*14:29 alleles. Specific PCR fragment of 225 bp in the C*06:40 allele.

21Primer mix 28: Specific PCR fragment of 90 bp in the C*06:41 and the C*12:32 alleles. Specific PCR fragment of 210 bp in the C*06:47 and the C*12:11 alleles.

22Primer mix 29: Specific PCR fragment of 175 bp in the C*06:43 allele and in addition in the B*15:207 allele. Specific PCR fragment of 210 bp in the C*06:47 and the C*12:11 alleles.

23Primer mix 32: Specific PCR fragment of 185 bp in the C*06:19 allele. Specific PCR fragment of 205 bp in the C*06:66 allele.

24Primer mix 33: Specific PCR fragment of 105 bp in the C*06:60 allele. Specific PCR fragment of 245 bp in the C*06:69 allele.

25Primer mix 35: Specific PCR fragment of 230 bp in the C*06:65 allele. Specific PCR fragment of 380 bp in the C*06:46N allele.

26Primer mix 36: Specific PCR fragment of 120 bp in the C*06:57 allele. Specific PCR fragment of 215 bp in the C*06:58 allele.

27Primer mix 38: Specific PCR fragment of 120 bp in the C*06:70 and the C*02:02:13 alleles. Specific PCR fragment of 470 bp in the C*06:73 and the C*08:20 and 08:40 alleles.

‘w’, may be weakly amplified.

1The sequence of the C*0601 allele has been shown to be identical to C*06:02.

The sequence of the C*060202 allele has been renamed to C*06:17.

2HLA-C*06 alleles in bold lettering are listed as confirmed alleles on the IMGT/HLA web page www.ebi.ac.uk/imgt/hla, release 3.8.0, April 2012.

3The C*06:07 and C*06:33 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 7.

4The C*06:16N and C*06:21 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 16.

5The C*06:24 and C*06:37 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 17.

6The C*06:25 and C*06:36 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 21.

7The C*06:27 and C*06:29 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 20.

8The C*06:28 and C*06:32 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 19.

9The C*06:46N and C*06:65 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 35.

10The C*06:57 and C*06:58 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 36.

11The C*06:60 and C*06:69 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 33.

12The C*06:70 and C*06:73 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 38.

13The HLA-C*06 primer set cannot separate the C*06:72 and the C*03:39 and 12:16 alleles. These alleles can be distinguished by the HLA-C low resolution kit and/or the HLA-C*03 and HLA-C*12 high resolution kit.

14Primer mix 5: Specific PCR fragment of 165 bp in the C*06:05 and 06:67 and in the C*05:01:01:01-05:01:18, 05:03-05:28, 05:30-05:47, 05:49-05:74, 08:10, 12:21, 12:33 and 17:05 alleles. Specific PCR fragment of 220 bp in the C*06:18 and 06:23 and the C*01:04, 01:09 and 02:21 alleles.

Primer mix 7: Specific PCR fragment of 110 bp in the C*06:07 allele. Specific PCR fragment of 185 bp in the C*06:19 allele. Specific PCR fragment of 235 bp in the C*06:33 allele.

Primer mix 9: Specific PCR fragment of 165 bp in the C*06:09 and the C*02:22, 04:94:01-04:94:02, 05:08, 05:52, 08:27, 08:29, 08:31, 12:31 and 18:03 alleles and in addition the B*15:137 allele. Specific PCR fragment of 210 bp in the C*06:23 and the C*01:04 and 01:09 alleles. Specific PCR fragment of 435 bp in the C*06:17 and the C*07:07, 07:09, 07:76, 18:01, 18:02, 18:04 and 18:05 alleles. Specific PCR fragments of 165 and 435 bp in the C*18:03 allele.

Primer mix 11: Specific PCR fragment of 130 bp in the C*06:11 and the C*07:01:13, 07:04:01-07:04:07, 07:11-07:12, 07:45, 07:63, 07:68, 07:101, 07:139, 07:142, 07:181, 07:199 and 12:03:09 alleles. Specific PCR fragment of 185 bp in the C*06:22 and the C*07:107, 07:224 and 16:31 alleles and in addition in the B*15:193 allele.

Primer mix 12: Specific PCR fragment of 205 bp in the C*06:12 allele. Specific PCR fragment of 275 bp in the C*06:20 and in the C*01:32, 02:56, 03:102, 07:81, 07:168 and 12:50 alleles.

Primer mix 13: Specific PCR fragment of 155 bp in the C*06:13 allele. Specific PCR fragment of 210 bp in the C*06:59 allele.

Primer mix 14: Specific PCR fragment of 225 bp in the C*06:55 allele. Specific PCR fragment of 305 bp in the C*06:14 and in the C*03:32, 03:45, 03:136, 04:80, 04:100, 07:10, 07:43, 07:196 and 15:25 alleles and in addition in the B*35:178 allele.

Primer mix 16: Specific PCR fragment of 235 bp in the C*06:16N allele. Specific PCR fragment of 340 bp in the C*06:21 allele.

Primer mix 17: Specific PCR fragment of 160 bp in the C*06:37 and the C*01:20 alleles. Specific PCR fragment of 220 bp in the C*06:24 and 06:59 alleles.

Primer mix 19: Specific PCR fragment of 85 bp in the C*06:28 and the C*02:14, 03:67, 04:42, 05:43, 07:20, 07:73, 07:172, 08:37, 15:23, 16:21 and 18:04 alleles and in addition in the B*08:56, B*15:142, B*51:68 and B*57:49 alleles. Specific PCR fragment of 160 bp in the C*06:32 allele.

Primer mix 20: Specific PCR fragment of 115 bp in the C*06:29 and the C*07:134 alleles. Specific PCR fragment of 275 bp in the C*06:27 allele.

Primer mix 21: Specific PCR fragment of 190 bp in the C*06:36 and the C*12:56 alleles. Specific PCR fragment of 380 bp in the C*06:25 and the C*04:81 alleles.

Primer mix 24: Specific PCR fragment of 160 bp in the C*06:09 and 06:34 and the C*02:22, 02:47, 04:94:01-04:94:02, 05:08, 05:52, 08:27, 08:29, 08:31, 12:31 and 18:03 alleles, and in addition in the B*13:31, B*13:41, B*15:58, B*15:73, B*15:137, B*39:36 and B*55:21 alleles. Specific PCR fragment of 210 bp in the C*06:35 allele.

Primer mix 27: Specific PCR fragment of 190 bp in the C*06:42 and the C*14:29 alleles. Specific PCR fragment of 225 bp in the C*06:40 allele.

Primer mix 28: Specific PCR fragment of 90 bp in the C*06:41 and the C*12:32 alleles. Specific PCR fragment of 210 bp in the C*06:47 and the C*12:11 alleles.

Primer mix 29: Specific PCR fragment of 175 bp in the C*06:43 allele and in addition in the B*15:207 allele. Specific PCR fragment of 210 bp in the C*06:47 and the C*12:11 alleles.

Primer mix 32: Specific PCR fragment of 185 bp in the C*06:19 allele. Specific PCR fragment of 205 bp in the C*06:66 allele.

Primer mix 33: Specific PCR fragment of 105 bp in the C*06:60 allele. Specific PCR fragment of 245 bp in the C*06:69 allele.

Primer mix 35: Specific PCR fragment of 230 bp in the C*06:65 allele. Specific PCR fragment of 380 bp in the C*06:46N allele.

Primer mix 36: Specific PCR fragment of 120 bp in the C*06:57 allele. Specific PCR fragment of 215 bp in the C*06:58 allele.

Primer mix 38: Specific PCR fragment of 120 bp in the C*06:70 and the C*02:02:13 alleles. Specific PCR fragment of 470 bp in the C*06:73 and the C*08:20 and 08:40 alleles.

‘w’, may be weakly amplified.