PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-C*12

Prod. No:	101.624-12/12u

Lot No:    	26S

Expiry Date:    	2015-October-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 32 primer mixes used for HLA-C*12 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-C*12 alleles3 | Other amplified HLA Class I alleles4 |
| --- | --- | --- | --- | --- |
| 16 | 235 bp | 800 bp | *12:02:01-12:03:12, 12:03:13w, 12:03:14-12:04:02, 12:06-12:08, 12:10:01-12:15, 12:17-12:20, 12:22-12:32, 12:34-12:48, 12:50-12:54, 12:56-12:94 | *02:12, 02:49, 02:55, 03:15, 03:27, 03:38:01-03:38:02, 03:53, 03:69, 03:130, 03:136, 03:163, 04:03, 04:06, 04:16, 04:80, 04:103, 04:107, 05:42, 05:46, 06:03:01-06:03:02, 06:76:01-06:76:02, 07:26, 07:92, 07:96:01-07:96:02, 08:05, 08:21, 08:25, 15:03, 15:16, 15:25, 16:15:01-16:15:02, 16:25, 17:01:01:01-17:19, B*07:13, B*07:15, B*07:160, B*67:02 |
| 25 | 100 bp | 1070 bp | *12:02:01-12:02:05, 12:02:07, 12:02:09, 12:03:19, 12:08, 12:10:01-12:10:02, 12:14:02, 12:16-12:18:01, 12:22, 12:27, 12:30, 12:36, 12:40-12:41, 12:44, 12:49, 12:56, 12:64, 12:67-12:69, 12:72-12:74, 12:80N, 12:83-12:86 | *01:04, 01:21 |
| 3 | 220 bp | 800 bp | *12:03:01:01-12:07, 12:11-12:13, 12:15, 12:23, 12:25-12:26, 12:28-12:29, 12:31-12:35, 12:37-12:39N, 12:42Q-12:43, 12:45-12:48, 12:50-12:55, 12:57-12:63, 12:65-12:66, 12:70-12:71, 12:75-12:79, 12:81-12:82, 12:87-12:94 | *01:04, 01:09, 02:05, 02:17, 06:02:01:01-06:02:01:02, 06:02:03-06:02:15, 06:02:17-06:03:02, 06:07-06:13, 06:15-06:34, 06:36-06:39, 06:41-06:71, 06:73-06:78, 06:80, 06:82-06:96, 14:16, 16:04:01, 16:29, 16:33, 16:42, 16:55 |
| 4 | 340 bp | 1070 bp | *12:04:01-12:05, 12:09, 12:21, 12:33, 12:41, 12:54, 12:60 | *01:14, 01:59, 02:02:01-02:02:03, 02:02:05-02:02:11, 02:02:13-02:11, 02:13-02:26:03, 02:28-02:40, 02:42-02:67, 03:07, 03:15, 03:45, 03:130, 03:140, 03:163, 04:01:01:01-04:01:28, 04:01:30-04:01:48, 04:03-04:10, 04:12-04:20, 04:23-04:28, 04:30-04:35, 04:37-04:54, 04:56-04:144, 05:01:01:01-05:01:26, 05:03-05:87, 06:02:01:01-06:02:01:02, 06:02:03-06:02:11, 06:02:13-06:10, 06:12-06:51, 06:53:01-06:96, 07:07, 07:09, 07:49, 07:76, 07:210, 07:238, 07:247, 08:10, 14:04, 14:12, 14:49, 15:02:01-15:06:03, 15:08-15:13, 15:15-15:19, 15:22-15:24, 15:26-15:42, 15:44-15:66, 16:02:01-16:02:09, 16:09, 16:12, 16:19, 16:25, 16:46-16:48, 17:01:01:01-17:19, 18:01-18:06 |
| 56 | 130 bp | 1070 bp | *12:05, 12:09, 12:21, 12:33, 12:49 | *02:02:01-02:02:03, 02:02:05-02:02:07, 02:02:09-02:02:12, 02:02:14-02:02:20, 02:02:21w, 02:02:22-02:11, 02:13-02:40, 02:42-02:48, 02:50-02:54, 02:56-02:62, 02:64-02:67, 03:04:25, 04:10-04:11, 04:36, 04:55, 05:01:01:01-05:01:11, 05:01:13-05:01:23, 05:01:24w, 05:01:25-05:01:26, 05:03-05:29:01, 05:30-05:41, 05:43-05:45, 05:47-05:87, 06:05, 08:01:01-08:02:02, 08:02:04-08:04:03, 08:06-08:20, 08:22-08:24, 08:26N-08:63, 08:65-08:72, 08:74, 14:02:03, 14:03, 14:08, 14:10, 14:22, 14:35N, 14:38, 14:41, 15:02:01-15:02:09, 15:02:11-15:02:15, 15:04-15:13, 15:15, 15:17-15:19, 15:21-15:24, 15:26-15:42, 15:44, 15:45w, 15:46-15:66, 16:01:01, 16:01:03-16:02:09, 16:04:01, 16:06-16:14, 16:16Q-16:24, 16:26-16:55 |
| 65,9 | 75 bp, 150 bp, 415 bp | 1070 bp | *12:06, 12:08, 12:48, 12:81 | *03:08, 03:29, 03:31, 04:112, 05:36, 06:44 |
| 7 | 140 bp | 800 bp | *12:04:02-12:05, 12:09, 12:21, 12:33, 12:41, 12:54, 12:60 | *02:02:01-02:02:03, 02:02:05-02:02:07, 02:02:09-02:02:11, 02:02:14-02:11, 02:13-02:26:03, 02:28-02:40, 02:42-02:62, 02:64-02:67, 04:01:01:01-04:01:09, 04:01:11-04:01:22, 04:01:24-04:01:28, 04:01:30-04:01:48, 04:03-04:10, 04:12-04:20, 04:23-04:28, 04:30-04:35, 04:37-04:54, 04:56-04:129, 04:131-04:144, 05:01:01:01-05:01:11, 05:01:13-05:01:23, 05:01:24w, 05:01:25-05:01:26, 05:03-05:29:01, 05:30-05:87, 06:05, 06:76:02, 08:10, 15:02:01-15:02:09, 15:02:11-15:06:03, 15:08-15:13, 15:15-15:19, 15:22-15:24, 15:26-15:42, 15:44-15:66, 16:02:01-16:02:09, 16:09, 16:12, 16:19, 16:25, 16:46-16:48, 17:01:04 |
| 85,10 | 95 bp, 155 bp, 195 bp, 245 bp | 1070 bp | *12:07, 12:15, 12:40, 12:80N | *15:02:14, 16:14 |
| 95 | 95 bp | 1070 bp | *12:02:01-12:04:02, 12:06-12:08, 12:10:01-12:20, 12:22-12:27, 12:29-12:32, 12:34-12:48, 12:50-12:57, 12:59-12:62, 12:64-12:94 | *01:17, 01:21, 02:12, 02:55, 03:27, 03:38:01-03:38:02, 03:130, 03:163, 04:33, 04:107, 05:46, 06:30, 07:07, 07:16, 07:51, 07:181, 08:05, 08:21, 08:25, 14:04, 15:03, 15:16, 16:15:01-16:15:02, 16:25, 17:01:01:01-17:10, 17:12-17:14, 17:16-17:19, B*07:13, B*67:02 |
| 10 | 155 bp | 1070 bp | *12:03:01:01-12:03:01:02, 12:03:03-12:03:07, 12:03:09-12:03:15, 12:03:17-12:03:18, 12:03:21-12:03:25, 12:04:02-12:07, 12:11-12:13, 12:15, 12:20, 12:23-12:25, 12:28-12:29, 12:31-12:32, 12:34-12:35, 12:37-12:39N, 12:42Q-12:43, 12:45-12:48, 12:50-12:55, 12:57-12:58, 12:60-12:63, 12:65-12:66, 12:70-12:71, 12:75-12:79, 12:81-12:82, 12:87-12:94 | *01:02:18, 06:76:02, 14:02:08, 16:15:02 |
| 118 | 220 bp | 1070 bp | *12:09, 12:24 | *01:02:01-01:03, 01:06-01:08, 01:10-01:20, 01:23-01:34, 01:37N-01:48, 01:51-01:54, 01:56N-01:75, 03:58, 03:86, 03:94, 03:99, 04:37, 05:16, 05:85, 06:05-06:06, 08:12, 14:02:01-14:05, 14:07N, 14:10-14:14, 14:17-14:27, 14:29-14:49, 16:53, B*14:03 |
| 12 | 140 bp | 1070 bp | *12:02:01-12:03:03, 12:03:05-12:03:08, 12:03:10-12:03:23, 12:03:24w, 12:03:25, 12:06-12:08, 12:10:01-12:20, 12:22-12:26, 12:28-12:32, 12:34-12:40, 12:42Q-12:53, 12:55-12:59, 12:61-12:71, 12:72w, 12:73-12:94 | *01:21, 02:12w, 02:27:01-02:27:02, 03:04:25, 04:11, 04:29, 04:36, 04:55, 07:02:09, 08:01:01-08:09, 08:11-08:63, 08:65-08:74, 14:02:03, 14:03, 14:08, 14:10, 14:22, 14:35N, 14:38, 14:41, 15:07, 15:21w, 15:25, 16:01:01, 16:01:03-16:01:13, 16:04:01, 16:06-16:08, 16:10-16:11, 16:13-16:18, 16:20-16:24, 16:26-16:36, 16:37w, 16:38-16:45, 16:49-16:55, B*35:08:02, B*35:08:05, B*67:02 |
| 135,11 | 105 bp, 150 bp | 1070 bp | *12:10:01-12:10:02, 12:31 | *04:01:05, 14:02:08 |
| 145,12 | 100 bp, 145 bp | 1070 bp | *12:11, 12:16 | *01:21, 02:42, 04:140, 06:05w, 07:02:09, 08:14, 15:63, B*67:02 |
| 158 | 140 bp | 1070 bp | *12:12 | *08:73, B*35:08:02, B*35:08:05 |
| 1613 | 185 bp, 225 bp | 1070 bp | *12:13-12:14:02 | *01:60, 04:58, 05:23, 05:62, 08:07, 08:47, 14:17, 15:65, 17:01:01:01-17:19 |
| 17 | 565 bp | 1070 bp | *12:03:04, 12:03:09 | *01:02:18, 14:02:08 |
| 1814 | 145 bp, 165 bp, 245 bp, 270 bp | 1070 bp | *12:17, 12:27, 12:35 | *03:53, 04:12 |
| 195 | 100 bp | 1070 bp | *12:14:02, 12:18:01, 12:25, 12:83 | *03:104, 07:01:20, 07:01:27, 07:02:38, B*18:77, B*40:29 |
| 205,15 | 105 bp, 170 bp, 220 bp | 1070 bp | *12:19, 12:22, 12:46N |  |
| 21 | 250 bp | 1070 bp | *12:14:01-12:14:02, 12:18:01-12:18:02, 12:20, 12:83 | *01:22, 01:35, 05:11, 05:17, 05:27, 05:68, 05:79, 06:04, 08:01:01-08:01:09, 08:03:01-08:04:03, 08:06, 08:08-08:11, 08:13-08:14, 08:16:01-08:16:02, 08:20-08:22, 08:24, 08:26N, 08:36N, 08:38-08:42, 08:44, 08:46, 08:50, 08:54, 08:56-08:61, 08:65-08:66, 08:72, 14:06, 14:15, 15:02:01-15:07, 15:09-15:13, 15:15-15:19, 15:21-15:24, 15:26-15:50, 15:52-15:66, 16:35, 16:40, 16:48, 17:01:01:01-17:16, 17:18-17:19, B*58:02 |
| 225, 16 | 95 bp, 110 bp, 590 bp | 1070 bp | *12:15, 12:21, 12:23 | *15:02:14 |
| 23 | 140 bp | 1070 bp | *12:26, 12:63 | *16:36 |
| 2417 | 185 bp, 425 bp | 1070 bp | *12:28, 12:43 | *04:01:05, 06:76:02 |
| 255,18 | 80 bp, 155 bp | 1070 bp | *12:02:06, 12:02:08, 12:21, 12:39N | *04:01:05, 08:02:02 |
| 26 | 355 bp | 800 bp | *12:44 | *03:38:01-03:38:02, 03:69, 03:130, 03:136, 03:163, 04:80, 04:100, 06:14, 07:10, 07:43, 07:196, 15:03, 15:16, 15:25 |
| 275,19 | 100 bp, 155 bp, 205 bp | 1070 bp | *12:03:19, 12:30, 12:36 | *01:04, 07:214 |
| 287,20 | 275 bp, 350 bp | 1070 bp | *12:45, 12:50 | *01:32, 02:56, 03:102, 05:81, 06:20, 06:87, 07:24, 07:81, 07:168, 07:218, 16:13 |
| 295,21 | 125 bp, 185 bp, 210 bp | 1070 bp | *12:29, 12:38, 12:42Q, 12:86 | B*57:50 |
| 305,22 | 90 bp, 230 bp | 1070 bp | *12:32, 12:34 | *06:41 |
| 315,23 | 120 bp, 145 bp, 190 bp | 1070 bp | *12:42Q, 12:47, 12:80N, 12:84N | A*26:67, A*68:95 |
| 325,24 | 50 bp, 115 bp | 1070 bp | *12:37, 12:54 | *01:59, 02:65, 03:130, 03:140, 04:114, 05:20, 06:82, 07:49, 07:204, 07:210, 07:238, 07:247, 14:04, A*02:211:01, A*68:46, A*68:76 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-C*12 high resolution SSP typings.

When the primers in a primer mix can give rise to HLA-specific PCR products of more than one length this is indicated if the size difference is more than 20 base pairs. Size differences of 20 base pairs or less are not given. For high resolution SSP kits the respective lengths of the HLA-specific PCR product(s) are given for the alleles amplified by these primer mixes.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-C*12 SSP subtyping.

In addition, wells number 3, 7 and 26 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several HLA Class I alleles 1st and/or 4th exon(s) and beyond, as well as intron nucleotide sequences, are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in these regions are conserved within allelic groups.

4Due to the sharing of sequence motifs between HLA Class I alleles non-HLA-C*12 alleles will be amplified by primer mixes 1 to 19, 21 to 28, 30 and 32. In addition, primer mix 1 amplifies the B*07:13, B*07:15, B*07:160 and B*67:02 alleles, primer mix 9 amplifies the B*07:13 and B*67:02 alleles, primer mix 11 amplifies the B*14:03 allele, primer mix 12 amplifies the B*35:08:02, B*35:08:05 and B*67:02 alleles, primer mix 14 amplifies the B*67:02 allele, primer mix 15 amplifies the B*35:08:02 and B*35:08:05 alleles, primer mix 19 amplifies the B*18:77 and B*40:29 alleles, primer mix 21 amplifies the B*58:02 allele, primer mix 29 amplifies the B*57:30 allele, primer mix 31 amplifies the A*26:67 and A*68:95 alleles and primer mix 32 amplifies the A*02:211:01, A*68:46 and A*68:76 alleles.

5HLA-specific PCR products shorter than 125 base pairs have a lower intensity and are less sharp than longer PCR products.

6Primer mixes 1 and 5 may give rise to a lower yield of HLA-specific PCR product than the other C*12 primer mixes.

7Primer mixes 8 and 28 have a tendency to giving rise to primer oligomer formation.

8In primer mix 11, the positive control band may be weaker than for other HLA-C*12 primer mixes.

9Primer mix 6: Specific PCR fragment of 75 bp in the C*12:48 allele. Specific PCR fragment of 150 bp in the C*12:06 allele. Specific PCR fragment of 415 bp in the C*12:08 and 12:81 and in the C*03:08, 03:29, 03:31, 04:112, 05:36 and 06:44 alleles.

10Primer mix 8: Specific PCR fragment of 95 bp in the C*12:15 and the C*15:02:14 alleles. Specific PCR fragment of 155 bp in the C*12:40 and in the C*16:14 alleles. Specific PCR fragment of 195 bp in the C*12:80N allele. Specific PCR fragment of 245 bp in the C*12:07 allele.

11Primer mix 13: Specific PCR fragment of 105 bp in the C*12:31 allele. Specific PCR fragment of 150 bp in the C*12:10:01-12:10:02 and  C*14:02:08 alleles. PCR fragment of 105 and 150 bp in the C*04:01:05 allele.

12Primer mix 14: Specific PCR fragment of 100 bp in the C*12:16 and the C*01:21, 02:42, 04:140, 06:05w, 07:02:09, 08:14, 15:63 and in the B*67:02 alleles. Specific PCR fragment of 145 bp in the C*12:11 allele.

13Primer mix 16: Specific PCR fragment of 185 bp in the C*12:13 allele. Specific PCR fragment of 225 bp in C*12:14:01-12:14:02 and the C*01:60, 04:58, 05:23, 05:62, 08:07, 08:47, 14:17, 15:65 and 17:01:01:01-17:19 alleles.

14Primer mix 18: Specific PCR fragment of 145 bp in the C*04:12 allele. Specific PCR fragment of 245 bp in C*03:53 allele. Specific PCR fragments of 145 bp and 245 bp in the C*12:17 and C*12:27 alleles. Specific PCR fragment of 165 and 270 bp in C*12:35 allele. All specific bands may not always be visible.

15Primer mix 20: Specific PCR fragment of 105 bp in the C*12:46N allele. Specific PCR fragment of 170 bp in the C*12:22 allele. Specific PCR fragment of 220 bp in C*12:19 allele.

16Primer mix 22:  Specific PCR fragment of 95 bp in the C*12:15 and the C*15:02:14 alleles

Specific PCR fragment of 110 bp in the C*12:23 allele. Specific PCR fragments of 590 bp in C*12:21 allele.

17Primer mix 24: Specific PCR fragment of 185 bp in the C*12:43 allele. Specific PCR fragment of 425 bp in C*12:28 and the C*04:01:05 and 06:76:02 alleles.

18Primer mix 25: Specific PCR fragment of 80 bp in the C*12:39N allele. Specific PCR fragment of 155 bp in the C*12:02:06, 12:02:08 and 12:21 and the C*04:01:05 and 08:02:02 alleles.

19Primer mix 27: Specific PCR fragment of 100 bp in the C*12:30 and the C*07:214 alleles. Specific PCR fragment of 155 bp in the C*12:03:19 and the C*01:04 alleles. Specific PCR fragment of 205 bp in C*12:36 allele.

20Primer mix 28: Specific PCR fragment of 275 bp in the C*12:50 and the C*01:32, 02:56, 03:102, 06:20, 07:81 and 07:168 alleles. Specific PCR fragment of 350 bp in C*12:45 and the C*05:81, 06:87, 07:24, 07:218 and 16:13 alleles.

21Primer mix 29: Specific PCR fragment of 125 bp in the C*12:38 and the B*57:50 alleles. Specific PCR fragment of 185 bp in the C*12:42Q allele. Specific PCR fragments of 210 bp in C*12:29 and 12:86 alleles.

22Primer mix 30: Specific PCR fragment of 90 bp in the C*12:32 and in the C*06:41 alleles. Specific PCR fragment of 230 bp in C*12:34 allele.

23Primer mix 31: Specific PCR fragment of 120 bp in the C*12:47 and the A*26:67 and A*68:95 alleles. Specific PCR fragment of 145 bp in the C *12:84N allele. Specific PCR fragment of 190 bp in the C*12:42Q and 12:80N alleles.

24Primer mix 32: Specific PCR fragment of 50 bp in the C*12:54 and the C01:59, 02:65, 03:130, 03:140, 04:114, 05:20, 06:82, 07:49, 07:210, 07:238, 07:247 and 14:04 and in the A*68:46 alleles. Specific PCR fragment of 115 bp in C*12:37 and the C*07:204 and in the A*02:211:01 and A*68:76 allele.

‘w’, might be weakly amplified.

1The HLA-Cw*1201 nucleotide sequence has been shown to be identical to C*12:02:02.

2HLA-C*12 alleles in bold lettering are listed as confirmed alleles on the IMGT/HLA web page www.ebi.ac.uk/imgt/hla, release 3.11.0, January 2013.

3The HLA-C*12 primer set cannot separate the C*12:09, C*05:16 and C*05:85 alleles. These alleles can be distinguished by the HLA-C low resolution kit and the HLA-C*01, HLA-C*02 or HLA-C*05 kit.

4The HLA-C*12 primer set cannot separate the C*12:16 and C*01:21 alleles. These alleles can be distinguished by the HLA-C low resolution kit and the HLA-C*02 kit.

5The HLA-C*12 primer set cannot separate the C*12:18:02 and C*08:21. These alleles can be distinguished by the HLA-C low resolution kit and the HLA-C*08 kit.

6The HLA-C*12 primer set cannot separate the C*12:33 and the C*02:05 and C*02:17 alleles. These alleles can be distinguished by the HLA-C low resolution kit and the HLA-C*02 kit.

7The C*12:06, 12:48 and 12:81 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 6.

8The C*12:29 and 12:38 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 29.

9The C*12:30 and 12:36 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 27.

10The C*12:32 and 12:34 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 30.

11The C*12:45 and 12:50 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 28.

12Primer mix 6: Specific PCR fragment of 75 bp in the C*12:48 allele. Specific PCR fragment of 150 bp in the C*12:06 allele. Specific PCR fragment of 415 bp in the C*12:08 and 12:81 and in the C*03:08, 03:29, 03:31, 04:112, 05:36 and 06:44 alleles.

Primer mix 8: Specific PCR fragment of 95 bp in the C*12:15 and the C*15:02:14 alleles. Specific PCR fragment of 155 bp in the C*12:40 and in the C*16:14 alleles. Specific PCR fragment of 195 bp in the C*12:80N allele. Specific PCR fragment of 245 bp in the C*12:07 allele.

Primer mix 13: Specific PCR fragment of 105 bp in the C*12:31 allele. Specific PCR fragment of 150 bp in the C*12:10:01-12:10:02 and  C*14:02:08 alleles. PCR fragment of 105 and 150 bp in the C*04:01:05 allele.

Primer mix 14: Specific PCR fragment of 100 bp in the C*12:16 and the C*01:21, 02:42, 04:140, 06:05w, 07:02:09, 08:14, 15:63 and in the B*67:02 alleles. Specific PCR fragment of 145 bp in the C*12:11 allele.

Primer mix 16: Specific PCR fragment of 185 bp in the C*12:13 allele. Specific PCR fragment of 225 bp in C*12:14:01-12:14:02 and the C*01:60, 04:58, 05:23, 05:62, 08:07, 08:47, 14:17, 15:65 and 17:01:01:01-17:19 alleles.

Primer mix 18: Specific PCR fragment of 145 bp in the C*04:12 allele. Specific PCR fragment of 245 bp in C*03:53 allele. Specific PCR fragments of 145 bp and 245 bp in the C*12:17 and C*12:27 alleles. Specific PCR fragment of 165 and 270 bp in C*12:35 allele. All specific bands may not always be visible.

Primer mix 20: Specific PCR fragment of 105 bp in the C*12:46N allele. Specific PCR fragment of 170 bp in the C*12:22 allele. Specific PCR fragment of 220 bp in C*12:19 allele.

Primer mix 22:  Specific PCR fragment of 95 bp in the C*12:15 and the C*15:02:14 alleles

Specific PCR fragment of 110 bp in the C*12:23 allele. Specific PCR fragments of 590 bp in C*12:21 allele.

Primer mix 24: Specific PCR fragment of 185 bp in the C*12:43 allele. Specific PCR fragment of 425 bp in C*12:28 and the C*04:01:05 and 06:76:02 alleles.

Primer mix 25: Specific PCR fragment of 80 bp in the C*12:39N allele. Specific PCR fragment of 155 bp in the C*12:02:06, 12:02:08 and 12:21 and the C*04:01:05 and 08:02:02 alleles.

Primer mix 27: Specific PCR fragment of 100 bp in the C*12:30 and the C*07:214 alleles. Specific PCR fragment of 155 bp in the C*12:03:19 and the C*01:04 alleles. Specific PCR fragment of 205 bp in C*12:36 allele.

Primer mix 28: Specific PCR fragment of 275 bp in the C*12:50 and the C*01:32, 02:56, 03:102, 06:20, 07:81 and 07:168 alleles. Specific PCR fragment of 350 bp in C*12:45 and the C*05:81, 06:87, 07:24, 07:218 and 16:13 alleles.

Primer mix 29: Specific PCR fragment of 125 bp in the C*12:38 and the B*57:50 alleles. Specific PCR fragment of 185 bp in the C*12:42Q allele. Specific PCR fragments of 210 bp in C*12:29 and 12:86 alleles.

Primer mix 30: Specific PCR fragment of 90 bp in the C*12:32 and in the C*06:41 alleles. Specific PCR fragment of 230 bp in C*12:34 allele.

Primer mix 31: Specific PCR fragment of 120 bp in the C*12:47 and the A*26:67 and A*68:95 alleles. Specific PCR fragment of 145 bp in the C *12:84N allele. Specific PCR fragment of 190 bp in the C*12:42Q and 12:80N alleles.

Primer mix 32: Specific PCR fragment of 50 bp in the C*12:54 and the C01:59, 02:65, 03:130, 03:140, 04:114, 05:20, 06:82, 07:49, 07:210, 07:238, 07:247 and 14:04 and in the A*68:46 alleles. Specific PCR fragment of 115 bp in C*12:37 and the C*07:204 and in the A*02:211:01 and A*68:76 allele.

‘w’, might be weakly amplified.