PHOTO DOCUMENT

Olerup SSP AB

Olerup SSPTM HLA-C low resolution

Prod. No:	101.601-24/12 – including Taq pol.

101.601-24u/12u– without Taq pol.

Lot No:    	Y22

Expiry Date:    	2009-August-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ug/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 23 primer mixes used for HLA-C low resolution SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA class I 3 alleles |
| --- | --- | --- | --- |
| 14 | 155, 370 bp | 800 bp | 010201-0119 |
| 25 | 225, 270 bp | 800 bp | 0110, 020201-020203, 020205-0220, 0608, 0806weakly, 0807, 1214, 1701-1704, 1803 |
| 3 | 280 bp | 800 bp | 020201-020203, 020205-0220, 030201-030203, 030401-0310, 0314-0317, 0319, 0323-0329, 0332-033802, 0340-0342, 0344-0346, 0403, 0406, 0416, 0603, 150201-1509, 151002, 1511, 1513, 1515-1521 |
| 46 | 155 bp | 1070 bp | 030201-030406, 0305-0315, 0317-0340, 0342-0346 |
| 55 | 225, 280 bp | 800 bp | 030301-030305, 031101-0313, 0320N-0322Q, 0330, 0331, 0343, 0807, 1214, 1512, 1701-1704 |
| 6 | 125 bp | 1070 bp | 020201-020203, 020205-0220, 04010101-040104, 0403-041502, 0417-0420, 0423-0431, 1511 |
| 7 | 165 bp | 1070 bp | 050101-050103, 0503-0517, 0605, 0810, 1221 |
| 8 | 130, 240, 355 bp | 800 bp | 0206, 0339, 06020101-0616N, 1215, 1216, 150201-1503, 1507, 1508, 151001-1513, 1515-1518, 1521 |
| 97 | 245, 425 bp | 1070 bp | 070101-0733N, 0735-0753 |
| 106 | 115, 175 bp | 800 bp | 080101-0812, 0814, 0815 |
| 11 | 340 bp | 1070 bp | 0114, 020201-020203, 020205-0211, 0213-0220, 0307, 0315, 0345, 04010101-040104, 0403-0410, 0412-0420, 0423-0428, 0430, 0431, 050101-0517, 06020101-0610, 0612-0616N, 0707, 0709, 0749, 0810, 120401-1205, 1209, 1221, 1404, 150201-1506, 1508-1513, 1515-1520, 1602, 1609, 1701-1704, 1801-1803 |
| 12 | 150, 185, 220 bp | 1070 bp | 0104, 120201-12030102, 120303-120305, 120402-1208, 1210-1213, 1215-1221 |
| 136 | 130, 160 bp | 800 bp | 0212, 04010101-040104, 0403-0409N, 0412-0420, 0423-0431, 0753, 0805, 120201-120303, 120305, 120402, 1206-1208, 1210-1220, 1503, 1516, 160101-1602, 1606-1610, B*6702 |
| 148 | 220 bp | 800 bp | 0104, 0109, 0205, 0217, 06020101-0603, 0607-0613, 0615, 0616N, 12030101-1207, 1211-1213, 1215, 1219, 160401 |
| 156 | 255 bp | 800 bp | 020201weakly, 020202-020203, 020205-0213, 0215-0220, 0307, 0310, 0315, 0329, 0345, 0403, 0406, 0416, 050101-050103, 0503-0517, 0603, 0810, 120401-1205, 1209, 1221, 150201-1506, 1508-1513, 1515-1521, 1602, 1609, 1701-1704 |
| 166 | 95, 255 bp | 1070 bp | 0411, 0429, 0511, 0517, 0804, 0813, 140201-1409 |
| 175,6 | 110, 325 bp | 1070 bp | 0206, 1208, 1215, 150201-1513, 1515-1521 |
| 185 | 190, 255 bp | 1070 bp | 0213, 0218, 04010101-040104, 0403-0410, 0412-0420, 0423-0431, 0517, 0605, 080101-080102, 0803, 0806, 0808-0811, 0814, 1214, 160101-1602, 160401, 1606-1610 |
| 19 | 240 bp | 800 bp | 1701-1704 |
| 20 | 220, 425 bp | 800 bp | 010201-0103, 0106-0108, 0110-0119, 0516, 0605, 0606, 0707, 0709, 0749, 0812, 1209, 140201-1405, 1407N, 1801-1803, B*1403 |
| 21 | 325, 380 bp | 1070 bp | 0103, 030301-030407, 0306-0312, 0314, 0318-0324, 0326, 0328-0332, 0334, 0337-0346, 04010101-040104, 0403-0420, 0424-0431, 050101-050103, 0503, 0505-0517, 0609, 0614, 0710, 0728, 0741, 0743, 080101-0808, 0810, 0812-0815, 150201-1513, 1515-1521, 1701-1704, 1801-1803 |
| 225 | 95, 135 bp | 1070 bp | 030201-0317, 0319-033802, 0340-0346, 0511, 0517, 0603, 0804, 0813 |
| 23 | 160, 225 bp | 1070 bp | 0212, 0403, 0406, 06020101-060203, 0604, 0606-0616N, 070101-0725, 072701-0732N, 0735-0738, 0741-0753, 1216, 160101-1602, 1606-1610, 1801-1803 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-C low resolution SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 bp or more. Size differences shorter than 20 bp are not given. For high resolution SSP kits the length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control band may sometimes be observed. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most tubes, or a band of 800 base pairs, for some tubes.

Tube number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-C low resolution typing.

In addition, tubes number 2, 3, 5, 8, 10, 13, 14, 15, 19 and 20 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several HLA-C alleles only partial 1st and 4th exon nucleotide sequences are available. In these instances it is not known whether some of the primers of the HLA-C low resolution SSP sets are completely matched with the target sequences or not. We assume that unknown sequences are conserved within allelic groups.

4Primer mix 1 will for most Cw*01 alleles give rise to two specific PCR fragments.

5Primer mixes 2, 5, 17, 18 and 22 have a tendency of giving rise to primer oligomer artifacts. Most pronounced for primer mixes 5 and 22.

6Primer mixes 4, 10, 13, 15, 16 and 17 yield somewhat less intense specific PCR fragments than the other HLA-C low resolution primer mixes.

7Primer mix 9 will for most Cw*07 alleles give rise to two specific PCR fragments.

8Primer mix 14 might faintly amplify the Cw*0102 to 0103, the Cw*0105 to Cw*0119 and the Cw*140201 to 1409 alleles.

Change in revision R01 compared to R00:

- Footnote that primer mix 22 may give rise to primer dimer formation added to the Specificity Table.

Change in revision R02 compared to R01:

- The Cw*0212. 0403 and 0406 alleles are amplified by primer mix 23. Information corrected in the Specificity and Interpretation Tables.

1The sequence of the Cw*0101 allele has been shown to be identical to Cw*0102.

The  sequence of the Cw*0201 allele has been shown to be identical to Cw*02022.

The  sequence of the Cw*020204 allele has been shown to be identical to Cw*0210.

The sequence of the Cw*0301 allele has been shown to be identical to Cw*0304.

The sequence of the Cw*0402 allele has been shown to be identical to Cw*04011.

The sequence of the Cw*0422 allele has been shown to be identical to Cw*0421.

The sequence of the Cw*0601 allele has been shown to be identical to Cw*0602.

The sequence of the Cw*1101 allele has been shown to be in error.

The sequence of the Cw*1201 allele has been shown to be identical toCw*12022.

The nucleotide sequence of Cw*1301 has been shown to be in error.

The sequence of the Cw*1401 allele has been shown to be identical toCw*1402.

The sequence of the Cw*1501 allele has been shown to be identical toCw*1502.

The sequence of the Cw*1603 allele has been shown to be identical toCw*1403.

The sequence of the Cw*16042 allele has been shown to be identical toCw*16041.

The sequence of the Cw*1605 allele has been shown to be identical toCw*16041.