PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-Cw*01

Prod. No:	101.621-12 – including Taq polymerase

101.621-12u – without Taq polymerase

Lot No:    	44E

Expiry Date:    	2010-April-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ug/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 16 primer mixes used for HLA-Cw*01 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-Cw*01 alleles | Other amplified HLA Class I alleles3 |
| --- | --- | --- | --- | --- |
| 14 | 90 bp | 800 bp | 010201-010205, 0106-0111, 0113-0120 |  |
| 24,5 | 90, 270 bp | 1070 bp | 0103, 0115 |  |
| 36 | 150, 265 bp | 800 bp | 0104, 0114 |  |
| 47 | 210, 240 bp | 1070 bp | 0105, 0116 | 0737 |
| 58 | 150, 200 bp | 800 bp | 0106, 0120 |  |
| 6 | 195 bp | 1070 bp | 0107 |  |
| 79 | 150, 195 bp | 1070 bp | 0108, 0120 |  |
| 8 | 210 bp | 1070 bp | 0104, 0109 |  |
| 9 | 230 bp | 800 bp | 0110 |  |
| 10 | 290 bp | 1070 bp | 0111 |  |
| 11 | 340 bp | 800 bp | 0112 | 0617, 120306, 1611 |
| 12 | 155 bp | 1070 bp | 0113 | 0509, 0517, 0815, B*1533 |
| 1310 | 155, 370 bp | 800 bp | 010201-0120 |  |
| 14 | 240 bp | 1070 bp | 0117 |  |
| 15 | 230 bp | 800 bp | 0118 |  |
| 16 | 255 bp | 1070 bp | 0119 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-Cw*01 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-Cw*01 SSP subtyping.

In addition, wells number 3, 5, 9, 11, 13 and 15 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3Due to the sharing of sequence motifs between HLA Class I alleles some non-HLA-Cw*01 alleles will be amplified by primer mixes 4, 11 and 12. In addition, the B*1533 allele will be amplified by primer mix 12.

4Short specific PCR fragments are less intense and not as sharp as longer specific bands.

5Primer mix 2: Specific PCR product of 90 bp in the Cw*0103 allele. Specific PCR product of 270 bp in the Cw*0115 allele.

6Primer mix 3: Specific PCR product of 150 bp in the Cw*0104 allele. Specific PCR product of 265 bp in the Cw*0114 allele.

7Primer mix 4: Specific PCR product of 210 bp in the Cw*0105 and *0737 alleles. Specific PCR product of 240 bp in the Cw*0116 allele.

8Primer mix 5: Specific PCR product of 150 bp in the Cw*0120 allele. Specific PCR product of 200 bp in the Cw*0106 allele.

9Primer mix 7: Specific PCR product of 150 bp in the Cw*0120 allele. Specific PCR product of 195 bp in the Cw*0108 allele.

10Primer mix 13: Specific PCR fragment of 155 bp in the Cw*0105 and *0112 alleles. Specific PCR fragments of 155 and 370 bp in the Cw*010201 to *0104, *0106 to *0111 and *0113 to *0120 alleles (both specific PCR fragments may not always be obtained).

1The HLA-Cw*0101 nucleotide sequence has been shown to be identical to Cw*0102.

2Primer mix 2: Specific PCR product of 90 bp in the Cw*0103 allele. Specific PCR product of 270 bp in the Cw*0115 allele.

Primer mix 3: Specific PCR product of 150 bp in the Cw*0104 allele. Specific PCR product of 265 bp in the Cw*0114 allele.

Primer mix 4: Specific PCR product of 210 bp in the Cw*0105 and *0737 alleles. Specific PCR product of 240 bp in the Cw*0116 allele.

Primer mix 5: Specific PCR product of 150 bp in the Cw*0120 allele. Specific PCR product of 200 bp in the Cw*0106 allele.

Primer mix 7: Specific PCR product of 150 bp in the Cw*0120 allele. Specific PCR product of 195 bp in the Cw*0108 allele.

Primer mix 13: Specific PCR fragment of 155 bp in the Cw*0105 and *0112 alleles. Specific PCR fragments of 155 and 370 bp in the Cw*010201 to *0104, *0106 to *0111 and *0113 to *0120 alleles (both specific PCR fragments may not always be obtained).

Changes in revision R01 compared to R00:

- Fragment size corrected in footnotes to primer mix 13 in the Specificity and Interpretation Tables.