PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-Cw*02

Prod. No:	101.622-12 – including Taq polymerase

101.622-12u – without Taq polymerase

Lot No:    	12E

Expiry Date:    	2010-January-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ug/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 16 primer mixes used for HLA-Cw*02 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-Cw*02 alleles | Other amplified HLA-Cw alleles3 |
| --- | --- | --- | --- | --- |
| 1 | 250 bp | 800 bp | 020201-020203, 020205-020206, 0204-0215, 0217, 0219, 0220 | 0104, 0109, 0508, 06020101-0603, 0607-0616N, 120201-1208, 1210-1213, 1215-1217, 1221, 160401, 1803 |
| 24 | 95 bp | 800 bp | 020201-020203, 020206, 0204, 0207-0209, 0211, 0213, 0215, 0219, 0220 |  |
| 34,6 | 95, 135 bp | 800 bp | 0203, 0218, 0220 | B*2734, B*400602, B*570302weakly |
| 4 | 150 bp | 1070 bp | 0204 |  |
| 5 | 240 bp | 1070 bp | 0205, 0217 | 0110, 0608 |
| 6 | 160 bp | 800 bp | 0206, 0219 | 0109, 0321, 1215 |
| 74 | 130 bp | 800 bp | 0207 | 1610 |
| 84,5 | 70 bp | 1070 bp | 0208 | 151002 |
| 9 | 200 bp | 1070 bp | 020201-020203, 020205-0209, 0211-0220 |  |
| 104 | 125 bp | 1070 bp | 020201-020203, 020205-0220 | 0403, 0406, 1511 |
| 114,7 | 80, 170 bp | 1070 bp | 0209, 0218 |  |
| 128 | 150, 230 bp | 1070 bp | 0211, 0214, 0217 | 0605weakly, 1216 |
| 13 | 225 bp | 1070 bp | 0212 |  |
| 144 | 80 bp | 800 bp | 0213 |  |
| 15 | 190 bp | 1070 bp | 0215 |  |
| 16 | 230bp | 1070 bp | 0203, 0216, 0218 | 040401-040402, 0406, 0413, 0511, 0517, 0604, 080101-080102, 0803, 0804, 0806, 0808-0811, 0813, 0814, 1214, 1218, 1220, 1406, 150201-1507, 1509-1513, 1515-1521, 1701-1704, B*5802 |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of DR low resolution SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most tubes, or a band of 800 base pairs, for some tubes.

Tube number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-Cw*02 SSP subtyping.

In addition, tubes number 2, 3, 6, 7 and 14 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band.

In the presence of a specific amplification the intensity of the control band often decreases.

3Due to the sharing of sequence motifs between HLA Class I alleles some non-HLA-Cw*02 alleles will be amplified by primer mixes 1, 5 to 8, 10, 12 and 16. In addition, the B*2734 and the B*400602 and B*570302 alleles will be amplified by primer mix 3 and the B*5802 allele by primer mix 16.

4Short specific PCR fragments are less intense and not as sharp as longer specific bands.

5Primer mix 8 has a tendency of primer oligomer formation.

6Primer mix 3: Specific PCR fragment of 95 bp in the Cw*0203 and Cw*0218 and the B*2734, B*400602 and B*570302weakly alleles. Specific PCR fragment of 135 bp in  the Cw*0220 allele.

7Primer mix 11: Specific PCR fragment of 80 bp in the Cw*0218 allele. Specific PCR fragment of 170 bp in the Cw*0209 allele.

8Primer mix 12: Specific PCR fragment of 150 bp in the Cw*0211,and Cw*0214 and the Cw*0605weakly and Cw*1216 alleles. Specific PCR fragment of 230 bp in the Cw*0217 allele.

1Cw*0201 has been deleted as it was identical to Cw*020202.

Cw*02024 has been deleted as it was identical to Cw*0210

2Primer mix 3: Specific PCR fragment of 95 bp in the Cw*0203 and Cw*0218 and the B*2734, B*400602 and B*570302weakly alleles. Specific PCR fragment of 135 bp in  the Cw*0220 allele.

Primer mix 11: Specific PCR fragment of 80 bp in the Cw*0218 allele. Specific PCR fragment of 170 bp in the Cw*0209 allele.

Primer mix 12: Specific PCR fragment of 150 bp in the Cw*0211,and Cw*0214 and the Cw*0605weakly and Cw*1216 alleles. Specific PCR fragment of 230 bp in the Cw*0217 allele.

‘w’, might be weakly amplified.

Changes in revision R01 compared to R00:

- The Cw*160401 allele is not amplified by primer mix 14, corrected in the Specificity and Interpretation Tables.