PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-Cw*03

Prod. No:	101.611-12/12u

Lot No:    	54G

Expiry Date:    	2011-December-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 45 primer mixes used for HLA-Cw*03 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-Cw*03 alleles3 | Other amplified HLA Class I alleles4 |
| --- | --- | --- | --- | --- |
| 16 | 280 bp | 800 bp | *030201-030205, 03040101-0310, 0314-0317, 0319, 0323-0329, 0332-033802, 0340-0342, 0344-0348, 0351, 0354, 0357, 0360, 0363-0365, 0370-0374 | *020201-020203, 020205-0203, 0204w, 0205-0213, 0214w, 0215-0225Q, 0227-0231, 0403, 0406, 0416, 0603, 070210w, 150201-1509, 151002, 1511, 1513, 1515-1522 |
| 2 | 210 bp | 1070 bp | *030201-030205, 0314, 0315, 0333, 0336, 0340, 0342-034302, 0360, 0371 | B*1596 |
| 37 | 280 bp | 800 bp | *030301-030311, 031101-0313, 0320N-0322Q, 0330, 0331, 034301, 034302, 0349, 0350, 0352, 0353, 0355, 0356, 0358, 0359, 0361, 0362, 0366, 0367w, 0368, 0369, 0375, 0376 | *1512 |
| 4 | 275 bp | 1070 bp | *030301-030414, 0306-0312, 0314, 0318-0324, 0326, 0328-0332, 0334, 0337-0340, 0342-0357, 0359, 0361-0370, 0372-0376 |  |
| 5 | 275 bp | 1070 bp | *0305, 0313, 0317, 0325, 0327, 0335, 0371 | B*1596 |
| 65,9 | 90 bp, 215 bp | 800 bp | *0306, 0321 | B*1596 |
| 75,6,10 | 110 bp, 185 bp | 1070 bp | *030301-030311, 0308, 031101-0313, 0318, 0320N-0322Q, 0329-0331, 0339, 034301, 034302, 0349, 0350, 0352, 0353, 0355, 0356, 0358, 0359, 0361, 0362, 0366-0369, 0375, 0376 | *070101-070111, 0706, 0707, 0709, 0716, 0718-0720, 0722, 0724, 0726, 0728, 0730, 0735, 0736, 0740, 0744, 0752, 0753, 0755N, 075601, 0757-0760, 0765, 0770, 0771, 0773, 0777-0779, 0781-0783, 0786, 0789, 0791, B*0793, B*0839, B*5176 |
| 8 | 250 bp | 1070 bp | *0309, 0322Q, 0342, 0371 |  |
| 9 | 240 bp | 1070 bp | *0307, 0315, 0345 | *020201-020203, 020205-0203, 0204w, 0205-0211, 0213, 0214w, 0215-0225Q, 0228-0231, 0403, 0406, 0416, 0603, 150201-1506, 1508, 1509, 151002-1513, 1515-1520, 1522 |
| 107 | 250 bp | 800 bp | *0307, 0310, 0315, 0329, 0345 | *020201w, 020202, 020203, 020205-0203, 0204w, 0205-0213, 0214w, 0215-0225Q, 0228-0231, 0403, 0406, 0416, 0603, 150201-1506, 1508, 1509, 151002-1513, 1515-1522 |
| 11 | 415 bp | 1070 bp | *0308, 0329, 0331 | *1208 |
| 12 | 260 bp | 1070 bp | *031101, 0318, 0339 | *075601, 0760, 0779, 1512 |
| 135,11 | 80 bp, 140 bp | 1070 bp | *030201-030205, 0315-0317, 0333, 0336, 0340, 0342, 034301, 0360, 0371 | *0437, 140201, 140203-1414 |
| 14 | 210 bp | 1070 bp | *0312, 0319 |  |
| 155 | 135 bp | 1070 bp | *030201-0317, 0319-033802, 0340-0366, 0367w, 0368-0376 | *0603w, 070210w |
| 16 | 150 bp | 1070 bp | *0307, 0310, 0315, 0329, 0345 | *0114, 06020101, 06020102, 060203-0604, 0606-0610, 0612-0628, 0707, 0709, 0776, 120401, 1412, 17010101-1705, 1801-1803 |
| 175 | 90 bp | 1070 bp | *0320N |  |
| 18 | 225 bp | 1070 bp | *0323 |  |
| 195,7,12 | 105 bp, 260 bp | 800 bp | *0324, 0333 |  |
| 208,13 | 165 bp, 255 bp | 1070 bp | *0325, 0347 |  |
| 21 | 210 bp | 1070 bp | *0326 |  |
| 2214 | 195 bp, 240 bp | 800 bp | *0315, 0327, 033801, 033802, 0357, 0369 | *0212, 0403, 0406, 0416, 0720, 1503, 1516 |
| 235 | 90 bp | 1070 bp | *0328, 0349 |  |
| 24 | 200 bp | 1070 bp | *0330, 0365 |  |
| 2515 | 305 bp, 355 bp | 1070 bp | *0332, 033801, 033802, 0345, 0369 | *0614, 0710, 0743, 1503, 1516 |
| 265,8,16 | 70 bp, 105 bp, 265 bp | 1070 bp | *0313, 0334-0336 | B*1596 |
| 275,17 | 80 bp, 275 bp | 1070 bp | *031101, 031102, 0315, 0332, 0337, 0345, 0360 | *0403, 0406, 0416, 0603, 070210w |
| 288 | 170 bp | 1070 bp | *0316, 0341 | *04010101-040104, 040106, 040108, 040110-040112, 0403, 040401, 0405-0420, 0423-0448, 140201, 140203-1414, 1801-1803 |
| 2918 | 165 bp, 285 bp | 1070 bp | *0339, 0351, 0367 | *075601, *0760, *0779, B*0839 |
| 30 | 155 bp | 1070 bp | *0346, 0361 |  |
| 315,19 | 100 bp, 210 bp | 800 bp | *0344, 0359 |  |
| 325,20 | 90 bp, 180 bp | 1070 bp | *0348, 0358 | *0103, 0124, 0437 |
| 335,21 | 110 bp, 365 bp | 1070 bp | *034301, 034302, 0362 | *0760, 0779, 1410 |
| 345,22 | 125 bp, 240 bp | 1070 bp | *0353, 0354 | *1217 |
| 355,23 | 70 bp, 120 bp | 1070 bp | *0356, 0364 | *0208, 151002 |
| 36 | 240 bp | 1070 bp | *0350, 0372 |  |
| 37 | 140 bp | 1070 bp | *0316, 0321, 0355 | *04010101-040104, 040108, 040110-040112, 0403, 040401, 0405-0407, 0409N-0420, 0423-0431, 0433, 0435-0448, 140201, 140203-1414, 1801, 1802 |
| 385,24 | 100 bp, 265 bp | 1070 bp | *0352, 0373 | *0443 |
| 39 | 170 bp | 1070 bp | *0363 |  |
| 408 | 260 bp | 1070 bp | *0366 |  |
| 415 | 120 bp | 1070 bp | *0368 |  |
| 42 | 205 bp | 1070 bp | *0370 | B*5530 |
| 437 | 225 bp | 1070 bp | *0374 |  |
| 44 | 160 bp | 1070 bp | *0375 |  |
| 45 | 295 bp | 1070 bp | *0376 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-Cw*03 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may  be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-Cw*03 subtyping.

In addition, wells number 3, 6, 10, 19, 22 and 31 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3For several HLA-Cw*03 alleles 1st, 4th, 5th, 6th and 7th exon nucleotide sequences are not available. In these instances it is not known whether some of the primers of the SSP sets are completely matched with the target sequences or not. We assume that unknown sequences in the 1st, 4th, 5th, 6th and 7th exons are conserved within allelic groups.

4Due to the sharing of sequence motifs between HLA-Cw alleles the primer pairs in wells 1, 3, 7, 9 to 13, 15, 16, 22, 25, 27 to 29, 32 to 35, 37 and 38 will amplify some non-HLA-Cw*03 alleles. In addition, the B*0793 and 5176 alleles are amplified by primer mix 7, the B*0839 allele is amplified by primer mix 7 and 29, the B*1596 allele is amplified by primer mixes 5, 6 and 26 and the B*5530 allele is amplified by primer mix 42.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6The primer pairs in well 1 and 7 may yield less specific PCR product than the other HLA-Cw*03 primer pairs.

7Primer mixes 3, 10, 19 and 43 may give rise to primer oligomer formation.

8Primer mixes 20, 26, 28 and 40 may give rise to nonspecific amplifications, most pronounced primer mixes 20 and 28..

9Primer mix 6: Specific PCR fragment of 90 bp in the Cw*0321 and B*1596 alleles. Specific PCR fragment of 215 bp in the Cw*0306 alleles.

10Primer mix 7: Specific PCR fragment of 110 bp in the Cw*0308 and 0329 and the Cw*070101-070111, 0706, 0707, 0709, 0716, 0718-0720, 0722, 0724, 0726, 0728, 0730, 0735, 0736, 0740, 0744, 0752, 0753, 0755N, 0757-0759, 0765, 0770, 0771, 0773, 0777, 0778, 0781-0783, 0786, 0789 and 0791 alleles. Specific PCR fragment of 185 bp in the Cw**030301-030311, 031101-0313, 0318, 0320N-0322Q, 0330, 0339, 034301, 034302, 0349, 0350, 0352, 0353, 0355, 0356, 0358, 0359, 0361, 0362, 0366-0369, 0375 and 0376, in the Cw*075601 and 0779 and in the B*0793, B*0839 and B*5176 alleles. Specific PCR fragments of 110 and 185 bp in the Cw*0331 and Cw*0760 alleles.

11Primer mix 13: Specific PCR fragment of 80 bp in the Cw*030201-030205, 0315, 0316, 0333, 0336, 0340, 0342, 034301 and 0360 and the Cw*1408 and 1409 alleles. Specific PCR fragment of 140 bp in the Cw*0317 and the Cw*0437 alleles. Specific PCR fragments of 80 and 140 bp in the Cw*0371 and in the Cw*140201, 140403 to 1407N and 1410 to 1414 alleles.

12Primer mix 19: Specific PCR fragment of 105 bp in the Cw*0324 allele. Specific PCR fragment of 260 bp in the Cw*0333 allele.

13Primer mix 20: Specific PCR fragment of 165 bp in the Cw*0325 allele. Specific PCR fragment of 255 bp in the Cw*0347 allele.

14Primer mix 22: Specific PCR fragment of 195 bp in the Cw*0315, 0327, 033801, 033802 and 0369 and the Cw*0212, 0403, 0406, 0416, 0720, 1503 and 1516 alleles. Specific PCR fragment of 240 bp in the Cw*0357 allele.

15Primer mix 25: Specific PCR fragment of 305 bp in the Cw*0332 and 0345 alleles. Specific PCR fragment of 355 bp in the Cw*033801-033802 and 0369 and the Cw*1503 and 1516 alleles. Specific PCR fragments of 305 and 355 bp in the Cw*0614, 0710 and 0743 alleles.

16Primer mix 26: Specific PCR fragment of 70 bp in the Cw*0334 allele. Specific PCR fragment of 105 bp in the Cw*0336 allele. Specific PCR fragment of 265 bp in the Cw*0313 and 0335 and the B*1596 alleles.

17Primer mix 27: Specific PCR fragment of 80 bp in the Cw*031101, 031102 and 0337 and the Cw* 0603 alleles. Specific PCR fragment of 275 bp in the Cw*0315, 0332, 0345 and 0360 and Cw*0403, 0406, 0416 and 0603 alleles. Specific PCR fragment of 80 and 275 bp in the Cw*070210w allele.

18Primer mix 29: Specific PCR fragment of 165 bp in the Cw*0351 allele. Specific PCR fragment of 285 bp in the Cw*0339 and 0367, the Cw*075601, 0760 and 0779 and the B*0839 alleles.

19Primer mix 31: Specific PCR fragment of 100 bp in the Cw*0359 allele. Specific PCR fragment of 210 bp in the Cw*0344 allele.

20Primer mix 32: Specific PCR fragment of 90 bp in the Cw*0358 and the Cw*0103, 0124 and 0437 alleles. Specific PCR fragment of 180 bp in the Cw*0348 allele.

21Primer mix 33: Specific PCR fragment of 110 bp in the Cw*0362 allele. Specific PCR fragment of 365 bp in the Cw *034301 and 034302 and the Cw*0760, 0779 and Cw*1410 alleles.

22Primer mix 34: Specific PCR fragment of 125 bp in the Cw*0354 allele. Specific PCR fragment of 240 bp in the Cw* 0353 and the Cw*1217 alleles.

23Primer mix 35: Specific PCR fragment of 70 bp in the Cw* 0364 and the Cw*0208 and 151002 alleles. Specific PCR fragment of 120 bp in the Cw*0356 allele.

24Primer mix 38: Specific PCR fragment of 100 bp in the Cw* 0352 and the Cw*0443 alleles. Specific PCR fragment of 265 bp in the Cw*0373 allele.

‘w’, might be weakly amplified.

1The nucleotide sequence of the HLA-Cw*0301 allele has been shown to be identical to Cw*0304.

2Primer mix 6: Specific PCR fragment of 90 bp in the Cw*0321 and B*1596 alleles. Specific PCR fragment of 215 bp in the Cw*0306 alleles.

Primer mix 7: Specific PCR fragment of 110 bp in the Cw*0308 and 0329 and the Cw*070101-070111, 0706, 0707, 0709, 0716, 0718-0720, 0722, 0724, 0726, 0728, 0730, 0735, 0736, 0740, 0744, 0752, 0753, 0755N, 0757-0759, 0765, 0770, 0771, 0773, 0777, 0778, 0781-0783, 0786, 0789 and 0791 alleles. Specific PCR fragment of 185 bp in the Cw**030301-030311, 031101-0313, 0318, 0320N-0322Q, 0330, 0339, 034301, 034302, 0349, 0350, 0352, 0353, 0355, 0356, 0358, 0359, 0361, 0362, 0366-0369, 0375 and 0376, in the Cw*075601 and 0779 and in the B*0793, B*0839 and B*5176 alleles. Specific PCR fragments of 110 and 185 bp in the Cw*0331 and Cw*0760 alleles.

Primer mix 13: Specific PCR fragment of 80 bp in the Cw*030201-030205, 0315, 0316, 0333, 0336, 0340, 0342, 034301 and 0360 and the Cw*1408 and 1409 alleles. Specific PCR fragment of 140 bp in the Cw*0317 and the Cw*0437 alleles. Specific PCR fragments of 80 and 140 bp in the Cw*0371 and in the Cw*140201, 140403 to 1407N and 1410 to 1414 alleles.

Primer mix 19: Specific PCR fragment of 105 bp in the Cw*0324 allele. Specific PCR fragment of 260 bp in the Cw*0333 allele.

Primer mix 20: Specific PCR fragment of 165 bp in the Cw*0325 allele. Specific PCR fragment of 255 bp in the Cw*0347 allele.

Primer mix 22: Specific PCR fragment of 195 bp in the Cw*0315, 0327, 033801, 033802 and 0369 and the Cw*0212, 0403, 0406, 0416, 0720, 1503 and 1516 alleles. Specific PCR fragment of 240 bp in the Cw*0357 allele.

Primer mix 25: Specific PCR fragment of 305 bp in the Cw*0332 and 0345 alleles. Specific PCR fragment of 355 bp in the Cw*033801-033802 and 0369 and the Cw*1503 and 1516 alleles. Specific PCR fragments of 305 and 355 bp in the Cw*0614, 0710 and 0743 alleles.

Primer mix 26: Specific PCR fragment of 70 bp in the Cw*0334 allele. Specific PCR fragment of 105 bp in the Cw*0336 allele. Specific PCR fragment of 265 bp in the Cw*0313 and 0335 and the B*1596 alleles.

Primer mix 27: Specific PCR fragment of 80 bp in the Cw*031101, 031102 and 0337 and the Cw* 0603 alleles. Specific PCR fragment of 275 bp in the Cw*0315, 0332, 0345 and 0360 and Cw*0403, 0406, 0416 and 0603 alleles. Specific PCR fragment of 80 and 275 bp in the Cw*070210w allele.

Primer mix 29: Specific PCR fragment of 165 bp in the Cw*0351 allele. Specific PCR fragment of 285 bp in the Cw*0339 and 0367, the Cw*075601, 0760 and 0779 and the B*0839 alleles.

Primer mix 31: Specific PCR fragment of 100 bp in the Cw*0359 allele. Specific PCR fragment of 210 bp in the Cw*0344 allele.

Primer mix 32: Specific PCR fragment of 90 bp in the Cw*0358 and the Cw*0103, 0124 and 0437 alleles. Specific PCR fragment of 180 bp in the Cw*0348 allele.

Primer mix 33: Specific PCR fragment of 110 bp in the Cw*0362 allele. Specific PCR fragment of 365 bp in the Cw *034301 and 034302 and the Cw*0760, 0779 and Cw*1410 alleles.

Primer mix 34: Specific PCR fragment of 125 bp in the Cw*0354 allele. Specific PCR fragment of 240 bp in the Cw* 0353 and the Cw*1217 alleles.

Primer mix 35: Specific PCR fragment of 70 bp in the Cw* 0364 and the Cw*0208 and 151002 alleles. Specific PCR fragment of 120 bp in the Cw*0356 allele.

Primer mix 38: Specific PCR fragment of 100 bp in the Cw* 0352 and the Cw*0443 alleles. Specific PCR fragment of 265 bp in the Cw*0373 allele.

‘w’, might be weakly amplified.