PHOTO DOCUMENT

Olerup SSP AB

Olerup SSPTM HLA-Cw*04

Prod. No:	101.612-12 – including Taq polymerase

101.612-12u – without Taq polymerase

Lot No:    	X77

Expiry Date:    	2009-April-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ug/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 24 primer mixes used for HLA-Cw*04 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-Cw*04 alleles | Other amplified HLA Class I alleles3 |
| --- | --- | --- | --- | --- |
| 1 | 250 bp | 800 bp | 04010101-040104, 0403, 0405, 0407-0412, 0415-0418, 0419weakly, 0420, 0421, 0423-0427 | 010201-0118, 020201-020203, 020205, 0204-0215, 0217, 050101-0510, 0512-0516, 06020101-0603, 0605-0615, 0802, 0805, 0807, 0812, 120201-1213, 1215-1217, 1221, 140201-1405, 1407N, 1408, 1508, 160401, 1801-1803 |
| 2 | 220 bp | 1070 bp | 04010101-040104, 040401-0405, 0407-0409N, 0412-0415, 0417-0421, 0423-0427 |  |
| 34 | 145 bp | 1070 bp | 04010101-040104, 040401-0405, 0408-0415, 0417-0421, 0423-0426 |  |
| 4 | 210 bp | 800 bp | 0403, 0406 | 0212 |
| 55 | 250 bp | 1070 bp | 040401-040402weakly, 0406weakly, 0413weakly | 0203, 0216, 0218, 0511, 0604, 080101-080102, 0803, 0804, 0806, 0808-0811, 0813, 0814, 1214, 1218, 1220, 1406, 150201-1507, 1509-1520, 1701-1704 |
| 64 | 95 bp | 1070 bp | 0405 |  |
| 74 | 145 bp | 1070 bp | 0407, 0427 |  |
| 85 | 270 bp | 1070 bp | 0408 | 1515 |
| 96,7 | 280 bp | 1070 bp | 0409N |  |
| 10 | 220 bp | 1070 bp | 0410, 0411 |  |
| 11 | 180 bp | 1070 bp | 04010101-040104, 0403-0410, 0412-0421, 0423-0427 | 0605 |
| 124 | 125 bp | 1070 bp | 0411 |  |
| 13 | 225 bp | 1070 bp | 0412 |  |
| 148 | 155, 190 bp | 1070 bp | 0413, 0416, 0418 | 0708 |
| 156 | 170 bp | 1070 bp | 0414 |  |
| 164 | 130 bp | 1070 bp | 0415 | 0305, 0325, 0327 |
| 174,6 | 90 bp | 800 bp | 0417 |  |
| 18 | 225 bp | 1070 bp | 0419 |  |
| 19 | 155 bp | 1070 bp | 0420 |  |
| 204 | 130 bp | 1070 bp | 0415, 0417, 0421 | 030201-030407, 0306-0313, 0315-0324, 0326, 0328-0340, 1405 |
| 214 | 85 bp | 1070 bp | 0423 |  |
| 224 | 130 bp | 1070 bp | 0424 |  |
| 234 | 85 bp | 1070 bp | 0425 |  |
| 24 | 170 bp | 1070 bp | 0426 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-Cw*04 SSP subtypings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 bp or more. Size differences shorter than 20 bp are not given. For high resolution SSP kits the length of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control band may sometimes be observed. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most tubes, or a band of 800 base pairs, for some tubes.

Tube number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-Cw*04 subtyping.

In addition, tubes number 4 and 17 contain the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3Due to the sharing of sequence motifs between HLA-Cw alleles some non-HLA-Cw*04 alleles will be amplified by primer mixes 1, 4, 5, 8, 11, 14, 16 and 20.

4Short specific PCR fragments are less intense and not as sharp as longer specific bands.

5Primer mixes 5 and 8 will amplify some B*5802-positive samples.

6The primers in primer mixes 9, 15 and 17 have a tendency of giving rise to nonspecific amplifications.

7The specific PCR product generated by the primers in primer mix 9 may be less intense than the other Cw*04 specific PCR products.

8Primer mix 14: Specific PCR fragment of 155 bp in the Cw*0416 allele. Specific PCR fragment of 190 bp in the Cw*0413, Cw*0418 and Cw*0708 alleles.

1The nucleotide sequence of the HLA-Cw*0402 allele has been shown to be identical to Cw*04010101.

The nucleotide sequence of the HLA-Cw*0422 allele has been shown to be identical to Cw*0421.

Primer mixes 5 and 8 will amplify some B*5802-positive samples.

2Primer mix 14: Specific PCR fragment of 155 bp in the Cw*0416 allele. Specific PCR fragment of 190 bp in the Cw*0413, Cw*0418 and Cw*0708 alleles.

Changes in revision R01 compared to R00:

- The Cw*040101-040102, Cw*0406 and Cw*0413 alleles might be weakly amplified by primer mix 5.