PHOTO DOCUMENT

Olerup SSP®

Olerup SSP® HLA-Cw*04

Prod. No:	101.612-12/12u

Lot No:    	06H

Expiry Date:    	2012-April-01

Name:________________Sample ID:_______________

DNA Extract Date:_________ Conc.(ng/ul):_________

Test  Date: _________Review Date:_______________

Tested By: _________Reviewed By:_______________

Interpretation:_________________________________

Specificities and sizes of the PCR products of the 31 primer mixes used for HLA-Cw*04 SSP typing.

| Primer Mix | Size of spec. PCR product1 | Size of control band2 | Amplified HLA-Cw*04 alleles3 | Other amplified HLA Class I alleles4 |
| --- | --- | --- | --- | --- |
| 1 | 250 bp | 800 bp | *04010101-040115, 0403, 0405, 0407-0412, 041501-0418, 0419w, 0420, 0423-0433, 0435-0453 | *010201-0121, 0123-0134, 020201-020203, 020205-020211, 0204-0215, 0217, 0219-0231, 05010101-050111, 0503-0510, 0512-0516, 0518-0526, 0528-0534, 06020101, 06020102, 060203-0603, 0605-0629, 080201-080203, 0805, 0807, 0812, 0815, 0817-0819, 0823, 0825, 0827-0831, 120201-1213, 1215-1217, 1221-1231, 140201-1405, 1407N-1414, 1508, 160401, 1801-1803 |
| 2 | 220 bp | 1070 bp | *04010101-040115, 040401-0405, 0407-0409N, 0412w, 0413-041502, 0417-0420, 0423-0435, 0437-0441, 0443-0453 | *0764 |
| 35 | 145 bp | 1070 bp | *04010101-040115, 040401-0405, 0408-041502, 0417-0420, 0423-0426, 0428-0441, 0443-0453 |  |
| 4 | 210 bp | 1070 bp | *0403, 0406 | *0212 |
| 5 | 250 bp | 1070 bp | *040401, 040402, 0406, 0413, 0434 | *0122, 0203, 021601, 021602, 0218, 0511, 0517, 0527, 0604, 080101, 080102, 080301, 080302, 0804, 0806, 0808-0811, 0813, 0814, 0816, 0820-0822, 0824, 0826N, 121401, 121402, 1218, 1220, 1406, 1415, 150201-1507, 1509-1513, 1515-1524, 1526, 17010101-1706, B*5802 |
| 65 | 95 bp | 1070 bp | *0405 |  |
| 75,6 | 145 bp | 1070 bp | *0407, 0427, 0432 | *0334, 0764, 1803 |
| 8 | 270 bp | 1070 bp | *0408, 0434 | 0527, 1515, B*5802 |
| 95,8 | 110 bp, 180 bp, 220 bp | 1070 bp | *0409N, 0430, 0435 |  |
| 109 | 195 bp, 220 bp | 1070 bp | *0410, 0411, 0431, 0436 |  |
| 11 | 180 bp | 1070 bp | *04010101-040109, 040111-040115, 0403-0410, 0412-0420, 0423-0426, 0428-0432, 0434-0451, 0453 | *0525, 0605, 070209, 0828, 1228, 1525 |
| 125,10 | 125 bp, 165 bp | 1070 bp | *0411, 0429, 0433, 0436 |  |
| 1311 | 225 bp, 270 bp | 1070 bp | *0412, 0452 |  |
| 1412 | 155 bp, 190 bp | 1070 bp | *0413, 0416, 0418 | *0708 |
| 157,13 | 170 bp, 190 bp | 1070 bp | *0414, 0428 | A*2496 |
| 165 | 130 bp | 1070 bp | *041501, 0437 | *0305, 0325, 0327, 1409 |
| 175,7 | 320 bp | 1070 bp | *0417 |  |
| 18 | 225 bp | 1070 bp | *0419 |  |
| 195,14 | 110 bp, 130 bp, 155 bp | 1070 bp | *0420, 0435, 0437 |  |
| 2015 | 165 bp, 250 bp, 545 bp | 1070 bp | *041502, 0417, 0444, 0447 |  |
| 215,16 | 85 bp, 145 bp, 240 bp | 1070 bp | *0423, 0438, 0439 |  |
| 225 | 130 bp | 1070 bp | *0424 |  |
| 235,17 | 85 bp, 145 bp, 215 bp | 1070 bp | *0425, 0440, 0441 |  |
| 246 | 160 bp | 1070 bp | *0426, 0430, 0442 |  |
| 25 | 190 bp | 1070 bp | *0443 |  |
| 267 | 215 bp | 800 bp | *0445 |  |
| 275,18 | 125 bp, 285 bp | 800 bp | *0446, 0450 |  |
| 28 | 215 bp | 1070 bp | *0448 |  |
| 29 | 185 bp | 1070 bp | *0449 |  |
| 305 | 75 bp | 1070 bp | *0453 | B*0790 |
| 31 | 180 bp | 1070 bp | *0451 |  |

1Alleles are assigned by the presence of specific PCR product(s). However, the sizes of the specific PCR products may be helpful in the interpretation of HLA-Cw*04 SSP typings.

When the primers in a primer mix can give rise to specific PCR products of more than one length this is indicated if the size difference is 20 base pairs or more. Size differences shorter than 20 base pairs are not given. For high resolution SSP kits the respective lengths of the specific PCR product(s) of the alleles amplified by these primer mixes are given.

Nonspecific amplifications, i.e. a ladder or a smear of bands, may sometimes be seen. GC-rich primers have a higher tendency of giving rise to nonspecific amplifications than other primers.

PCR fragments longer than the control bands may sometimes be observed. Such bands should be disregarded and do not influence the interpretation of the SSP typings.

PCR fragments migrating faster than the control bands, but slower than a 400 bp fragment may be seen in some gel read-outs. Such bands can be disregarded and do not influence the interpretation of the SSP typings.

Some primers may give rise to primer oligomer artifacts. Sometimes this phenomenon is an inherit feature of the primer pair(s) of a primer mix. More often it is due to other factors such as too low amount of DNA in the PCR reactions, taking too long time in setting up the PCR reactions, working at elevated room temperature or using thermal cyclers that are not pre-heated.

2The internal positive control primer pairs amplify segments of the human growth hormone gene. The two different control primer pairs give rise to either an internal positive control band of 1070 base pairs, for most wells, or a band of 800 base pairs, for some wells.

Well number 1 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to help in the correct orientation of the HLA-Cw*04 subtyping.

In addition, wells number 26 and 27 contains the primer pair giving rise to the shorter, 800 bp, internal positive control band in order to allow kit identification.

In the presence of a specific amplification the intensity of the control band often decreases.

3The Cw*041502, Cw*0444 and Cw*0447 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 20, the Cw*0423, Cw*0438 and Cw*0439 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 21, the Cw*0425, Cw*0440 and Cw*0441 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 23 and the Cw*0446 and Cw*0450 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 27.

4Due to the sharing of sequence motifs between HLA-Cw alleles some non-HLA-Cw*04 alleles will be amplified by primer mixes 1, 2, 4, 5, 7, 8, 11, 14 and 16. In addition, the A*2496 allele will be amplified by primer mix 15, the B*5802 allele will be amplified by primer mixes 5 and 8 and the B*0790 allele will be amplified by primer mix 30.

5Short specific PCR fragments are less intense and not as sharp as longer specific bands.

6The primers in primer mix 7 and 24 may give rise to primer oligomer formation.

7Primer mix 26 may have tendencies of unspecific amplification.

8Primer mix 9: Specific PCR fragment of 110 bp in the Cw*0435 allele. Specific PCR fragment of 180 bp in the Cw*0430 allele. Specific PCR fragment of 220 bp in the Cw*0409N allele.

9Primer mix 10: Specific PCR fragmentof 195 bp in the Cw*0431 allele. Specific PCR fragment of 220 bp in the Cw*0410, Cw*0411 and Cw*0436 alleles.

10Primer mix 12: Specific PCR fragment of 125 bp in the Cw*0429 and Cw*0436 alleles. Specific PCR fragment of 165 bp in the Cw*0433 allele. Specific PCR fragment of 125 and 165 bp in the Cw*0411 allele.

11Primer mix 13: Specific PCR fragment of 225 bp in the Cw*0412 allele. Specific PCR fragment of 270 bp in the Cw*0452 allele.

12Primer mix 14: Specific PCR fragment of 155 bp in the Cw*0416 allele. Specific PCR fragment of 190 bp in the Cw*0413, Cw*0418 and Cw*0708 alleles.

13Primer mix 15: Specific PCR fragment of 170 bp in the Cw*0414 and in the A*2496 alleles. Specific PCR fragment of 190 bp in the Cw*0428 allele.

14Primer mix 19: Specific PCR fragment of 110 bp in the Cw*0435 allele. Specific PCR fragment of 130 bp in the Cw*0437 allele. Specific PCR fragment of 155 bp in the Cw*0420 allele.

15Primer mix 20: Specific PCR fragment of 165 bp in the Cw*0444 allele. Specific PCR fragment of 250 bp in the Cw*0447 allele. Specific PCR fragment of 545 bp in the Cw* 041502 and Cw*0417 alleles.

16Primer mix 21: Specific PCR fragment of 85 bp in the Cw*0423 allele. Specific PCR fragment of 145 bp in the Cw*0438 allele. Specific PCR fragment of 240 bp in the Cw*0439 allele.

17Primer mix 23: Specific PCR fragment of 85 bp in the Cw*0425 allele. Specific PCR fragment of 145 bp in the Cw*0440 allele. Specific PCR fragment of 215 bp in the Cw*0441 allele.

18Primer mix 27: Specific PCR fragment of 125 bp in the Cw*0450 allele. Specific PCR fragment of 285 bp in the Cw* 0446 allele.

‘w’, may be weakly amplified.

1The nucleotide sequence of the Cw*0402 allele has been shown to be identical to Cw*04010101.

The nucleotide sequence of the Cw*0421 allele has been renamed to Cw*041502.

The nucleotide sequence of the Cw*0422 allele has been shown to be identical to Cw*0421.

2The Cw*041502, Cw*0444 and Cw*0447 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 20.

3The Cw*0423, Cw*0438 and Cw*0439 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 21.

4The Cw*0425, Cw*0440 and Cw*0441 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 23.

5The Cw*0446 and Cw*0450 alleles can be distinguished by the different sizes of the specific PCR products generated by primer mix 27.

6Primer mix 9: Specific PCR fragment of 110 bp in the Cw*0435 allele. Specific PCR fragment of 180 bp in the Cw*0430 allele. Specific PCR fragment of 220 bp in the Cw*0409N allele.

Primer mix 10: Specific PCR fragmentof 195 bp in the Cw*0431 allele. Specific PCR fragment of 220 bp in the Cw*0410, Cw*0411 and Cw*0436 alleles.

Primer mix 12: Specific PCR fragment of 125 bp in the Cw*0429 and Cw*0436 alleles. Specific PCR fragment of 165 bp in the Cw*0433 allele. Specific PCR fragment of 125 and 165 bp in the Cw*0411 allele.

Primer mix 13: Specific PCR fragment of 225 bp in the Cw*0412 allele. Specific PCR fragment of 270 bp in the Cw*0452 allele.

Primer mix 14: Specific PCR fragment of 155 bp in the Cw*0416 allele. Specific PCR fragment of 190 bp in the Cw*0413, Cw*0418 and Cw*0708 alleles.

Primer mix 15: Specific PCR fragment of 170 bp in the Cw*0414 and in the A*2496 alleles. Specific PCR fragment of 190 bp in the Cw*0428 allele.

Primer mix 19: Specific PCR fragment of 110 bp in the Cw*0435 allele. Specific PCR fragment of 130 bp in the Cw*0437 allele. Specific PCR fragment of 155 bp in the Cw*0420 allele.

Primer mix 20: Specific PCR fragment of 165 bp in the Cw*0444 allele. Specific PCR fragment of 250 bp in the Cw*0447 allele. Specific PCR fragment of 545 bp in the Cw* 041502 and Cw*0417 alleles.

Primer mix 21: Specific PCR fragment of 85 bp in the Cw*0423 allele. Specific PCR fragment of 145 bp in the Cw*0438 allele. Specific PCR fragment of 240 bp in the Cw*0439 allele.

Primer mix 23: Specific PCR fragment of 85 bp in the Cw*0425 allele. Specific PCR fragment of 145 bp in the Cw*0440 allele. Specific PCR fragment of 215 bp in the Cw*0441 allele.

Primer mix 27: Specific PCR fragment of 125 bp in the Cw*0450 allele. Specific PCR fragment of 285 bp in the Cw* 0446 allele.

‘w’, may be weakly amplified.

Change in revision R01 compared to R00:   1. Primer mix 26 may have tendencies of unspecific amplification.